## Slide 1: Annotation Strategies & Machine Languages
Annotation Strategies, Introduction to Assembly Languages, Machine Language Specifications, The Hack Assembly Language

## Slide 2: Lecture Outline
Annotation Strategies
  The What and How of Annotating Texts
Introduction to Assembly Languages
  Producing Machine Code
Machine Language Specifications
  Operations, Addressing Modes, & Flow Control
The Hack Assembly Language
  Registers, A-Instructions, Symbols, & C-Instructions

## Slide 3: Annotating Your Texts
WHAT Intentionality of interacting with a text to enhance the reader's understanding of, recall of, and reaction to the text
WHY DO WE CARE?!

## Slide 4: Annotating Your Texts
HOW
  Highlighting, underlining or using [brackets] to note key points or ideas
WHY DO WE CARE?!
WHAT Intentionality of interacting with a text to enhance the reader's understanding of, recall of, and reaction to the text

## Slide 5: Annotating Your Texts
HOW
  Highlighting, underlining or using [brackets] to note key points or ideas
  Circling unfamiliar words or confusing parts of the text
WHY DO WE CARE?!
WHAT Intentionality of interacting with a text to enhance the reader's understanding of, recall of, and reaction to the text

## Slide 6: Annotating Your Texts
HOW
  Highlighting, underlining or using [brackets] to note key points or ideas
  Circling unfamiliar words or confusing parts of the text
  Paraphrasing or summarizing passages/chapters/sections
WHY DO WE CARE?!
WHAT Intentionality of interacting with a text to enhance the reader's understanding of, recall of, and reaction to the text

## Slide 7: Annotating Your Texts
HOW
  Highlighting, underlining or using [brackets] to note key points or ideas
  Circling unfamiliar words or confusing parts of the text
  Paraphrasing or summarizing passages/chapters/sections
  Commenting or reacting to the text 🤯
WHY DO WE CARE?!
WHAT Intentionality of interacting with a text to enhance the reader's understanding of, recall of, and reaction to the text

## Slide 8: Lecture Outline
Annotation Strategies
  The What and How of Annotating Texts
Introduction to Assembly Languages
  Producing Machine Code
Machine Language Specifications
  Operations, Addressing Modes, & Flow Control
The Hack Assembly Language
  Registers, A-Instructions, Symbols, & C-Instructions

## Slide 9: Project 4 Check-in
Which chips in Project 4 gave or are giving you the most trouble?
What skills or concepts have you struggled with most?
  E.g., certain aspects of HDL, rules of sequential logic, etc.
Any other questions, comments, or concerns about anything?

## Slide 10: Project 4 Resources
Take advantage of hints in Project 4 readings
Reach out to your classmates and course staff
  Post on the Ed discussion board
  Come to office hours today after lecture
Chapter 3
HDL Survival Guide

## Slide 11
Assembly languages are translated to binary by a compiler
Assembly languages were created to provide a more human-readable format for specifying machine code
Registers are temporary storage locations that are stored in memory
The Hack computer architecture supports multiplication and division
We’re lost…
Which of the following statements about assembly languages and machine code is TRUE?

## Slide 12: Revisiting The Von Neumann Architecture
COMPUTER
MEMORY
(This picture will get more detailed as we go!)
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
PROGRAM
DATA

## Slide 13: Machine Code
Instructions are stored in memory, so they must be able to be encoded in binary
When we refer to machine code, we are typically talking about this binary representation of code
Each instruction is a sequence of 0s and 1s
  Our computer / hardware specification is what gives meaning to each part of this sequence
  “Is this an add or subtract instruction? What are the inputs?”

## Slide 14: Storing the Program
(This picture will get more detailed as we go!)
COMPUTER
MEMORY
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2

## Slide 15: Assembly Languages
Writing code using 0s and 1s is tedious and error prone
Assembly languages are a human-readable format of binary instructions that a CPU runs
Each human-readable assembly instruction has a corresponding binary machine code instruction
  Example: addq reg1, reg2 == 0b1011000101010100
Assembly is often used as an intermediary between a high-level programming language and machine code

## Slide 16: Producing Machine Code
16
MEMORY
CPU
REGISTERS
CONTROL
PROGRAM
DATA
0101110011100110
1011000101010100
1110001011111100
...
Machine Code Instructions
while (i < 100) {
sum += arr[i];
i++;
}
Java
Load & Execute
Compile

## Slide 17: Producing Machine Code
17
MEMORY
CPU
REGISTERS
CONTROL
PROGRAM
DATA
0101110011100110
1011000101010100
1110001011111100
...
Machine Code Instructions
while (i < 100) {
sum += arr[i];
i++;
}
Java
movq $5, %rdx
addq %rsx, %rdx
movq %rdx, %rax
ret
Assembly Language
Load & Execute
Compile
Assemble

## Slide 18: Producing Machine Code
18
MEMORY
CPU
REGISTERS
CONTROL
PROGRAM
DATA
0101110011100110
1011000101010100
1110001011111100
...
Machine Code Instructions
while (i < 100) {
sum += arr[i];
i++;
}
Java
movq $5, %rdx
addq %rsx, %rdx
movq %rdx, %rax
ret
Assembly Language
Load & Execute
Compile
Assemble
Compile

## Slide 19: Lecture Outline
Annotation Strategies
  The What and How of Annotating Texts
Introduction to Assembly Languages
  Producing Machine Code
Machine Language Specifications
  Operations, Addressing Modes, & Flow Control
The Hack Assembly Language
  Registers, A-Instructions, Symbols, & C-Instructions

## Slide 20: Machine Language
Specification of the Hardware / Software interface
  What operations are supported?
  What do they operate on?
  How is the program controlled?
Usually in close correspondence with the hardware architecture
  Different specification for different hardware platforms
Cost and Performance Tradeoffs
  Silicon area and complexity
  Time to complete instruction
  Power consumption

## Slide 21: Machine Operations
Correspond to the operations supported by hardware:
  Arithmetic (+, –)
  Logical (And, Or)
  Flow Control (“go to instruction n”, “if (condition) then go to instruction n”)
Differences between machine languages:
  Instruction set richness (e.g., division? bulk copy?)
  Data types (e.g., word size, floating point)

## Slide 22: Registers
CPU typically has a small number of registers
  Very efficient to access
  Used for intermediate, short-term “scratch work”
Number and use of registers is a central part of any machine language
CPU
REGISTERS
22
CONTROL
0101110011100110
rsp
0101110011100110
reg2
0101110011100110
D

## Slide 23: Addressing Modes
Ways to specify operands or inputs in assembly
Some useful options:
  Register
    add reg1, reg2
  Direct Memory Access
    add reg1, Memory[200]
  Indirect Memory Access
    add reg1, Memory[reg2]
  Immediate
    add 100, reg2
Access the giant array (i.e., memory) at index 200
Register names

## Slide 24: Flow Control
COMPUTER
MEMORY
24
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
Which instruction should execute next?

## Slide 25: Flow Control
Usually, the CPU just executes machine instructions in a sequence
  Typically moves to the instruction with the next highest address
Sometimes we want to always “jump” to another location
  Example: At the end of an infinite loop
High Level Code (similar to Java) | Assembly Code
while (true) { reg1++; <more loop body> } <code after loop> | TOP: add 1, reg1 <more loop body> jmp TOP <code after loop>

## Slide 26: Flow Control
Usually, the CPU just executes machine instructions in a sequence
  Typically moves to the instruction with the next highest address
Sometimes we want to “jump” only if a condition is met
  Example: At the condition of an if statement
High Level Code (similar to Java) | Assembly Code
if (reg1 < reg2) { reg1++; } reg2++; | cmp reg1, reg2 jge SKIP add 1, reg1 SKIP: add 1, reg2

## Slide 27: Five-minute Break!
Feel free to stand up, stretch, use the restroom, drink some water, review your notes, or ask questions
We’ll be back at:
Research shows mid-lecture breaks reduce the decline of attention in the middle of lecture (Olmsted, 1999)
Olmsted III, John. “The Mid-Lecture Break: When Less Is More.” Journal of Chemical Education (1999). https://pubs.acs.org/doi/abs/10.1021/ed076p525.

## Slide 28: Lecture Outline
Annotation Strategies
  The What and How of Annotating Texts
Introduction to Assembly Languages
  Producing Machine Code
Machine Language Specifications
  Operations, Addressing Modes, & Flow Control
The Hack Assembly Language
  Registers, A-Instructions, Symbols, & C-Instructions

## Slide 29: The Hack Computer
The hardware you will build
  16-bit word size
  ROM: sequence of instructions
    ROM[0], RAM[1]…
  RAM: data sequence
    RAM[0], RAM[1]…
29
COMPUTER
MEMORY
KEYBOARD
CPU
REGISTERS
CONTROL
SCREEN
ROM
(16-bit Instructions, Read-Only)
1110001011111100
RAM
(16-bit Data,
Read / Write)
1100101010010101
PC
A/M
D

## Slide 30: The Hack Machine Language
Two types of instructions (16-bit)
  A-instructions load data
  C-instructions perform computations
Program: sequence of instructions
30
COMPUTER
MEMORY
KEYBOARD
CPU
REGISTERS
CONTROL
SCREEN
ROM
(16-bit Instructions, Read-Only)
1110001011111100
RAM
(16-bit Data, Read/Write)
1100101010010101
PC
A/M
D

## Slide 31: Hack: Control Flow
Startup
  Hack instructions loaded into ROM
  Reset signal initializes computer state (instruction 0)
Execution
  Usually, advance to next instruction each cycle
  On jump instruction, write a different address into the PC
0101110011100110
1011000101010100
1110001011111100
0101110101101110
0001011000111010
0010111011011001
0110111110101001
0001110010110110
ROM (Instructions)
0
1
2
3
4
5
6
7
...

## Slide 32: Program Counter (PC)
Keeps track of what instruction we are executing
  If the PC outputs 24, on the next clock cycle the computer runs the instruction at address 24 in the code segment
PC
load
in
16
out
16
inc
reset
Next cycle, replace counter value with in
(E.g., method calls)
Next cycle, add 1 to counter value
(E.g., normal operation)
Next cycle, set counter to 0
(E.g., program start)

## Slide 33: Hack: Registers
D Register: For storing Data
A Register: For storing data and Addressing memory
M “Register”: The 16-bit word in Memory currently being referenced by the address in A
REGISTERS
A
108
D
RAM
1100101010010101
...
106
107
108
109
110
...
M

## Slide 34: Hack: A-Instructions
Syntax:
value can either be:
  A non-negative decimal constant
  A symbol referring to a constant
Semantics:
  Stores value in the A register
@value

## Slide 35: Hack: A-Instructions
Symbolic Syntax
  Loads a value into the A register
Example:
Binary Syntax
0000000000010101
Family:
A-Instruction
Value:
Binary encoding of 21
@value
A Register
0
D Register
0
A Register
21
D Register
0
...
@21
...

## Slide 36: Hack: Symbols
Symbols are simply an alias for some address
  Only in the symbolic code—don’t turn into a binary instruction
  Assembler converts use of that symbol to its value instead
Example:
@3
D=0
(LOOP)
@21
D=1
@LOOP
...
00
01
02
03
04
0000000000000011
1110101010010000
0000000000010101
1110111111010000
0000000000000010
...
00
01
02
03
04
Assemble
LOOP = 02

## Slide 37: Hack: Built-In Symbols
Using ( ) defines a symbol in ROM / Instructions
Assembler knows a few built-in symbols in RAM / Data
R0, R1, ..., R15: Correspond to addresses at the very beginning of RAM (0, 1, …, 15)
  “Virtual registers,” Useful to store variables
SCREEN, KBD: Base of I/O Memory Maps
Example:
A Register
0
D Register
0
A Register
3
D Register
0
...
@R3
...

## Slide 38: Hack: C-Instructions
Syntax: (dest and jump optional)
  dest is a combination of destination registers:
  comp is a computation:
  jump is an unconditional or conditional jump:
Semantics:
  Computes value of comp
  Stores results in dest (if specified)
  If jump is specified and condition is true (by testing comp result), jump to instruction ROM[A]
dest = comp ; jump
M, D, MD, A, AM, AD, AMD
0, 1, -1, D, A, !D, !A, -D, -A, D+1, A+1, D-1, A-1, D+A, D-A, A-D, D&A, D|A, M, !M, -M, M+1, M-1, D+M, D-M, M-D, D&M, D|M
JGT, JEQ, JGE, JLT, JNE, JLE, JMP

## Slide 39: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Jump:
Condition for jumping
Dest:
Where to store result
Comp:
ALU Operation (a bit chooses between A and M)
Unused
Family:
C-Instruction

## Slide 40: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Jump:
Condition for jumping

## Slide 41: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Dest:
Where to store result

## Slide 42: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Comp:
ALU Operation (a bit chooses between A and M)
Chapter 4
Important: just pattern matching text!
Cannot have “1+M”

## Slide 43: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
00
01
A Register
55
D Register
56

## Slide 44: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
@R2
M=D
00
01
02
03
RAM
0
1
2
?
?
56
...
A Register
55
D Register
56
A Register
2
D Register
56

## Slide 45: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
@R2
M=D
@EXAMPLE
D;JGT
00
01
02
03
04
05
RAM
0
1
2
?
?
56
...
A Register
0
D Register
56
(Will jump to instruction 0, since D > 0)
A Register
2
D Register
56
A Register
55
D Register
56

## Slide 46: Project 5: Tools
Running a Test Script (recommended flow):
Quickly Iterating or Experimenting:
Max.asm
Max.hack
Assembler
CPUEmulator
The test scripts use the .hack files directly! Don’t let your .asm and .hack get out of sync!
Max.asm
CPUEmulator
Can still “run” the program, even without a script

## Slide 47: Tools Exercise: Run SimpleAdd.tst
In GitLab, a projects/lecture/ folder was added with a SimpleAdd.asm example
Open the assembly file SimpleAdd.asm. What does this program do?
Assemble SimpleAdd.asm using the Assembler to produce SimpleAdd.hack
Run SimpleAdd.tst using the CPUEmulator and verify there are no errors

## Slide 48: Lecture 7 Wrap-up
Project Reminders
  Project 3 grades released by Thursday (feedback on Gradescope)
  Project 4 due Thursday (4/21) at 11:59pm PDT
Project Scores and Late Days are updated weekly and can be viewed on Canvas under “Assignments”
Lecture 8 Reading: Final Memory Chip