## Slide 1: Study Environment & Boolean Logic
Study Environment Discussion, Boolean Logic and Functions, Foundational Logic Gates, Hardware Descriptive Languages

## Slide 2: Checking in on Project 1
Remember to double-check your submission on GitLab
  Navigate to GitLab, open tags, and verify that the associated commit includes your expected changes
How has Project 1 been coming along?
What questions do you have about Project 1?

## Slide 3: Lecture Outline
Study Environment Discussion
Boolean Logic and Functions
  Boolean Expressions, Circuit Diagrams, Truth Tables
  Boolean Function Synthesis Strategy
Hardware Descriptive Languages (HDL)
  HDL Syntax, And Gate Example
Foundational Logic Gates
  Nand, Not, And, Or, Xor, Mux, DMux Gates
  Example of Implementing an Xor Gate in HDL

## Slide 4: Study Environment Discussion
In groups of 3-4, discuss the following questions about study environments:
On a typical day, what does your study environment look like? Be specific!
What contributes to an effective study environment? Why?
  What changes can you make to introduce some of these factors?
What factors hinder a study environment from being effective? Why?
  What changes can you make to remove some of these factors?

## Slide 5: Ideal Study Environment
Free from distractions (phones, computer tabs, etc.)
Ensure your study environment is well organized and free from clutters
Peaceful and quiet, possibly with some background noise
  Listening to music may help depending on genre and the person
Add decoration that can be an inspiration to your study environment (e.g., plants, quotes, stickers)
Have your study material out ahead of time

## Slide 6: Lecture Outline
Study Environment Discussion
Boolean Logic and Functions
  Boolean Expressions, Circuit Diagrams, Truth Tables
  Boolean Function Synthesis Strategy
Hardware Descriptive Languages (HDL)
  HDL Syntax, And Gate Example
Foundational Logic Gates
  Nand, Not, And, Or, Xor, Mux, DMux Gates
  Example of Implementing an Xor Gate in HDL

## Slide 7: Boolean Values
A binary choice: True or False
Also known as a “low” signal (false, “off,” or 0) and a “high” signal (true, “on”, or 1)
“Off”
False
0
“On”
True
1

## Slide 8: Boolean Operations
Use logical operations to combine Boolean values
  Truth table: A table that lists every possible set of inputs and the corresponding output of the operation
  Operations correspond to physical hardware gates
Examples:
A | B | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | F
0 | 1
1 | 0

## Slide 9: Boolean Functions
Combinations of Boolean inputs resulting in single output
Multiple ways to specify a Boolean function:
  Boolean expression: F = (A AND B) OR (NOT(A) AND C)
  Circuit diagram with logic gates:
  Truth table:
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 10: Boolean Expression → Truth Table
We can build a truth table from an expression
  Evaluate the Boolean expression on all possible inputs
F(A, B, C) = (A AND B) OR (NOT(A) AND C)
A | B | C | F
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 11: Boolean Expression → Truth Table
We can build a truth table from an expression
  Evaluate the Boolean expression on all possible inputs
F(A, B, C) = (A AND B) OR (NOT(A) AND C)
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 12: Boolean Expression ← Truth Table
But can we do it in reverse?
F(A, B, C) = (A AND B) OR (NOT(A) AND C)
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
?

## Slide 13: Boolean Expression ← Truth Table
We can describe a single row with AND and NOT
A | B | C | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 14: Boolean Expression ← Truth Table
We can describe a single row with AND and NOT
A | B | C | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | NOT(A) AND NOT(B) AND C
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 15: Boolean Expression ← Truth Table
We can describe a single row with AND and NOT
A | B | C | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | NOT(A) AND NOT(B) AND C
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | NOT(A) AND B AND C
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 

## Slide 16: Boolean Expression ← Truth Table
We can describe a single row with AND and NOT
A | B | C | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | NOT(A) AND NOT(B) AND C
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | NOT(A) AND B AND C
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | A AND B AND NOT C
1 | 1 | 1 | 1 | 

## Slide 17: Boolean Expression ← Truth Table
We can describe a single row with AND and NOT
A | B | C | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | NOT(A) AND NOT(B) AND C
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | NOT(A) AND B AND C
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | A AND B AND NOT C
1 | 1 | 1 | 1 | A AND B AND C

## Slide 18: Boolean Expression ← Truth Table
Then, we can combine the rows using OR operations
F = NOT(A) AND NOT(B) AND C OR NOT(A) AND B AND C OR
A AND B AND NOT C OR A AND B AND C
A | B | C | F | 
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | NOT(A) AND NOT(B) AND C
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | NOT(A) AND B AND C
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | A AND B AND NOT C
1 | 1 | 1 | 1 | A AND B AND C

## Slide 19: Boolean Expression ← Truth Table
But can we do it in reverse?
  Yes, we can! The strategy we used is Boolean Function Synthesis
F(A, B, C) = (A AND B) OR (NOT(A) AND C)
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
✓

## Slide 20
The Boolean Function Synthesis strategy works on every truth table
In CSE 390B, we will be asking you to write Boolean expressions that must be simplified
The abstraction of voltages on a physical wire represents two values
A truth table lists every possible combination of inputs for a Boolean operation
We’re lost…
Which of the following statements is FALSE?

## Slide 21: Lecture Outline
Study Environment Discussion
Boolean Logic and Functions
  Boolean Expressions, Circuit Diagrams, Truth Tables
  Boolean Function Synthesis Strategy
Hardware Descriptive Languages (HDL)
  HDL Syntax, And Gate Example
Foundational Logic Gates
  Nand, Not, And, Or, Xor, Mux, DMux Gates
  Example of Implementing an Xor Gate in HDL

## Slide 22: Hardware Design Language (HDL)
HDL is a programming language to specify hardware components and how they’re connected
  Another way of describing a Boolean function!
Many Hardware Design Languages are used today
  E.g., VHDL, Verilog, SystemVerilog
  In this course, we’ll use a simple HDL language called “HDL”
Unlike Java, HDL is a declarative language. This means the following:
  The order of statements (lines of code) doesn’t matter
  We are describing a physical system

## Slide 23: Hardware Design Language (HDL)
Format of an HDL file
  File comment describes expected behavior
  IN names chip inputs, OUT names chip outputs
  PARTS specify the components (i.e., other gates) that implement the chip
/**
* And gate:
* out = 1 only if both a and b are 1
*/ CHIP And {
  IN a, b;
  OUT out;
  PARTS:
  // Put your code here:
  }

## Slide 24: Reusing Components
You can (and should!) use chips you have already implemented to implement subsequent chips
We give you one gate, Nand, to start out with
  Implication: The entire computer you will be building will be use Nand gates as its foundation
We also provide you with some chips you can use without implementing

## Slide 25: HDL Component Example: AND
The chip specification tells us the name of the input and output wires
Goal: Implement w1 AND w2
  HDL Syntax for using (being a client of the And gate): And(a=w1, b=w2, out=w3);
  Equivalent circuit diagram:
CHIP And {
  IN a, b;
  OUT out;
  ... }
a
b
out

## Slide 26: Multi-bit Buses in HDL
/**
* Bit-wise And of two 4-bit inputs
*/
CHIP And4 {
IN a[4], b[4];
OUT out[4];
PARTS:
And (a=a[0], b=b[0], out=out[0]);
And (a=a[1], b=b[1], out=out[1]);
And (a=a[2], b=b[2], out=out[2]);
And (a=a[3], b=b[3], out=out[3]);
}
It can be useful to manipulate groups of wires
  Called a “bus” of wires
HDL provides array like syntax for manipulating buses
  And4 chip example:

## Slide 27: HDL Resources
HDL will feel unfamiliar at first, and that’s okay
Resources for helping you navigate HDL linked under the Resources page on the course website
  HDL Survival guide
  Appendix A (HDL Spec)
  Chip Set Overview (to help you remember the inputs/outputs for various chips)
  Chapter readings

## Slide 28: Lecture Outline
Study Environment Discussion
Boolean Logic and Functions
  Boolean Expressions, Circuit Diagrams, Truth Tables
  Boolean Function Synthesis Strategy
Hardware Descriptive Languages (HDL)
  HDL Syntax, And Gate Example
Foundational Logic Gates
  Nand, Not, And, Or, Xor, Mux, DMux Gates
  Example of Implementing an Xor Gate in HDL

## Slide 29: The Foundational Building Block
It all starts with the NAND gate
NAND is short for “Not And”
  The same output as the AND gate, but every output bit is negated (flipped)
A | B | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 30: Building Gates From Nand
Recall the Boolean Function Synthesis strategy from today’s reading
  We saw how we can represent any truth table in terms of three gates: Not, And, Or
First, we can represent Not directly from Nand
  Not a = a Nand a
Then, we can represent And in terms of Not and Nand
  a And b = Not(a Nand b)
Represent Or in terms of Not and And
  Apply De Morgan’s Law
  a Or b = Not(Not(a) And Not(b)) [De Morgan’s Law]

## Slide 31: Making Decisions in Hardware
We write if/else statements in Java with the understanding that only one of the branches will run
  For example, in the following code, we expect to compute one of a & b or a | b (not both)
In hardware, the entire circuit is always executing
  We can’t “turn off” a part of a circuit based on a condition
  Instead, we create circuits for different conditions and choose which output based on a condition instead
if (c == 0) {
out = a & b;
} else {
out = a | b;
}

## Slide 32: Decisions in Hardware: Mux Gate
We can use a Multiplexer (Mux) gate to choose which singular input to output
  Takes three inputs: a, b, and sel
  If sel == 0, then out = a
  Otherwise, out = b
Mux Gate Truth Table:
Mux
a
b
sel
out
0
1
a | b | sel | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 33: Decisions in Hardware: DMux Gate
A Demultiplexer (DMux) gate passes one input to one of two outputs and 0 to the rest
  Takes two inputs: in and sel
  If sel == 0, then a = in and b = 0
  Otherwise, a = 0 and b = in
DMux Gate Truth Table:
0
DMux
a
b
sel
in
1
in | sel | a | b
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 34: Implementing an Xor Gate: Overview
/**
* Xor gate:
* out = not(a == b)
*/ CHIP Xor {
  IN a, b;
  OUT out;
  PARTS:
  // Put your code here:
  }
Let’s walk through an example of building a gate that you will work on in Project 2, the Xor gate
Together, we’ll implement the Xor gate

## Slide 35: Implementing an Xor Gate: Overview
Plan of action:
  Step 1: Create the logic operation’s truth table
  Step 2: Use truth table to generate a Boolean function using strategies we’ve learned, such as the Boolean Function Synthesis
  Step 3: Convert Boolean function to HDL
/**
* Xor gate:
* out = not(a == b)
*/ CHIP Xor {
  IN a, b;
  OUT out;
  PARTS:
  // Put your code here:
  }

## Slide 36: Implementing an Xor Gate: Step 1
Step 1: Create the truth table for Xor
  Interpret the specification: F = NOT(A == B)
A | B | F
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 37: Implementing an Xor Gate: Step 1
Step 1: Create the truth table for Xor
  Interpret the specification: F = NOT(A == B)
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 38: Implementing an Xor Gate: Step 2
Step 2: Use truth table to generate a Boolean function
  Let’s use the Boolean Function Synthesis strategy from the reading
  Row 2 = NOT(A) AND B
A | B | F | 
0 | 0 | 0 | (Row 1)
0 | 1 | 1 | (Row 2)
1 | 0 | 1 | (Row 3)
1 | 1 | 0 | (Row 4)

## Slide 39: Implementing an Xor Gate: Step 2
Step 2: Use truth table to generate a Boolean function
  Let’s use the Boolean Function Synthesis strategy from the reading
  Row 2 = NOT(A) AND B
  Row 3 = A AND NOT(B)
A | B | F | 
0 | 0 | 0 | (Row 1)
0 | 1 | 1 | (Row 2)
1 | 0 | 1 | (Row 3)
1 | 1 | 0 | (Row 4)

## Slide 40: Implementing an Xor Gate: Step 2
Step 2: Use truth table to generate a Boolean function
  Let’s use the Boolean Function Synthesis strategy from the reading
  Row 2 = NOT(A) AND B
  Row 3 = A AND NOT(B)
  F = ?
A | B | F | 
0 | 0 | 0 | (Row 1)
0 | 1 | 1 | (Row 2)
1 | 0 | 1 | (Row 3)
1 | 1 | 0 | (Row 4)

## Slide 41: What is the unsimplified Boolean expression result from performing Boolean function synthesis on F = A XOR B?
  (A AND NOT(B)) AND (NOT(A) AND B)
  (NOT(A) AND B) AND (A AND B)
  (A AND B) OR (NOT(A) AND NOT(B))
  (NOT(A) AND B) OR (A AND NOT(B))
  We’re lost…
A | B | F = A XOR B | 
0 | 0 | 0 | (Row 1)
0 | 1 | 1 | (Row 2)
1 | 0 | 1 | (Row 3)
1 | 1 | 0 | (Row 4)
  Row 2 = NOT(A) AND B
  Row 3 = A AND NOT(B)

## Slide 42: Implementing an Xor gate: Step 2
Step 2: Use truth table to generate a Boolean function
  Let’s use the Boolean function synthesis strategy from the reading
  Row 2 = NOT(A) AND B
  Row 3 = A AND NOT(B)
  F = Row 2 OR Row 3
  = (NOT(A) AND B) OR (A AND NOT(B))
A | B | F | 
0 | 0 | 0 | (Row 1)
0 | 1 | 1 | (Row 2)
1 | 0 | 1 | (Row 3)
1 | 1 | 0 | (Row 4)

## Slide 43: Implementing an Xor gate: Step 3
Now that we have a Boolean expression, we can implement the Xor gate in HDL
Optionally, it can help to express the Boolean expression as a circuit diagram
A XOR B = (NOT(A) AND B) OR (A AND NOT(B))

## Slide 44: Implementing an Xor gate: Step 3
Step 3: Convert Boolean function to HDL syntax
  A XOR B = (NOT(A) AND B) OR (A AND NOT(B))
  Assumes Not, And, and Or are already implemented
  Note the use of intermediary wires: nota, notb, x, and y
CHIP Xor {
  IN a, b;
  OUT out;
  PARTS:
  Not (in=a, out=nota);
  Not (in=b, out=notb);
  And (a=a, b=notb, out=x);
  And (a=nota, b=b, out=y);
  Or (a=x, b=y, out=out);
  }

## Slide 45: Project 2 Overview
Metacognitive Component: Study Skills Inventory
  Reflect on your academic behaviors, strategies, and practices
  You will be graded on completing the form, not your responses
  This activity is for your own benefit, and the more honest you are, the more beneficial it will be
Technical Component: GitLab Setup
  Will help prepare you for future CSE 390B projects
Estimated time to complete: 6-8 hours
Project 2 is released and will be due next Thursday (4/6) at 11:59pm

## Slide 46: Post-Lecture 2 Reminders
Project 1 due tonight (3/30) at 11:59pm
Project 2 (Study Skills Inventory & Boolean Logic) released today, due next Thursday (4/6) at 11:59pm
Anam has office hours after class in CSE2 121
First Student-TA meetings starting next week
  Your TA will be in contact with you about the first meeting