## Slide 1: Growth Mindset & Sequential Logic
Growth vs. Fixed Mindset, Introduction to Sequential Logic, Representing Time in Hardware, The Data Flip-Flop (DFF)

## Slide 2: Lecture Outline
Growth vs. Fixed Mindset
  Setting SMART Goals
Introduction to Sequential Logic
  The Problem of Combinational Logic
  Autopilot Control Circuit Example
Representing Time in Hardware
  Clock Signals and Units of Time in Hardware
The Data Flip-Flop (DFF)
  Implementation and Examples

## Slide 3: Growth vs. Fixed Mindset

## Slide 4: Setting SMART Goals
S – Be specific, simple and significant.
M – Make sure your goals are measurable. How many times within a week, month, the quarter do you want to do x goal?
A – Make sure your goals are achievable. Is your goal within your scope of control?
R – Be realistic and reasonable.
T – Be time-bound. When will you accomplish your goal?

## Slide 5: SMART Goals Group Discussion
SMART GOAL FRAMEWORK
S — Specific
M — Measurable
A — Achievable
R — Realistic
T — Timebound
Attending CSE 390B
office hours at least 5x this quarter (or once every other week)
SPRING QUARTER GOALS
What are skills, practices or habits that are not strengths YET?
SPHERE OF CONTROL
Getting a 4.0 in a course vs.
Attending course office hours

## Slide 6: Lecture Outline
Growth vs. Fixed Mindset
  Setting SMART Goals
Introduction to Sequential Logic
  The Problem of Combinational Logic
  Autopilot Control Circuit Example
Representing Time in Hardware
  Clock Signals and Units of Time in Hardware
The Data Flip-Flop (DFF)
  Implementation and Examples

## Slide 7: Why Consider Time Now?
Needed for our abstraction
  We need to talk about hardware maintaining state for memory
  We need vocabulary to talk about time
Needed for our implementation
  Physical implementations of chips cannot be instantaneous
  We need to account for physical delays in signal propagation

## Slide 8: The Problem with Combinational Logic
Consider the following circuit:
Let’s assume that a=0, b=1, and c=0
  The output should be 1
What’s the result if we change b=0 and c=1?
  The result should still be 1
  However, out is briefly 0 if we change c first

## Slide 9: Autopilot Control Circuit Example
Consider this autopilot control circuit:
  Either the pilot or copilot is flying at any time
  The pilot and copilot can separately request autopilot
  Only the person flying can request autopilot
Thanks to Justin Hsia for this example!
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)

## Slide 10: Autopilot Control Circuit Example
Consider this autopilot control circuit:
  Either the pilot or copilot is flying at any time
  The pilot and copilot can separately request autopilot
  Only the person flying can request autopilot
Let’s assume every logic gate takes 1ms to compute
  For example, if an input changes at t=4ms, the gate will only output the new result at t=5ms
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)
Thanks to Justin Hsia for this example!

## Slide 11: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 |  |  |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)

## Slide 12
Describe the behavior of the Autopilot Engaged (AE) output between 1ms to 6ms.
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | 1 |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)

## Slide 13: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 |  |  |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
?
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)

## Slide 14: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 |  |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)

## Slide 15: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | ? |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)

## Slide 16: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | 1 |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)

## Slide 17: Autopilot Control Circuit Example
Copilot Autopilot Request (CAR)
Pilot Autopilot Request (PAR)
Pilot Flying (PF)?
Autopilot Engaged (AE)
Critical Path
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | 1 | 1 | 1 | 1
B | 0 | 0 | 0 | 1 | 1 | 1
C | 1 | 1 | 0 | 0 | 0 | 0
AE | 1 | 1 | 1 | 0 | 1 | 1
0ms
1ms
2ms
3ms
4ms
5ms
6ms

## Slide 18: Combinational vs. Sequential Logic
So far, we have ignored “time” in our circuits
Our chips used combinational logic
  When given inputs, the chip computes its output instantaneously
  The output is a function of the current inputs, with no memory of previous events
Today, we’ll start exploring what happens when we consider time, ultimately building to sequential logic

## Slide 19: What is Sequential Logic?
Sequential logic incorporates time in hardware
Output depends on present value of its input signals and a sequence of past inputs
Sequential logic resolves the problem introduced with combinational logic
  Does so by adding a delay for the entire circuit before evaluating the result
  All the circuits will be evaluated between one clock cycle and the output will be evaluated at the end of the clock cycle

## Slide 20: Combinational vs. Sequential Abstraction
Clock Signal
0
1
in
out
t=1
t=2
t=3
t=4
t=0
in
out
Combinational: a function of the current inputs
Sequential: a function of previous inputs (has “memory”)
a
b
c
d
e
f(a)
f(b)
f(c)
f(d)
f(e)
a
b
c
d
e
f(a)
f(b)
f(c)
f(d)

## Slide 21: Lecture Outline
Growth vs. Fixed Mindset
  Setting SMART Goals
Introduction to Sequential Logic
  The Problem of Combinational Logic
  Autopilot Control Circuit Example
Representing Time in Hardware
  Clock Signals and Units of Time in Hardware
The Data Flip-Flop (DFF)
  Implementation and Examples

## Slide 22: Representing Time: Clock Signals
We physically represent time in hardware with a clock signal
  A clock signal changes its frequency at a set time rate
  Alternates between a low signal and a high signal of equal length
A cycle is a period of time between a low and high signal
  Represents one unit of time in hardware
  We can change how long a unit of time is by alternating the length of the low and high signals

## Slide 23: Physical Timekeeping
Hardware keeps track of time using an alternating signal
  Creates the idea of discrete time: state changes only occur in discrete intervals, right when signal alternates
Physical Time
Clock Signal
0
1

## Slide 24: Physical Timekeeping
Hardware keeps track of time using an alternating signal
  Creates the idea of discrete time: state changes only occur in discrete intervals, right when signal alternates
Physical Time
Clock Signal
0
1
Discrete Time Intervals
t=1
t=2
t=3
t=4
t=0

## Slide 25: Adding a Clock: Ideal
We want this behavior from a simple, combinational Not gate:
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0

## Slide 26: Adding a Clock: Reality
Combinational logic may be incorrect for a period immediately after inputs change
  Computation delays (logic gates) and propagation delays (wires)
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0
In the autopilot example, this arrow would represent the 3ms of uncertainty after inputs change

## Slide 27: Adding a Clock: Clock Cycles
Choose a clock cycle length slightly longer than the delays
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0
> 3ms

## Slide 28: Adding a Clock: Abstraction
If we use a long enough clock cycle, we can pretend that combinational chips (like Not) work instantly
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0

## Slide 29
Which of the following statements about sequential logic is FALSE?
We represent time with a clock signal that alternates between high and low signals
The DFF allows us to reuse outputs as inputs in a circuit
The outputs for a DFF at time t=2 is determined by the inputs at time t=3
Sequential logic is important because it addresses slight delays caused in circuit gates
We’re lost…

## Slide 30: Lecture Outline
Growth vs. Fixed Mindset
  Setting SMART Goals
Introduction to Sequential Logic
  The Problem of Combinational Logic
  Autopilot Control Circuit Example
Representing Time in Hardware
  Clock Signals and Units of Time in Hardware
The Data Flip-Flop (DFF)
  Implementation and Examples

## Slide 31: The Data Flip-Flop Gate
Simplest state-keeping component
  1-bit input, 1-bit output
  Wired to the clock signal
  Always outputs its previous input: out(t) = in(t-1)
Implementation: a gate that can flip between two stable states (remembering 0 vs. remembering 1)
  Gates with this behavior are “Data Flip Flops” (DFFs)

## Slide 32: Aside: Treating the DFF as a Primitive
Disclaimer: DFFs can be made from Nand gates exclusively
  But requires wiring them together in a “messy” loop that the hardware simulator can’t simulate and isn’t very educational
For simplicity, we will treat the DFF as a primitive in the projects
  Just like Nand, you can use the built-in implementation

## Slide 33: Data Flip-Flop (DFF) Behavior
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0

## Slide 34: Sequential Chips
A category of chips that utilize the clock signal, in addition to any combinational logic
Capable of:
  Maintaining state
  Optionally, acting on that state and the current inputs
    Can incorporate combinational logic as well
Constructed from:
  DFFs
  Combinational logic (which is entirely constructed from Nand)

## Slide 35: Sequential Chips
Combinational Logic
f
DFF
output
output(t) = f(state(t-1), input(t))
DFF
DFF
input

## Slide 36: D Flip-Flop: Time Series
DFF Specification:
out(t) = in(t-1)
in | 0 | 0 | 1 | 1 | 0 | 1 | 0 | ...
out | 0 | 0 | 0 | 1 | 1 | 0 | 1 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...
Example: out(t=3) = in(t=2)

## Slide 37: DFF Example 1: Specification
Example specification: out(t) = Xor(a(t-1), b(t-1))
Takes two inputs, a and b, and outputs the Xor of them
  Note that out at time t is determined by a and b at time t-1
  We will need to use a DFF
Exercise: Draw out the corresponding circuit diagram and HDL implementation

## Slide 38: DFF Example 1: Time Series
Example specification: out(t) = Xor(a(t-1), b(t-1))
Example: out(t=3) = Xor(a(t=2), b(t=2))
a | 0 | 0 | 1 | 1 | 1 | 0 | 0 | ...
b | 0 | 1 | 0 | 1 | 1 | 1 | 0 | ...
out | 0 | 0 | 1 | 1 | 0 | 0 | 1 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...

## Slide 39: DFF Example 1: Circuit Diagram & HDL
Example specification: out(t) = Xor(a(t-1), b(t-1))
Circuit diagram:
HDL:

## Slide 40: DFF Example 1: Circuit Diagram & HDL
Example specification: out(t) = Xor(a(t-1), b(t-1))
Circuit diagram:
HDL:
CHIP Example1 {
IN a, b;
OUT out;
PARTS:
Xor(a=a, b=b, out=xorout);
DFF(in=xorout, out=out);
}

## Slide 41: DFF Example 2: Specification
Example specification: out(t) = Xor(out(t-1), in(t-1))
Notice how the specification uses out(t-1) as an input for out(t)
  Implies the necessity of circular wiring, separated by a DFF
Exercise: Draw out the corresponding circuit diagram and HDL implementation

## Slide 42: DFF Example 2: Time Series
Example specification: out(t) = Xor(out(t-1), in(t-1))
Example: out(t=1) = Xor(in(t=0), out(t=0))
in | 0 | 0 | 1 | 1 | 1 | 0 | 0 | ...
out | 0 | 0 | 0 | 1 | 0 | 1 | 1 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...

## Slide 43: DFF Example 2: Circuit Diagram & HDL
Example specification: out(t) = Xor(out(t-1), in(t-1))
Circuit diagram:
HDL:

## Slide 44: DFF Example 2: Circuit Diagram & HDL
Example specification: out(t) = Xor(out(t-1), in(t-1))
Circuit diagram:
HDL:
CHIP Example2 {
IN in;
OUT out;
PARTS:
Xor(a=in, b=prevout, out=xorout);
DFF(in=xorout, out=prevout, out=out);
}

## Slide 45: DFF Example 3: Specification
Example specification: out(t) = And(Not(out(t-1)), in(t-1))
Exercise: Draw out the corresponding circuit diagram and HDL implementation

## Slide 46: DFF Example 3: Time Series
Example specification: out(t) = And(Not(out(t-1)), in(t-1))
Example: out(t=1) = And(Not(out(t=0)), in(t=0))
in | 1 | 1 | 0 | 1 | 1 | 0 | 0 | ...
out | 0 | 1 | 0 | 0 | 1 | 0 | 0 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...

## Slide 47: DFF Example 3: Circuit Diagram & HDL
Example specification: out(t) = And(Not(out(t-1)), in(t-1))
Circuit diagram:
HDL:

## Slide 48: DFF Example 3: Circuit Diagram & HDL
Example specification: out(t) = And(Not(out(t-1)), in(t-1))
Circuit diagram:
HDL:
CHIP Example3 {
IN in;
OUT out;
PARTS:
Not(in=prevout, out=notprevout);
And(a=in, b=notprevout, out=andout);
DFF(in=andout, out=prevout, out=out);
}

## Slide 49: Post-Lecture 5 Reminders
Topics this Thursday:
  Metacognitive Subject: Cornell Note-taking
  Technical Subject: Building Memory
Project 3 due this Thursday (4/13) at 11:59pm
Preston has office hours after class in CSE2 152
  Feel free to post your questions on the Ed board as well