## Slide 1: Exam Preparation & Building a Computer
Exam Preparation, Multiplication Implementation Exercise, Building a Computer, Hack CPU Interface

## Slide 2: Lecture Outline
Exam Preparation
  Study Strategies, Mock Exam Problem
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Building a Computer
  Architecture, Fetch and Execute Cycle
Hack CPU Interface
  Implementation and Operations

## Slide 3: Exams Preparation Discussion
What are some exam preparation strategies that you have found helpful?
What is one thing that is effective and ineffective about the way you study? Why?
How might you implement some of these effective strategies for change your exam preparation strategy for this quarter?

## Slide 4: Gearing Up For Exams
Make a Study Plan
  What key topics / concepts does your exam cover?
  How might your study guides look different for specific classes?
  What resources, materials, or people might you engage with?
Create a Schedule
  Avoid cramming
  Office hours, review sessions, study groups
  Reference your weekly time commitments & quarterly calendar
Test Yourself
  What are ways that you can test yourself?
  Replicate exam-like environments

## Slide 5: Project 6, Part I: Mock Exam Problem
Schedule a 30-minute session based on your group members' availability to complete one mock exam problem
Determine how you will connect with each other and where your session will be located
Mock exam problem groups:
  Please have one person from your group email Eric when you will meet for the mock exam problem by 4/27
Group Number | Group Members
Group 1 | Guadalupe, Rodas, Vicky
Group 2 | Delano, Richard
Group 3 | Tai, Yohannes, David
Group 4 | Nathaniel, Simon
Group 5 | Benito, Ty
Group 6 | Deya, Elainie
Group 7 | Alex, Matthew, Said
Group 8 | Kris, Binh

## Slide 6: Lecture Outline
Exam Preparation
  Study Strategies, Mock Exam Problem
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Building a Computer
  Architecture, Fetch and Execute Cycle
Hack CPU Interface
  Implementation and Operations

## Slide 7: Review: What is Binary?
A base-n number system is a system of number representation with n symbols
Decimal system is a base-10 number system
  Base-10 symbols: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9
  Increase a number by moving to the next greatest symbol
  Add another digit when we run out of symbols
Binary is a base-2 number system
  Often prefixed with 0b (e.g., 0b1101, 0b10)
  Base-2 symbols: 0, 1

## Slide 8: Hexadecimal
Base-16 number system
  Symbols: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Commonly used for referring to memory addresses
  Simple to convert between binary and hexadecimal
  Hexadecimal uses fewer digits to represent a value than binary
Uses the prefix 0x to indicate a number is written in hexadecimal
  32 is decimal, 0x32 is hexadecimal

## Slide 9: Number Representation Comparison
Decimal | Hexadecimal | Binary
0 | 0x0 | 0b0000
1 | 0x1 | 0b0001
2 | 0x2 | 0b0010
3 | 0x3 | 0b0011
4 | 0x4 | 0b0100
5 | 0x5 | 0b0101
6 | 0x6 | 0b0110
7 | 0x7 | 0b0111
8 | 0x8 | 0b1000
9 | 0x9 | 0b1001
10 | 0xA | 0b1010
11 | 0xB | 0b1011
12 | 0xC | 0b1100
13 | 0xD | 0b1101
14 | 0xE | 0b1110
15 | 0xF | 0b1111

## Slide 10: Binary and Hexadecimal Conversion
One-to-one correspondence between binary and hexadecimal
To convert from binary to hexadecimal, swap out binary bits digits for the corresponding hexadecimal digit (or vice versa)
Example: 0x3A is 0b0011_1010
  0x3 == 0b0011
  0xA == 0b1010

## Slide 11: Exercise: Implementing Multiplication
Write a program that multiplies R0 and R1 and stores the result in R2
  Remember we don’t have a multiply operation
  We will have to use add and loops to get the job done
Roadmap
  Start with pseudocode using if statements, loops, etc.
  Remove conditionals and loops by using jumps in pseudocode
  Convert pseudocode to assembly

## Slide 12: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly

## Slide 13: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly
Approach: add R0 to the result R1 times
Notes: Have students write out the pseudocode

## Slide 14: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly
Approach: add R0 to the result R1 times
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}

## Slide 15: Exercise: Implementing Multiplication
Remove loops from pseudocode
Use labels to notate important sections of the code
Attempt 1: What happens when R1 is 0? What should happen?
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}
START:
R2 = 0
LOOP:
R2 = R0 + R2
R1 = R1 - 1
IF R1 > 0 JMP LOOP
END:
INFINITE LOOP
Notes: What’s the problem with this? Will always execute the first two lines in loop at the beginning

## Slide 16: Exercise: Implementing Multiplication
Remove loops from pseudocode
Use labels to notate important sections of the code
Attempt 1: What happens when R1 is 0? What should happen?
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 17: Exercise: Implementing Multiplication
Convert to Hack Assembly
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP
(START)
@R2
M = 0
(LOOP)
(END)
5 | 2 | 
R0 | R1 | R2
D | A
Registers:
Memory (M):

## Slide 18: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP
5 | 2 | 
R0 | R1 | R2
D | A
Registers:
Memory (M):

## Slide 19: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP
5 | 2 | 
R0 | R1 | R2
D | A
Registers:
Memory (M):

## Slide 20: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
@R1
M = M - 1
@LOOP
0; JMP
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP
5 | 2 | 
R0 | R1 | R2
D | A
Registers:
Memory (M):

## Slide 21: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
@R1
M = M - 1
@LOOP
0; JMP
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP
5 | 2 | 
R0 | R1 | R2
D | A
Registers:
Memory (M):

## Slide 22: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
@R1
M = M – 1
@LOOP
0; JMP
(END)
@END
0; JMP
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP
5 | 2 | 
R0 | R1 | R2
D | A
Registers:
Memory (M):
Notes: Walk through an example at the end
Test with R0 = 5, R1 = 2

## Slide 23: Lecture Outline
Exam Preparation
  Study Strategies, Mock Exam Problem
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Building a Computer
  Architecture, Fetch and Execute Cycle
Hack CPU Interface
  Implementation and Operations

## Slide 24: Building a Computer
All your hardware efforts are about to pay off!
Perspective: BUILDING A COMPUTER
In Project 6, you will build Computer.hdl, the final, top-level chip in this course
  For all intents and purposes, a real computer
  Simplified, but organization very similar to your laptop
Project 7 onward, we will write software to make it useful

## Slide 25: Von Neumann Architecture
COMPUTER
MEMORY
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2

## Slide 26: Connecting the Computer: Buses
COMPUTER
MEMORY
INPUT
CPU
OUTPUT
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
Address Bus
Data Bus
CONTROL
REGISTERS
Control Bus
Notes: Control: Instructions, program counter, ALU output control bits (determine whether you should jump or not)
Address: A register communicates which item in item in memory to access, output of control is an address that tells us which instruction to execute
Question: Why two arrows for the address bus?
Data: D register that feeds into the ALU, the output of the ALU may be stored in the D register, to update data in memory

## Slide 27: Basic CPU Loop
Repeat forever:
  Fetch an instruction from the program memory
  Execute that instruction

## Slide 28: Fetching
Specify which instruction to read as the address input to our memory
Data output: actual bits of the instruction
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
MEMORY
Memory Input: Address
Memory Output: Data
Instruction
D=A;JMP
Instruction Address

## Slide 29: Executing
The instruction bits describe exactly “what to do”
  A-instruction or C-instruction?
  Which operation for the ALU?
  What memory address to read? To write?
  If I should jump after this instruction, and where?
Executing the instruction involves data of some kind
  Accessing registers
  Accessing memory

## Slide 30: Combining Fetch & Execute
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
MEMORY
Memory Input: Address
Memory Output: Data
Instruction
D=M;JMP
Instruction Address
Data Address (From instruction or register)
Data
245

## Slide 31: Combining Fetch & Execute
Could we implement with RAM16K.hdl?
  (Hint: Think about the I/O of RAM)
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
MEMORY
Memory Input: Address
Memory Output: Data
Instruction
D=M;JMP
Instruction Address
Data Address (From instruction or register)
Data
245

## Slide 32: Combining Fetch & Execute
Could we implement with RAM16K.hdl?
  No! Our memory chips only have one input and one output
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
MEMORY
Memory Input: Address
Memory Output: Data
Instruction
D=M;JMP
Instruction Address
Data Address (From instruction or register)
Data
245

## Slide 33: Solution 1: Handling Single Input / Output
Can use multiplexing to share a single input or output
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
MEMORY
Memory Input: Address
Memory Output: Data
Instruction, when fetching
Data, when executing
Instruction Address
Fetching vs. Executing
Data Address
Mux
DMux

## Slide 34: Solution 1: Fetching / Executing Separately
Need to store fetched instruction so it’s available during execution phase
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
MEMORY
Memory Input: Address
Memory Output: Data
Instruction, when fetching
Data, when executing
Instruction Address
Fetching vs. Executing
Fetching vs. Executing
Data Address
Mux
DMux
Register

## Slide 35: Solution 2: Separate Memory Units
Separate instruction memory and data memory into two different chips
  Each can be independently addressed, read from, written to
Pros:
  Simpler to implement
Cons:
  Fixed size of each partition, rather than flexible storage
  Two chips → redundant circuitry

## Slide 36: Lecture Outline
Exam Preparation
  Study Strategies, Mock Exam Problem
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Building a Computer
  Architecture, Fetch and Execute Cycle
Hack CPU Interface
  Implementation and Operations

## Slide 37: Hack CPU
COMPUTER
ROM
(Instructions)
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0
1
2
RAM
(Data)
100110010111
100011001111
000000000010
...
Data
0
1
2
addr of next instruction
data out
data in
instr
010111001110
101100010101
111000101111
...
Instructions

## Slide 38: Hack CPU Interface Inputs
inM: Value coming from memory
instruction: 16-bit instruction
reset: if 1, reset the program

## Slide 39: Hack CPU Interface Outputs
outM: value used to update memory if writeM is 1
writeM: if 1, update value in memory at addressM with outM
addressM: address to read from or write to in memory
pc: address of next instruction to be fetched from memory
Notes: Why is addressM only 15 bits? Because updating the A register, which can only store 15 bits for the value itself
Why is pc only 15 bits?
I thought we were using 16-bit words

## Slide 40: Hack CPU Implementation
pc
Diving beneath the hood… next lecture!

## Slide 41: Post-Lecture 9 Reminders
Project 5 due this Thursday (4/27) at 11:59pm
Midterm exam coming up on 5/4 during lecture time
Preston has office hours after class in CSE2 152
  Feel free to post your questions on the Ed board as well