## Slide 1: Hack CPU Logic & Midterm Practice
Hack CPU Logic, Midterm Topics Brainstorm and Practice Problems, Project 6 Overview

## Slide 2: Lecture Outline
Hack CPU Logic
  Implementation and Operations
CSE 390B Midterm Practice Problems
  Midterm Topics Brainstorming
Project 6 Overview
  Project Tips and Workflow

## Slide 3: Hack CPU Interface Inputs
inM: Value coming from memory
instruction: 16-bit instruction
reset: if 1, reset the program

## Slide 4: Hack CPU Interface Outputs
outM: value used to update memory if writeM is 1
writeM: if 1, update value in memory at addressM with outM
addressM: address to read from or write to in memory
pc: address of next instruction to be fetched from memory

## Slide 5: Hack CPU Implementation
pc

## Slide 6: Hack CPU Implementation
(each "C" symbol represents a control bit)

## Slide 7: CPU Operation: Instruction Handling
(each "C" symbol represents a control bit)

## Slide 8: CPU Operation: Instruction Handling
0000000000000101
A-instruction
@5

## Slide 9: CPU Operation: Instruction Handling
0000000000000101
A-instruction
@5
CPU handling of an A-instruction:
Decodes the instruction into:
  op-code
  15-bit value
Stores the value in the A-register
Outputs the value (not shown in this diagram)

## Slide 10: CPU Operation: Instruction Handling
C-instruction
D=D+1;JMP
1110011111010111

## Slide 11: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Jump:
Condition for jumping
Dest:
Where to store result
Comp:
ALU Operation (a bit chooses between A and M)
Unused
Family:
C-Instruction

## Slide 12: CPU Operation: Instruction Handling
C-instruction
D=D+1;JMP
1110011111010111
CPU handling of a C-instruction:
Decodes the instruction bits into:
  Op-code
  ALU control bits
  Destination load bits
  Jump bits
Routes these bits to their chip-part destinations
The chip-parts (most notably, the ALU) execute the instruction

## Slide 13: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Comp:
ALU Operation (a bit chooses between A and M)
Chapter 4
Important: just pattern matching text!
Cannot have “1+M”

## Slide 14: CPU Operation: Handling C-Instructions
1110011111010111
011111
writeM
1…01
1…10
ALU data inputs:
Input 1: from the D-register
Input 2: from either:
      A-register, or
      data memory
ALU control inputs:
Control bits (from the instruction)

## Slide 15: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Dest:
Where to store result

## Slide 16: CPU Operation: Handling C-Instructions
1110011111010111
writeM
1…01
1…10
0…11
0
1
0
ALU data output:
Result of ALU calculation
Fed simultaneously to: D-register, A-register, data memory
Which destination actually commits to the ALU output is determined by the instruction’s destination bits
011111

## Slide 17: CPU Operation: Handling C-Instructions
ALU control outputs:
Is the output negative?
Is the output zero?
1110011111010111
writeM
1…01
0…11
1…10
011111

## Slide 18: CPU Operation: Control
pc

## Slide 19: CPU Operation: Control

## Slide 20: CPU Operation: Control
PC operation (abstraction)
Outputs the address of the next instruction:
Restart: PC = 0
No jump: PC++
Go to: PC = A
Conditional go to: if (condition) PC = A
    else PC ++
load
16
1
16
pc
Address of next instruction

## Slide 21: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Jump:
Condition for jumping

## Slide 22: CPU Operation: Control
load
16
1
16
Address of next instruction
pc
PC operation (implementation)
if (reset==1) PC = 0
else
// In the course of handling the current instruction:
load = f (jump bits, ALU control outputs)
if (load == 1) PC = A // jump
else PC++ // next instruction
111 a c c c c c c d d d j j j

## Slide 23: Hack CPU Implementation: That’s It!

## Slide 24: Lecture Outline
Hack CPU Logic
  Implementation and Operations
CSE 390B Midterm Practice Problems
  Midterm Topics Brainstorming
Project 6 Overview
  Project Tips and Workflow

## Slide 25: CSE 390B Midterm Topics Brainstorm
Based on what we have covered thus far in class, what are topics, concepts, questions that you might expect to show up on next week’s CSE 390B midterm?

## Slide 26: CSE 390B Review Session
Practice Problems
  Circuit Design, Writing Assembly, Tracing Assembly
For each problem:
  Step 1: Spend 10 minutes working on the problem individually
  Step 2: Spend 10 minutes discussing the problem as a group, describing tips, approaches, and test-taking strategies
  Step 3: As a group, present to the class your discussion from step 2 and lead the class in working through the problem

## Slide 27: Review Session Debrief
Based on your experience with this exercise, how does it inform how you approach your studying?
What resources can you utilize to help you deepen your understanding?

## Slide 28: Previous CSE 390B Midterms
Four midterms from previous quarters
  20sp midterm likely more difficult than midterm this quarter
  Midterms from 21wi, 21sp, 22wi, 22sp, 22au are more like what this quarter’s midterm will look like
20sp midterm recommended to become familiar with problem types
21wi, 21sp, 22wi, 22sp, and 22au midterms recommended for practicing a timed exam
  Set a timer for 60 minutes and take the exam in its entirety
  Helps practice time management and simulate exam environment

## Slide 29: Lecture Outline
Hack CPU Logic
  Implementation and Operations
CSE 390B Midterm Practice Problems
  Midterm Topics Brainstorming
Project 6 Overview
  Project Tips and Workflow

## Slide 30: Project 6: Overview
Part I: Mock Exam Problem
Part II: Building a Computer
  LoadAReg.hdl, LoadDReg.hdl (Easier)
  JumpLogic.hdl (Medium)
  CPU.hdl (Harder)
  Computer.hdl (Easier)
Part III: Project 6 Reflection

## Slide 31: Project 6, Part I: Mock Exam Problem
Your group will meet for a 30-minute session to do one mock exam problem
  Your group’s mock exam problem will be emailed right before your session
Your 30-minute session will include:
  Set up: 5 minutes
  Mock Exam Problem: 10 minutes
  Debrief & Reflection: 15 minutes
Part I task: Submit the completed mock exam problem and complete the reflection questions

## Slide 32: Project 6 Tips
CPU.hdl: We provide an overview diagram, but there are details to fill in, especially control
  Draw your own detailed diagram first
  Handling jumps will require a lot of logic—sketch out the cases
  Textbook chapter 4 and 5 helpful for Project 6
Multi-Bit Buses: MSB to the left, LSB to the right
  Important to keep in mind when taking apart the instruction
Debugging: Consult .out and .cmp files to debug, then look at internal wires in simulator
  See also the “Debugging tips” section of the specification

## Slide 33: Lecture 10 Reminders
Project 5 due tonight (2/2) at 11:59pm
CSE 390B midterm next Thursday (2/9) during lecture
Project 6 (Mock Exam Problem & Building a Computer) released today, due in two Thursdays (2/16) at 11:59pm
Eric has office hours after class in CSE2 153
  Feel free to post your questions on the Ed board as well