## Slide 1: Final Project Reflection & Computer Networks
Final Project Reflection, Overview of Computer Networks

## Slide 2: Lecture Outline
Final Project Reflection
  E-Portfolio Details and Topics Brainstorming
E-Portfolio Workshop
  Reflection Work Session and Feedback
Overview of Computer Networks
  Connecting Computers to The Internet

## Slide 3: Final Project E-Portfolio Overview
You will create an E-Portfolio that is geared toward a new Allen School student
Your E-Portfolio is a culminating project in having you reflect on the metacognitive skills you’ve learned and providing advice for entering the program
During our final class, you will give a short presentation on your E-Portfolio

## Slide 4: Final Project Due Dates
Part I: E-Portfolio Outline
  Due next Wednesday (3/6) at 11:59pm
Part II: Final E-Portfolio
  Due Thursday of finals week (3/14) at 2:00pm
Part III: E-Portfolio Presentations
  During the scheduled CSE 390B final
  CSE 390B Final Time: Thursday, 3/14 from 2:30-4:20pm
  CSE 390B Final Location: CSE2 271 (same as usual classroom)

## Slide 5: Reflection on Metacognitive Skills
Individually first, take some time to reflect on the following questions, and then discuss in groups:
Which two metacognitive topics would you consider including in your E-Portfolio and why?
  Reflect on which ones you’ve grown the most in, have impacted you the most, were most challenging to grow in, etc.
What are some examples of yourself demonstrating those two metacognitive skills?
  Please be specific here! Aim to share these skills as if you are telling a story and showing concrete applications of these skills

## Slide 6: Reflection on a Technical Skill
Individually first, take some time to reflect on the following questions, and then discuss in groups:
What technical topic from CSE 390B would you consider including in your E-Portfolio and why?
  Reflect on technical skills that helped connect the dots, were most interesting to you, most challenging for you to grasp, etc.
What is the impact of having knowledge of that technical skill? In other words, why is that technical skill useful?
  Please be specific here as well — think about how this technical skill would be useful in an academic or personal setting

## Slide 7: Lecture Outline
Final Project Reflection
  E-Portfolio Details and Topics Brainstorming
E-Portfolio Workshop
  Reflection Work Session and Feedback
Overview of Computer Networks
  Connecting Computers to The Internet

## Slide 8: E-Portfolio Workshop
Individually, spend 15-20 minutes completing the following steps:
  Aim to finalize the two metacognitive skills, two examples of you applying them, and one technical skill you plan on reflecting on
  Begin drafting your reflection on a document (should be in paragraph form in final e-portfolio, but bullet points ok for now)
Goal by the end of class today is to receive feedback on your reflections and complete part one of the final project, the E-Portfolio outline

## Slide 9: E-Portfolio Workshop
Now, get into groups and complete the following:
  One group member presents on their reflection so far
  Each group member listening should provide one question, comment, constructive feedback, or complement to the presenter
  Repeat until everyone has had a chance to present

## Slide 10: Lecture Outline
Final Project Reflection
  E-Portfolio Details and Topics Brainstorming
E-Portfolio Workshop
  Reflection Work Session and Feedback
Overview of Computer Networks
  Connecting Computers to The Internet

## Slide 11: Overview of Computer Networks
We will go over an overview of networks
  Take CSE 333 (Systems Programming), CSE 461 (Computer Networks), and CSE 452 (Distributed Systems) to learn more
Our focus:
  Brief intro to what connecting to the internet looks like under the hood
  What that connection might look like implemented in our computer

## Slide 12: How Do Computer Networks Work?
How do you think we connect computers in different physical locations?
What modes of communication do you think computers use to network with one another?

## Slide 13: Networks = Really, Really Long Wires
At a fundamental level, there’s nothing magic about the Internet—it’s the same concepts we used to build our CPU, just with longer wires
  Still 1s and 0s, still just combinational + sequential logic
13
Combinational & Sequential Logic
Computer.hdl
Combinational & Sequential Logic
Computer.hdl
≈

## Slide 14: Thinking about the Network: Layers
To manage the complexity, we think about the network in layers
It’s all 0s and 1s, but each layer is a different way of “framing” or thinking about those 0s and 1s
  Each layer zooms out a little more
Application Layer
Physical Layer
0
0
1
0
1
1
0
0
1
1
0
0
webpage (.html)
meme (.png)
dest address
source address
data
Data Link Layer
Other layers exist between here; out of 390B scope

## Slide 15: Application Layer
Conceptually the “top” layer: looking at internet traffic as direct communication between applications
Common use: HTTP (HyperText Transfer Protocol)
  Your browser sends an HTTP request to a server
  The server sends back an HTTP response with data attached
I found it:
15
I would like to load: http://instagram.com/dog/latest_story.png
Browser
Server

## Slide 16: Application Layer
I would like to load: http://instagram.com/dog/latest_story.png
Conceptually the “top” layer: looking at internet traffic as direct communication between applications
Common use: HTTP (HyperText Transfer Protocol)
  Your browser sends an HTTP request to a server
  The server sends back an HTTP response with data attached
I found it:
16
Browser
Server
dest address
source address
data
dest address
source address
data
dest address
source address
data
dest address
source address
data
Data Link Layer

## Slide 17: Data Link Layer
A computer network is simply multiple computers connected by a single wire
Why is it better to send smaller chunks of data?
17
computer
00:1d:4f:47
computer
4c:44:1e:8f
computer
de:ad:be:ef
dest address
4c:44:1e:8f
source address
24:48:96:12
data
router
(also a computer)
24:48:96:12
Gets data from Internet (beyond scope of 390B)

## Slide 18: Data Link Layer
Every computer will “hear” the message
How do the other computers know to ignore an incoming packet of data?
18
computer
00:1d:4f:47
computer
4c:44:1e:8f
computer
de:ad:be:ef
dest address
4c:44:1e:8f
source address
24:48:96:12
data
router
(also a computer)
24:48:96:12
Gets data from Internet (beyond scope of 390B)

## Slide 19: NIC (Network Interface Card)
We don’t want the CPU to waste time always listening to the network wire, especially when it’s not even the destination computer
Solution: the NIC—a new piece of the computer dedicated to dealing with the network wire
  Listens to the network wire until it hears a destination address, checks if it matches this computer, and only sends to CPU if so
computer
00:1d:4f:47
dest address
4c:44:1e:8f
source address
24:48:96:12
data
NIC

## Slide 20: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)

## Slide 21: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend Mux.hdl!

## Slide 22: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!

## Slide 23: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl

## Slide 24: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl!

## Slide 25: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl!
Selectable read/write? Sounds like RAM.hdl!

## Slide 26: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl!
Selectable read/write? Sounds like RAM.hdl!

## Slide 27: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl!
Bitwise/multi-bit operations? Sounds like And16.hdl!
Selectable read/write? Sounds like RAM.hdl!
Bitwise/multi-bit operations? Sounds like And16.hdl!

## Slide 28: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Bitwise/multi-bit operations? Sounds like And16.hdl!
Constantly incrementing an address? Sounds like PC.hdl!
Selectable read/write? Sounds like RAM.hdl!
Bitwise/multi-bit operations? Sounds like And16.hdl!

## Slide 29: Connecting NIC to Memory
The keyboard and screen communicated with the CPU via memory maps—agreed-upon regions of RAM that can be read/written by the hardware of the devices themselves
The NIC could be implemented in the same way
  Every time the right address is detected, copy the following data into part of RAM where the CPU can retrieve it once it gets a chance
CPU
NIC
Screen
Keyboard

## Slide 30: Takeaways: Computer Networks
The network is fundamentally the same hardware we’ve been looking at
Its incredible power comes from scale: how much data and how many computers it connects
  To manage this complexity, we think of it in layers
Interfacing with the network can be done with specialized hardware
  This frees the CPU from monitoring constantly
  Access data only when needed

## Slide 31: Lecture 18 Reminders
Project Reminders
  Project 7, Part II (Professor Meeting Report) due tonight (3/1) at 11:59pm
  Project 8 (Debugging & Implementing a Compiler) due next Wednesday (3/6) at 11:59pm
  Final Project, Part I (E-Portfolio Outline) due next Wednesday (3/6) at 11:59pm
Eric has office hours after class in CSE2 153
  Feel free to post your questions on the Ed board as well
Lecture next week will be led by your TAs!