## Slide 1: Cornell Note-taking & Machine Language
Cornell Note-taking Method, Machine Languages, Control Flow of Computer Instructions, The Hack Assembly Language

## Slide 2: Lecture Outline
Cornell Note-taking Method
  System for Taking, Organizing, and Reviewing Notes
Machine Languages
  Assembly Languages, Producing Machine Code
Control Flow of Computer Instructions
  Jumps in Assembly, The Program Counter
The Hack Assembly Language
  Registers, A-Instructions, Symbols, & C-Instructions

## Slide 3: Recap: Bloom’s Taxonomy
Remembering
Understanding
Applying
Analyzing
Creating
Evaluating
Recalling facts and basic concepts
Explaining ideas or concepts
Using information in a new (or similar) situation
Drawing connections among ideas
Justifying your decisions or position
Producing something new

## Slide 4: Cornell Note Taking Method
Notes
Questions
Summary
Main Topic
  Sub point
  definition
  example **
Object-Oriented Programming
  Encapsulates the data and the operations for a given data type
  Provides abstractions - you don’t need to know how a car is implemented in order to use it
  Extensibility - easier to add new data types
Functional Programming
  Extensibility - easier to add new operations
Compose a question that corresponds to the notes you took
In what ways is object-oriented programming more extensible than functional programming?
Object-oriented programming and functional programming are two types of programming paradigms…

## Slide 5: Cornell Note Taking Method
Notes
Questions
Summary
Main Topic
  Sub point
  definition
  example **
Object-Oriented Programming
  Encapsulates the data and the operations for a given data type
  Provides abstractions - you don’t need to know how a car is implemented in order to use it
  Extensibility - easier to add new data types
Functional Programming
  Extensibility - easier to add new operations
Compose a question that corresponds to the notes you took
In what ways is object-oriented programming more extensible than functional programming?
Object-oriented programming and functional programming are two types of programming paradigms…

## Slide 6: Applying the Cornell Note-Taking Method
Try it during today’s technical lecture!
You will have a chance to reflect on your experience taking Cornell Notes in Project 4

## Slide 7: Lecture Outline
Cornell Note-taking Method
  System for Taking, Organizing, and Reviewing Notes
Machine Languages
  Assembly Languages, Producing Machine Code
Control Flow of Computer Instructions
  Jumps in Assembly, The Program Counter
The Hack Assembly Language
  Registers, A-Instructions, Symbols, & C-Instructions

## Slide 8: Revisiting The Von Neumann Architecture
COMPUTER
MEMORY
(This picture will get more detailed as we go!)
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
PROGRAM
DATA

## Slide 9: Machine Code
Instructions are stored in memory, so they must be able to be encoded in binary
When we refer to machine code, we are typically talking about this binary representation of code
Each instruction is a sequence of 0s and 1s
  Our computer / hardware specification is what gives meaning to each part of this sequence
  “Is this an add or subtract instruction? What are the inputs?”

## Slide 10: Storing the Program
(This picture will get more detailed as we go!)
COMPUTER
MEMORY
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2

## Slide 11: Assembly Languages
Writing code using 0s and 1s is tedious and error prone
Assembly languages are a human-readable format of binary instructions that a CPU runs
Each human-readable assembly instruction has a corresponding binary machine code instruction
  Example: addq reg1, reg2 == 0b1011000101010100
Assembly is often used as an intermediary between a high-level programming language and machine code

## Slide 12: Producing Machine Code
12
MEMORY
CPU
REGISTERS
CONTROL
PROGRAM
DATA
0101110011100110
1011000101010100
1110001011111100
...
Machine Code Instructions
while (i < 100) {
sum += arr[i];
i++;
}
Java
Load & Execute
Compile

## Slide 13: Producing Machine Code
13
MEMORY
CPU
REGISTERS
CONTROL
PROGRAM
DATA
0101110011100110
1011000101010100
1110001011111100
...
Machine Code Instructions
while (i < 100) {
sum += arr[i];
i++;
}
Java
movq $5, %rdx
addq %rsx, %rdx
movq %rdx, %rax
ret
Assembly Language
Load & Execute
Compile
Assemble

## Slide 14: Producing Machine Code
14
MEMORY
CPU
REGISTERS
CONTROL
PROGRAM
DATA
0101110011100110
1011000101010100
1110001011111100
...
Machine Code Instructions
while (i < 100) {
sum += arr[i];
i++;
}
Java
movq $5, %rdx
addq %rsx, %rdx
movq %rdx, %rax
ret
Assembly Language
Load & Execute
Compile
Assemble
Compile

## Slide 15: Machine Language
Specification of the Hardware / Software interface
  What operations are supported?
  What do they operate on?
  How is the program controlled?
Usually in close correspondence with the hardware architecture
  Different specification for different hardware platforms
Cost and Performance Tradeoffs
  Silicon area and complexity
  Time to complete instruction
  Power consumption

## Slide 16: Machine Operations
Correspond to the operations supported by hardware:
  Arithmetic (+, –)
  Logical (And, Or)
  Flow Control (“go to instruction n”, “if (condition) then go to instruction n”)
Differences between machine languages:
  Instruction set richness (e.g., division? bulk copy?)
  Data types (e.g., word size, floating point)

## Slide 17: Registers
CPU typically has a small number of registers
  Very efficient to access
  Used for intermediate, short-term “scratch work”
Number and use of registers is a central part of any machine language
CPU
REGISTERS
17
CONTROL
0101110011100110
rsp
0101110011100110
reg2
0101110011100110
D

## Slide 18: Addressing Modes
“What locations can I specify in my assembly code?”
Some useful options:
  Register
    add reg1, reg2
  Direct Memory Access
    add reg1, Memory[200]
  Indirect Memory Access
    add reg1, Memory[reg2]
  Immediate
    add 100, reg2
Access the giant array (i.e., memory) at index 200
Register names

## Slide 19: Lecture Outline
Cornell Note-taking Method
  System for Taking, Organizing, and Reviewing Notes
Machine Languages
  Assembly Languages, Producing Machine Code
Control Flow of Computer Instructions
  Jumps in Assembly, The Program Counter
The Hack Assembly Language
  Registers, A-Instructions, Symbols, & C-Instructions

## Slide 20: Flow Control
COMPUTER
MEMORY
20
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
Which instruction should execute next?

## Slide 21: Flow Control: Unconditional Jumps
Usually, the CPU just executes machine instructions in a sequence
  Typically moves to the instruction with the next highest address
Sometimes we want to always “jump” to another location
  Example: At the end of an infinite loop
High Level Code (similar to Java) | Assembly Code
while (true) { reg1++; <more loop body> } <code after loop> | TOP: add 1, reg1 <more loop body> jmp TOP <code after loop>

## Slide 22: Flow Control: Conditional Jumps
Usually, the CPU just executes machine instructions in a sequence
  Typically moves to the instruction with the next highest address
Sometimes we want to “jump” only if a condition is met
  Example: At the condition of an if statement
High Level Code (similar to Java) | Assembly Code
if (reg1 < reg2) { reg1++; } reg2++; | cmp reg1, reg2 jge SKIP add 1, reg1 SKIP: add 1, reg2

## Slide 23: Program Counter (PC)
Memory is used to store data as well as code
Instructions and operations are stored at different addresses in memory
Program Counter in the CPU keeps track of which address contains the instruction that should be executed next
COMPUTER
MEMORY
Data and instructions
CPU
Program Counter (which line of code should I execute)

## Slide 24: Program Counter (PC)
Keeps track of what instruction we are executing
  If the PC outputs 24, on the next clock cycle the computer runs the instruction at address 24 in the code segment
Next cycle, replace counter value with in
(E.g., method calls)
Next cycle, add 1 to counter value
(E.g., normal operation)
Next cycle, set counter to 0
(E.g., program start)
PC
load
in
16
out
16
inc
reset

## Slide 25: Program Counter (PC)
Keeps track of what instruction we are executing
  If the PC outputs 24, on the next clock cycle the computer runs the instruction at address 24 in the code segment
Program counter specification:
if (reset[t] == 1) out[t+1] = 0
else if (load[t] == 1) out[t+1] = in[t]
else if (inc[t] == 1) out[t+1] = out[t] + 1
else out[t+1] = out[t]
PC
load
in
16
out
16
inc
reset

## Slide 26: Lecture Outline
Cornell Note-taking Method
  System for Taking, Organizing, and Reviewing Notes
Machine Languages
  Assembly Languages, Producing Machine Code
Control Flow of Computer Instructions
  Jumps in Assembly, The Program Counter
The Hack Assembly Language
  Registers, A-Instructions, Symbols, & C-Instructions

## Slide 27: The Hack Computer
The hardware you will build
  16-bit word size
  ROM: sequence of instructions
    ROM[0], RAM[1]…
  RAM: data sequence
    RAM[0], RAM[1]…
27
COMPUTER
MEMORY
KEYBOARD
CPU
REGISTERS
CONTROL
SCREEN
ROM
(16-bit Instructions, Read-Only)
1110001011111100
RAM
(16-bit Data, Read/Write)
1100101010010101
PC
A/M
D

## Slide 28: The Hack Machine Language
Two types of instructions (16-bit)
  A-instructions load data
  C-instructions perform computations
Program: sequence of instructions
28
COMPUTER
MEMORY
KEYBOARD
CPU
REGISTERS
CONTROL
SCREEN
ROM
(16-bit Instructions, Read-Only)
1110001011111100
RAM
(16-bit Data, Read/Write)
1100101010010101
PC
A/M
D

## Slide 29: Hack: Control Flow
Startup
  Hack instructions loaded into ROM
  Reset signal initializes computer state (instruction 0)
Execution
  Usually, advance to next instruction each cycle
  On jump instruction, write a different address into the PC
0101110011100110
1011000101010100
1110001011111100
0101110101101110
0001011000111010
0010111011011001
0110111110101001
0001110010110110
ROM (Instructions)
0
1
2
3
4
5
6
7
...

## Slide 30: Hack: Registers
D Register: For storing Data
A Register: For storing data and Addressing memory
M “Register”: The 16-bit word in Memory currently being referenced by the address in A
REGISTERS
A
108
D
RAM
1100101010010101
...
106
107
108
109
110
...
M

## Slide 31: Hack: A-Instructions
Syntax:
value can either be:
  A non-negative decimal constant
  A symbol referring to a constant
Semantics:
  Stores value in the A register
@value

## Slide 32: Hack: A-Instructions
Symbolic Syntax
  Loads a value into the A register
Example:
Binary Syntax
0000000000010101
Family:
A-Instruction
Value:
Binary encoding of 21
@value
A Register
0
D Register
0
A Register
21
D Register
0
...
@21
...

## Slide 33: Hack: Symbols
Symbols are simply an alias for some address
  Only in the symbolic code—don’t turn into a binary instruction
  Assembler converts use of that symbol to its value instead
Example:
@3
D=0
(LOOP)
@21
D=1
@LOOP
...
00
01
02
03
04
0000000000000011
1110101010010000
0000000000010101
1110111111010000
0000000000000010
...
00
01
02
03
04
Assemble
LOOP = 02

## Slide 34: Hack: Built-In Symbols
Using ( ) defines a symbol in ROM / Instructions
Assembler knows a few built-in symbols in RAM / Data
R0, R1, ..., R15: Correspond to addresses at the very beginning of RAM (0, 1, …, 15)
  “Virtual registers,” Useful to store variables
SCREEN, KBD: Base of I/O Memory Maps
Example:
A Register
0
D Register
0
A Register
3
D Register
0
...
@R3
...

## Slide 35: Hack: C-Instructions
Syntax: (dest and jump optional)
  dest is a combination of destination registers:
  comp is a computation:
  jump is an unconditional or conditional jump:
Semantics:
  Computes value of comp
  Stores results in dest (if specified)
  If jump is specified and condition is true (by testing comp result), jump to instruction ROM[A]
dest = comp ; jump
M, D, MD, A, AM, AD, AMD
0, 1, -1, D, A, !D, !A, -D, -A, D+1, A+1, D-1, A-1, D+A, D-A, A-D, D&A, D|A, M, !M, -M, M+1, M-1, D+M, D-M, M-D, D&M, D|M
JGT, JEQ, JGE, JLT, JNE, JLE, JMP

## Slide 36: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Jump:
Condition for jumping
Dest:
Where to store result
Comp:
ALU Operation (a bit chooses between A and M)
Unused
Family:
C-Instruction

## Slide 37: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Jump:
Condition for jumping

## Slide 38: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Dest:
Where to store result

## Slide 39: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Comp:
ALU Operation (a bit chooses between A and M)
Chapter 4
Important: just pattern matching text!
Cannot have “1+M”

## Slide 40: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
00
01
A Register
55
D Register
56

## Slide 41: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
@R2
M=D
00
01
02
03
RAM
0
1
2
?
?
56
...
A Register
55
D Register
56
A Register
2
D Register
56

## Slide 42: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
@R2
M=D
@EXAMPLE
D;JGT
00
01
02
03
04
05
RAM
0
1
2
?
?
56
...
A Register
0
D Register
56
(Will jump to instruction 0, since D > 0)
A Register
2
D Register
56
A Register
55
D Register
56

## Slide 43: Lecture 7 Reminders
Lectures will be in CSE2 271 starting this Friday until the rest of the quarter
Project 4 due this Friday (1/26) at 11:59pm
Amy has office hours tomorrow at 1:30pm in CSE2 151
  Feel free to post your questions on the Ed board as well
Midterm exam coming up in around two weeks (2/9) during lecture time
  More details to come, along with metacognitive strategies for preparing for exams