## Slide 1: CSE 451: Operating Systems Spring 2012 Module 20 Redundant Arrays of Inexpensive Disks (RAID)
Ed Lazowska
lazowska@cs.washington.edu
Allen Center 570
Notes: 1

## Slide 2: The challenge
Disk transfer rates are improving, but much less fast than CPU performance
We can use multiple disks to improve performance
  by striping files across multiple disks (placing parts of each file on a different disk), we can use parallel I/O to improve access time
Striping reduces reliability
  10 disks have 1/10th the MTBF (mean time between failures) of one disk
So, we need striping for performance, but we need something to help with reliability

## Slide 3: Reliability
At the scales we’re currently considering (tens of disks), it’s typically enough to be resilient to the failure of a single disk
  What are the chances that a second disk will fail before you’ve replaced the first one?
    Er, it has happened to us!
To achieve this level of reliability, add redundant data that allows a single disk failure to be tolerated
  We’ll see how in a minute
So:
  Obtain performance from striping
  Obtain reliability from redundancy (which steals back some of the performance gain)

## Slide 4: RAID
A RAID is a Redundant Array of Inexpensive Disks
Disks are small and cheap, so it’s easy to put lots of disks (10s, say) in one box for increased storage, performance, and availability
Data plus some redundant information is striped across the disks in some way
How striping is done is key to performance and reliability
The RAID controller deals with this – it is invisible to the operating system

## Slide 5: Some RAID tradeoffs
Granularity
  fine-grained: stripe each file over all disks
    high throughput for the file
    limits transfer to 1 file at a time
  course-grained: stripe each file over only a few disks
    limits throughput for 1 file
    allows concurrent access to multiple files
Redundancy
  uniformly distribute redundancy information on disks
    avoids load-balancing problems
  concentrate redundancy information on a small number of disks
    partition the disks into data disks and redundancy disks

## Slide 6: RAID Level 0: Non-Redundant Striping
6
RAID Level 0 is a non-redundant disk array
Files/blocks are striped across disks, no redundant info
High (single-file) read throughput
Best write throughput (no redundant info to write)
Any disk failure results in data loss
data disks

## Slide 7: RAID Level 1: Mirrored Disks
7
Files are striped across half the disks, and mirrored to the other half
  2x space expansion
Reads: Read from either copy
Writes: Write both copies
On failure, just use the surviving disk
data disks
mirror copies
identical
identical

## Slide 8: Prelude to RAID Levels 2-5: A parity refresher
8
To each byte, add a bit whose value is set so that the total number of 1’s is even
Any single missing bit can be reconstructed
(Why does memory parity not work quite this way?)
More sophisticated schemes (e.g., based on Hamming codes) can correct multiple bit errors – called ECC (error correcting codes)
1
0
1
1
0
1
1
0
1

## Slide 9: RAID Levels 2, 3, and 4: Striping + Parity Disk
9
RAID levels 2, 3, and 4 use parity or ECC disks
  e.g., each byte on the parity disk is a parity function of the corresponding bytes on all the other disks
  details between the different levels have to do with kind of ECC used, and whether it is bit-level or block-level
A read accesses all the data disks, a write accesses all the data disks plus the parity disk
On disk failure, read the remaining disks plus the parity disk to compute the missing data
data disks
parity disk

## Slide 10: RAID Level 5
10
RAID Level 5 uses block interleaved distributed parity
Like parity scheme, but distribute the parity info (as well as data) over all disks
  for each block, one disk holds the parity, and the other disks hold the data
Significantly better performance
  parity disk is not a hot spot
0
1
2
3
PO
5
6
7
P1
4
10
11
P2
8
9
data & parity drives
File Block
Numbers

## Slide 11: RAID Level 6
11
Basically like RAID 5 but with replicated parity blocks so that it can survive two disk failures.
Useful for larger disk arrays where multiple failures are more likely.

## Slide 12: Example RAID Storage
12
Promise 3U rack-mountable 16-disk RAID Storage System
Hot swappable drives
Dual controllers with 4 host interface ports for reliability
Can be ganged together into larger units