## Slide 1
Shyam Gollakota
Slides from David Wetherall, Arvind Krishnamurthy, John Zahorjan

## Slide 2: The Main Point
To learn how the Internet works »
  What really happens when you “browse the web”?
  What are TCP/IP, DNS, HTTP, NAT, VPNs, 802.11 etc. anyway?
To learn the fundamentals of computer networks

## Slide 3: Why learn about the Internet?
Curiosity »
Impact on our world »
Job prospects!

## Slide 4: From this experimental network …
ARPANET ~1970
(a) Dec. 1969. (b) July 1970. (c) March 1971.
Notes: Figure taken from CN5E Figures Ch 1 #28

## Slide 5: To this!
An everyday institution used at work, home, and on-the-go
Visualization contains millions of links
Attribution: By The Opte Project [CC-BY-2.5], via Wikimedia Commons
Internet ~2005

## Slide 6: Question
What do you think are the issues that one has to tackle to grow from a small network to an extremely large network?

## Slide 7: Internet – Societal Impact
An enabler of societal change
  Easy access to knowledge
  Electronic commerce
  Personal relationships
  Discussion without censorship
Notes: Logos as trademark fair usage

## Slide 8: Internet – Economic impact
An engine of economic growth
  Advertising-sponsored search
  “Long tail” online stores
  Online marketplaces
  Crowdsourcing
Notes: Logos as trademark fair usage

## Slide 9: The Main Point (2)
To learn how the Internet works
To learn the fundamentals of computer networks
  What hard problems must they solve?
  What design strategies have proven valuable?

## Slide 10: Why learn the Fundamentals?
Apply to all computer networks
Intellectual interest »
Change / reinvention »

## Slide 11: Fundamentals – Intellectual Interest
Example key problem: Reliability!
  Any part of the Internet might fail
  Messages might be corrupted
  So how do we provide reliability?

## Slide 12: Fundamentals – Intellectual Interest (2)
Key problem | Example solutions
Reliability despite failures | Codes for error detection/correction (§3.2, 3.3) Routing around failures (§5.2)
Network growth and evolution | Addressing (§5.6) and naming (§7.1) Protocol layering (§1.3)
Allocation of resources like bandwidth | Multiple access (§4.2) Congestion control (§5.3, 6.3)
Security against various threats | Confidentiality of messages (§8.2, 8.6) Authentication of communicating parties (§8.7)
Notes: Table taken from CN5E Slides Ch 1 #18.

## Slide 13: Fundamentals – Reinvention
The Internet is constantly being re-invented!
  Growth over time and technology trends drive upheavals in Internet design and usage »
Today’s Internet is different from yesterday’s
  And tomorrow’s will be different again
  But the fundamentals remain the same

## Slide 14: Fundamentals – Reinvention (2)
At least a billion Internet hosts and growing …
Notes: Graph from http://www.isc.org/solutions/survey with permission via http://www.isc.org/solutions/survey/faq:
Can I have permission to reproduce your data or charts?
You have permission to reproduce our data provided that you mention the source as "Source: Internet Systems Consortium, Inc. (http://www.isc.org/)". However you must ask our permission to publish derivative works based on our data. In those cases you must say your data or charts are "Based on data from Internet Systems Consortium, Inc. (http://www.isc.org/)"

## Slide 15: Fundamentals – Reinvention (3)
Examples of upheavals in the past 1-2 decades
Growth / Tech Driver | Upheaval
Emergence of the web | Content Distribution Networks
Digital songs/videos | Peer-to-peer file sharing
Falling cost/bit | Voice-over-IP calling
Many Internet hosts | IPv6
Wireless advances | Mobile devices

## Slide 16: Not a Course Goal
To learn IT job skills
  How to configure equipment
    e.g., Cisco certifications
  But course material is relevant, and we use hands-on tools

## Slide 17: Course Mechanics
Course Administration
  Everything you need to know will soon be on the course web page: http://www.cs.washington.edu/461/
Teaching Assistants:
  Pei-an Lee
  Isaac Ackerman

## Slide 18: Course Logistics
Reading
Projects/Homeworks: 60%
Mid-term/final: 40%

## Slide 19
Uses of Networks (§1.1)

## Slide 20: Example Uses of Networks
Work:
  Email, file sharing, printing, …
Home:
  Movies / songs, news, calls / video / messaging, e-commerce, …
Mobile:
  Calls / texts, games, videos, maps, information access …

## Slide 21: Example Uses of Networks
Work:
  Email, file sharing, printing, …
Home:
  Movies / songs, news, calls / video / messaging, e-commerce, …
Mobile:
  Calls / texts, games, videos, maps, information access …
What do these uses tell us about why we build networks?

## Slide 22: For User Communication
From the telephone onwards:
  VoIP (voice-over-IP)
  Video conferencing
  Instant messaging
  Social networking
What is the metric we need to be optimizing for these uses?

## Slide 23: For Resource Sharing
Many users may access the same underlying resource
  E.g., 3D printer, search index, machines in the cloud
More cost effective than dedicated resources per user
  Even network links are shared via statistical multiplexing »

## Slide 24: Statistical Multiplexing
Sharing of network bandwidth between users according to the statistics of their demand
  (Multiplexing just means sharing)
  Useful because users are mostly idle and their traffic is bursty
Key question:
  How much does it help?

## Slide 25: Statistical Multiplexing (2)
Example: Users in an ISP network
  Network has 100 Mbps (units of bandwidth)
  Each user subscribes to 5 Mbps, for videos
  But a user is active only 50% of the time …
How many users can the ISP support?
  With dedicated bandwidth for each user:
  Probability all bandwidth is used:
ISP
100
5
5
5
. . .
Notes: User icon public domain from openclipart.org or pixabay or wikimedia commons

## Slide 26: Statistical Multiplexing (3)
With 30 users, still unlikely (2% chance) to need more than 100 Mbps!
  Binomial probabilities
Can serve more users with the same size network
  Statistical multiplexing gain is 30/20 or 1.5X
  But may get unlucky; users will have degraded service
Notes: Screenshot of using binomial applet

## Slide 27: For Content Delivery
Same content is delivered to many users
  Videos (large), songs, apps and upgrades, web pages, …
What is the metric that we want to optimize in such cases?

## Slide 28: Content Delivery (2)
Sending content from the source to 4 users takes 4 x 3 = 12 “network hops” in the example
Source
User
User
. . .
Notes: Go over paths
Icons from Cisco icon library, http://www.cisco.com/web/about/ac50/ac47/2.html. “Cisco icons are globally recognized and generally accepted as standard for network icon topologies. You may use them freely, but you may not alter them.”

## Slide 29: Content Delivery (3)
But sending content via replicas takes only 4 + 2 = 6 “network hops”
Source
User
User
. . .
Replica
Notes: Circle replica
Icons from Cisco icon library, http://www.cisco.com/web/about/ac50/ac47/2.html. “Cisco icons are globally recognized and generally accepted as standard for network icon topologies. You may use them freely, but you may not alter them.”

## Slide 30
Network Components (§1.2)

## Slide 31: Parts of a Network
host
app
link
router
Notes: Icons from Cisco icon library, http://www.cisco.com/web/about/ac50/ac47/2.html. “Cisco icons are globally recognized and generally accepted as standard for network icon topologies. You may use them freely, but you may not alter them.”

## Slide 32: Component Names
Component | Function | Example
Application, or app, user | Uses the network | Skype, iTunes, Amazon
Host, or end-system, edge device, node, source, sink | Supports apps | Laptop, mobile, desktop
Router, or switch, node, intermediate system, … | Relays messages between links | Access point, cable/DSL modem
Link, or channel | Connects nodes | Wires, wireless

## Slide 33: Types of Links
Full-duplex
  Bidirectional
Half-duplex
  Bidirectional
Simplex
  unidirectional
Notes: Draw links

## Slide 34: Wireless Links
Message is broadcast
  Received by all nodes in range
  Not a good fit with our model
Notes: AP from pixabay.com.
Icons from Cisco icon library, http://www.cisco.com/web/about/ac50/ac47/2.html. “Cisco icons are globally recognized and generally accepted as standard for network icon topologies. You may use them freely, but you may not alter them.”

## Slide 35: Example Networks
WiFi (802.11)
Enterprise / Ethernet
ISP (Internet Service Provider)
Cable / DSL
Mobile phone / cellular (2G, 3G, 4G)
Bluetooth
Telephone
Satellite ...

## Slide 36: Network names by scale
Scale | Type | Example
Vicinity | PAN (Personal Area Network) | Bluetooth (e.g., headset)
Building | LAN (Local Area Network) | WiFi, Ethernet
City | MAN (Metropolitan Area Network) | Cable, DSL
Country | WAN (Wide Area Network) | Large ISP
Planet | The Internet (network of all networks) | The Internet!
Notes: Underline PAN / LAN / MAN / WAN terms.
Table derived from CN5E Slides Ch 1 #7

## Slide 37: Internetworks
An internetwork, or internet, is what you get when you join networks together
  Just another network
The Internet (capital “I”) is the internet we all use

## Slide 38
Source: Internet2
Notes: Hello David,
It is fine to use the maps for this course. Thank you for letting us know.
Best regards,
Beth
Beth Miller,
Marketing Communications Manager
Internet2
beth@internet2.edu
(734)352-7044
Visit our website: www.internet2.edu Follow us on Twitter: www.twitter.com/internet2 Find us on Facebook: www.internet2.edu/facebook
Begin forwarded message:
From: David Wetherall <djw@cs.washington.edu>
Date: November 15, 2012 8:59:05 AM EST
To: info@internet2.edu
Subject: permission request
Hello,
I would like permission to reprint the Internet2 network topology map given at
http://www.internet2.edu/pubs/Internet2-Network-Infrastructure-Topology.pdf
as part the course "Introduction to Computer Networks" by Arvind Krishnamurthy, David Wetherall and John Zahorjan. This course will be offered beginning January 2013 on the Coursera platform for massive open online courses.
I am making this request because Coursera is a commercial platform and thus not covered by your "non-commercial permission". However, the course is public and free to students.
Please let me know how to proceed. Thank you,
David

## Slide 39: Key Interfaces
Between (1) apps and network, and (2) network components
  More formal treatment later on
host
app
Notes: Draw and number interfaces 1 and 2.
Icons from Cisco icon library, http://www.cisco.com/web/about/ac50/ac47/2.html. “Cisco icons are globally recognized and generally accepted as standard for network icon topologies. You may use them freely, but you may not alter them.”

## Slide 40: Key Interfaces (2)
Network-application interfaces define how apps use the network
  Sockets are widely used in practice
host
app
Notes: Icons from Cisco icon library, http://www.cisco.com/web/about/ac50/ac47/2.html. “Cisco icons are globally recognized and generally accepted as standard for network icon topologies. You may use them freely, but you may not alter them.”

## Slide 41: Key Interfaces (3)
Network-network interfaces define how nodes work together
  Traceroute can peek in the network
host
app
Notes: Icons from Cisco icon library, http://www.cisco.com/web/about/ac50/ac47/2.html. “Cisco icons are globally recognized and generally accepted as standard for network icon topologies. You may use them freely, but you may not alter them.”