## Slide 1: Hamming It Up with Hamming Codes
CSE 461 Section Week 3

## Slide 2: Error Detection/Correction
We want to know when there are errors in communication
Correcting errors would be even better! Why?
  It’d save lots of time
What are some ways we can correct errors?
  Send data multiple times
  Send longer symbols
  Send data with the payload that’s a function of the payload
    E.g., parity bits

## Slide 3: Parity Bits
    Problem
      We want to send 1101
      Last bit gets flipped
      1100 is sent instead
    How can we detect this?
      Add another bit at the end: the sum (without carry) of all the bits
      So instead of 1101 we send…
        11011
      If 11001 is received, we know that it’s wrong—how?
        The parity bit for 1100 should be 0, but it’s not… something was flipped!
      Even and odd parity

## Slide 4: Error Detection/Correction
Parity bits don’t let us correct errors (by themselves)
Can we do any better?
What’s the best way to detect and correct?

## Slide 5: Hamming Codes: Background
Richard Hamming
Worked at Bell Labs
Developed Hamming Codes to save time on punchcard reading errors
Mixed message bits and parity bits to detect and correct specific errors
Hamming codes now used for network communications as well as hard drive RAIDs

## Slide 6: Hamming Codes: How They Work
00100101100
Bits in 1, 2, 4, 8, etc. positions are parity bits
All other bits are message bits

## Slide 7: Hamming Codes: How They Work
We want to send 1011100
We put its message bits into the non-2n places, like so:
? ? 1 ? 0 1 1 ? 1 0 0
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11

## Slide 8: Hamming Codes: How They Work
? ? 1 ? 0 1 1 ? 1 0 0
Each message bit is added to the parity bits that sum up to that message bit’s place
For m3, 3 = 2 + 1, so we add to p1 and p2
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1

## Slide 9: Hamming Codes: How They Work
? ? 1 ? 0 1 1 ? 1 0 0
For m5, 5 = 4 + 1, so we add to p4 and p1
  But m5 = 0, so we don’t add anything
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1

## Slide 10: Hamming Codes: How They Work
? ? 1 ? 0 1 1 ? 1 0 0
For m6, 6 = 4 + 2, so we add to p4 and p2
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1

## Slide 11: Hamming Codes: How They Work
? ? 1 ? 0 1 1 ? 1 0 0
For m7, 7 = 4 + 2 + 1, so we add to p4, p2 and p1
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1

## Slide 12: Hamming Codes: How They Work
? ? 1 ? 0 1 1 ? 1 0 0
What would we do for m9?
  9 = 8 + 1, so we add to p8 and p1
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 13: Hamming Codes: How They Work
? ? 1 ? 0 1 1 ? 1 0 0
What would we do for m10?
  10 = 8 + 2, so we add to p8 and p2
  But m10 = 0, so we don’t add anything
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 14: Hamming Codes: How They Work
? ? 1 ? 0 1 1 ? 1 0 0
What would we do for m11?
  11 = 8 + 2 + 1, so we add to p8, p2 and p1
  But m11 = 0, so we don’t add anything
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 15: Hamming Codes: How They Work
? ? 1 ? 0 1 1 ? 1 0 0
Now we add up all of the parity bits
  What would each one be? (Even parity)
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 16: Hamming Codes: How They Work
1 ? 1 ? 0 1 1 ? 1 0 0
Now we add up all of the parity bits
  What would each one be? (Even parity)
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 17: Hamming Codes: How They Work
1 1 1 ? 0 1 1 ? 1 0 0
Now we add up all of the parity bits
  What would each one be? (Even parity)
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 18: Hamming Codes: How They Work
1 1 1 0 0 1 1 ? 1 0 0
Now we add up all of the parity bits
  What would each one be? (Even parity)
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 19: Hamming Codes: How They Work
1 1 1 0 0 1 1 1 1 0 0
Now we add up all of the parity bits
  What would each one be? (Even parity)
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 20: Hamming Codes
So we get 11100111100 as our bit string to send
The receiver can recalculate the parity bits and make sure they match

## Slide 21: Error Syndromes
The sender sent 11100111100 but what if we received 11000111100 ?
Can we correct this?

## Slide 22: Error Syndromes
1 1 0 0 0 1 1 1 1 0 0
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
Recalculate parity bits and you get the numbers in blue:
0 0 0 1
(We know there’s an error because we didn’t get 1101)

## Slide 23: Error Syndromes
1 1 0 0 0 1 1 1 1 0 0
P1 p2 m3 p4 m5 m6 m7 p8 m9 m10 m11
Add calculated parity bits to parity bits in received data:
0 0 0 1
=1 =1 =0 =0
Then reverse the sum and it will tell you the bit in error:
0011 -> third bit is wrong!

## Slide 24: Now, you try! Decode this ASCII message (0b1000001 = 65 = ‘A’)
1011 0101 000 1111 0011 001
1100 0001 111
There may be bit errors! Assume each line encodes one byte of message data. (I.e., pad with a leading zero.)

## Slide 25: Answers
1011 0101 000 1111 0011 001
1100 0001 111
1011 0100 000 1111 0011 001
1110 0001 111
Correct errors
Extract message bits
1010 000 1001 001
1000 111
Convert to ASCII
PIG