## Slide 1: CSE 461
Midterm Review

## Slide 2: Midterm overview
50 minutes
Closed book, closed notes
Covers topics in lectures, projects and homeworks
Not intended to test things you can easily look up
  If something seems like you could Google it in a second, ask JZ
Mixture of straightforward questions and conceptual thought questions
Bonus Question: name both TAs (first and last name) for 461
  Nat Guy and Paul Vines

## Slide 3: Network Layers & Encapsulation
Application
Application
Transport
Transport
Network
Data Link/ Physical
Network
Data Link/ Physical

## Slide 4: Application Layer
Application
Application
Used by applications
Protocol is arbitrary

## Slide 5: Transport Layer
Transport
Transport
Involves packaging of data for transport
UDP/TCP and ports

## Slide 6: Network Layers & Encapsulation
Network
Network
Handles issues related to routing on the network
Data treated as packets

## Slide 7: Data link/Physical Layers
Data Link/ Physical
Data Link/ Physical
Data link layer
  Puts data onto the actual line
  Error-correcting codes to account for line noise are in the data link layer
    At this level, data consists of frames
Physical layer
  Actual electrical or wireless oscillations

## Slide 8: Addressing
MAC addresses
IP addresses
Ports
Sockets

## Slide 9: MAC Addresses
48-bit
Identify instance of specific network interface hardware

## Slide 10: IP addresses
32-bit (in IPv4) or 128-bit (in IPv6)
Identify a host on a network
Can change dynamically
Bonus Question : what does IP stand for?
  Internet protocol

## Slide 11: Ports
16-bit
Identify communication channels on a specific host
Often map to applications
Bonus Question : what application uses port 21?
  FTP

## Slide 12: sockets
Programming interface for networking
Most common implementation is Berkeley sockets
Allows data to be sent with file descriptor-like structures
Bonus Question : name two valid type arguments you can specify for a socket
  SOCK_STREAM, SOCK_DGRAM, SOCK_SEQPACKET, SOCK_RAW

## Slide 13: Udp vs. tcp
UDP | TCP
Unreliable | Reliable
Connection-less | Connection-oriented
No acknowledgements | Acknowledgements
No flow control | Sliding window
No sequence numbers | Sequence numbers

## Slide 14: Telnet vs. FTP
Telnet | FTP
Used for sending text data; originally for remote login into a server | Used for sending files
Data transfer and control on same channel | Separate channels for control and data transfer; control channel uses Telnet
Uses TCP | Also uses TCP
Once connected, server and client essentially the same | Server and client behave very differently
Not secure; largely replaced by SSH | Not secure; somewhat replaced by SFTP

## Slide 15: metrics
Bandwidth
Latency
Throughput, goodput
Channel utilization
Shannon’s theorem
Nyquist rate

## Slide 16: FREQUENCY & bandwidth
Frequency: rate of an oscillation
Bandwidth: measures the width of a range of frequencies
Bandwidth = frequpper - freqlower
Human hearing bandwidth: ~20kHz (20kHz - 20 Hz)
“Bandwidth” and “bitrate” are often used interchangeably; this is a different definition
Bonus Question: what’s the frequency range and bandwidth of 802.11 b/g?
  2.4 GHz to 2.5 GHz; 100 MHz

## Slide 17: latency
Time between source and destination
Shortest possible latency bounded by c
Ping can measure round-trip latency
Why might latency vary between ping tests?

## Slide 18: Throughput & goodput
Throughput: measures how much data can be sent in a given time period (a.k.a. bitrate)
E.g., 100 Gbps
Bits that you can send (i.e., put onto the wire) per amount of time
Goodput: excludes protocol bits and retransmitted data packets
What factors might cause goodput < throughput?
  Protocol overhead
  Dropped or corrupted packets
  Flow control

## Slide 19: Channel utilization
Calculates how much of the channel is being used
Percent of the time the channel is in use
(sent data size) / ((channel bitrate) * (round-trip latency))
If the time to send data is non-negligible, you will want to add the (sent data size) *
If you’re using stop-and-wait and only sending 1KB at a time over a 1MBps channel with round-trip latency of 10s (and negligible ACK size), what’s the channel utilization?
  2^10 / (2^20 * 10) = ~0.01%

## Slide 20: Shannon theorem
Tells about maximum bitrate in the presence of noise
Capacity = bandwidth * log2(1 + signal/noise)
C = B log2(1 + S/N)
What are the implications of this?

## Slide 21: Nyquist RATE
To recover a waveform, the sampling rate must be at least two times the highest frequency
Telephone sampling rate is 8kHz; what are the implications of this?
What sampling rate would be required to recover all frequencies audible by humans? (Up to 20kHZ)
  Audio CDs use 44.1kHz sampling rates for this reason

## Slide 22: Http
HTTP 1.0
  Initial connection over TCP acts as a preamble
  Content-length can designate payload end
    Bad for streaming
    Alternative: drop the connection!
  Caching used heavily
HTTP 1.1
  Data comes as a stream, chunked into defined lengths
  Connections are reused, reducing overhead
  Some pipelining possible, but limited (HOL blocking)
HTTP 2.0
  Reduces latency through compression
  Allows asynchronous sending/multiplexing

## Slide 23: Error Handling
Parity bits
Hamming codes
Checksums
CRCs
Bursty errors and error locality

## Slide 24: Parity bits
Bits check parity on a set of bits
Even parity: bits add to 0
Odd parity: bits add to 1
Multiple parity bits (on odd bits/ on even bits, etc.) can increase effectiveness
  Bonus Question : What parity bit would need to go in the x to achieve even parity? 0010101x
    1

## Slide 25: Hamming codes
An extension of bit parity, where parity check bits are in “powers of two” positions
  Bit string: 0 0 1 0 0 0 0 1 0 0 1 Bit number: 1 2 3 4 5 6 7 8 9 10 11 Par/msg: p p m p m m m p m m m
Each data bit is checked (with even parity) by check bits that make up its “power of two” sum
  E.g., for data bit 7, add to sum for parity bits 4 + 2 + 1
  Possible to recover from single errors
  See section notes for more details
Hamming distance: minimum number of bit flips necessary to change one string into another

## Slide 26: Checksums & CRCs
Checksums:
  Adds all words in data as unsigned numbers, allowing to overflow
  Sum was then compared to check data integrity
CRCS:
  Specific type of checksum that uses polynomial division
Both are integrity checks using a fixed size of data

## Slide 27: Idempotence
Property that an operation can be applied multiple times without changing the result beyond the initial application
Essential for servers where the same packet may arrive multiple times
Limerick
  There once was a misconfigured client
  Its registrations were quite noncompliant.
  It sent the same thing 20 times,
  But the operation worked fine;
  Idempotent protocols aren't state-reliant!

## Slide 28: Carrier sense multiple access with collision detection (CSMA/cd)
Nodes detect traffic on the line and wait to transmit until it’s clear
Collisions are detected, and a random amount of time is waited before a retransmit
Bonus question: Why doesn’t Ethernet use this anymore?
  Hosts can communicate directly with Ethernet switches, completely avoiding collisions.

## Slide 29: Hidden terminal problem
Issue that can cause wireless interference
Bonus Question: what are some ways to mitigate this?
  Static
    Increase both stations’ power so they can hear each other
    Relocate the stations or obstacles
  Dynamic
    RTS/CTS

## Slide 30: Binary exponential backoff
Wait a random number of slots between 0 and n
n starts at 1 and doubles each time there’s a collision
Useful for collision-heavy environments
Stable, because it’ll eventually get through

## Slide 31: Code division multiplexing
All stations send at the same time, with same frequencies
Each station has a unique chip sequence, all orthogonal to each other
E.g., (1,1,1,1) ⊥ (1,1,-1,-1) ⊥ (1,-1,1,-1)
Each station sends that sequence for 1, and the negation of that sequence for 0
Receiver decodes signal by taking the dot product of the received signal with the chip sequence for each station

## Slide 32: Code division multiplexing (2)
Signals on the right are all orthogonal (including each one’s negation)
If added on top of each other, they’re always separable with the method on the previous slide

## Slide 33: Other Topics
Protocol design
  Data and control channels can be separate or mixed
  Necessary reliability influences whether data needs to be checked and to what degree
Sliding window protocol
  Receiver must receive a certain minimum number of segments before sender can send new data
  Used in TCP
Cumulative ACKing
  ACKing a sequence number means you’ve received all data preceding that sequence number

## Slide 34: Project 1 questions
Could you use cumulative ACKs without breaking the protocol? Would it be useful?
Why use headers?
Why does the registration server need to be idempotent?
  Idempotent: can be applied multiple times without changing the result beyond the initial application

## Slide 35: Sample exam questions

## Slide 36: Sample question
Ethernet and 802.11 both support multiple data rates. When an Ethernet cable is plugged into the device, it communicates with the other end, chooses a rate to use, and then sticks with it. 802.11 devices, however, continuously talk to the AP to choose a specific rate to use for the next short while, adjusting that rate up and down as they please.
Why is it a good idea for 802.11 to repeatedly choose transmission rates? Why is it not a good idea for Ethernet to do this? (Discuss with someone near you.)

## Slide 37: Answer
The 802.11 signal-to-noise ratio can change dramatically over time, which strongly affects the possible transmission rates. Unless 802.11 adapted, it would have to choose between wide coverage at low rates and high rates at low coverage. Dynamic adaptation lets it try to achieve both. Ethernet operates in a much more constrained environment, with strict limits on signal quality imposed by the specification. The environment does not change dynamically.

## Slide 38: Sample question
A sender and receiver are using the sliding window protocol, with cumulative ACKs. The receiver has a bug where it repeats the last ACK it sent whenever it hasn’t received a data frame in the last 10 msec. The connection is bad enough that some data and ACK frames may be lost. Will the sender and receiver achieve reliable transmission? Will this protocol fail? ? (Discuss with someone near you.)

## Slide 39: Answer
They’ll achieve reliable transmission, assuming no bugs other than those described. The extra ACKs will simply repeat a previously sent ACK. They won’t affect the sender’s window; the sender will view them as duplicate ACKs and drop them.

## Slide 40: Sample question
In Project 1 your code sent UDP packets from a client to a server. If we were to look at the bits actually being carried on the wire (assuming we're using a wired network), we'd find the destination IP address and port were part of the bits being sent. Did the bits on the wire also carry a destination MAC address, or not?

## Slide 41: Answer
Yes. All data delivery happens at the link layer, which uses MAC addresses. Higher level protocols, like UDP, are encapsulated in link layer frames.

## Slide 42: Sample question
Sliding window protocols specify a sending window and a receiving window. Can it ever be useful for the sending window to be larger than the receiving window? Briefly explain your answer.

## Slide 43: Answer
Yes, possibly. The sending window limits the amount of data that can be in flight but unacknowledged. The receiver window is a limit on the memory available for buffering and reordering. If the receiver is capable of consuming each incoming frame basically as it arrives, it could have a very small receive window. In that case, the send window could be larger than the receive, to allow frames to be in flight (on the wire).

## Slide 44: Additional study suggestions
Read through your project 0 & 1 code and diagram what it’s doing
Review HW problems; do similar problems
Watch David Wetherall’s Coursera course videos (link)
Review old midterms
  Available on CSE site (but cover somewhat different material than what ours will)

## Slide 45: Any questions?