## Slide 1: CSE461 LAB Helper Protocols

## Slide 2: Internet Control Message Protocol (ICMP)
Address resolution Protocol (ARP)

## Slide 3: ICMP
Problem: What happens when something goes wrong during forwarding?
  Need to be able to find the problem
Yikes!
What happened?
XXXXXXX

## Slide 4: Internet Control Message Protocol
ICMP is a companion protocol to IP
  They are implemented together
  Sits on top of IP (IP Protocol=1)
Provides error report and testing
  Error is at router while forwarding
  Also testing that hosts can use

## Slide 5: ICMP Errors
When router encounters an error while forwarding:
  It sends an ICMP error report back to the IP source
  It discards the problematic packet; host needs to rectify
Report then toss it!
Oh, now I see …
XXXXXXX
ICMP report

## Slide 6: ICMP Message Format (2)
Each ICMP message has a Type, Code, and Checksum
Often carry the start of the offending packet as payload
Each message is carried in an IP packet
Src=router, Dst=A
Protocol = 1
Type=X, Code=Y
Src=A, Dst=B
XXXXXXXXXXXXX
Portion of offending packet,
starting with its IP header
ICMP header
IP header
ICMP data

## Slide 7: Example ICMP Messages

## Slide 8: Ping

## Slide 9: Traceroute
IP header contains TTL (Time to live) field
  Decremented every router hop, with ICMP error at zero
  Protects against forwarding loops

## Slide 10: Traceroute (2)
Traceroute repurposes TTL and ICMP functionality
  Sends probe packets increasing TTL starting from 1
  ICMP errors identify routers on the path
. . .
Local
Host
Remote
Host
1 hop
2 hops
3 hops
N-1 hops
N hops
Notes: Icons from Cisco icon library, http://www.cisco.com/web/about/ac50/ac47/2.html.

## Slide 11: Traceroute (3)

## Slide 12: ARP
Problem:
  A node needs Link layer addresses to send a frame over the local link
  How does it get the destination link address from a destination IP address?
Uh oh …
My IP is 1.2.3.4
Notes: Icons from cisco icon library

## Slide 13: ARP (Address Resolution Protocol)
Node uses to map a local IP address to its Link layer addresses
Source
Ethernet
Dest.
Ethernet
Source IP
Dest.
IP
Payload …
Link layer
From
DHCP
From
NIC
From ARP

## Slide 14: ARP Protocol Stack
ARP sits right on top of link layer
  No servers, just asks node with target IP to identify itself
  Uses broadcast to reach all nodes
Ethernet
ARP

## Slide 15: ARP Messages
Node
Target
One link
Notes: Icons from cisco icon library

## Slide 16: ARP Messages (2)
[root@host ~]# tcpdump -lni any arp & ( sleep 1; arp -d 10.0.0.254; ping -c1 -n 10.0.0.254 )
listening on any, link-type LINUX_SLL (Linux cooked), capture size 96 bytes
17:58:02.155495 arp who-has 10.2.1.224 tell 10.2.1.253
17:58:02.317444 arp who-has 10.0.0.96 tell 10.0.0.253
17:58:02.370446 arp who-has 10.3.1.12 tell 10.3.1.61
Node
Target
request
Broadcast
Who has IP 1.2.3.4?
reply
I do at 1:2:3:4:5:6
Notes: Icons from cisco icon library

## Slide 17: ARP Table
Notes: Ping –c 3 google.com
Traceroute google.com
Arp -a
netstat -nr

## Slide 18: Route command
Notes: Mac –
Ping –c 3 google.com
Traceroute google.com
Arp -a
netstat -nr