## Slide 1: CSE 461: Review
Chunjong Park

## Slide 2: Internet Reference Model - Layering
The classic OSI model has seven layers
In practice, there are more like four
Application
Transport
Network
Link
Move data between nodes that can hear each other’s transmissions.
Ethernet, WiFi
Move data between applications anywhere on the Internet.
UDP, TCP
Application-specific data
HTTP, SMTP, P0P (project 0)
Move data from one machine to another, anywhere on the Internet.
IP

## Slide 3: Encapsulation/Decapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 4: Application Layer - DNS
Built on UDP messages, port 53
Names  Addresses
Resolution
Iterative vs recursive
Cache

## Slide 5: Application Layer - HTTP
Static vs Dynamic Web pages
URL structures
Browser steps:
  Resolve the server name to an IP address (DNS)
  Set up a TCP connection to the server
  Send HTTP request for the page
  Wait for and then read HTTP response
  (Assuming no errors) Process response data and render page
  Clean up any idle TCP connections
HTTP methods
HTTP response codes
HTTP 1.0 vs HTTP 1.1 vs HTTP 2.0

## Slide 6: Transport
 | Reliable | Unreliable
Packets |  | Datagrams (UDP)
Bytestream | Streams(TCP) | 
TCP | UDP
Streams | Datagrams
Connections | Connectionless
Bytes are delivered to receiving app reliably (once, and in order) | Packets may be lost, reordered, duplicated (but not corrupted)
Arbitrary length content | Fixed maximum datagram size
Connection latency | No delay
Segment delivery latency (“nagling”) | Datagram is sent now
Flow control matches sender’s rate to receiver’s capability | No flow control (can lead to many lost datagrams)
Congestion control matches sender’s rate to network’s capability | No congestion control (can lead to many lost datagrams)

## Slide 7: Transport – Mux/demux – UDP
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?

## Slide 8: Transport – Mux/demux –TCP
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server

## Slide 9: Transport – TCP
Reliable transfer – retransmission
  Stop-and-wait
  Sliding windows
  Go-Back-N
  Selective Repeat

## Slide 10: Transport – TCP
Connection establishment
Flow control
Sliding windows
Connection teardown

## Slide 11: Transport – TCP Congestion Control
Fairness vs. efficiency
AIMD
Congestion signals
Signal | Example Protocol | Pros / Cons
Packet loss (RTO, DupACK) | TCP NewReno Cubic TCP (Linux) | Hard to get wrong Hear about congestion late
Packet delay | Compound TCP (Windows) | Hear about congestion early Need to infer congestion
Router indication | TCPs with Explicit Congestion Notification | Hear about congestion early Require router support

## Slide 12: Transport – TCP Congestion Control – SS
We want to quickly near the right rate, cwndIDEAL, but it varies greatly
Slow Start solution
  Start by doubling cwnd every RTT
  Exponential growth (1, 2, 4, 8, 16, …)
  Start slow, quickly reach large values

## Slide 13: Transport – TCP Congestion Control
Fast recovery
Network-Side Congestion Control
  Random Early Detection
  Explicit Congestion Notification

## Slide 14: Network
How to deliver packets globally
Scaling
  Hierarchy, in the form of prefixes
Heterogeneity
  IP for internetworking
Bandwidth Control
  Lowest-cost routing

## Slide 15: Network
Network service models
  Datagrams (packets), virtual circuits
IP (Internet Protocol)
  Internetworking
  Forwarding (Longest Matching Prefix)
  Helpers: ARP and DHCP
  Fragmentation and MTU discovery
  Errors: ICMP (traceroute!)
  IPv6, scaling IP to the world
  NAT, and “middleboxs”
Routing Algorithms

## Slide 16: Network – Datagrams vs Virtual Circuits
Issue | Datagrams | Virtual Circuits
Setup phase | Not needed | Required
Router state | Per destination | Per connection
Addresses | Packet carries full address | Packet carries short label
Routing | Per packet | Per circuit
Failures | Easier to mask | Difficult to mask
Quality of service | Difficult to add | Easier to add
Datagrams: packets contain a destination address; each router uses it to forward packets, maybe on different paths
Virtual circuits: Packets contain a short label (unique on a link) to identify the circuit

## Slide 17: Network – IP Prefix/Forwarding
IP prefix: “IP address/length”
  128.13.0.0/16 is 128.13.0.0 to 128.13.255.255
Longest Matching Prefix

## Slide 18: Network – Routing
Routing versus Forwarding
Forwarding is the process of sending a packet on its way
Routing is the process of deciding in which direction to send traffic

## Slide 19: Network – Subnet/Aggregation

## Slide 20: Link

## Slide 21: Link – Error detection and correction
Hamming Distance
  Distance is the number of bit flips needed to change D1 to D2
  Hamming distance of a coding is the minimum distance between any pair of valid codewords
Error detection:
  For a coding of distance d+1, up to d errors will always be detected
  Parity bit
  Cyclic Redundancy Check (CRC)
Error correction
  For a coding of distance 2d+1, up to d errors can always be corrected
  map to the closest valid codeword (there can be only one)

## Slide 22: Link – ARQ
ARQ often used when errors are common or must be corrected
  E.g., WiFi, and TCP
Rules at sender and receiver:
  Receiver automatically acknowledges correct frames with an ACK
  Sender automatically resends after a timeout, until an ACK is received
Should retransmissions occur at link layer
  Depends on expected error rate
  Think of them as a performance optimization (relative to just leaving it to TCP) when they’re implemented
Because latencies are typically small(ish) and tightly bounded on a single link
  Timeout estimation is simpler
  Less motivation to use sliding window, rather than stop-and-wait

## Slide 23: Link – Multiple Access
TDM
  Users take turns on a fixed schedule
FDM
  Put different users on different frequency bands

## Slide 24: Link – Multiple Access
TDM
  Users take turns on a fixed schedule
FDM
  Put different users on different frequency bands

## Slide 25: Link – Ethernet – CSMA/CD
spatial layout of nodes
Collision detection

## Slide 26: Link – CSMA/CD
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions

## Slide 27: Wireless
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 28: Link – CSMA/CA
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 29: Real-world scenario

## Slide 30: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 31: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 32: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 33: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 34: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demux’ed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 35: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 36: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed