EE/CSE 469 – Computer Design and Organization
HW #7 – Due 28 February, 2018

1.) The code below is the assembly for the toUpper example.  Figure out the prediction accuracy for each of the three branch instructions below (individually) with a 1-bit predictor, as well as for the first branch (CBZ) with a 2-bit predictor.  Thus, your answer will be 4 percentages.  You can assume:

- The code has been executing for a long time, so the predictors are “warm”.

- The predictors do not conflict in the branch history table.

- The string is 40 characters long (including the final null).

- Each of the 39 non-null characters in the string are randomly distributed in the range 1-255.

- ASCII code (the numeric representation of characters) is given in the book.

// string is a pointer held at Memory[100].	
// X0=index, ‘A’ = 65, ‘a’ = 97, ‘z’ = 122	
	LDUR	X0, [X31, #100]	// index = string	
LOOP:
	LDURB	X1, [X0, #0]	// load byte *index	
	CBZ	X1, END	// exit if *index == 0	
	CMPI	X1, #97	// is *index < ‘a’?	
	B.LT	NEXT	// don’t change if < ‘a’	
	CMPI	X1, #122	// is *index > ‘z’?	
	B.GT	NEXT	// don’t change if > ‘z’	
	SUBI	X1, X1, #32	// X1 = *index + (‘A’ - ‘a’)	
	STURB	X1, [X0, #0]	// *index = new value;	
NEXT:
	ADDI	X0, X0, #1	// index++;	
	B	LOOP	// continue the loop	
END:

2.) For the code below draw the constraint graph.  Label each edge with the cause of the constraint (i.e “RAW X2”, etc.).  Then adjust the code to run as fast as possible on a pipelined processor like that in lab #4.  Note that if you carefully adjust the program you should be able to fill all the delay slots of the program (tricky!).

LOOP:
	LDUR	X2, [X10, #0]	
	SUB	X4, X2, X3	
	STUR	X4, [X10, #0]	
	LDUR	X5, [X10, #8]	
	SUB	X6, X5, X3	
	STUR	X6, [X10, #8]	
	SUBI	X10, X10, #16	
	CBNZ	X10, LOOP