## Slide 1
Bruce Davie
Systems Approach, LLC
Software-Defined Networks
A Systems Approach

## Slide 2
There’s a simple answer:
  SDN (software-defined networking) is the separation of control and data planes
  The separation allows control topology to be independent of physical network topology
The more interesting question is:
  Why would anyone want to do this?
  That question has a lot of answers…
Logically centralized control plane
Data Plane
e.g. OpenFlow
What is SDN?
Notes: CP is important; OF is a detail

## Slide 3
History of SDN
  Challenges faced by IP networks
SDN architecture
Case Studies:
  Network Virtualization
  Traffic Engineering
  SD-WAN
  Bare metal switching
Outline

## Slide 4
A Revolution in Networking

## Slide 5
4D, Greenberg et al. – part of a broader set of “Clean Slate” initiatives
Ipsilon General Switch Management Protocol – RFC 2297 (1996)
IETF Forces WG (2001-2015!!)
Ethane (2007)
Foundations of SDN

## Slide 6
Lack of abstractions
Inability to express intent
Unpredictable outcome from complex distributed algorithms
Interactions among protocols (e.g. IGP & EGP)
Can’t manage a device unless it’s properly configured
  bootstrap issue – control & management plane dependent on correct data plane
  Fragility, risk of change
Glacial pace of innovation
Challenges with IP networks

## Slide 7
Terminal Protocol: Telnet
Terminal Protocol: SSH
1996
2016
Evolution of network provisioning: 1996-2016
Notes: Could mention MPLS as example of how hard innovation was pre SDN

## Slide 8
Centralizing the control plane enables more powerful abstractions
  E.g. X and Y should be able to communicate
  Express intent network-wide
Distributed systems techniques to make central control scalable and fault tolerant
Central control means a single API for the network, rather than an API per box
Networks provisioned by software, not humans
Disaggregation → innovation
Network-wide intent → better security
Key SDN Insights

## Slide 9
Specialized
OS
Specialized
Hardware
App
App
App
App
App
App
Specialized
Applications
Open Interface
Linux
Mac
OS
Windows
or
or
Open Interface
Microprocessors
Disaggregation of computing Industry

## Slide 10
Specialized
OS
Specialized
Hardware
App
App
App
App
App
App
Specialized
Applications
Open Interface
Open Interface
Merchant Silicon
Switching Chips
Network
OS
or
or
Network
OS
Network
OS
Disaggregation of networking Industry

## Slide 11
Just because an idea has been tried before without success doesn’t mean it’s a bad idea
Random side observation

## Slide 12: SDN Architecture

## Slide 13
Routing Table
(RIB)
Forwarding Table
(FIB)
Data Plane
Control Plane
Traditional Control and Data Planes
Control Plane
  Protocols: BGP, OSPF, RIP
  RIB: Collection of Link/Path Attributes
  Northbound Configuration Interface
    e.g., Cisco CLI
Data Plane
  Protocols: IP
  FIB: Optimized for Fast Lookup
  Northbound Control Interface
    Historically Private/Internal

## Slide 14
Control
App
. . .
Control Plane
Data Plane
Flow Rules
Control
App
Control
App
Control
App
Network OS
Global
Network
Map
SDN Control and Data Planes

## Slide 15
OpenFlow Switch
Table
0
Table
1
Table
n
Execute
Action
Set
. . .
Packet
In
Packet
Out
Action
Set = {}
Action
Set
Packet +
Metadata
Action
Set
Packet
OpenFlow-style data plane
(MAC)
(VLAN)
(IP)
MAC
Header
… Payload …
IP
Header
TCP/UDP
Header
Src
Addr
Dst
Addr
Type
Src
Addr
Dst
Addr
Proto
…
…
…
Src
Port
Dst
Port
…
VLAN ID
Ctl
Type
Optional 802.1Q VLAN Tag
Notes: Non intuitive: you need a model of the data plane to be able to separate it from control

## Slide 16
Programmable
Parser
Programmable
Deparser
Programmable Match-Action Pipeline
Memory
Memory
Memory
Memory
Memory
Memory
ALU
ALU
ALU
ALU
ALU
ALU
Memory
Memory
Memory
Memory
Memory
Memory
ALU
ALU
ALU
ALU
ALU
ALU
Memory
Memory
Memory
Memory
Memory
Memory
ALU
ALU
ALU
ALU
ALU
ALU
Memory
Memory
Memory
Memory
Memory
Memory
ALU
ALU
ALU
ALU
ALU
ALU
PISA: Protocol Independent Switching Architecture

## Slide 17
Programmable Switch
API
Merchant Silicon
Stratum + ONL
gNMI + gNOI + P4Runtime/OpenFlow
Tofino (Barefoot),
Tomahawk (Broadcom)
forward.p4
arch.p4
P4
Compiler
Control
App
Control
App
Control
App
gRPC
Trellis
Network Operating System
gRPC
API
Switch OS
ONOS
gNMI + gNOI + FlowObjectives
SDN Software Stack

## Slide 18
Scaling the Central Control Plane
Controller
Controller
Controller
Controller
Controller
Node5
Node4
WebService API
Persistent Storage
Logical Network
Transport Network
Node1
Node2
Node3
Controller
Cluster

## Slide 19
Summary
Definition of SDN
  A network in which the control plane is physically separate from the forwarding plane, and a single control plane controls several forwarding devices. – Nick McKeown (2013)
Dimensions
  Disaggregated Control and Data planes
  Centralized vs Decentralized Control Plane
  Fixed-Function vs Programmable Data Plane
Phases of SDN
  Phase 1: Network operators took ownership of the control plane.
  Phase 1a: Non-traditional entrants to the networking business (via disaggregation)
  Phase 2: Network operators are taking ownership of the data plane.

## Slide 20
Network Virtualization
SD-WAN
Traffic Engineering
Bare Metal Switching
Inband Network Telemetry
Use Cases

## Slide 21
Physical Compute & Memory
Hypervisor
Requirement: x86
Virtual Machine
Virtual Machine
Virtual Machine
Application
Application
Application
x86 Environment
Physical Network
Network Virtualization Platform
Requirement: IP Transport
Virtual Network
Virtual Network
Virtual Network
Workload
Workload
Workload
L2, L3, L4-7 Network Services
Decoupled
Network Virtualization – An Analogy

## Slide 22: 2009

## Slide 23: 2012

## Slide 24
Network, storage, compute
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
Virtualization layer
Virtual Machines to Virtual Networks

## Slide 25
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
vSwitch
Hypervisor
Network, storage, compute
Virtualization layer
“Network hypervisor”
Virtual Data Centers
Virtual Machines to Virtual Networks

## Slide 26
Cloud Consumption
Manager
Controller
Data Plane
Self Service Portal
OpenStack, Kubernetes, etc
High–Performance Data Plane
Scale-out Distributed Forwarding Model
Single configuration portal
REST API entry-point
Manages Logical networks
Run-time state
Scale out, HA
Separation of Control and Data Plane
vSwitch
Hypervisor
Distributed Services
Logical Switch
Distributed Logical Router
Firewall
Load Balancer
Virtual Edge
Network Virtualization Components
Notes: Hyperv possible

## Slide 27
MANAGEMENT
PLANE
CONTROL
PLANE
DATA
PLANE
Translated State
Discovered State
Network topology request
Request stored and acknowledged
Calculate data plane state
Identify data plane resources
Desired State
Realized State
Management, Control and Data Planes
Notes: Show a logical topology getting mapped from top to bottom with animation

## Slide 28
Perimeter-centric network security has proven insufficient
Data Center Perimeter
Internet
VM
VM
VM
VM
VM
VM
VM
Today’s security model focuses on perimeter defense
Chart: 
| 2010 | 2011 | 2012 | 2013
IT Spend | 1.75 | 2 | 3 | 3.25
Security Spend | 1 | 1.5 | 2.5 | 4.5
Security Breaches | 0.5 | 1.5 | 3 | 5.5
But continued security breaches show this model is not enough
Problem: Data Center Network Security

## Slide 29
App VLAN
DMZ VLAN
Services VLAN
DB VLAN
Perimeter firewall
Inside
firewall
Finance
VM
VM
Finance
VM
VM
Finance
VM
VM
VM
VM
HR
VM
VM
HR
VM
VM
HR
IT
VM
VM
IT
VM
VM
IT
VM
VM
AD
VM
VM
NTP
VM
DHCP
VM
DNS
VM
CERT
Microsegmentation and Zero Trust
Notes: All Apps on a VLAN can communicate freely
Once one App is compromised, lateral movement cannot be restricted
Micro-segmentation can granularly control apps even on shared VLAN

## Slide 30
Historically challenging to troubleshoot connectivity between VMs
  Is the problem in vswitch or physical network?
  What’s the path through the physical network?
  Is there a (misconfigured) middlebox in the path?
Network virtualization gives us tools to handle this:
  Decomposition: separate the physical from the virtual
  Global view: see all the logical network state (port stats, drops, etc.) and tunnel health from the controller API
  Synthetic traffic: insert packets at vswitch as if the VM generated them
Visibility: changing the laws of physics

## Slide 31
90% of Fortune 100 have deployed network virtualization
Foundational to hyperscale data centers
Network configuration no longer the “long pole”
A key step towards better network security (but much work remains)
Increasingly important for microservices, kubernetes etc.
Commodifying effect on physical networking
Service Mesh can be viewed as a form of Network Virtualization
Network Virtualization – Discussion

## Slide 32
SD-WAN
Cloud Services
Corporate
Datacenter
Branch
SD-WAN Controller
Main Office
SD-WAN Edge
Overlay Tunnel
Network Policies

## Slide 33
Datacenter
Datacenter
Datacenter
Traffic Engineering
Controller
Network Policies

## Slide 34
Leaf
Leaf
Leaf
Leaf
Spine
Spine
Spine
Datacenter Switching Fabric
Leaf-Spine Topology
  Leaf Switches = Top-of-Rack (ToR)
  Optimized for East-West Traffic
  Built-in Redundancy (not shown)
  Scale with additional layers
Well-Established in Commodity Clouds
  Bare-Metal Switches
  Control Plane running in the cloud
Internet

## Slide 35
Leaf-Spine Switching Fabric
Trellis Design
  Intra-Rack: L2 Domain within L3 Subnet
  Inter-Rack: L3 Routing between Subnets
  Segment Routing across Fabric
Trellis Features
  VLANs / QinQ
  End-to-End L2 Tunnels
  IPv4 / IPv6 Routing
  Multicast (with IGMP)
  ARP (IPv4) / NDP (IPv6)
  DHCPv4 / DHCPv6
  High Availability
Leaf
Leaf
Leaf
Leaf
Spine
Spine
Spine

## Slide 36
S1
Add Switch ID, arrival time, departure, queue delay, etc.
Log, analyze, replay, visualize
Generate report with switch metadata
Header
Metadata S1
Payload
Header
Payload
Header
Payload
Header
Metadata S1
Payload
Metadata S2
Metadata S1
Metadata S2
Metadata S5
S2
S3
S4
S5
Inband Network Telemetry (INT)
Fine-Grain Telemetry
  Flow Rule(s) that matched
  Queuing delays of individual packets
  Other flows being buffered
  …
Uses
  Verify correct behavior
  Identify micro-bursts
  …

## Slide 37
Scale
Stability & Correctness
Timeliness
Inter-domain
SDN Challenges
Notes: Scale example – from NSX-mh to NSX-T (fewer hosts etc), API scale for NSX-T

## Slide 38
Discussion
Notes: What do you think is next? – Fully automated networks?
Does the innovation argument hold up?
How does BGP play into this? Interdomain still seems broken.
Architecture papers are the exception. Networking people love protocols.