## Slide 1: DCTCP and DCQCN

## Slide 2: How to read a systems/networking paper*
*Measurement papers excluded

## Slide 3
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?
I would have done this so differently, and so much better …

## Slide 4: DCTCP
Presenting work of many teams in Microsoft

## Slide 5
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 6: Poor search performance due to TCP incast resulting from partition/aggregate pattern

## Slide 7
Kamala Harris?
Wikipedia, news, tweets, ….
Bing
Web search ….

## Slide 8
Kamala Harris?
Top level aggregator (TLA)
Mid level aggregator (MLA)
Mid level aggregator (MLA)
Workers
Twitter ..
Web index
Images
Mid level aggregator (MLA)
Workers
Workers

## Slide 9
Wikipedia, news, tweets, ….
Top level aggregator (TLA)
Mid level aggregator (MLA)
Mid level aggregator (MLA)
Workers
Twitter ..
Web index
Images
Mid level aggregator (MLA)
Workers
Workers

## Slide 10
…
Top of Rack (ToR) Router
MLA
W
W
W
W
W

## Slide 11
…
Top of Rack (ToR) Router
MLA
W
W
W
W
W

## Slide 12
ASIC inside the ToR Router
W
MLA
W
W
W

## Slide 13: Why is this loss a problem?
Because responses are short (few KB)
Packet loss on short flows  TCP timeout
TCP minimum timeout (used to be) 300ms on Windows …

## Slide 14: Are you convinced that this is a real problem?

## Slide 15
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 16: Time is money
Return results “quickly” else no adclicks
TLA and MLAs have tight latency budgets
Results from “late” workers ignored
Poor quality results: no adclicks
The Cost of Latency – Perspectives (mvdirona.com)

## Slide 17: In summary
Partition/aggregate  Incast
Incast  Packet loss
Loss  TCP Timeouts
TCP Timeouts  Delayed/missing results
Delayed/missing results  loss of revenue

## Slide 18: Do you agree that this problem is worth solving?

## Slide 19
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 20: How would you solve the problem? Poor search performance due to TCP incast resulting from partition/aggregate pattern

## Slide 21: Don’t do scatter/gather
No other way to “scale horizontally”
More MLAs do not fundamentally fix incast
Caching etc. possible but not always feasible

## Slide 22: Use more workers
Take first “N” who finish
Often used as a strategy to deal with “stragglers”
Good idea if “straggling” not coorelated with load
Bad idea here: makes incast worse!

## Slide 23: Schedule flows centrally to avoid collision
Proposed by MIT and Facebook
Does not scale

## Slide 24: RTS/CTS to avoid collision
Request to send/clear to send
This (partly) how WiFi works
Adds latency – trading median for tail
Used by Microsoft to beat sorting record

## Slide 25: Jitter to avoid collision
Workers add random delay before responding
This is (partly) how WiFi protocol works
Adds latency – trading median for tail
Original solution attempted at Bing

## Slide 26: Bigger buffers at routers
Router buffer has to support line rates
64x100G  6.4 Tbps read/write bandwidth!
Very expensive and power hungry!

## Slide 27: Reduce TCP timeout
Microsecond timers can be CPU expensive
Does not avoid drops!
Must retransmit dropped packets
Proposed by CMU

## Slide 28: What else can you think of?

## Slide 29
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 30: Prior work oversimplified the problem by focusing only on short flows

## Slide 31
Database held by workers is continuously being refreshed
Long-lived, throughput sensitive flows
these flows also eat up switch buffer

## Slide 32: DCTCP Key Insights
Congestion from two sources:
  Long flows: throughput
  Short query flows: Latency
Convey congestion as soon as possible
  long flows react quickly
  short flows have chance to react
Maintain persistently low buffer occupancy

## Slide 33
Reaction
Point (RP)
Congestion Point (CP)
Notification Point (NP)
Router
Sender
Receiver
If qlen >= K, mark ECN
Echo ECN to RP
Estimate fraction of marked packets
Adjust cwnd accordingly
Data
Data
Ack
DCTCP at a glance
See paper for more details

## Slide 34: What would you have done differently?

## Slide 35
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 36: Results Summary (see paper for details)
Comparison to TCP w/o RED, and w/ RED
High throughput for long flows, short FCT for query flows
Lower queue length
Better/comparable convergence and fairness

## Slide 37: Used by
Microsoft
Google
Morgan Stanley
….
IETF standard

## Slide 38
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 39: DCTCP was about Bing.
We will now switch to Azure.

## Slide 40
Forget everything about DCTCP.

## Slide 41: RDMA Remote Direct Memory Access
Presenting work of many teams in Microsoft

## Slide 42
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 43: High throughput, low-latency Disk I/O with minimal CPU overhead

## Slide 44: How does Azure make money?
We buy CPUs from Intel and AMD in bulk
We rent them out (VMs)
Minimize cores spent on non-chargeable tasks

## Slide 45: Public cloud VMs
VMs “run” on compute servers
  Lots of cores, lots of RAM and some flash
Mount disks from dedicated storage servers
  Few cores, some RAM, and a ton of flash drives
Allows for better resource management, fault tolerance etc.
wee bit of disaggregated computing

## Slide 46: Disk I/O traffic
“east-west”
Dominant traffic in data centers (bytes, packets, flows ..)
Affects performance of databases, Spark clusters …
We own “both ends”

## Slide 47
“Write the block of data to remote disk y, address z”
TCP: Waste of CPU, high latency due to CPU processing
Application
Application
TCPIP
TCPIP
Post
Packetize
Indicate
Interrupt
Stream
Copy
CPU
CPU

## Slide 48: Reducing CPU usage for disk IO
More cores left to sell on compute VMs
Can buy fewer/cheaper storage servers
Millions of dollars to our bottom line
Better performance for customers

## Slide 49: Do you agree that this is a real problem, worth solving?

## Slide 50
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 51: Nope…not when we started
Public clouds were (still) relatively new
The scale, the cost equations, customer expectations, were rapidly evolving
Somewhat akin to research in DC fabric design
Lot of recent work, some which we will cover

## Slide 52: How would you solve the problem? High throughput, low-latency Disk I/O with minimal CPU overhead

## Slide 53: Improve TCP performance
Stack optimizations
Large Send Offload
Not enough – latency due to context switch remains

## Slide 54: Some other transport protocol
We do own both ends …
Congestion control etc. is not the key issue
If it burns CPUs, same problem

## Slide 55: DPDK
Low latency, yes.
Low CPU: most definitely not
If cores become cheap, this may the way to go

## Slide 56
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 57
“Write the block of data to remote disk y, address z”
TCP: Waste of CPU, high latency due to CPU processing
Application
Application
TCPIP
TCPIP
Post
Packetize
Indicate
Interrupt
Stream
Copy
CPU
CPU
  RDMA: NIC handles all transfers via DMA
Application
Application
Memory
Buffer A
Write local buffer at Address A to remote
buffer at Address B
Buffer B is filled
DMA
Memory
Buffer B
DMA

## Slide 58: Microbenchmarks
High throughput
without CPU
overhead
Low latency

## Slide 59: Do you agree that RDMA is the way to go?

## Slide 60: But ….
Prior RDMA deployments:
  Small scale – O(1K) servers only
  InfiniBand: Not compatible with Ethernet/IP
How to run RDMA over standard Ethernet/IP at datacenter scale?

## Slide 61: Challenges
Mapping IB to Ethernet/IP
Scaled-out lossless fabric
Congestion control
Switch buffer management
Deadlocks
…….

## Slide 62: RoCEv2 Routable RDMA over Converged Ethernet
Ethernet
IP
UDP
InfiniBand L4
RoCEv2 packet format
Very efficient, but
requires a lossless* fabric
for optimal performance
*Lossless: no congestion packet drop
Payload

## Slide 63: Why Lossless Fabric
Fast start
  Reduce short flow latency in common cases
No retransmission due to congestion drop
  Reduce tail latency
  Simplifies transport protocol
ACK consolidation
  Improve efficiency

## Slide 64: Lossless Ethernet
Ethernet
IP
UDP
InfiniBand L4
RoCEv2 packet format
Needs a lossless fabric
for fast start, no retransmission…
Priority-based Flow Control (PFC)
IEEE 802.1Qbb
Lossless Ethernet
Payload

## Slide 65: Priority-based Flow Control (PFC)
PAUSE upstream neighbor when queue size reaches PFC threshold
  No congestion packet drop
PFC troublesome in large-scale deployments
PFC PAUSE threshold: 3
PAUSE
Congestion

## Slide 66: PFC problems
Need headroom reservation
  Enough to buffer all packets in flight
  Lots of buffer needed if link is loing
Deadlock (A->B->C->B->A)
  Circular buffer dependdency
Victim flows …

## Slide 67: Victim Flow Problem
Cascading link PAUSEing
PFC operates on port-level, instead of flow-level
Red flow is victimized
H1
H2
H3
R
Ideal throughput 40-13.3=26.6Gbps
Throughput (Gbps)
H1 H2 H3
0
10
20
30
S
Host
D
S
1
2
3
4
40/3=13.3Gbps

## Slide 68: Possible Solutions
Don’t use PFC
  We’ll come back to this later if we have time
Separate priorities for each flow
  Not scalable

## Slide 69: Our Solution PFC as last resort
Keep PFC
Use per-flow E2E congestion control
Per flow CC reduces PFC generation
BUT… lossless fast start, no retransmission, ...

## Slide 70: What kind of CC do we need?
Must work with commodity hardware
Must be configurable to minimize PFC generation
Can’t rely on packet drops
Easy to implement in hardware

## Slide 71: If you can’t rely on packet drops
ECN
Delay
Explicit feedback from routers

## Slide 72
Forget everything about DCTCP.
Remember DCTCP?

## Slide 73
Reaction
Point (RP)
Congestion Point (CP)
Notification Point (NP)
Router
Sender
Receiver
Mark ECN
Kmin, Kmax and Pmax adjusted to ensure ECN before PFC
Echo ECN to RP
Via CNP
Count CNPs
Adjust rate accordingly
Data
Data
Ack
DCQCN at a glance
See paper for more details

## Slide 74
Just to impress you with our math skills ….

## Slide 75: In summary
Azure makes money by renting CPUs
TCP wastes CPU
Hence need RDMA
RDMA needs PFC
PFC causes problems
Hence DCQCN

## Slide 76: What would you have done?

## Slide 77
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 78: Results summary
DCQCN reduce PFCs by a factor of 1000
Unfairness, deadlock etc. not seen
Azure RDMA deployment would have been impossible without DCQCN
67% of Azure traffic is on RDMA : O(1018) bytes /day
TCP is a distant second
The trend will accelerate

## Slide 79: Finally
(we believe that) Azure has the world’s largest RDMA deployment
Took lot more than just DCQCN to make it work
See our papers for more … (and more will be written)
Lot of ongoing work: customized rdma, long-haul, many other domains, RDMA to VMs …

## Slide 80
What’s your problem? What are you trying to solve, really?
Okay, fine. Why should anyone care about this problem?
But .. there is so much prior work. That wasn’t enough?
FINE. What’s your secret sauce?
Right …right. You are so smart. Prove to me that your secret sauce indeed works as promised.
Umm … is anyone really using it? What next?

## Slide 81: Questions? we are hiring …
H/T Sarah McClure, for comments and editing