## Slide 1: Topology Design
CSE 561, Winter 2021
Radhika Niranjan Mysore

## Slide 2: What we read
How data center topology design can impact lifecycle cost
Deploy
Operate
Expand
Time to bring up network
  Ordering components, cabling
  O(types), O(connections)
Cost of the network
  O(components)
Time spent on management tasks
  Planned: configuring, control
  O(failure domains), O(controllers), O(heterogeneity), O(corner cases)
  Unplanned: debugging
  O(1/visibility)
Time to bring up new network
  Ordering, cabling
  O(types), O(connections)
Duration of degraded capacity
  O(1/redundant capacity)
Cost of new network
  O(components)
Notes: Write down polynomial time complexity

## Slide 3: What we didn’t read (my hypothesis)
How data center topology design can impact lifecycle cost
Time to bring up network
  Ordering components, cabling
  O(types), O(connections)
Duration of degraded capacity
  O(size of network upgraded)
Cost of upgraded network
  O(components)
Time spent on management tasks
  Planned: configuring, control
  O(failure domains), O(controllers), O(heterogeneity), O(corner cases)
  Unplanned: debugging
  O(1/visibility)
Time to tear down network
  Cabling
  O(connections)
Duration of degraded capacity
  O(1/redundant capacity)
Upgrade
Operate
Decommission

## Slide 4: What we didn’t read (my hypothesis)
How data center topology design can impact lifecycle cost
Upgrade
Operate
Decommision
Time to bring up network
  Ordering components, cabling
  O(types), O(connections)
Duration of degraded capacity
  O(size of network upgraded)
Cost of upgraded network
  O(components)
Time spent on management tasks
  Planned: configuring, control
  O(failure domains), O(controllers), O(heterogeneity), O(corner cases)
  Unplanned: debugging
  O(1/visibility)
Time to tear down network
  Cabling
  O(connections)
Duration of degraded capacity
  O(1/redundant capacity)

## Slide 5: This talk
Design of data center network topologies
*Topology: L1-L3 structure and components
  Inputs
    What parameters do you usually start with?
  Trade-off considerations
    What choices do you have to make?
  Outputs
    What kinds of network designs emerge?
  Design constructs
    What are certain recurring abstractions of network design?

## Slide 6: This talk
Design of data center network topologies
*Topology: L1-L3 structure and components
  Inputs
    What parameters do you usually start with?
  Trade-off considerations
    What choices do you have to make?
      Connecting DCs to campus/WAN (Iris SIGCOMM 2020)
      Reacting to failures
      Moving to optical cores (Sirius SIGCOMM 2020)
  Outputs
    What kinds of network designs emerge?
  Design constructs
    What are certain recurring abstractions of network design?

## Slide 7: Topology design constructs in the paper
Wiring
Chassis backplane
Cable bundles (regularity)
Expansion
Fat Edge
Servers
Southbound links
Switches
Deployment
Building blocks (modularity)
Northbound links
Figure 9 and 13 from Jupiter Rising: A Decade of Clos Topologies and Centralized Control in Google’s Datacenter Network, SIGCOMM 2015

## Slide 8: This talk
WCMP: Weighted Cost Multipathing for Improved Fairness in Data Centers, Eurosys 2014
Jupiter Rising: A Decade of Clos Topologies and Centralized Control in Google’s Datacenter Network, SIGCOMM 2015
Experience with B4: Google's Private SDN Backbone, Subhasree Mandal, Usenix ATC 2015
Pluggable DWDM: Considerations For Campus and Metro DCI Applications, ECOC 2016
Sirius: A Flat Datacenter Network with Nanosecond Optical Switching, SIGCOMM 2020
Beyond the mega-data center: networking multi-data center regions, SIGCOMM 2020
Condor: Better Topologies Through Declarative Design, SIGCOMM 2015
Understanding Lifecycle Management Complexity of Datacenter Topologies, NSDI 2019

## Slide 9: Problem: Designing (data center) networks
How do you connect compute, memory, storage so that it …
  .. fits power budgets (including cooling)
  .. fits space constraints
  .. leverages current and emerging network hardware
  .. supports current and future application traffic
  .. is resilient to failures
  .. is cheap to build (deploy, upgrade, expand, decommission)
  .. is cheap to operate

## Slide 10: Problem: Designing (data center) networks with CSE 561
How do you connect compute, memory, storage so that it …
  .. fits power budgets (including cooling)
  .. fits space constraints
  .. leverages current and emerging hardware
    Congestion control (buffers, table sizes, switching elements)
  .. supports current and future application traffic
    Application placement, routing, traffic (topology) engineering
  .. is resilient to failures
    Routing, traffic (topology) engineering
  .. is cheap to build (deploy, upgrade, expand, decommission)
    Reading for this talk
  .. is cheap to operate
    SDN control, BGP, MPLS, ECMP, WCMP, L2, monitoring and diagnosis, modularity and function decoupling (Jupiter SIGCOMM 2015, B4 ATC 2015), configuration (DAC 2010), out-of-band network management …
Input

## Slide 11: Data center design inputs (rough)
Inputs | Determined by | Example
Server or compute count (scale) | Space and power constraints | 500-4000 servers
Rack space specification | Space and power constraints | 52U rack
Candidate hardware (switches, cable, patch panels/OCS) | Existing hardware, scale, budget/vendor partnership considerations | 32 port 100G switches
Oversubscription ratio | Application requirements (projected), end-host hardware | 3:1
Internal connectivity requirements | Application requirements (projected) | Full bisection bandwidth within DC
External connectivity requirements | Application requirements (projected) | 20-30% Egress bandwidth to Campus, WAN network
Initial server deployment count | Application requirements (current vs. projected) | ~500

## Slide 12: Connectivity
Network building blocks
  For each block
    Decide the number of layers or desired port count out of the block
    More layers  more scale
  Split switch ports into downlinks and uplinks
    Server links, WAN links
WAN link placement (Jupiter SIGCOMM 2015)
  Identify which switches WAN controller must talk to
    Explore trade-offs
      More switches  More updates, controller bugs impact all switches (blast radius)
      More switches  More resilient to switch failures
      Bouncing WAN traffic across spines allows opportunities for loadbalancing

## Slide 13: Connecting the data center in blocks
..4..
..16..
16x8 uplinks
4x32 downlinks
20x2 servers, 4 WAN links per ToR
Spine
ToR
~640 servers in one block
.. 8..
..32..
32x16 uplinks
8x32 downlinks
24x2 servers (blue ToR x 26), 6 WAN ToRs
Spine
ToR
~1040 servers in one block
More space
Larger applications
More resilience
Equivalent (~20%) WAN bandwidth
..4..
..8..
24x2 servers
Aggregation
ToR
~320 servers in one block
8x8 uplinks
4x16 downlinks
4x16 uplinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
..8..
To Campus/WAN
Aggregation
ToR
4 Campus/WAN blocks
8x8 uplinks
4x16 downlinks
4x16 uplinks
..16..
..16..
1
2
3
~3840 servers in one block
Even more space
Much larger applications
Much more resilience
~30% WAN bandwidth

## Slide 14: Connecting the data center in blocks
1
Small power/space footprint (mini DC)
  Suitable for colos, edge
*Small application footprint
~20% WAN bandwidth out of each ToR
  Limited WAN burst bandwidth, but more resilient to ToR failures
  Changes to WAN fabric connectivity will be reflected in the ToR switches (blast radius)
..4..
..16..
16x8 uplinks
4x32 downlinks
20x2 servers, 4 WAN links per ToR
Spine
ToR
~640 servers in one block

## Slide 15: Connecting the data center in blocks
~640 servers in one block
.. 8..
..32..
32x16 uplinks
8x32 downlinks
24x2 servers (blue ToR x 26), 6 WAN ToRs
Spine
ToR
~1040 servers in one block
More space
Larger applications
More resilience
1
2
Small power/space footprint (mini DC)
  Suitable for colos, edge.
*Small application footprint
~20% WAN bandwidth from reserved ToRs
  WAN traffic bounces off spines  flexible burst bandwidth
  Changes to WAN fabric connectivity will be reflected in the WAN ToRs *and* spines (blast radius)
..4..
..16..
16x8 uplinks
4x32 downlinks
20x2 servers, 4 WAN links per ToR
Spine
ToR

## Slide 16: Connecting the data center in blocks
..4..
..8..
24x2 servers
Aggregation
ToR
~320 servers in one block
8x8 uplinks
4x16 downlinks
4x16 uplinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
..8..
To Campus/WAN
Aggregation
ToR
4 Campus/WAN blocks
8x8 uplinks
4x16 downlinks
4x16 uplinks
..16..
..16..
3
~3840 servers in one block
Large power/space footprint
Large application footprint
~30% egress bandwidth out of Campus/ WAN blocks
  WAN traffic routed to WAN blocks  flexible burst bandwidth
  Changes to WAN fabric connectivity will be reflected in WAN blocks (blast radius)

## Slide 17: Design construct: Wan connectivity design
Keep WAN blocks separate (blast radius)
  Bugs in WAN controllers do not impact intra-data center traffic
Design full bisection bandwidth to WAN blocks to absorb bursts
..4..
..8..
24x2 servers
Aggregation
ToR
~320 servers in one block
8x8 uplinks
4x16 downlinks
4x16 uplinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
..8..
To Campus/WAN
Aggregation
ToR
4 Campus/WAN blocks
4x16 downlinks
4x16 uplinks
..16..
..16..
~3840 servers in one block

## Slide 18: Connecting the data center in blocks
..4..
..8..
24x2 servers
Aggregation
ToR
~320 servers in one block
8x8 uplinks
4x16 downlinks
4x16 uplinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
..8..
To Campus/WAN
Aggregation
ToR
4 Campus/WAN blocks
8x8 uplinks
4x16 downlinks
4x16 uplinks
..4..
..16..
4
~3840 servers in one block
..4..
..8..
24x2 servers
Aggregation
ToR
~320 servers in one block
4x16 downlinks
4x16 uplinks
Replace spines by direct optical links
  Reduced bisection bandwidth but reduced cost
WCMP, non-shortest path routing to utilize links effectively

## Slide 19: Resilience
.. 8..
..32..
Link failure
Spine
ToR
.. 8..
..32..
Spine switch failure
Spine
ToR
.. 8..
..32..
WAN link failure
Spine
ToR
Identify switches impacted by failure (blast radius)
Identify how controller will handle the failure
  How many updates are required to change the routing tables?
  How much space will the new routing table occupy?
1
2
3

## Slide 20: Resilience: blast radius
.. 8..
..32..
Spine
ToR
.. 8..
..32..
Spine
ToR
.. 8..
..32..
Spine
ToR
Identify switches impacted by failure (blast radius)
Identify how controller will handle the failure
  How many updates are required to change the routing tables?
  How much space will the new routing table occupy?
Link failure
Spine switch failure
WAN link failure
1
2
3

## Slide 21: Resilience: control decision
Use WCMP to avoid drops at spine
Blacklist spine (trade-off redundancy for table updates)
.. 8..
..32..
Spine
ToR
.. 8..
..32..
Spine
ToR
.. 8..
..32..
Spine
ToR
Avoid spine
Readjust reachable prefixes in every spine
Use supertrunks to avoid prefix explosion (B4, ATC 2015)
Use WCMP to readjust load to supertrunk
Link failure
Spine switch failure
WAN link failure
1
2
3

## Slide 22: Design construct: Supertrunks
Multiple links between switches combined into a “trunk” with single prefix (trade-off WAN increment granularity for table space)
Single link failure masked by trunk
  Prefix is still reachable but with reduced capacity
.. 8..
..32..
WAN router

## Slide 23: Using optical cores for connectivity
To connect mini data centers within a region (120km radius)
  Beyond the mega-data center: networking multi-data center regions, SIGCOMM 2020
Within the datacenter
  Sirius: A Flat Datacenter Network with Nanosecond Optical Switching, SIGCOMM 2020
*Thoughts are my own, contact authors for clarifications
Trade-off ease of connectivity/routing for reduced power, lower latency
  Optical switches require establishing n2 connections
    A 128 port optical switch can connect 64 server pairs at a time. In contrast a 128 port electrical switch can connect all 128 servers to each other (16256 server pairs)
http://www.fiber-optical-networking.com/how-to-arrange-the-fiber-cables-in-the-fibre-optic-patch-panel.html

## Slide 24: Connecting data centers (Google)
Figure from Pluggable DWDM: Considerations For Campus and Metro DCI Applications, ECOC 2016

## Slide 25: Connecting data centers (Google)
Sirius
Iris
Figure from Pluggable DWDM: Considerations For Campus and Metro DCI Applications, ECOC 2016

## Slide 26: Iris: Connecting datacenters within 120km
Motivation
  Data center space premium, cannot build mega data centers
  Large amounts of unlit fiber already deployed in metro regions
.. 8..
..32..
32x16 uplinks
8x32 downlinks
24x2 servers (blue ToR x 26), 6 WAN ToRs
Spine
ToR
.. 8..
..32..
32x16 uplinks
8x32 downlinks
24x2 servers (blue ToR x 26), 6 WAN ToRs
Spine
ToR
.. 8..
..32..
32x16 uplinks
8x32 downlinks
24x2 servers (blue ToR x 26), 6 WAN ToRs
Spine
ToR
A
B
C
Fiber hut
Fiber hut

## Slide 27: Iris: Connecting datacenters within 120km
Problem: what network connectivity must we overlay to manage traffic between data centers?
  Solution 1: Use electrical switches at fiber huts to route traffic
  Solution 2: Use optical switches
.. 8..
..32..
32x16 uplinks
8x32 downlinks
24x2 servers (blue ToR x 26), 6 WAN ToRs
Spine
ToR
.. 8..
..32..
32x16 uplinks
8x32 downlinks
24x2 servers (blue ToR x 26), 6 WAN ToRs
Spine
ToR
.. 8..
..32..
32x16 uplinks
8x32 downlinks
24x2 servers (blue ToR x 26), 6 WAN ToRs
Spine
ToR
A
B
C
Fiber hut
Fiber hut

## Slide 28: Iris: Connecting datacenters within 120km
Solution: Use optical switches
  Electrical switches require optical transceivers to convert light to electrical signal and vice versa. Transceiver cost increases with cable length
  Trade-off # of optical transceivers by using extra fiber (additional capacity) between DCs
  Challenge: Managing amplification for light from optical cables of different length
    Design construct:
      power-limiters before each amplifier to bound input optical power
      amplified spontaneous emission noise for unused spectrum

## Slide 29: Sirius: Connecting ToRs with optics
Motivation
  End of Dennard scaling (+slowing of Moore’s law)  mega data centers with electrical switches are much more power hungry than data centers with optical switches
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks
..4..
..8..
24x2 servers
Aggregation
ToR
~320 servers in one block
8x8 uplinks
4x16 downlinks
4x16 uplinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
Spine
4x16 downlinks
2x32 downlinks
..4..
..8..
To Campus/WAN
Aggregation
ToR
4 Campus/WAN blocks
4x16 downlinks
4x16 uplinks
..16..
..16..
~3840 servers in one block
Much more space
Much larger scale
64 port 400-800G ToR

## Slide 30: Sirius: Connecting ToRs with optics
Key Ideas
  Each ToR port connects twice (logically?) to 16 gratings (shown as uplink and downlink)
  Each ToR port connects to a different destination ToR port by cycling through 16 wavelengths
    Disaggregated tunable laser
  Switching wavelengths takes 1ns
  Packets can bounce of intermediate ToRs on their way to destination
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1 ns
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks

## Slide 31: Sirius: Connecting ToRs with optics
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1ns
Reachability: How are 4096 ToRs connected to each other?
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks

## Slide 32: Sirius: Connecting ToRs with optics
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1 ns
Reachability: How are 4096 ToRs connected to each other?
  Each ToR port reaches 16 different ports using 16 wavelengths, one at a time  Spread through time
  Each ToR has 16 uplinks  Each ToR reaches 16 wavelengths * 16 ports = 256 different ToRs
  If these are intermediate ToRs, each of the 256 ToRs can reach 16 other ToRs via their uplinks  256 * 16 = 4096 ToR switches  Spread through time
Contrast to equivalent electrical switches
  Any switch can reach any other switch (spatial)
  Paths have latency corresponding to switching latency
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks

## Slide 33: Sirius: Connecting ToRs with optics
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1 ns
Throughput: What is the effective bandwidth of each port?
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks

## Slide 34: Sirius: Connecting ToRs with optics
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1ns
Throughput: What is the effective bandwidth of each port?
  Transmission time of 576B packet
  Time to transmit 16, 576B packets to 16 destinations
  Throughput of the port
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks

## Slide 35: Sirius: Connecting ToRs with optics
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1ns
Throughput: What is the effective bandwidth of each port?
  Transmission time of 576B packet
    576*8/800 = 5.76ns
  Time to transmit 16, 576B packets to 16 destinations
    (5.76ns + 1ns) * 16 = 108.16ns
  Throughput of the port
    16 packets * 576 *8 bits/ 108.16 ns = 681.7Gbps
Contrast to equivalent electrical switches
  Each port will be 800Gbps
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks

## Slide 36: Sirius: Connecting ToRs with optics
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1ns
  100ns FEC
Buffering: How much receive buffering do you need at intermediate ToRs?*
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks
*Calculation depends on ToR hardware design

## Slide 37: Sirius: Connecting ToRs with optics
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1ns
  100ns FEC
Buffering: How much receive buffering do you need at intermediate ToRs?*
  Total time to receive 16 576B packets from 16 ports
  Number of packets received in that time
  Amount of buffering needed to absorb 10us of that delay
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks
*Calculation depends on ToR hardware design

## Slide 38: Sirius: Connecting ToRs with optics
Exercise parameters
  64 port 800Gbps ToR switches
  576B cells/packets
  Switching time 1ns
  100ns FEC
Buffering: How much receive buffering do you need at intermediate ToRs?*
  Total time to receive 16 576B packets from 16 ports
    6.76ns + 100ns = 106.76ns
  Number of packets received in that time
    106.76 ns / 6.76 ns * 16 = 252.69 packets (145547.36B)
  Amount of buffering needed to absorb 10us of that delay
    10000 ns * 145547.36 B/106.76 ns = 13633136.09B = 13.63MB
Contrast to equivalent electrical switches
  Tomahawk 3 ( 64port 200Gbps switch) already has 64MB buffering (40us)
    Backpressure Flow Control, arXiv 2019
  Sirius might need additional buffering for intermediate switching
Gratings
..16..
..4096..
65536-131072 servers (16-32 servers per ToR)
ToR
16 x 16 uplinks
..4096..
ToR
16 x 16 downlinks
*Calculation depends on ToR hardware design

## Slide 39: This talk
Design of data center network topologies
  Inputs
    What parameters do you usually start with?
  Trade-off considerations
    What choices do you have to make?
      Connecting DCs to campus/WAN (Iris SIGCOMM 2020)
      Reacting to failures
      Moving to optical cores (Sirius SIGCOMM 2020)
  Outputs
    What kinds of network designs emerge?
  Design constructs
    What are certain recurring abstractions of network design?

## Slide 40: Happy to connect and chat more
rniranjan@vmware.com

## Slide 41: Examples of component features influencing topology structure
Number of hash functions in a chip  number of effective outgoing links for ECMP
North/South port connection restrictions in patch panels
Table size, e.g., number of WCMP/ECMP entries in a table