## Slide 1: Tree-Growing Sample-Based Motion Planning

## Slide 2: Probabilistic Roadmaps
What if omnidirectional motion in C-space is not permitted?
What if only a small portion of the space needs to be explored?

## Slide 3: Tree-growing planners
Idea: grow a tree of feasible paths from the start until it reaches a neighborhood of the goal
  Sampling bias toward “boundary” of currently explored region, helps especially if the start is in a region with poor visibility
Many variants:
  Rapidly-exploring Random Trees (RRTs) are popular, easy to implement (LaValle and Kuffner 2001)
  Expansive space trees (ESTs) use a different sampling strategy (Hsu et al 2001)
  SBL (Single-query, Bidirectional, Lazy planner) often efficient in practice (Sanchez-Ante and Latombe, 2005)

## Slide 4: RRT
Build a tree T of configurations, starting at xstart
Extend:
  Sample a configuration xrand from C at random
  Find the node xnear in T that is closest to xrand
  Extend a short path from xnear toward xrand
T

## Slide 5: RRT
Build a tree T of configurations, starting at xstart
Extend:
  Sample a configuration xrand from C at random
  Find the node xnear in T that is closest to xrand
  Extend a short path from xnear toward xrand
xrand
xnear

## Slide 6: RRT
Build a tree T of configurations, starting at xstart
Extend:
  Sample a configuration xrand from C at random
  Find the node xnear in T that is closest to xrand
  Extend a short path from xnear toward xrand
xrand
xnear

## Slide 7: RRT
Build a tree T of configurations, starting at xstart
Extend:
  Sample a configuration xrand from C at random
  Find the node xnear in T that is closest to xrand
  Extend a short path from xnear toward xrand
xrand
xnear

## Slide 8: RRT
Build a tree T of configurations, starting at xstart
Extend:
  Sample a configuration xrand from C at random
  Find the node xnear in T that is closest to xrand
  Extend a short path from xnear toward xrand

## Slide 9: RRT
Build a tree T of configurations, starting at xstart
Extend:
  Sample a configuration xrand from C at random
  Find the node xnear in T that is closest to xrand
  Extend a short path from xnear toward xrand
xrand
xnear

## Slide 10: RRT
Build a tree T of configurations, starting at xstart
Extend:
  Sample a configuration xrand from C at random
  Find the node xnear in T that is closest to xrand
  Extend a short path from xnear toward xrand

## Slide 11: RRT
Build a tree T of configurations, starting at xstart
Extend:
  Sample a configuration xrand from C at random
  Find the node xnear in T that is closest to xrand
  Extend a short path from xnear toward xrand
Governed by a step size parameter d

## Slide 12: Implementation Details
Bottleneck: finding nearest neighbor each step
  O(n) with naïve implementation => O(n2) overall
  KD tree data structure O(n1-1/d)
  Approximate nearest neighbors often very effective
Terminate when extension reaches a goal set
  Usually visibility set of goal configuration
Bidirectional strategy
  Grow a tree from goal as well as start, connect when closest nodes in either tree can “see” each other

## Slide 13: What is the sampling strategy?
Probability that a node gets selected for expansion is proportional to the volume of its Voronoi cell

## Slide 14: Planning with Differential Constraints
(Kinodynamic Planning)

## Slide 15: Paths for a Car-Like Robot
Notes: 15

## Slide 16: Setting
Differential constraints
Dynamics, nonholonomic systems
dq/dt = Sk fk(q)uk
Vector fields
Controls
We’ll consider fewer control dimensions than state dimensions

## Slide 17: Example: 1D Point Mass
Mass M
2D configuration space (state space)
Controlled force f
Equations of motion:
x
v
dx/dt = v dv/dt = f / M

## Slide 18: Example: 1D Point Mass
x
v
dx/dt = dv dv/dt = f / M
Solution:
v(t) = v(0)+t f /M
x(t) = x(0)+t v(0) + ½ t2 f / M
x
v
f=0

## Slide 19: Example: 1D Point Mass
x
v
x
v
f>0
dx/dt = dv dv/dt = f / M
Solution:
v(t) = v(0)+t f /M
x(t) = x(0)+t v(0) + ½ t2 f / M

## Slide 20: Example: 1D Point Mass
x
v
x
v
f<0
dx/dt = dv dv/dt = f / M
Solution:
v(t) = v(0)+t f /M
x(t) = x(0)+t v(0) + ½ t2 f / M

## Slide 21: Example: 1D Point Mass
x
v
x
v
|f|<=fmax
dx/dt = dv dv/dt = f / M
Solution:
v(t) = v(0)+t f /M
x(t) = x(0)+t v(0) + ½ t2 f / M

## Slide 22: Example: Car-Like Robot
Configuration space is 3-dimensional: q = (x, y, q)
But control space is 2-dimensional: (v, f) with |v| = sqrt[(dx/dt)2+(dy/dt)2]
y
x
L
q
f
f
q
dx/dt = v cosq
dy/dt = v sinq
dq/dt = (v/L) tan f
|f| < F
dx sinq – dy cosq = 0
Notes: 22

## Slide 23: Example: Car-Like Robot
q = (x,y,q)
q’= dq/dt = (dx/dt,dy/dt,dq/dt) dx sinq – dy cosq = 0 is a particular form of f(q,q’)=0
A robot is nonholonomic if its motion is constrained by a non-integrable equation of the form f(q,q’) = 0
dx/dt = v cosq
dy/dt = v sinq
dq/dt = (v/L) tan f
|f| < F
dx sinq – dy cosq = 0
y
x
L
q
f
f
q
Notes: 23

## Slide 24: Example: Car-Like Robot
y
x
L
q
f
f
q
dx/dt = v cosq
dy/dt = v sinq
dq/dt = (v/L) tan f
|f| < F
dx sinq – dy cosq = 0
Lower-bounded turning radius
Notes: 24

## Slide 25: How Can This Work? Tangent Space/Velocity Space
y
x
L
q
f
f
q
x
y
q
(x,y,q)
q
(dx,dy,dq)
(dx,dy)
dx/dt = v cosq
dy/dt = v sinq
dq/dt = (v/L) tan f
|f| < F
Notes: 25

## Slide 26: How Can This Work? Tangent Space/Velocity Space
y
x
L
q
f
f
q
x
y
q
(x,y,q)
q
(dx,dy,dq)
(dx,dy)
dx/dt = v cosq
dy/dt = v sinq
dq/dt = (v/L) tan f
|f| < F
Notes: 26

## Slide 27: Nonholonomic Path Planning Approaches
Two-phase planning (path deformation):
  Compute collision-free path ignoring nonholonomic constraints
  Transform this path into a nonholonomic one
  Efficient, but possible only if robot is “controllable”
  Need for a “good” set of maneuvers
Direct planning (control-based sampling):
  Use “control-based” sampling to generate a tree of milestones until one is close enough to the goal (deterministic or randomized)
  Robot need not be controllable
  Applicable to high-dimensional c-spaces
Notes: 27

## Slide 28: Control-Based Sampling
PRM sampling technique: Pick each milestone in some region
Control-based sampling:
  Pick control vector (at random or not)
  Integrate equation of motion over short duration (picked at random or not)
  If the motion is collision-free, then the endpoint is the new milestone
  Tree-structured roadmaps
  Need for endgame regions
Notes: 28

## Slide 29: Example
1. Select a milestone m
2. Pick v, f, and dt
3. Integrate motion from m
 new milestone m’
dx/dt = v cosq
dy/dt = v sinq
dq/dt = (v/L) tan f
|f| < F
Notes: 29

## Slide 30: Example
Indexing array: A 3-D grid is placed over the configuration space. Each milestone falls into one cell of the grid. A maximum number of milestones is allowed in each cell (e.g., 2 or 3).
Asymptotic completeness: If a path exists, the planner is guaranteed to find one if the resolution of the grid is fine enough.
Notes: 30

## Slide 31: Computed Paths
jmax=45o, jmin=22.5o
Car That Can Only Turn Left
jmax=45o
Tractor-trailer
Notes: 31

## Slide 32: Control-Sampling RRT
Configuration generator f(x,u)
Build a tree T of configurations
Extend:
  Sample a configuration xrand from X at random
  Find the node xnear in T that is closest to xrand
  Pick a control u that brings f(xnear,u) close to xrand
  Add f(xnear,u) as a child of xnear in T

## Slide 34: Weaknesses of RRT’s strategy
Depends on the domain from which xrand is sampled
Depends on the notion of “closest”
A tree that is grown “badly” by accident can greatly slow convergence

## Slide 35: Other strategies
Dynamic-domain RRTs (Yershova et al 2008)
Perturb samples in a neighborhood (EST, SBL)
Lazy planning: delay expensive collision checks until end