## Slide 1: 3D Sensing
Camera Model and 3D Transformations
Camera Calibration (Tsai’s Method)
Depth from General Stereo (overview)
Pose Estimation from 2D Images (skip)
3D Reconstruction

## Slide 2: Camera Model: Recall there are 5 Different Frames of Reference
Object
World
Camera
Real Image
Pixel Image
yc
xc
zc
zw
C
W
yw
xw
A
a
xf
yf
xp
yp
zp
pyramid
object
image

## Slide 3: Rigid Body Transformations in 3D
zw
W
yw
xw
instance of the
object in the
world
pyramid model
in its own
model space
xp
yp
zp
rotate
translate
scale

## Slide 4: Translation and Scaling in 3D

## Slide 5: Rotation in 3D is about an axis
x
y
z

rotation by angle 
about the x axis
Px´
Py´
Pz´
1
1 0 0 0
0 cos  - sin  0
0 sin  cos  0
0 0 0 1
Px
Py
Pz
1
=

## Slide 6: Rotation about Arbitrary Axis
Px´
Py´
Pz´
1
r11 r12 r13 0
r21 r22 r23 0
r31 r32 r33 0
0 0 0 1
Px
Py
Pz
1
=
T
R1
R2
One translation and two rotations to line it up with a
major axis. Now rotate it about that axis. Then apply
the reverse transformations (R2, R1, T) to move it back.

## Slide 7: The Camera Model
How do we get an image point IP from a world point P?
c11 c12 c13 c14
c21 c22 c23 c24
c31 c32 c33 1
s Ipr
s Ipc
s
Px
Py
Pz
1
=
image
point
camera matrix C
world
point
What’s in C?

## Slide 8: The camera model handles the rigid body transformation from world coordinates to camera coordinates plus the perspective transformation to image coordinates.
1. CP = T R WP
2. IP = (f) CP
s Ipx
s Ipy
s
1 0 0 0
0 1 0 0
0 0 1/f 1
CPx
CPy
CPz
1
=
perspective
transformation
image
point
3D point in
camera
coordinates

## Slide 9: Camera Calibration
In order work in 3D, we need to know the parameters
of the particular camera setup.
Solving for the camera parameters is called calibration.
yw
xw
zw
W
yc
xc
zc
C
intrinsic parameters are
of the camera device
extrinsic parameters are
where the camera sits
in the world

## Slide 10: Intrinsic Parameters
principal point (u0,v0)
scale factors (dx,dy)
aspect ratio distortion factor 
focal length f
lens distortion factor 
(models radial lens distortion)
C
(u0,v0)
f

## Slide 11: Extrinsic Parameters
translation parameters
t = [tx ty tz]
rotation matrix
r11 r12 r13 0
r21 r22 r23 0
r31 r32 r33 0
0 0 0 1
R =

## Slide 12: Calibration Object
The idea is to snap
images at different
depths and get a
lot of 2D-3D point
correspondences.

## Slide 13: The Tsai Procedure
The Tsai procedure was developed by Roger Tsai
at IBM Research and is most widely used.
Several images are taken of the calibration object
yielding point correspondences at different distances.
Tsai’s algorithm requires n > 5 correspondences
{(xi, yi, zi), (ui, vi)) | i = 1,…,n}
between (real) image points and 3D points.

## Slide 14: In this* version of Tsai’s algorithm,
The real-valued (u,v) are computed from their pixel
positions (r,c):
u =  dx (c-u0) v = -dy (r - v0)
where
- (u0,v0) is the center of the image
- dx and dy are the center-to-center (real) distances
between pixels and come from the camera’s specs
-  is a scale factor learned from previous trials
* This version is for single-plane calibration.

## Slide 15: Tsai’s Geometric Setup
Oc
x
y
principal point p0
z
pi = (ui,vi)
Pi = (xi,yi,zi)
(0,0,zi)
x
y
image plane
camera
3D point

## Slide 16: Tsai’s Procedure
1. Given the n point correspondences ((xi,yi,zi), (ui,vi))
Compute matrix A with rows ai
ai = (vi*xi, vi*yi, -ui*xi, -ui*vi, vi)
These are known quantities which will be used to
solve for intermediate values, which will then be
used to solve for the parameters sought.

## Slide 17: Intermediate Unknowns
2. The vector of unknowns is  = (1, 2, 3, 4, 5):
1=r11/ty 2=r12/ty 3=r21/ty 4=r22/ty 5=tx/ty
where the r’s and t’s are unknown rotation and translation parameters.
3. Let vector b = (u1,u2,…,un) contain the u image coordinates.
4. Solve the system of linear equations
A  = b
for unknown parameter vector .

## Slide 18: Use  to solve for ty, tx, and 4 rotation parameters
5. Let U = 1 + 2 + 3 + 4 . Use U to calculate ty .
6. Try the positive square root ty = (ty ) and use it to
compute translation and rotation parameters.
2
2
2
2
2
2
1/2
r11 = 1 ty
r12 = 2 ty
r21 = 3 ty
r22 = 4 ty
tx = 5 ty
(see text)
Now we know
2 translation parameters and
4 rotation parameters.
except…

## Slide 19: Determine true sign of ty and compute remaining rotation parameters.
7. Select an object point P whose image coordinates
(u,v) are far from the image center.
8. Use P’s coordinates and the translation and rotation
parameters so far to estimate the image point
that corresponds to P.
If its coordinates have the same signs as (u,v),
then keep ty, else negate it.
9. Use the first 4 rotation parameters to calculate
the remaining 5.

## Slide 20: Solve another linear system.
10. We have tx and ty and the 9 rotation parameters.
Next step is to find tz and f.
Form a matrix A´ whose rows are:
ai´ = (r21*xi + r22*yi + ty, vi)
and a vector b´ whose rows are:
bi´ = (r31*xi + r32*yi) * vi
11. Solve A´*v = b´ for v = (f, tz).

## Slide 21: Almost there
12. If f is negative, change signs (see text).
13. Compute the lens distortion factor  and improve
the estimates for f and tz by solving a nonlinear
system of equations by a nonlinear regression.
14. All parameters have been computed.
Use them in 3D data acquisition systems.

## Slide 22: We use them for general stereo.
P
P1=(r1,c1)
P2=(r2,c2)
y1
y2
x1
x2
e1
e2
C1
C2

## Slide 23: For a correspondence (r1,c1) in image 1 to (r2,c2) in image 2:
1. Both cameras were calibrated. Both camera matrices are
then known. From the two camera equations we get
4 linear equations in 3 unknowns.
r1 = (b11 - b31*r1)x + (b12 - b32*r1)y + (b13-b33*r1)z
c1 = (b21 - b31*c1)x + (b22 - b32*c1)y + (b23-b33*c1)z
r2 = (c11 - c31*r2)x + (c12 - c32*r2)y + (c13 - c33*r2)z
c2 = (c21 - c31*c2)x + (c22 - c32*c2)y + (c23 - c33*c2)z
Direct solution uses 3 equations, won’t give reliable results.

## Slide 24: Solve by computing the closest approach of the two skew rays.
If the rays
intersected
perfectly in 3D,
the intersection
would be P.
V
Instead, we solve for the shortest line
segment connecting the two rays and
let P be its midpoint.
P1
Q1
P
solve for
shortest

## Slide 25: Application: Kari Pulli’s Reconstruction of 3D Objects from light-striping stereo.

## Slide 26: Application: Zhenrong Qian’s 3D Blood Vessel Reconstruction from Visible Human Data