## Slide 1: Edge Operators
a kind of filtering that leads to useful features

## Slide 2: Lines and Arcs Segmentation
In some image sets, lines, curves, and circular arcs
are more useful than regions or helpful in addition
to regions.
Lines and arcs are often used in
object recognition
stereo matching
document analysis

## Slide 3: Edge Detection
Basic idea: look for a neighborhood with strong signs
of change.
81 82 26 24
82 33 25 25
81 82 26 24
Problems:
neighborhood size
how to detect change

## Slide 4: Differential Operators
Differential operators
attempt to approximate the gradient at a pixel via masks
threshold the gradient to select the edge pixels

## Slide 5: Example: Sobel Operator
-1 0 1 1 2 1
Sx = -2 0 2 Sy = 0 0 0
-1 0 1 -1 -2 -1
On a pixel of the image I
let gx be the response to Sx
let gy be the response to Sy
And g = (gx2 + gy2 )1/2 is the gradient magnitude.
 = atan2(gy,gx) is the gradient direction.
Then the gradient is
I = [gx gy]
T

## Slide 6: Sobel Operator on the Blocks Image
original image gradient thresholded
magnitude gradient
magnitude

## Slide 7: Common Masks for Computing Gradient
Sobel:
Prewitt:
Roberts
-1 0 1
-1 0 1
-1 0 1
1 1
0 0 0
-1 -1 -1
-1 0 1
-2 0 2
-1 0 1
2 1
0 0 0
-1 -2 -1
0 1
-1 0
0
0 -1
Sx
Sy

## Slide 8: Zero Crossing Operators
Motivation: The zero crossings of the second derivative
of the image function are more precise than
the peaks of the first derivative.
step edge
smoothed
1st derivative
2nd derivative
zero crossing

## Slide 9: How do we estimate the Second Derivative?
Laplacian Filter:  f =  f / x +  f / y
0 1 0
1 -4 1
0 1 0
2
2
2
2
Standard mask implementation
Derivation: In 1D, the first derivative
can be computed with mask [-1 0 1]
The 1D second derivative is [1 -2 1]
The Laplacian mask estimates the
2D second derivative.
2

## Slide 10: Properties of Derivative Masks
Coordinates of derivative masks have opposite signs in order to obtain a high response in regions of high contrast.
The sum of coordinates of derivative masks is zero, so that a zero response is obtained on constant regions.
First derivative masks produce high absolute values at points of high contrast.
Second derivative masks produce zero-crossings at points of high contrast.

## Slide 11: Marr/Hildreth Operator
First smooth the image via a Gaussian convolution.
Apply a Laplacian filter (estimate 2nd derivative).
Find zero crossings of the Laplacian of the Gaussian.
This can be done at multiple resolutions.

## Slide 12: Haralick Operator
Fit the gray-tone intensity surface to a piecewise
cubic polynomial approximation.
Use the approximation to find zero crossings of the
second directional derivative in the direction that
maximizes the first directional derivative.
The derivatives here are calculated from direct
mathematical expressions wrt the cubic polynomial.

## Slide 13: Canny Edge Detector
Smooth the image with a Gaussian filter with spread .
Compute gradient magnitude and direction at each pixel of
the smoothed image.
Zero out any pixel response  the two neighboring pixels
on either side of it, along the direction of the gradient.
Track high-magnitude contours.
Keep only pixels along these contours, so weak little
segments go away.

## Slide 14: Canny on Kidney

## Slide 15: Canny Characteristics
The Canny operator gives single-pixel-wide images with good continuation between adjacent pixels
It is the most widely used edge operator today; no one has done better since it came out in the late 80s. Many implementations are available.
It is very sensitive to its parameters, which need to be adjusted for different application domains.