## Slide 1: Reconstruction
EE/CSE 576
Linda Shapiro

## Slide 2: 3D model
“Digital copy” of real object
Allows us to
  Inspect details of object
  Measure properties
  Reproduce in different material
Many applications
  Cultural heritage preservation
  Computer games and movies
  City modelling
  E-commerce

## Slide 3: Applications: cultural heritage
SCULPTEUR European project
Notes: To sum up,

## Slide 4: Applications: art
Domain Series Domain VIII Crouching 1999 Mild steel bar 81 x 59 x 63 cm
Block Works Precipitate III 2004 Mild steel blocks 80 x 46 x 66 cm

## Slide 5: Applications: structure engineering
BODY / SPACE / FRAME, Antony Gormley, Lelystad, Holland
Notes: To sum up,

## Slide 6: Applications: 3D indexation
SCULPTEUR European project
medical, industrial and cultural heritage indexation
? ?
? ? ?
?
? ?
?

## Slide 7: Applications: archaeology
1186 fragments
“forma urbis romae” project
Fragments of the City: Stanford's Digital Forma Urbis Romae Project David Koller, Jennifer Trimble, Tina Najbjerg, Natasha Gelfand, Marc Levoy Proc. Third Williams Symposium on Classical Architecture, Journal of Roman Archaeology supplement, 2006.

## Slide 8: Applications: large scale modelling
[Pollefeys08]
[Furukawa10]
[Goesele07]
[Cornelis08]

## Slide 9: Applications: Medicine

## Slide 10: Scanning technologies
Laser scanner, coordinate measuring machine
  Very accurate
  Very Expensive
  Complicated to use
Minolta
Contura CMM
“Michelangelo” project

## Slide 11: Medical Scanning System

## Slide 12: The “Us” Data Set (subset)

## Slide 13: 3d shape from photographs
“Estimate a 3d shape that would generate the input photographs given the same material, viewpoints and illumination”
material
illumination
viewpoint
geometry
image
?

## Slide 14: Photometric Stereo
Estimate the surface normals of a given scene given multiple 2D images taken from the same viewpoint, but under different lighting conditions.
Basic photometric stereo required a Lambertian reflectance model:
I =  n · v
where I is pixel intensity, n is the normal, v is the lighting direction, and  is diffuse albedo constant, which is a reflection coefficient.

## Slide 15: Basic Photometric Stereo

## Slide 16: Basic Photometric Stereo

## Slide 17: Basic Photometric Stereo
K light sources
Lead to K images R1(p,q), ...,RK(p,q) each from just one of the light sources being on
For any (p,q), we get K intensities I1,...IK
Leads to a set of linear equations of the form
Ik = nvk
Solving leads to a surface normal map.

## Slide 18: Photometric Stereo
Inputs
3D normals

## Slide 19: 3d shape from photographs
Photograph based 3d reconstruction is:
  practical
  fast
  non-intrusive
  low cost
  Easily deployable outdoors
  “low” accuracy
  Results depend on material properties

## Slide 20: Reconstruction
Generic problem formulation: given several images of the same object or scene, compute a representation of its 3D shape

## Slide 21: Reconstruction
Generic problem formulation: given several images of the same object or scene, compute a representation of its 3D shape
“Images of the same object or scene”
  Arbitrary number of images (from two to thousands)
  Arbitrary camera positions (camera network or video sequence)
  Calibration may be initially unknown
“Representation of 3D shape”
  Depth maps
  Meshes
  Point clouds
  Patch clouds
  Volumetric models
  Layered models

## Slide 22: Multiple-baseline stereo
I1
I2
I10
M. Okutomi and T. Kanade, “A Multiple-Baseline Stereo System,” IEEE Trans. on Pattern Analysis and Machine Intelligence, 15(4):353-363 (1993).

## Slide 23: Reconstruction from silhouettes
Can be computed robustly
Can be computed efficiently
-
=
background
+
foreground
background
foreground

## Slide 24: Reconstruction from Silhouettes
Binary Images
The case of binary images: a voxel is photo-consistent if it lies inside the object’s silhouette in all views

## Slide 25: Reconstruction from Silhouettes
Binary Images
Finding the silhouette-consistent shape (visual hull):
  Backproject each silhouette
  Intersect backprojected volumes
The case of binary images: a voxel is photo-consistent if it lies inside the object’s silhouette in all views
voxel space

## Slide 26: Calibrated Image Acquisition
Calibrated Turntable
360° rotation (21 images)
Selected Dinosaur Images
Selected Flower Images

## Slide 27: Space Carving in General
Space Carving Algorithm
Image 1
Image N
…...
  Initialize to a volume V containing the true scene
  Repeat until convergence
  Choose a voxel on the outside of the volume
  Carve if not photo-consistent (inside object’s silhouette)
  Project to visible input images
K. N. Kutulakos and S. M. Seitz, A Theory of Shape by Space Carving, ICCV 1999

## Slide 28: Our 4-camera light-striping stereo system
projector
rotation
table
cameras
3D
object
(now deceased)

## Slide 29: Calibration Object
The idea is to snap
images at different
depths and get a
lot of 2D-3D point
correspondences.

## Slide 34
image plane
depth map
(u,v,d)
OUTSIDE
one of many cubes
in virtual 3D cube space
3D space is made up of many cubes.
((x,y,z)
(

## Slide 43: More: Space Carving Results: African Violet
Input Image (1 of 45)
Reconstruction
Reconstruction
Reconstruction
Source: S. Seitz

## Slide 44: More: Space Carving Results: Hand
Input Image
(1 of 100)
Views of Reconstruction

## Slide 45: Stereo from community photo collections
Up to now, we’ve always assumed that camera calibration is known
For photos taken from the Internet, we need structure from motion techniques to reconstruct both camera positions and 3D points. (SEE POSTED VIDEO)

## Slide 47: Head Reconstruction from Uncalibrated Internet Photos
Input: Internet photos in different poses and expressions
Output: 3D model of the head
work of
Shu Liang