## Slide 1: Cameras and Stereo
ECE/CSE 576
Linda Shapiro

## Slide 2: Müller-Lyer Illusion
http://www.michaelbach.de/ot/sze_muelue/index.html
What do you know about perspective projection?
Vertical lines?
Other lines?

## Slide 3: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Film
Object

## Slide 4: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
  How does this transform the image?
Film
Object
Barrier

## Slide 5: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 6: Lenses
A lens focuses parallel rays onto a single focal point
  focal point at a distance f beyond the plane of the lens
    f is a function of the shape and index of refraction of the lens
  Aperture of diameter D restricts the range of rays
    aperture may be on either side of the lens
  Lenses are typically spherical (easier to produce)
  Real cameras use many lenses together (to correct for aberrations)
focal point
F
optical center
(Center Of Projection)

## Slide 7: Thin lenses
Thin lens equation:
  Any object point satisfying this equation is in focus
Notes: manipulate eq to show shape of focus region

## Slide 8: Digital camera
A digital camera replaces film with a sensor array
  Each cell in the array is a Charge Coupled Device (CCD)
    light-sensitive diode that converts photons to electrons
  CMOS is becoming more popular (esp. in cell phones)
    http://electronics.howstuffworks.com/digital-camera.htm

## Slide 9: Issues with digital cameras
Noise
    big difference between consumer vs. SLR-style cameras
    low light is where you most notice noise
Compression
    creates artifacts except in uncompressed formats (tiff, raw)
Color
    color fringing artifacts from Bayer patterns
Blooming
    charge overflowing into neighboring pixels
In-camera processing
    oversharpening can produce halos
Interlaced vs. progressive scan video
    even/odd rows from different exposures
Are more megapixels better?
    requires higher quality lens
    noise issues
Stabilization
    compensate for camera shake (mechanical vs. electronic)
More info online, e.g.,
http://electronics.howstuffworks.com/digital-camera.htm
http://www.dpreview.com/

## Slide 11: Projection
Mapping from the world (3d) to an image (2d)
Can we have a 1-to-1 mapping?
How many possible mappings are there?
An optical system defines a particular projection. We’ll talk about 2:
Perspective projection (how we see “normally”)
Orthographic projection (e.g., telephoto lenses)

## Slide 12: Modeling projection
The coordinate system
  We will use the pin-hole model as an approximation
  Put the optical center (Center Of Projection) at the origin
  Put the image plane (Projection Plane) in front of the COP
  The camera looks down the negative z axis
    we need this if we want right-handed-coordinates
3D point
negative z axis
C

## Slide 13: Modeling projection
Projection equations
  Compute intersection with PP of ray from (x,y,z) to COP
  Derived using similar triangles
We get the projection by throwing out the last coordinate:
y/z = y´/-d
y´ = -d(y/z)
(x´,y´)

## Slide 14: Homogeneous coordinates
Is this a linear transformation?
Trick: add one more coordinate:
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
no—division by z is nonlinear

## Slide 15: Perspective Projection
Projection is a matrix multiply using homogeneous coordinates:
divide by third coordinate
This is known as perspective projection
The matrix is the projection matrix
projection matrix 3D point 2D point

## Slide 16: Perspective Projection Example
1. Object point at (10, 6, 4), d=2
2. Object point at (25, 15, 10)
Perspective projection is not 1-to-1!

## Slide 17: Perspective Projection
How does scaling the projection matrix change the transformation?
SAME

## Slide 18: Perspective Projection
What happens to parallel lines?
What happens to angles?
What happens to distances?

## Slide 19: Perspective Projection
What happens when d?

## Slide 20: Orthographic projection
Special case of perspective projection
  Distance from the COP to the PP is infinite
  Good approximation for telephoto optics
  Also called “parallel projection”: (x, y, z) → (x, y)
  What’s the projection matrix?
Image
World

## Slide 21
3D
2D Parallel
Projection

## Slide 22: Orthographic Projection
What happens to parallel lines?
What happens to angles?
What happens to distances?

## Slide 23: Camera parameters
How many numbers do we need to describe a camera?
We need to describe its pose in the world
We need to describe its internal parameters

## Slide 24: A Tale of Two Coordinate Systems
“The World”
Camera
x
y
z
v
w
u
o
COP
Two important coordinate systems:
1. World coordinate system
2. Camera coordinate system

## Slide 25: Camera parameters
To project a point (x,y,z) in world coordinates into a camera
First transform (x,y,z) into camera coordinates
Need to know
  Camera position (in world coordinates)
  Camera orientation (in world coordinates)
Then project into the image plane
  Need to know camera intrinsics
These can all be described with matrices

## Slide 26: 3D Translation
3D translation is just like 2D with one more coordinate
x′ 1 0 0 tx x
y′ = 0 1 0 ty y
z′ 0 0 1 tz z
1 0 0 0 1 1
= [x+tx, y+ty, z+tz, 1]T

## Slide 27: 3D Rotation (just the 3 x 3 part shown)
About X axis: 1 0 0 About Y: cosθ 0 sinθ
0 cosθ –sinθ 0 1 0
0 sinθ cosθ -sinθ 0 cosθ
About Z axis: cosθ –sinθ 0
sinθ cosθ 0
0 0 1
General (orthonormal) rotation matrix used in practice:
r11 r12 r13
r21 r22 r23
r31 r32 r33

## Slide 28: Camera parameters
A camera is described by several parameters
Translation T of the optical center from the origin of world coords
Rotation R of the image plane
focal length f, principal point (x’c, y’c), pixel size (sx, sy)
blue parameters are called “extrinsics,” red are “intrinsics”
The definitions of these parameters are not completely standardized
especially intrinsics—varies from one book to another
Projection equation
The projection matrix models the cumulative effect of all parameters
Useful to decompose into a series of operations
projection
intrinsics
rotation
translation
identity matrix
[tx, ty, tz]T

## Slide 29: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
image
plane
camera

## Slide 30: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
How do we represent translation as a matrix multiplication?

## Slide 31: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R
3x3 rotation matrix

## Slide 32: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R

## Slide 33: Perspective projection
(intrinsics)
in general,
: aspect ratio (1 unless pixels are not square)
: skew (0 unless pixels are shaped like rhombi/parallelograms)
: principal point ((0,0) unless optical axis doesn’t intersect projection plane at origin)
f is the focal
length of the camera
(converts from 3D rays in camera coordinate system to pixel coordinates)

## Slide 34: Focal length
Can think of as “zoom”
Related to field of view
24mm
50mm
200mm
800mm

## Slide 35: Projection matrix
translation
rotation
projection
intrinsics

## Slide 36: Projection matrix
0
=
(in homogeneous image coordinates)
arbitrary 3D point
image plane

## Slide 37: Distortion
Radial distortion of the image
  Caused by imperfect lenses
  Deviations are most noticeable for rays that pass through the edge of the lens
No distortion
Pin cushion
Barrel
Notes: Many wide –angle lenses have radial distortion – visible curvature in the projection of straight lines. To create good reconstructions / panoramas etc. this distortion shouldbe taken into account. Barrel usually a product of wide angle lenses and pincushion usually in telephoto lenses.

## Slide 38: Correcting radial distortion
from Helmut Dersch

## Slide 39: Where does all this lead?
We need it to understand stereo
And 3D reconstruction
It also leads into camera calibration, which is usually done in factory settings to solve for the camera parameters before performing an industrial task.
The extrinsic parameters must be determined.
Some of the intrinsic are given, some are solved for, some are improved.

## Slide 40: Camera Calibration
The idea is to snap
images at different
depths and get a
lot of 2D-3D point
correspondences.
x1, y1, z1, u1, v1
x2, y2, z1, u2, v2
.
.
xn, yn, zn, un, vn
Then solve a system
of equations to get
camera parameters.

## Slide 41: Stereo

## Slide 43: Amount of horizontal movement is …
…inversely proportional to the distance from the camera

## Slide 44: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
f
x
x’
Baseline B
z
C
C’
X
f
X
x
x'

## Slide 45: Depth from disparity
f
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth.
x

## Slide 46: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
Sub-Problems
  Calibration: How do we recover the relation of the cameras (if not already known)?
  Correspondence: How do we search for the matching point x’?
X
x
x'

## Slide 47: Correspondence Problem
We have two images taken from cameras with different intrinsic and extrinsic parameters
How do we match a point in the first image to a point in the second? How can we constrain our search?
x
?

## Slide 48: Key idea: Epipolar constraint
Potential matches for x have to lie on the corresponding line l’.
Potential matches for x’ have to lie on the corresponding line l.
x
x’
X
x’
X
x’
X

## Slide 49: Epipolar geometry: notation
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers
X
x
x’

## Slide 50: Epipolar geometry: notation
Epipolar Lines - intersections of epipolar plane with image planes (always come in corresponding pairs)
X
x
x’
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers

## Slide 51: Example: Converging cameras

## Slide 52: Example: Motion parallel to image plane

## Slide 53: Epipolar constraint
If we observe a point x in one image, where can the corresponding point x’ be in the other image?
x
x’
X

## Slide 54: Epipolar constraint
Potential matches for x have to lie on the corresponding
epipolar line l’.
Potential matches for x’ have to lie on the corresponding
epipolar line l.
x
x’
X
x’
X
x’
X

## Slide 55: Epipolar constraint example

## Slide 56: Epipolar constraint: Calibrated case
X
x
x’
Assume that the intrinsic and extrinsic parameters of the cameras are known
We can multiply the projection matrix of each camera (and the image points) by the inverse of the calibration matrix to get normalized image coordinates
We can also set the global coordinate system to the coordinate system of the first camera. Then the projection matrices of the two cameras can be written as [I | 0] and [R | t]

## Slide 57: Simplified Matrices for the 2 Cameras
= (R | T)

## Slide 58: Epipolar constraint: Calibrated case
X
x
x’ = Rx+t
R
t
The vectors Rx, t, and x’ are coplanar
= (x,1)T
Notes: X’ is X in the second camera’s coordinate system
We can identify the non-homogeneous 3D vectors X and X’ with the homogeneous coordinate vectors x and x’ of the projections of the two points into the two respective images

## Slide 59: Epipolar constraint: Calibrated case
Essential Matrix E
(Longuet-Higgins, 1981)
X
x
x’
The vectors Rx, t, and x’ are coplanar

## Slide 60: Epipolar constraint: Calibrated case
X
x
x’
E x is the epipolar line associated with x (l' = E x)
ETx' is the epipolar line associated with x' (l = ETx')
E e = 0 and ETe' = 0
E is singular (rank two)
E has five degrees of freedom

## Slide 61: Epipolar constraint: Uncalibrated case
The calibration matrices K and K’ of the two cameras are unknown
We can write the epipolar constraint in terms of unknown normalized coordinates:
X
x
x’

## Slide 62: Epipolar constraint: Uncalibrated case
X
x
x’
Fundamental Matrix
(Faugeras and Luong, 1992)

## Slide 63: Epipolar constraint: Uncalibrated case
F x is the epipolar line associated with x (l' = F x)
FTx' is the epipolar line associated with x' (l' = FTx')
F e = 0 and FTe' = 0
X
x
x’

## Slide 64: The eight-point algorithm
Minimize:
under the constraint ||F||2=1
Smallest eigenvalue of ATA
A

## Slide 65: Comparison of estimation algorithms
 | 8-point | Normalized 8-point | Nonlinear least squares
Av. Dist. 1 | 2.33 pixels | 0.92 pixel | 0.86 pixel
Av. Dist. 2 | 2.18 pixels | 0.85 pixel | 0.80 pixel

## Slide 66: Moving on to stereo…
Fuse a calibrated binocular stereo pair to produce a depth image
image 1
image 2
Dense depth map
Many of these slides adapted from Steve Seitz and Lana Lazebnik

## Slide 67: Depth from disparity
f
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth.
x

## Slide 68: Basic stereo matching algorithm
If necessary, rectify the two stereo images to transform epipolar lines into scanlines
For each pixel x in the first image
  Find corresponding epipolar scanline in the right image
  Search the scanline and pick the best match x’
  Compute disparity x-x’ and set depth(x) = fB/(x-x’)

## Slide 69: Basic stereo matching algorithm
For each pixel in the first image
  Find corresponding epipolar line in the right image
  Search along epipolar line and pick the best match
  Triangulate the matches to get depth information
Simplest case: epipolar lines are scanlines
  When does this happen?

## Slide 70: Simplest Case: Parallel images
Epipolar constraint:
R = I t = (T, 0, 0)
The y-coordinates of corresponding points are the same
t
x
x’

## Slide 71: Stereo image rectification

## Slide 72: Stereo image rectification
Reproject image planes onto a common plane parallel to the line between camera centers
Pixel motion is horizontal after this transformation
Two homographies (3x3 transform), one for each input image reprojection
C. Loop and Z. Zhang. Computing Rectifying Homographies for Stereo Vision. IEEE Conf. Computer Vision and Pattern Recognition, 1999.

## Slide 73: Example
Unrectified
Rectified

## Slide 74
Matching cost
disparity
Left
Right
scanline
Slide a window along the right scanline and compare contents of that window with the reference window in the left image
Matching cost: SSD, SAD, or normalized correlation

## Slide 75: Correspondence search
Left
Right
scanline
SSD

## Slide 76: Correspondence search
Left
Right
scanline
Norm. corr

## Slide 77: Effect of window size
W = 3
W = 20
Smaller window
  + More detail
  More noise
Larger window
  + Smoother disparity maps
  Less detail
  Fails near boundaries
Notes: smaller window: more detail, more noise
bigger window: less noise, more detail

## Slide 78: Failures of correspondence search
Textureless surfaces
Occlusions, repetition
Non-Lambertian surfaces, specularities

## Slide 79: Results with window search
Window-based matching
Ground truth
Data

## Slide 80: How can we improve window-based matching?
So far, matches are independent for each point
What constraints or priors can we add?

## Slide 81: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image

## Slide 82: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views

## Slide 83: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views
Ordering constraint doesn’t hold

## Slide 84: Priors and constraints
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views
Smoothness
  We expect disparity values to change slowly (for the most part)

## Slide 85: Stereo as energy minimization
What defines a good stereo correspondence?
  Match quality
    Want each pixel to find a good match in the other image
  Smoothness
    If two pixels are adjacent, they should (usually) move about the same amount

## Slide 86: Matching windows:
Similarity Measure | Formula
Sum of Absolute Differences (SAD) | 
Sum of Squared Differences (SSD) | 
Zero-mean SAD | 
Locally scaled SAD | 
Normalized Cross Correlation (NCC) | 
http://siddhantahuja.wordpress.com/category/stereo-vision/
SAD
SSD
NCC
Ground truth
Notes: smaller window: more detail, more noise
bigger window: less noise, more detail

## Slide 87: Real-time stereo
Used for robot navigation (and other tasks)
  Several software-based real-time stereo techniques have been developed (most based on simple discrete search)
Nomad robot searches for meteorites in Antartica
  http://www.frc.ri.cmu.edu/projects/meteorobot/index.html

## Slide 88: Stereo reconstruction pipeline
  Camera calibration errors
  Poor image resolution
  Occlusions
  Violations of brightness constancy (specular reflections)
  Large motions
  Low-contrast image regions
Steps
  Calibrate cameras
  Rectify images
  Compute disparity
  Estimate depth
What will cause errors?

## Slide 89: Multi-view stereo ?

## Slide 90: Using more than two images
Multi-View Stereo for Community Photo Collections M. Goesele, N. Snavely, B. Curless, H. Hoppe, S. Seitz Proceedings of ICCV 2007,