## Slide 1: Computer Vision CSE/ECE 576 Image Coordinates and Resizing Linda Shapiro Professor of Computer Science & Engineering Professor of Electrical & Engineering

## Slide 2: What is an image?

## Slide 3: Eyes: projection onto retina

## Slide 4: Model: pinhole camera

## Slide 5: Model: pinhole camera

## Slide 6: At each point we record incident light

## Slide 7: An image is a matrix of light

## Slide 8: Values in matrix = how much light

## Slide 9: Values in matrix = how much light
Higher = more light
Lower = less light
Bounded
  No light = 0
  Sensor/device limit = max
  Typical ranges:
    [0-255], fit into byte
    [0-1], floating point
Called pixels

## Slide 10: Addressing pixels
Ways to index:
  (r,c)
    Like matrix notation
    (3,6) is row 3 column 6
  (x,y)
    Like cartesian coordinates (but from
    the TOP)
    (3,6) is column 3 row 6
We use (x,y)
  So does your homework!
  Arbitrary
  Only thing that matters is consistency

## Slide 11: Color image: 3d tensor in colorspace

## Slide 12: RGB information in separate “channels”
Remember: we can match “real” colors using a mix of primaries.
Each channel encodes one primary. Adding the light produced from each primary mimics the original color.

## Slide 13: Addressing pixels
We use (x,y,c)
  (1,2,0):
    column 1, row 2, channel 0
Be consistent
But do what we do for homeworks :-)
Also for size:
  1920 x 1080 x 3 image:
    1920 px wide
    1080 px tall
    3 channels

## Slide 14: How do we store them?
129 | 131 | 152 | 159 | 135 | 163 | 142 | 82 | 182 | ...

## Slide 15: Storage: row major vs column major
Row Major Column Major

## Slide 16: Storage: row major vs column major
HW
WH

## Slide 17: Typically use row-major or HW

## Slide 18: In 3d we have more choices!

## Slide 19: HWC: channels interleaved
129 | 131 | 152 | 159 | 135 | 163 | 142 | 82 | 182 | ...

## Slide 20: CHW: channels separated
129 | 131 | 152 | ... | 135 | 163 | 142 | ... | 182 | ...

## Slide 21: CHW Pop quiz
We’ll use CHW, it’s what a lot of other libraries use.
In an array for a 1920 x 1080 x 3 image what entry would contain the pixel (15,192,2)?
Formula:
x + y*W + z*W*H
x
y
z
H
W

## Slide 22: CHW Pop quiz
In an array for a 1920 x 1080 x 3 image what entry would contain the pixel (15,192,2)?
In general for (x,y,z) of image (W,H,C)
x + y*W + z*W*H
15 + 192*1920 + 2*1920*1080 = 4,515,855
Remember, everything is 0 indexed
Where does (0,0,0) go?
Position 0 + 0 + 0 = 0

## Slide 23: In your homework
class Image: w: int h: int c: int data: np.ndarray

## Slide 24: Image interpolation and resizing

## Slide 25: An image is kinda like a function
An image is a mapping from indices to pixel value:
Im: I x I x I -> R
We may want to pass in
non-integers:
Im’: R x R x I -> R

## Slide 26: A note on coordinates in images
integer pixels

## Slide 27: A note on coordinates in images
We can think of their
values as being at the
centers.

## Slide 28: A note on coordinates in images
Now we can move to
a real coordinate
system.

## Slide 29: A note on coordinates in images
On the image

## Slide 30: A note on coordinates in images
So, the value of the
pixel (x,y) is now
centered at (x,y).

## Slide 31: A note on coordinates in images
But there are other
real-valued points.

## Slide 32: A note on coordinates in images
This point is:
(-.25, -.25)

## Slide 33: Just be careful
This point is:
(-.25, -.25)

## Slide 34: Interpolation
How do we find out the VALUE of a non-integer point, when the image only comes with integer points, ie (25,45,3).
For our assignment:
1. Nearest-Neighbor Interpolation
2. Bilinear Interpolation

## Slide 35: Nearest neighbor: what it sounds like
f(x,y,z) = Im(round(x), round(y), z)
Looks blocky
Common pitfall: Integer division rounds down in C
Note: z is still int

## Slide 36: Triangle interpolation: for less structured image (alternate approach)
Sometimes you have a regular grid, sometimes you don’t.
When you don’t, you can look for triangles!

## Slide 37: Triangle interpolation: for less structured image
Sometimes you have a regular grid, sometimes you don’t.
When you don’t look for triangles!

## Slide 38: Triangle interpolation: for less structured image
Sometimes you have a regular grid, sometimes you don’t.
When you don’t look for triangles!

## Slide 39: Triangle interpolation: for less structured image
Sometimes you have a regular grid, sometimes you don’t.
When you don’t look for triangles!

## Slide 40: Triangle interpolation: for less structured image
Weighted sum using triangles:
Q = V1*A1 + V2*A2 + V3*A3
WHY?
V1 is the furthest from q and A1 gives the smallest area.
V2 is next furthest from 1 and A2 gives the next smallest area…
Should normalize this based on total area, but we won’t use this.

## Slide 41: Bilinear interpolation: for grids, pretty good; easier than triangles
This time find the closest pixels in a box

## Slide 42: Bilinear interpolation: for grids, pretty good
This time find the closest pixels in a box

## Slide 43: Bilinear interpolation: for grids, pretty good
This time find the closest pixels in a box

## Slide 44: Bilinear interpolation: for grids, pretty good
This time find the closest pixels in a box
Same plan, weighted sum based on area of opposite rectangle
Q = V1*A1 + V2*A2 + V3*A3 + V4*A4

## Slide 45: Bilinear interpolation: for grids, pretty good
A1 = d2*d4
A2 = d1*d4
A3 = d2*d3
A4 = d1*d3
q = V1*A1 + V2*A2 + V3*A3 + V4*A4

## Slide 46: Bilinear interpolation: for grids, pretty good
Smoother than NN
More complex
  4 lookups
  Some math
Often the right tradeoff of speed vs final result

## Slide 47: Bicubic sampling: more complex, maybe better?
A cubic interpolation of 4 cubic interpolations
Smoother than bilinear, no “star”
16 nearest neighbors
Fit 3rd order poly:
  f(x) = a + bx + cx^2 + dx^3
Interpolate along axis
Fit another poly to interpolated values

## Slide 48: Bicubic vs bilinear

## Slide 49: Bicubic vs bilinear

## Slide 50: Resize algorithm:
For each pixel in new image:
  1. Map to old im coordinates
  2. Interpolate value
  3. Set new value in image

## Slide 51: What about shrinking?
NN and Bilinear only look at small area
Lots of artifacting
Staircase pattern on diagonal lines
We’ll fix this next class with filters!

## Slide 52: So what is this interpolation useful for?

## Slide 53: Image resizing!
Say we want to increase the size of an image…
This is a beautiful image of a sunset… it’s just very small…

## Slide 54: Image resizing!
Say we want to increase the size of an image…
This is a beautiful image of a sunset… it’s just very small…
Say we want to increase size 4x4 -> 7x7

## Slide 55: Resize 4x4 -> 7x7
Create our new image

## Slide 56: Resize 4x4 -> 7x7
Create our new image
Match up coordinates

## Slide 57: Resize 4x4 -> 7x7
Create our new image
Match up coordinates

## Slide 58: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
(-0.5, -0.5)
(3.5, 3.5)

## Slide 59: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5

## Slide 60: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5
    a*7 = 4

## Slide 61: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5
    a*7 = 4
    a = 4/7

## Slide 62: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5
  a = 4/7

## Slide 63: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5
  a = 4/7
    a*-.5 + b = -.5

## Slide 64: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5
  a = 4/7
    a*-.5 + b = -.5
    4/7*-1/2 + b = -1/2

## Slide 65: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5
  a = 4/7
    a*-.5 + b = -.5
    4/7*-1/2 + b = -1/2
    -4/14 + b = -7/14

## Slide 66: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5
  a = 4/7
    a*-.5 + b = -.5
    4/7*-1/2 + b = -1/2
    -4/14 + b = -7/14
    b = -3/14

## Slide 67: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  System of equations
  aX + b = Y
  a*-.5 + b = -.5
  a*6.5 + b = 3.5
  a = 4/7
  b = -3/14
So, we can start with any coordinate X of the big (new) image and use a and b to get Y on the smaller (old) image.

## Slide 68: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y

## Slide 69: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y

## Slide 70: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts

## Slide 71: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords (Y is old)

## Slide 72: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords (Y is old)
  (1, 3)

## Slide 73: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3)
  4/7*1 - 3/14
  4/7*3 - 3/14

## Slide 74: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3)
  4/7*1 - 3/14
  4/7*3 - 3/14
  (5/14, 21/14)

## Slide 75: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)

## Slide 76: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)
  Interpolate old values

## Slide 77: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)
  Interpolate old values
(0,1) (1,1)
(0,2) (1,2)

## Slide 78: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)
  Interpolate old values
    Size of opposite rects
(0,1) (1,1)
(0,2) (1,2)

## Slide 79: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)
  Interpolate old values
    Yar = (1/2)(5/14)
    Bar = (1/2)(9/14)
    R1ar = (1/2)(5/14)
    R2ar = (1/2)(9/14)
  V = Yval*Yar+Bval*Var+R1val*R1ar+R2val*R2ar
For each channel c, put the interpolated value from that channel in position (1,3,c).
(0,1) B (1,1) R1
(0,2) R2 (1,2) Y

## Slide 80: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)
  Interpolate old values

## Slide 81: Resize 4x4 -> 7x7
Create our new image results
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)
  Interpolate old values

## Slide 82: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)
  Interpolate old values
Fill in the rest
  On outer edges use padding!

## Slide 83: Resize 4x4 -> 7x7
Create our new image
Match up coordinates
  4/7 X - 3/14 = Y
Iterate over new pts
  Map to old coords
  (1, 3) -> (5/14, 21/14)
  Interpolate old values
Final result 7 x 7

## Slide 84: We did it!

## Slide 85: Let’s do something interesting already!!

## Slide 86: Want to make image smaller

## Slide 87: 448x448 -> 64x64

## Slide 88: 448x448 -> 64x64

## Slide 89: 448x448 -> 64x64

## Slide 90: 448x448 -> 64x64

## Slide 91: 448x448 -> 64x64

## Slide 92: 448x448 -> 64x64

## Slide 93: 448x448 -> 64x64

## Slide 94: 448x448 -> 64x64

## Slide 95: 448x448 -> 64x64

## Slide 96: 448x448 -> 64x64

## Slide 97: 448x448 -> 64x64

## Slide 98: 448x448 -> 64x64

## Slide 99: 448x448 -> 64x64

## Slide 100: 448x448 -> 64x64

## Slide 101: 448x448 -> 64x64

## Slide 102: 448x448 -> 64x64

## Slide 103: 448x448 -> 64x64

## Slide 104: 448x448 -> 64x64

## Slide 105: 448x448 -> 64x64

## Slide 106: 448x448 -> 64x64

## Slide 107: 448x448 -> 64x64

## Slide 108: 448x448 -> 64x64

## Slide 109: 448x448 -> 64x64

## Slide 110: 448x448 -> 64x64

## Slide 111: 448x448 -> 64x64

## Slide 112: 448x448 -> 64x64

## Slide 113: 448x448 -> 64x64

## Slide 114: 448x448 -> 64x64

## Slide 115: 448x448 -> 64x64

## Slide 116: 448x448 -> 64x64

## Slide 117: 448x448 -> 64x64

## Slide 118: 448x448 -> 64x64

## Slide 119: 448x448 -> 64x64

## Slide 120: 448x448 -> 64x64

## Slide 121: 448x448 -> 64x64

## Slide 122: 448x448 -> 64x64

## Slide 123: 448x448 -> 64x64

## Slide 124: 448x448 -> 64x64

## Slide 125: 448x448 -> 64x64

## Slide 126: 448x448 -> 64x64

## Slide 127: IS THIS ALL THERE IS??

## Slide 128: THERE IS A BETTER WAY!

## Slide 129
Next Time: Filtering