## Slide 1: Mutual Information Based Registration of Medical Images
Pluim et al: Survey
Mattes et al: CT/PET Registration

## Slide 2: Background
Mutual information-based registration was proposed
by Viola and Wells (MIT) in 1994-5.
It has become commonplace in many clinical applications.
It comes from information theory: the Shannon entropy
H =  pi log (1/pi) = -pi log pi
The more rare an event, the more meaning is associated
with its occurrence

## Slide 3
Entropy comes from information theory. The higher the entropy the more the information content.
Entropy =
  pi is the probability of event i
  Compute it as the proportion of event i in the set.
16/30 are green circles; 14/30 are pink crosses
log2(16/30) = -.9; log2(14/30) = -1.1
Entropy = -(16/30)(-.9) –(14/30)(-1.1) = .99
ENTROPY

## Slide 4
2-Class Case:
What is the entropy of a group in which all examples belong to the same class?
  entropy = - 1 log21 = 0
What is the entropy of a group with 50% in either class?
  entropy = -0.5 log20.5 – 0.5 log20.5 =1
minimum
entropy
maximum
entropy

## Slide 5: Entropy for Images
Shannon entropy can be computed for a gray-tone image.
It then focuses on the distribution of the gray tones.
An image consisting of almost a single intensity will have
low entropy.
An image with roughly equal quantities of different
gray tones will have high entropy.

## Slide 6: Histograms of Image Intensity

## Slide 7: Mutual Information
Woods introduced a registration measure for multimodality
images in 1992.
The measure was based on the assumption that regions of
similar tissue (and similar gray tones) in one image would
correspond to regions in the other image that also consist of
similar gray values (but not the same as in the first image).
Instead of defining regions of similar tissue in the image,
they defined the regions in a feature space.
When the images are correctly registered, the joint histogram
of the two images will show certain clusters for gray tones of
matching structures.

## Slide 8: CT/MRI Example
CT Image MR Image Joint Histogram
CT gray tones
MRI gray tones
For each pair of corresponding points (x,y)
with x in the CT image and y in the MR image,
there is a gray tone correspondence (gx,gy).
The joint histogram counts how many times
each gray tone correspondence occurs.

## Slide 9: Joint Gray-tone Histograms of an MR Image with itself at Different Rotations
0 degrees 2 degrees 5 degrees 10 degrees
Because the images are identical, all gray-tone correspondences lie on
the diagonal of the histogram matrix.
joint entropy

## Slide 10: Measures of Mutual Information
H = -pi,j log pi,j is the Shannon entropy for a joint distribution; pij is probability of co-occurence of i and j.
Def. 1: I(A,B) = H(B) – H(B|A)
Def. 2: I(A,B) = H(A) + H(B) – H(A,B)
Def. 3: Kullback-Leibler distance
joint gray values
joint in case of
independent images
P(b|a) is the
probability of voxel
having value
b in B given a in A
Maximizing mutual info is
like minimizing entropy.

## Slide 11: Different Aspects of Mutual Information Procedures
Preprocessing (ie. filtering)
Measures (entropy measure, normalization measures)
Spatial Information (not just gray tones, but where)
Transformation (applied to register images)
  rigid
  affine
  deformable
Implementation
  interpolation
  probability distribution estimation
  optimization

## Slide 12: Modalities
MR with CT, PET, SPECT, US
CT with PET, SPECT, other (video, fluoroscopy)
Microscopy with other

## Slide 13: Anatomical Entities
brain
thorax/lungs
spine
heart
breast
abdomen/liver
pelvis
tissue
other

## Slide 14
PET-CT Image Registration in the Chest
Using Free-Form Deformations
David Mattes, David Haynor, et al
UW Medical Center
Popular implementation of mutual information registration
Available in ITK package
We use it in our research.

## Slide 15: Application
PET-to-CT image registration in the chest
Fuse images from a modality with high anatomic detail (CT)
With images from a modality delineating biological function (PET)
Producing a nonparametric deformation that registers them.

## Slide 16: Overall Method
The PET image has a corresponding transmission image (TR)
The TR image is similar to a CT attenuation map with
a higher energy radiation beam, resulting in less
soft-tissue detail and limited resolution
Once the TR and CT images are registered, the resulting
transformation can be applied to the emission image for
improved PET image interpretation.
GOAL: find a deformation map that aligns the TR image
with the CT image and evaluate the accuracy.

## Slide 17
Axial Slice Coronal Slice
CT Image
TR Image

## Slide 18: Methodology
Notation
  fT(x) is a test image over domain VT
  fR(x) is a reference image over domain VR
  g(x | ) is a deformation from VT to VR
   is the set of parameters of the transformation
  We want to find the set of parameters 
  that minimizes an image discrepancy function S
  They hypothesize that the set of transformation
  parameters that minimizes S brings the transformed test image into best registration with the reference image.
 = arg min S(fR , fT  g( | ))

## Slide 19: Image Representation
Optimizing a function requires taking derivatives.
Thus it is easier if the function can be represented in
a form that is explicitly differentiable.
This means that both the deformations and the
similarity criterion must be differentiable.
So images are represented using a B-Spline basis.
Parzen windows are used instead of simple, bilinear
interpolation.

## Slide 20: SOME of the Math
An image f(x), coming in as a set of sampled values,
is represented by a cubic spline function that can be interpolated
at any between-pixel position.
The spline function is differentiable.
The smoothed joint histogram of (fR , fT  g( | ))
is defined as a cross product of the two spline functions.
Computation of mutual information requires
  the smoothed joint histogram
  the marginal smoothed histogram for the test image
  the marginal probability for the reference image, which
  is independent of the transformation parameters

## Slide 21
The image discrepancy measure is the negative of
mutual information S between the reference image
and the transformed test image expressed as a
function of the transformation parameters .
where p, pT, and pR are the joint, marginal test,
and marginal reference probability distributions,
respectively.
The variables  and  are the histogram bin indexes
for the reference and test images, respectively.
Joint
Marginals

## Slide 22: Deformations
Deformations are also modeled as cubic B-splines.
They are defined on a much coarser grid.
A deformation is defined on a sparse, regular grid
of control points placed over the test image.
A deformation is varied by defining the
motion g(j) at each control point j.

## Slide 23: Transformation
The transformation of the test image is specified
by mapping reference image coordinates according to
a locally perturbed rigid body transformation.
The parameters of the transformation are:
 = { , , , tx, ty, tz; j }
{, , } are the roll-pitch-yaw Euler angles,
[tx, ty, tz] is the translation vector,
and j is the set of deformation coefficients (2200 of them)

## Slide 24: Multiresolution Optimization Strategy
The registration process is automated by varying the
deformation in the test image until the discrepancy
between the two images is minimized.
The alignment process is divided into two registrations:
one for the rigid body part and one for the deformation
A limited-memory, quasi-Newton minimization package
is used.
To avoid local minima and decrease computation time,
a hierarchical multiresolution optimization scheme is used.

## Slide 26: Results
28 patients, 27 successful registrations
205 slices per image
average of 100 minutes per registration
10 minutes for the rigid body part
90 minutes for the deformable part
error index of .54, which is in the 0 to 6mm error range

## Slide 27
axial coronal
CT
registered TR
unregistered TR

## Slide 28: Sample Images from 7 Anatomic Locations