## Slide 1: Handling Memory Problems
Though the PRAM model does not suffice, memory sharing could be good given a realistic cost assessment.
The challenge in shared memory is the delay, called latency, between the time the memory is requested and the time at which the value is delivered. It slows computation.

## Slide 2: Conclusion from Last Week
Our idea of a parallel machine will be defined by the CTA model
The relevant properties are …
    P von Neumann processors operating concurrently
    Connected by an unspecified, but sparse network where
    Memory reference is either local, requiring unit time, or nonlocal requiring >>1 time

## Slide 3: Sharing ...
There are two aspects to sharing memory
  (True) shared memory means every processor can reference every memory location of a “single coherent memory,” i.e every processor sees the same values
  Shared address space means every processor can reference every memory location in the machine but the memory is not kept coherent
The problem: Suppose in time sequence
  Processor A reads location 1000
  Processor B writes location 1000
  Processors A and C use 1000 in later computation
When A, C use values are they the same or different?

## Slide 4: Memory Sharing on a CTA
With many processors referencing a single memory image, the probability that a given reference is nonlocal is (P-1)/P
So, by the CTA nearly all memory references will take  time implying that each processor can do little work
Responses
    A “sea” of small processors that can be used “inefficiently”
    Have many threads for processors to switch among
    Find a way to greatly reduce 
    Change processors from vN to something else

## Slide 5: “Sea” of Processors
The idea of zillions of simple processors derives from early theory on cellular automata and neural modeling
Ken Batcher built MASPAR ca. 1983
Danny Hillis built CM-1 and CM-2 ca. 85-87
Machines must be SIMD (single instruction, multiple data) because they are too simple to be full vN machines
All processors doing the same thing at the same time is too constraining

## Slide 6: Hiding Latency
To hide memory reference latency ( of the CTA model) requires that there be many more threads (work) than there are processors
    A thread is a sequence of instructions operating on a small quantity of data -- for example, a loop iteration
    The idea is that a processor with many threads to execute, can switch to execute another thread when it is stalled waiting for a memory reference, getting productive work done during the wait time
The idea can be used in either a programming model or hardware implementation

## Slide 7: Latency Hiding In Programming Model
Bulk-synchronous programming (BSP) is a solution by Valiant
Computation executes in supersteps:
  Assume threads execute 3-address code a:=b op c;
    [Load] Fetch operands from memory for many threads
    [Compute] For all threads having available operands compute a:=b op c
    [Store] Return the result to memory
With many threads, there is compute work enough to hide the data transmission time
Each thread may not execute on each cycle

## Slide 8: BSP Skews A Synchronous Step in Time
Consider a series of steps
Enough operands must be shipped on step n to enable enough threads at computation step n to cover the latency of the store of n-1 and the fetch of n+1
Load: n+1
Load: n
Load: n+2
Comp: n+1
Comp: n
Comp: n+2
Store: n+1
Store: n
Store: n+2
Store: n-1
Store: n-2
Comp: n-1
Notice that the strategy ignores locality
A parallelogram represents many threads at the same step & phase

## Slide 9: Many Threads = More Parallelism
When enabled-threads are numerous, the processors keep busy; “compute bound”
    More parallelism exists than can be used by processors
    Communication subsystem operates “below saturation”
Load: n+1
Load: n
Load: n+2
Comp: n+1
Store: n+1
Store: n
Store: n-1
Store: n-2
Comp: n+2
Comp: n
Comp: n+1
MM is example: 2m values imply m2 operations

## Slide 10: Too Few Threads = Waiting
When the enabled threads are too few to cover the latency, processors finish computing before next data arrives
    Not enough parallelism
    Communication subsystem may be less efficient
Load: n+1
Load: n
Load: n+2
n+1
n
n+2
Store: n+1
Store: n
Store: n-1
Store: n-2
n-1
Theoretically, P log P threads are needed, minimum

## Slide 11: Parallel Slackness
Valiant called the amount of “excess” parallelism needed to cover latency parallel slackness
In the “best case” a parallel slackness of logP is required because in the best case latency will be proportional to log P
Any additional delays require further slackness

## Slide 12: Problems With BSP
Though threads are often very numerous, it is difficult always to have P log P available
Other considerations
    The network needs to have high bandwidth (explained in later lecture, but meaning O(n) bisection bandwidth)
    Network congestion can be magnified when operating at peak capacity
    Memory contention requires that a value be fetched from each processor’s memory at each cycle …what happens when multiple values are in the same memory unit?
    What are the implications of slow memories and fast processors?

## Slide 13: Reducing 
Reducing  requires good engineering and some clever programming
NYU’s Ultracomputer Group tried both using 2-3 very slick ideas
Though they were ultimately unsuccessful, the approach stands as a fair test of a true shared memory parallel system
J.T. Schwartz, Ultracomputers, ACM Transactions on Programming Languages and Systems 2(4):484-521, 1980

## Slide 14: Historical caution ...
Jack Schwartz wrote a paper called Ultracomputer in which he observed
    The ideal parallel computer would be a PRAM (he called it a paracomputer), but it can’t work
    The realistic alterative would be an “ultracomputer” which was a specific (CTA-type architecture) using a shuffle-ex network, vN processors, etc.
    Allen Gottlieb started a project to build an ultracomputer, but after getting started, i.e. after the computer was already named, decided they’d build a paracomputer
Although the original ultracomputer doesn’t have a shared memory the machine that was built did … confusing

## Slide 15: An Alternate Concurrency Primitive
Rather than using the Test&Set to guard shared data, use Fetch&Add
    Fetch&Add is an atomic read-modify-write operation on memory -- requires special hardware, to be discussed
    Use Fetch&Add as a semaphore and as a scheduler
Operation: Fetch&Add(V,e)
    V is a memory location
    e is an integer expression
    Contents of V are returned
    New value of V is V+e
    Operation is atomic
V: 0
Fetch&Add(V,1)
V: 1
0 is returned

## Slide 16: Concurrent Fetch&Adds
When multiple Fetch&Adds are executed simultaneously, they are serializable
Assume Fetch&Add(V, e1) and Fetch&Add(V, e2) are execute simultaneously
    Assuming an initial value of e0
    Final value is e0+e1+e2
    The 1st process receives either e0 or e0+e2, implying it was first (e0) or second (e0+e2)
    The 2nd process receives either e0 or e0+e1, implying it was second (e0+e1) or first (e0)
Suppose both execute Fetch&Add(I,1), then one gets I back, the other I+1, and final is I+2

## Slide 17: Fetch&Add on Work List
Let TD[1..n] be a Todo list of TaskIDs
Let Next be the index of the first unassigned task
Processes execute
    Fetch&Add(Next, 1)
    Receive an index back
    If index  n, wrap around => Fetch&Add(Next,-n)
Such automatic scheduling can be useful for rows of an array or other ordered data structure

## Slide 18: Generalizing Fetch&Add
Fetch&(V,e) is a generalization for arbitrary binary, associative operation 
Define (a,b) = a+b to define Fetch&Add( )
If is associative, the final value is independent of the serializing order
Test&Set(V) is just Fetch&Or(V, 1)
Load and Store use 1(a,b)=a, 2(a,b)=b
    Load R <-- Fetch&1(V,*)
    Store * <-- Fetch&2(V,L)
* means value doesn’t matter

## Slide 19: Break
Problem to think about at the break … are test&set and fetch&add equivalent?

## Slide 20: Fetch&Add vs. Test&Set
Compare K concurrent processes using Fetch&Add(I,1) and Test&Set(V)
  The Fetch&Add distinguishes among and orders the competing processes, assigning each one a unique number
    Excellent for allocating work and scheduling
  Test&Set returns the FALSE to at most one of the processes, and so divides the set of competing processes into two groups, the winner and K-1 others
    Excellent for mutual exclusion
T&S is a potential bottleneck

## Slide 21: Fetch&Add Exploits Sharing
Though earlier solutions attempt to reduce sharing to reduce the amount of invalidation and acknowledgment, Fetch&Add does better with greater sharing
Sharing is used to schedule or allocate, which is then independent activity
    Sharing is concentrated in a few variables
    Fine grain size is possible
Since load/store, Test&Set, etc. are implementable, it is a sufficient primitive

## Slide 22: Implementing Fetch&Add
Fetch&Add assumes a flat shared memory as implemented by a “dance hall architecture”
P0
PNI
P1
PNI
P2
PNI
P6
PNI
P7
PNI
P3
PNI
P4
PNI
P5
PNI
Interconnection Network
M0
MNI
M1
MNI
M2
MNI
M3
MNI
M4
MNI
M6
MNI
M5
MNI
M7
MNI

## Slide 23: Omega Network
The interconnection network is an -network
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111
Connection between 2 and 6 … follow bits to destination lsb to msb
Processor ID
Hi Memory Bits

## Slide 24: Notice Details
The -Network requires O(P log P) routers
The given network uses 2x2 but 2bx2b work
Wiring is consistent at each stage
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111
Long Wires Are Necessary

## Slide 25: Routing In -Network
The network is pipelined
There is a unique path between any processor and memory port pair
Conflicts are possible because there exist permutations in which packets collide
What happens when two packets collide at a router?
    Packet is delayed, leaving its “file”
    Pipelining is affected, here comes more
0 0
1 1
The separate packets must be serialized

## Slide 26: Two Processors Make Fetch&Add(V,1)
Simultaneous requests collide in network
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111
Fetch&Add(V)
Fetch&Add(V)
V
Fetch&Add increases potential for collisions
Hot spot

## Slide 27: The Bright Idea: Combine Requests
Idea: Combine requests for same dest. In the limit all nodes could be referencing same loc.
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
0 0
1 1
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111
V

## Slide 28: Combining Loads and Stores
At a switch combine loads and stores to a common location as follows
    Load/Load -- forward one of the loads towards the memory, and when the value is returned, satisfy both
    Load/Store -- forward the store, and when the ACK arrives back at the switch, return value to satisfy load
    Store/Store -- forward one of the stores, and when the ACK arrives back at the switch, return it for both
Processors are restricted to having only one outstanding request at a time to a given location

## Slide 29: Implementing Fetch&Add
Include an adder with the Memory Network Interface chips
For Fetch&Add(V,e)
    Fetch the value of V, say e0
    Return e0 to processor requesting
    Add e0+e
    Store e0+e back into V
It is probably necessary to do these concurrently
MNI
Mem
Mem

## Slide 30: Combining Fetch&Adds at Switch
Suppose Fetch&Add(V,e) and Fetch&Add(V,f) arrive at a switch together …
  Form the sum f+e
  Send Fetch&Add(V,f+e) on to the memory
  Store e locally
  When g0 is returned by the memory
    Return g0 as response to Fetch&Add(V,e)
    Return g0+e as response to Fetch&Add(V,f)
Switch
F&E(V,e+f)
g0
F&E(V,f)
g0+e
F&E(V,e)
g0

## Slide 31: Combine Fetch&Add with other requests
Combining can apply to all memory traffic to a location V
Consider the following cases
    Fetch&Add/Fetch&Add -- as just described
    Fetch&Add/Load -- Treat Load as Fetch&Add(V,0)
    Fetch&Add/Store -- If Fetch&Add(V,e) meets Store(V,f) send Store(V,e+f) to memory; when ACK is received, return f as value of F&A
Conclusion -- it is possible to combine all requests to the same memory location

## Slide 32: Will It Work?
Potential Problems …
    Network routing is driven entirely by performance, so a complicated switch is usually a problem
    Routers typically forward non-blocked packets in <= 3 tix
    Matching to recognize that two requests collide is an “add” operation
    Combining is an “add” operation after the previous add
    Combining relies on the requests getting to the switch simultaneously, or at worst, before the forwarded packet leaves … this is improbable
    Most traffic is non-combinable -- head for different places
    A combining router was created by Susan Dickey

## Slide 33: A Backup Strategy
If the network switch is too slow then …
  Do not combine at every stage … so that some stages can be fast
  Use two networks, one fast and one that does combining -- it can handle the sharing requests
  Combine only like requests, e.g. loads/loads
  Limit combining at a node to two requests
  As it happened
    Only like requests have ever been implemented in switch
    IBM used the two network solution in the RP3

## Slide 34: More Globally
Norton and Pfister discovered in simulation for the RP3 computer that the -Network develops hot-spots
It was thought that combining would remove the hot-spots … it seemed to for 64-way network
The problem is that once a node becomes hot, a “back-up” tree forms “behind” the node

## Slide 35: More Globally
But Lee, Kruskal and Kuck showed by simulation and also proved it won’t work
    LKK discovered and named the “back-up tree”
    Showed in simulation that the 64-way network is a lucky case
    Combining doesn’t help because it is the other traffic that is really the problem
0.125% traffic directed at a hot spot

## Slide 36: Assessment
It was a good idea but it didn’t work
What was good and bad
  Good
    Fetch&Add is clever -- a primitive with good properties
    Shifting from protecting data to allocating work is better
    Computation at memory is powerful, worth doing
  Bad
    Pipelined multistage networks probably just don’t work
    Complexity in a switch is wrong -- speed is essential
    Failed to exploit locality -- caching essentially impossible
Can other designs include the good ideas?

## Slide 37: Summary
We introduced the concept of the Fetch&Add
Showed how F&A can be used to implement many basic parallel operations
Considered the implementation
    -network
    Switches and interface structure
Introduced combining at switches w/ examples
Combining may fix hotspots, but its slow performance can slow down other operations

## Slide 38: Homework
Write two procedures -- Put_Task() and Get_Task() -- in any language, e.g. C, and using Fetch&Add for synchronization as follows
    Define TD[1..n], the ToDo array; n=c*Processors for some c
    Define FF, for first free, pointing in TD to first free cell
    Define NA, for next available, pointing to next task in TD
    Put_Task(a) takes a task as input, and places it in TD; Get_Task() returns the next task from TD if there is one
    The management of TD is completely decentralized
Submit solution by email to Adam prior to class