## Slide 1: Symmetric Multiprocessors
Implementing a single memory image operated upon by multiple processors is possible at small scales. The SMP is a standard design in which cache coherency allows all processors to see the same image.

## Slide 2: Homework
Write two procedures -- Put_Task() and Get_Task() -- in any language, e.g. C, and using Fetch&Add for synchronization as follows
    Define TD[1..n], the ToDo array; n=c*Processors for some c
    Define FF, for first free, pointing in TD to first free cell
    Define NA, for next available, pointing to next task in TD
    Put_Task(a) takes a task as input, and places it in TD; Get_Task() returns the next task from TD if there is one
    The management of TD is completely decentralized

## Slide 3: Homework
Strategy: The TD[1..n] is several times larger than the number of processors; system assumes at least 1 producer and 1 consumer
Put_Task(a) {
slot = Fetch&Add(FF,1);
if slot == n then Fetch&Add(FF, -n);
if slot > n then slot = slot - n;
while TD[slot] != 0 do wait(rand());
TD[slot] = a;
}
Get_Task { var temp;
slot = Fetch&Add(NA,1);
if slot == n then Fetch&Add(NA,-n);
if slot > n then slot = slot - n;
while TD[slot] == 0 do wait(rand());
temp=TD[slot]; TD[slot]=0; return temp;
}
Put waits if the slot is
occupied to avoid overrun; Get waits if slot is empty
No task has is “0”

## Slide 4: Shared Memory
Shared memory was claimed to be a poor model because it is does not scale
  Many vendors have sold small shared memory machines
    Some like SMPs work well (but modeled poorly by PRAM)
    Some never worked -- KSR
    Some worked because of a technology opportunity -- slow processors with a “fast interconnect”
    Some work on small scale, but not beyond 64 processors and everyone tries to ignore that fact -- Origin-2000
  Many researchers have come up with great ideas, but they still remain unproved

## Slide 5: Citation
David Culler and J.P. Singh
Parallel Computer Architecture
Morgan Kaufmann, 1999

## Slide 6: Share Memory Image
Previous models of shared memory have literally implemented a single memory unit where all data resides
Besides being a point of contention, a single memory doesn’t permit caching (though “read-only” caching is OK)
The SMP turns the idea around and exploits caching to implement a shared memory

## Slide 7: Architecture of an SMP
A symmetric multiprocessor (SMP) is a set of processor/cache pairs connected to a bus
The bus is both good news and bad news
    The (memory) bus is a point at which all processors can “see” memory activity, and can know what is happening
    A bus is used “serially,” and becomes a “bottleneck,” limiting scaling
P0
Cache
P1
Cache
P2
Cache
P3
Cache
Memory
Bus

## Slide 8: Recall Caches
Cache blocks (lines) contain several words
Blocks have state
  Valid
  Invalid
  Dirty = diff from mem
Cache writing
  Write through means update memory on all writes
  Write back means wait and update when block is invalidated
  “allocate” vs “no-allocate”
Cache
...
...
addr
...

## Slide 9: Cache Coherence -- The Problem
Processors can modify shared locations without other processors being aware of it unless special hardware is added
P1 reads a into its cache
P3
P1
P3
P1
4
P2
P3
4 Memory
a:
a:

## Slide 10: Cache Coherence -- The Problem
Processors can modify shared locations without other processors being aware of it unless special hardware is added
P1 reads a into its cache
P3 reads a into its cache
P1
P3
P1
4
P2
P3
4
4 Memory
a:
a:

## Slide 11: Cache Coherence -- The Problem
Processors can modify shared locations without other processors being aware of it unless special hardware is added
P1 reads a into its cache
P3 reads a into its cache
P1 changes a to 5 and writes the result through to main memory leaving P3 with stale data
P3
P1
4 5
P2
P3
4
4 5 Memory
a:
a:

## Slide 12: Cache Coherence -- The Problem
Processors can modify shared locations without other processors being aware of it unless special hardware is added
P1 reads a into its cache
P3 reads a into its cache
P1 changes a to 5 and writes the result through to main memory leaving P3 with stale data
P3 reads a … incoherent
P1
4 5
P2
P3
4
4 5 Memory
a:
a:

## Slide 13: Cache Coherency -- The Goal
A multiprocessor memory system is coherent if for every location there exists a serial order for the operations on that location consistent with the results of the execution such that
    The subsequence of operations for any processor are in the order issued
    The value returned by each read is the value written by the last write in serial order
p1:i, p3:j, p2:k, p1:i+1, p3:j+1, ...
P1
4 5
P2
P3
4
4 5 Memory
a
a
w:a
r:a

## Slide 14: Write Serialization
For fulfilling “seen by all processors” a bus is a perfect solution
Implied property of Cache Coherency:
Write Serialization … all writes to a location are seen in the same order by all processors

## Slide 15: Snooping To Solve Coherency
The cache controllers can “snoop” on the bus, meaning that they watch the events on the bus even if they do not issue them, noting any action relevant to cache lines they hold
There are two possible actions when a location held by processor A is changed by processor B
    Invalidate -- mark the local copy as invalid
    Update -- make the same change B made
The unit of cache coherency is a cache line or block

## Slide 16: Snooping
P3
When the cache controller “snoops” it sees requests by its processor or bus activity by other processors that is not local to them
P1
P2
Memory
Activity from processor
Activity form others

## Slide 17: Snooping At Work I
P3
4
By snooping the cache controller for processor P3 can take action in response to P1’s write
P1 reads a into its cache
P3 reads a into its cache
P1 changes a to 5 and writes through to main memory; P3 sees the action and invalidates the location
P3
P1
4 5
P2
4 5 Memory
a:
a:

## Slide 18: Snooping At Work II
P3
4 5
By snooping the cache controller for processor P3 can take action in response to P1’s write
P1 reads a into its cache
P3 reads a into its cache
P1 changes a to 5 and writes through to main memory; P3 sees the action and invalidates the location or updates it
P3
P1
4 5
P2
4 5 Memory
a:
a:

## Slide 19: Write-through Coherency
State diagrams show the protocol
PrRd/--
PrWr/BusWr
PrWr/BusWr
V
I
PrRd/BusRd
BusWr/--
States of a cache line
V is valid
I is invalid
Transactions
Reads (Rd) or Writes (Wr)
by processor or bus
Labeling A/B
If A is observed
Then transaction B is
generated

## Slide 20: Applying the WT Protocol
Consider the transactions
PrRd/--
PrWr/BusWr
PrWr/BusWr
V
I
PrRd/BusRd
BusWr/--
P1 reads a into its cache
P3 reads a into its cache
P1 changes a to 5 and writes through to main memory
P3 sees the action and invalidates the location
P2 reads a into its cache
P1 : I --> V PrRd/BusRd P3 : I --> V PrRd/BusRd P1 : V --> V PrWr/BusWr P3 : V --> I BusWr/-- P2 : I --> V PrRd/BusRd

## Slide 21: Partial Order On Memory Operations
Write bus transactions define a global sequence of events; between writes processors can read … any total order produced by interleaving
R
R
R
R
R
R
R
R
W
R
R
R
R
R
R
R
W

## Slide 22: Memory Consistency
What should it mean for processors to see a consistent view of memory?
Coherency is too weak because it only requires ordering with respect to individual locations, but there are other ways of binding values together
P0 : [a, flag initially 0]
a := 1;
flag := 1;
P1 :
while(flag != 1)do; -- spin
print (a);
Coherency requires only that the 0 --> 1 transition of a be seen eventually by P1

## Slide 23: Basic Write-back Snoopy Cache Design
Write-back protocols are more complex than write-through because modified data remains in the cache
Introduce more cache states to handle that
    Modified, or dirty, the value differs from memory
    Exclusive, no other cache has this location
Consider an MSI protocol with three states:
    Modified -- data is correct locally, different from memory
    Shared (Valid) -- data at this location is correct
    Invalid -- data at this location not correct

## Slide 24: MSI Protocol
Rdx means that the cache holds a modified value of the location and asks for exclusive permission to read
Reply means put the value on the bus for another processor to read
PrWr/BusRdx
BusRd/Reply
PrRd/-
BusRd/-
BusRdx/--
PrRd/BusRd
PrWr/BusRdx
PrRd/--
PrWr/--
M
S
I
BusRdx/Reply
Conceptually: Manage dirty value within caches

## Slide 25: MSI Protocol In Action
PrWr/BusRdx
BusRd/Reply
PrRd/-
BusRd/-
BusRdx/--
PrRd/BusRd
PrWr/BusRdx
PrRd/--
PrWr/--
M
S
I
BusRdx/Reply
Proc Data
Action P0 P1 P2 Bus From
P0:r a S - - BRd Mem
P2:r a S - S BRd Mem
P2:w a I - M BRdx
P0:r a S - S BRd P2
P1:r a S S S BRd Mem

## Slide 26: Critique of MSI
Bad: 2 bus ops to load
and update a value even
without any sharing
Add an Exclusive State, opposite of Shared
PrWr/BusRdx
BusRd/Reply
PrRd/-
BusRd/-
BusRdx/--
PrRd/BusRd
PrWr/BusRdx
PrRd/--
PrWr/--
M
S
I
BusRdx/Reply
Proc Data
Action P0 Pi Bus From
P0:r a S - BRd Mem
P0:w a M - BRdx

## Slide 27: Break

## Slide 28: Illinois Protocol
PRd/--
PWr/--
M
S
I
E
PWr/BRdx
PRd/BRd
PWr/BRdx
PWr/-
PrRd/-
PrRd/- BRd/Rp'
PRd/BRdx'
BRd/Rp
BRd/Rp
BRdx/Rp'
BRdx/Rp
BRdx/Rp'
P=processor
B=Bus
Rd=Read
Rdx=Read Ex
RdS=Read Sh
RdS'=Read Ex
Rp=Reply
Rp=Reply Someone
Proc Data
Action P0 Pi Bus From
P0:r a E - BRdx' Mem
P0:w a M -

## Slide 29: Alternative … Updating
One caching issue is “invalidation” vs “update”: Dragon
E
M
SC
SM
Proc Data
Action P0 P1 P2 Bus From
P1:r a E - - BRd Mem
P3:r a Sc - Sc BRd Mem
P3:w a Sc - Sm Bupd P3
P1:r a Sc - Sm null -
P2:r a Sc Sc Sm BRd P3

## Slide 30: Invalidation vs Update
1 Repeat k times: P1 writes V, P2-Pp read V
… perhaps representing work allocation
2 Repeat k times: P1 writes V M times, P2 reads
… perhaps representing sharing pair
invl = 6B, update = 14B, miss = 70B
P = 16, M = 10, k = 10
U1: 1,260B I1:10,624B
U2: 1,400B I2: 824B

## Slide 31: Implications of Blocksize
Larger blocks exploit spatial locality better
Bus transactions take more time with larger blocks
Fewer large blocks for a given amount of memory or more small blocks
There are implications on sharing

## Slide 32: True/False Sharing
If two processors reference the same cache line and the same word, they are “truly” sharing
If two processors reference the same cache line but a different word, they are “falsely” sharing
Cache
...
...
addr
...
P0 references
P1 references

## Slide 33: Discussion
What is the best model of an SMP … PRAM?
P1
P0
P3
P2
P5
P4
P7
P6
Memory
A
B
C

## Slide 34: Summary
SMPs solve shared memory by snooping
Key to SMP’s success is the bus, a site for serializing memory references
Buses work, but only for a small number (64 is upper limit, but fewer is better) of processors
Relative to the two requirements of shared memory -- acceptable costs, coherency -- the SMP meets both