## Slide 1: Shared Memory Without A Bus
In SMPs the bus is a centralized point where the writes can be serialized. When no such point exists, as in large parallel computers, the situation gets very much more complicated. We continue our examination of shared memory implementations
Source: Culler/Singh, Parallel Computer Architectures, MK ‘99

## Slide 2: Preliminaries
The computers implementing shared memory without a central bus are called “distributed shared memory” (DSM) machines
The subclass is the CC-NUMA machines, for cache coherent non-uniform memory access
On an access-fault by the processor
    Find out information about the state of the cache block in other machines
    Determine the exact location of copies, if necessary
    Communicate with other machines to implement the shared memory protocol

## Slide 3: “Distributed” Applies to Memory
DSM computers have a CTA architecture with additional hardware to maintain coherency
Collectively, the controllers make the memory look shared
P0
Cache
P1
Cache
P2
Cache
P3
Cache
$$$
Mem
$$$
Mem
$$$
Mem
$$$
Mem
Control
Control
Control
Control
Interconnection Network

## Slide 4: Directory Based Cache-coherence
Since broadcasting the memory references is impractical -- that’s what buses do -- a directory-based scheme is an alternative
A directory is a data structure giving the state of each cache block in the machine
P0
$ Mem
Directory
Controller
Directory
P1
$ Mem
Directory
Controller
Directory
Interconnection Network

## Slide 5: How Does It Work?
Using the directory it is possible to maintain cache coherency in a DSM, but its complex (and time consuming)
To illustrate, we work through the protocols to maintain memory coherency
Concepts
  Events: A read or write access fault
  Cache fields these for local data, controller fields these for remotely allocated data
  Proc/Proc communication is by packets through the interconnection network

## Slide 6: Terminology
Node, a processor, cache and memory
Home node, node whose main memory has the block allocated
Dirty node, a node with a modified value
Owner, node holding a valid copy, usually the home or dirty node
Exclusive node, holds only valid cached copy
Requesting node, (local) node asking for the block

## Slide 7: Sample Directory Scheme
Local node has access fault
Sends request to home node for directory information
    Read -- directory tells which node has the valid data and the data is requested
    Write -- directory tells nodes with copies ... Invalidation or update requests are sent
Acknowledgments are returned
Processor waits for all ACKs before completion
Notice that many transactions can be “in the air” at once, leading to possible races

## Slide 8: A Directory Entry
Directory entries don’t usually keep cache state
Use a P-length bit-vector to tell in which processors the block is present … presence bit
Clean/dirty bit implies exactly 1 presence bit on
Sufficient?
    Determine who has valid copy for read-miss
    Determine who has copies to be invalidated
Dirty
P0
P1
P2
1
P3
P4
1
P5
P6
P7
Presence Bits

## Slide 9: A Closer Look (Read) I
Postulate 1 processor per node, 1 level cache, local MSI protocol [from last week]
On a read access fault at Px, the local directory controller determines if block is locally/remotely allocated
    If local, it delivers data
    If remote it finds the home … by high order bits probably
Controller sends request to home node for blk
Home controller looks up directory entry for blk
    Dirty bit OFF, controller finds blk in memory, sends reply, sets xth presence bit ON

## Slide 10: A Closer Look (Read) II
Dirty bit ON -- controller sends reply to Px of the processor ID of Py, the owner
Px requests data from owner Py
Owner Py controller, sets state to “shared,” forwards data to Px and sends data to home
At home, data is updated, dirty bit is turned OFF and the xth presence bit is set ON and yth presence bit remains ON
This is basically the protocol for the LLNL S-1 multicomputer from the late ‘70s

## Slide 11: A Closer Look (Write) I
On a write access fault at Px, the local directory controller checks if the block is locally/remotely allocated; if remote it finds the home
Controller sends request to home node for blk
Home controller looks up directory entry of blk
  Dirty bit OFF, the home has a clean copy
    Home node sends data to Px w/presence vector
    Home controller clears directory, sets xth bit ON and sets dirty bit ON
    Px controller sends invalidation request to all nodes listed in the presence vector

## Slide 12: A Closer Look (Write) II
    Px controller awaits ACKs from all those nodes
    Px controller delivers blk to cache in dirty state
  Dirty bit is ON
    Home notifies owner Py of Px’s write request
    Py controller invalidates its blk, sends data to Px
    Home clears yth presence bit, turns xth bit ON and dirty bit stays ON
  On writeback, home stores data, clears both presence and dirty bits

## Slide 13: Detailed Example
P1
$
Ctlr
a:4
01000
P2
$
Ctlr
P3
$
Ctlr
Consider the example similar to last week
The assumptions are …
    a is globally allocated
    a has it’s home at P1
    P0 previously read a
P1 reads a into its cache
P3 reads a into its cache
P3 changes a to 5
{P2 reads a into its cache
P2 writes a in its cache}
P0
a:V:4
Ctlr
Interconnection Network

## Slide 14: P1 Reads a Into Cache
The local directory controller determines if block is locally/remotely allocated
    If remote it finds the home … by high order bits probably
Controller asks home node for blk: No-op
Home controller looks up directory entry for blk
    Dirty bit OFF, controller finds blk in memory, sends reply, sets xth presence bit ON
P1
a:V:4
Ctlr
a:4
01100
P2
$
Ctlr
P3
$
Ctlr
P0
a:V:4
Ctlr
Interconnection Network
In the special case that a processor references it’s own globally allocated data no communication is required, only manage the presence bits

## Slide 15: P3 Reads a Into Cache
The local directory controller determines if block is locally/remotely allocated
    If remote it finds the home … by high order bits probably
Controller asks home node for blk: Message to P1
Home controller looks up directory entry for blk
    Dirty bit OFF, controller finds blk in memory, sends message to P3, sets xth presence bit ON
P1
a:V:4
Controller
a:4
01101
P2
$
Controller
P3
a:V:4
Controller
P0
a:V:4
Controller
Interconnection Network
Msg: P3 to P1, Read a
Msg: P1 to P3, Here’s a

## Slide 16: P3 Writes a Changing It To 5 Part I
On a write access fault at Px, local controller checks and finds it remote; finds the home
Controller sends request to home node for blk
Home controller looks up directory entry of blk
  Dirty bit OFF, the home has a clean copy
    Home node sends data to Px w/presence vector
    Home controller clears directory, sets xth bit and dirty ON
    Px controller sends invalidation request to all nodes listed
P1
a:V:4
Controller
a:4
10001
P2
$
Controller
P3
Stalled
a:V:4
Controller
P0
a:V:4
Controller
Interconnection Network
Msg: P3 to P1, Write a
Msg: P1 to P3, a:01101
Msg: P3 to P0, Invalid a
Msg: P3 to P1, Invalid a

## Slide 17: P3 Writes a Changing It To 5 Part II
Processor continues to be stalled
    Px controller awaits ACKs from all those nodes
    Px controller delivers blk to cache in dirty state
Total messages when clean copy exists: ToHome, FromHome, (Invalidate, ACK)*s
P1
a:I:4
Controller
a:4
10001
P2
$
Controller
P3
a:M:5
Controller
P0
a:I:4
Controller
Interconnection Network
Msg: P0 to P3, ACK
Msg: P1 to P3, ACK

## Slide 18: P2 Reads a Into Cache
Dirty bit ON -- home controller sends reply to Px of the processor ID of Py, the owner; Px asks Py for data
Owner Py controller, sets state to “shared,” forwards data to Px and sends data to home
At home, data is updated, dirty bit is turned OFF and the xth presence bit is set ON and yth presence bit remains ON
P1
a:I:4
Controller
a:5
00011
P2
a:V:5
Controller
P3
a:V:5
Controller
P0
a:I:4
Controller
Interconnection Network
Msg: P2 to P1, Read a
Msg: P1 to P2, P3 has it
Msg: P2 to P3, Read a
Msg: P3 to P2, Here’s a
Msg: P3 to P1, Here’s a

## Slide 19: Instead Let P2’s Request Be Write 6
That is … this action replaces the previous slide
Dirty bit is ON
    Home notifies owner Py of Px’s write request
    Py controller invalidates its block, sends data to Px
    Home clears yth presence bit, turns xth bit ON and dirty bit stays ON
P1
a:I:4
Controller
a:4
10010
P2
a:M:6
Controller
P3
a:I:5
Controller
P0
a:I:4
Controller
Interconnection Network
Msg: P2 to P1, Write a
Msg: P1 to P3, P2 asking
Msg: P3 to P2, Here’s a

## Slide 20: Summarizing The Example
The controller sends out a series messages to keep the writes to the memory locations coherent
The scheme differs from the bus solution in that all processors get the information at the same time using the bus, but at different times using the network
The number of messages is potentially large if there are many sharers

## Slide 21: Homework Assignment
Suppose a 100x100 array S is distributed by blocks across four processors, so that each contains a 50x50 subarray. At each position S[i,j] is updated by the sum of its 8 nearest neighbors:
S’[i,j]=(S[i-1,j-1]+S[i-1,j]+S[i-1,j+1]+S[i,j+1]+S[i+1,j+1]
+S[i+1,j]+S[i+1,j-1]+S[i,j-1])/8;
If each processor updates its own elements, how many messages must are produced to maintain concurrency for a directory based CC-NUMA?
HINT: Assume that an extra row and column, initialized to zero, surrounds A, A is allocated in rmo, and storage for S alternates with S’

## Slide 22: Break

## Slide 23: Alternative Directory Schemes
The “bit vector directory” is storage-costly
Consider improvements to Mblk*P cost
  Increase block size, cluster processors
  Just keep list of Processor IDs of sharers
    Need overflow scheme
    Five slots probably suffice
  Link the shared items together
    Home keeps the head of list
    List is doubly-linked
    New sharer adds self to head of list
    Obvious protocol suffices, but watch for races

## Slide 24: Assessment
An obvious difference between directory and bus solutions is that for directories, the invalidate request grows as the number of processors that are sharing
Directories take memory
    1 bit per block per processor + c
    If a block is B bytes, 8B processors imply 100% overhead to store the directory

## Slide 25: Performance Data
To see how much sharing takes place and how many invalidations must be sent, experiments were run
Summarizing the data
    Usually there are few shares
    The mode is 1 other processor(s) sharing ~ 60
    The “tail” of the distribution stretches out for some applications
Remote activity increases as the number of processors
Larger block sizes increase traffic, 32 is good

## Slide 26: Protocol Optimizations I
Read Request to Exclusively Held Block
L
H
R
2
1
3
4a
4b
L
H
R
4
1
2
3
L
H
R
1
2
3a
3b
1: Request
2: Response
3: Intervention
4a: Revise
4b: Response
1: Request
2: Intervention
3: Revise
4: Response
1: Request
2: Intervention
3a: Revise
3b: Response
Strict Request/ Response
Intervention Forwarding
Reply Forwarding

## Slide 27: Protocol Optimizations II (Lists)
Improved Invalidation
L
S1
S2
2:A
1:I
3:I
4:A
S3
5:I
6:A
ACK includes next sharer on list
L
S1
S2
2b:A
1:I
2a:I
3b:A
S3
3a:I
4:A
ACK and next invalidate in parallel
ACK comes from the last sharer
L
S1
S2
1:I
2:I
S3
3:I
4:A

## Slide 28: Higher Level Optimization
Organizing nodes as SMPs with one coherent memory and one directory controller can improve performance since one processor might fetch data that the next processor wants … it is already present
The main liability is that the controller resource and probably its channel into the network are shared
P0
Cache
Directory
Controller
Directory
P2
Cache
Interconnection Network
P1
Cache
P3
Cache

## Slide 29: Serialization
The bus defines the ordering on writes in SMPs
For directory systems, memory (home) does
If home always has value, FIFO would work
  Consider a block in modified state and two nodes requesting exclusive access in an invalidation protocol: The requests reach home in one order, but they could reach the owner in a different order; which order prevails?
Fix: Add “busy state” indicating transaction in flight

## Slide 30: Four Solutions To Ensure Serialization
Buffer at home -- keep request at home, service in order … lower concurrency, overflow
Buffer at requesters with linked list; follow Py
NACK and retry -- when directory is busy, just “return to sender”
Forward to dirty node -- serialize at home for clean, serialize at owner otherwise

## Slide 31: Coherency != Memory Consistency
Assume A and B initially 0
P0
$ Mem
Directory
Controller
P2
$ Mem
Directory
Controller
Interconnection Network
P1
$ Mem
Directory
Controller
A=1; while (A==0)do;
B=1; while (B==0)do;
print A;
A=1;
B=1;
A=1;
Delay
Print 0

## Slide 32: Sequential Consistency
Sequential Consistency is a very strict form of memory consistency
A MP is sequentially consistent if the result of any execution is the same as some sequential order and operations of each processor are in program order
A=1; while (A==0)do;
B=1; while (B==0)do;
print A;

## Slide 33: Relaxed Consistency Models
Since sequential consistency is so strict, alternative schemes allow reordering of reads and writes to improve performance
    total store ordering (TSO)
    partial store ordering (PSO)
    relaxed memory ordering (RMO)
    processor consistency (PC)
    weak ordering (WO)
    release consistency (RC)
Many are difficult to use in practice

## Slide 34: Relaxing Write-to-Read Program Order
While a write miss is in the write buffer and not yet visible to other processors, the processor can issue and complete reads that hit in its cache or even a single read that misses in its cache. TSO and PSO allow this.
This matches intuition often …
This code works as expected
P0 P1 P0 P1
A=1; while (Flag==0)do; A=1; print B;
Flag=1; print A; B=1; print A;

## Slide 35: Less Intuitive
Some programs don’t work as expected
We expect to get one of the following:
    A=0, B=1
    A=1, B=0
    A=1, B=1
But not A=0, B=0 … but TSO would permit it
Solution: Insert a memory barrier after write
P0 P1
A=1; B=1;
print B; print A;

## Slide 36: Origin 2000
Intellectual descendant of Stanford DASH
Two processors per node
Caches use MESI protocol
Directory has 7 states:
  Stable: unowned, shared, exclusive (cl/dirty in $)
  Busy: Processor not ready to handle new requests to block, read, readex, uncached
Generally O2000 follows protocols discussed
    Proves basic ideas actually apply
    Shows that simplifying assumptions must be revisited to get a system built and deployed

## Slide 37: Summary
Shared memory support is much more difficult when there is no bus
A directory scheme achieves the same result, but the protocol requires a substantial number of messages, proportional to the amount of sharing
Coherency applies to individual locations
Consistent memory requires additional software or hardware to assure that updates or invalidations are complete