## Slide 1: Interprocessor Communication
There are two main differences between sequential computers and parallel computers -- multiple processors and the hardware to connect them together. That hardware is the most important part of the design.

## Slide 2: Basics of Network Routing
Routers can be integrated with the processors or they can be a separate interconnection topology -- the two approaches are logically the same
Proc
Mem
NIC
3,1:3.14159
R
Router
Packet
Dest Addr
Payload

## Slide 3: Goals of Network Routing
Must have …
    High Throughput
    Low Latency
Must be …
    Deadlock-free
    Livelock-free
    Starvation-free
Should be insensitive to…
    Congestion
    Bursts
    Faults
D
S

## Slide 4: Physical Connection
The wires connecting switches can be either unidirectional -- all wires transmit the same way, which alternates -- or bidirectional -- half of the wires are permanently set to transmit in each direction
    For sustained information flow in both directions, the bandwidth and latency are the same
    For one packet in the network, the latency is the same, but the bandwidth is doubled with unidirectional
A “flit” is a flow-control unit
A “phit” is a physical-transmission unit

## Slide 5: Destination Addressing
In a regular topology the switches can compute the path to the destination based only on its address
    Fitting the destination address into the first phit allows the node to begin addressing immediately
For irregular networks packets are “source routed” -- the path to the destination is computed at the source, and prefixed to the information
    At each hop its own address is removed from the front
Source routing sets path w/o considering congestion

## Slide 6: Transport Approaches -- Circuit Switching
Circuit Switching
    A static path is set-up between source and destination
    Once set up the information is pipelined along the path
    The path is “torn down” when the transmission is over
The set-up and tear-down are overhead
Very effective for large
quantities of data
Concept inherited from
telephone switching
D
S

## Slide 7: Transport Approaches -- Packet Switching
In packet switching the information is divided up into packets, and the destination address is prefixed to each packet
    Each packet is treated independently, preventing any packet from monopolizing resources
    Biased to favor short transmissions
    The header is overhead; pipelining is less effective
    Allows for adaptivity
Original approach for store & forward nets
Virtual Cut-through has replaced S&F
3,1:3.14159

## Slide 8: Store and Forward vs Virtual Cut-through
S&F allows for more sophisticated protocol, with higher reliability
Virtual cut-through allows for greater speed
NIC
R
NIC
R

## Slide 9: Xport Approaches -- Wormhole Switching
Worm-hole routers send entire message as a single packet -- dynamically circuit switched
    Eliminates the overhead of set-up and tear-down
    Fully exploits pipelining, minimizes overhead of headers
    Monopolizes resources and penalizes short messages
    Messages delivered in order of transmission
WH is the most popular transmission method of communication networks -- simple
Compromise schemes
    Large, e.g. page, variable length packets
    Allow small messages to “play through”

## Slide 10: Virtual Channels
A single physical network can transmit information for multiple logical networks
Keep separate buffers for each network
Virtual channels are often used to safeguard against deadlock in a single network design

## Slide 11: Router Design
Router design is an intensively studied topic
Inventing a routing algorithm is the easy part … demonstrating that it is low latency, high throughput, deadlock free, livelock free, starvation free, reliable, etc. is tougher
Generally ...
    Low latency is the most significant part
    Throughput -- delivered bits -- is next most significant
    The only interesting case is “performance under load,” so the challenge is handling contention

## Slide 12: Topologies
Many regular network topologies have been considered … there is no best topology
A common family of useful topologies are the k-ary d-cubes, which have k nodes in each of d dimensions
    2-ary d-cude is the d-dimensional binary hypercube
    n-ary 2-cube is the nxn mesh or torus
All routing algorithms considered here will at least apply to the k-ary, d-cubes

## Slide 13: Oblivious Routing
Oblivious Routers use a single path between any [source, destination] pair
    Dimension order
    Simple logic, fast
    Virtual cut-through
    State-of-the-art for
    MIMD computers
D
S
Though any path in the gray area is possible, oblivious uses only one

## Slide 14: Oblivious Router
Oblivious router’s speed comes from very simple decision logic
Row-first and Column-first are alternatives
When a packet arrives, a node must decide
    Stop? The destination has been reached
    Turn? The column has been reached
    Otherwise, continue
D
S

## Slide 15: Deadlock Free
Is the oblivious mesh router deadlock free?
    Can packets get in a state where they block each other?
    Give separate L/R, U/D wires and 1 turn
D
S

## Slide 16: Row, Then Column Gets Hot
For a mesh most traffic crosses the center
D
S
Congestion in the middle means communication is often delayed there

## Slide 17: Topological Solution
The mesh gets hot because not all edges are “equally useful” … change to a torus
D
S

## Slide 18: The Torus Is Tough for Oblivious
Oblivious routers are fast, but not clever … it is easy to deadlock a torus oblivious router
D
s
S
Dally and Seitz showed that it is possible to route worm-hole packets on a torus without deadlock … used virtual channels
d

## Slide 19: Randomized Oblivious Routing
Pick at random an intermediate destination
Better for better-connected topologies, e.g. hypercube
D
S
I
The expected path-length is doubled

## Slide 20: Adaptive Routing
Adaptive routers try to make routing decisions adaptively to by-pass congestion
Two types …
    Minimal adaptive ...
    adaptive path is a
    shortest path; always
    go forward
    Non-minimal adaptive
    … any path is allowed
D
S

## Slide 21: Minimal Adaptive -- It Doesn’t Work
Choosing among shortest paths seems like the best way to be adaptive, but it doesn’t work
Once hot spot develops, rows, cols build up because there is no more flexibility left
Congested rows and cols. act as barriers
The congestion spreads

## Slide 22: Deflection Routing
“Hot Potato” routers try to keep going
    An adaptive synchronous approach
    Incoming packets are matched to outgoing channels
    Losers are assigned arbitrarily
    All packets leave on the next step
Livelock is a potential problem

## Slide 23: Hot Potato Routers
Deflection routing used in Tera Computer
Perhaps it causes too much turbulence in the network … waiting one step might save one
Collision
Protocol
Alternative

## Slide 24: Break

## Slide 25: Chaos Router
Chaos Router is a randomizing, non-minimal adaptive packet router (It is not related to Chaos theory of physics)
Chaos Router sends packets along minimal paths in almost all cases, but when blocked by severe congestion, it sends packets along any path
    Avoids the hot potato router’s “too eager policy” to send packets the wrong direction
    Avoids the minimal adaptive router’s “catch-22” of discovering congestion after all of the flexibility is gone

## Slide 26: The Chaos Algorithm
The Chaos router directs packets according to the following scheme
  0 Transmit packets with virtual cut-through
  1 Send packets along a random shortest-path whenever possible, i.e. when traffic is light
  2 Wait briefly inside the switch (no store-and-forward) when traffic is moderate
  3 In heavy traffic when there is no more space in the switch to wait, “deroute” some (randomly chosen) waiting packet
Derouting (probably) takes a packet further from its destination

## Slide 27: Chaos Example
Steps of Chaos between a source (S) and a destination (D)
  1 Take random shortest
  path (A)
  2 Wait briefly inside of
  a switch (B)
  3 When no waiting room
  is available deroute a
  random packet (C)
S
D
A
B
C

## Slide 28: Chaos Router Properties
Packets take random minimal path except in cases of extreme congestion
Chaos Routers are inherently fault tolerant
Adaptivity reduces latency
and increases throughput
because packets select
paths incrementally based
on congestion …they take
productive paths if available
Packets can be delivered out of order and must be reassembled
D
S
misunderstanding
actual

## Slide 29: Chaos Router Design (2-ary, n-cube)
S
W
E
N
W
E
N
S
Input from NIC
Output to NIC
Cross Bar
Input Frames
Output Frames
Multi-queue


## Slide 30: Management of Multi-queue
Multi-queue implements logical queue discipline
    Physical position in list of frames is unimportant
    2 packets with same destination serviced in arrival order
    When multiple output channels are possible, packet takes the first free
    Multi-queue packets take precedence over newly arriving packets
    No packet moves to MQ until it is fully arrived -- implying there is no chance of cutting through
    One multi-queue frame must always be empty, ready to receive a packet -- for livelock protection
    Derouting victims are chosen fairly at random from MQ
    Packets can go from input frame directly into multi-queue

## Slide 31: Connecting Channels with Virtual C-Thru
S
W
E
N
W
E
N
S
Input from NIC
Output to NIC
Cross Bar
Input Frames
Output Frames
Multi-queue


## Slide 32: Waiting In The Multi-queue
S
W
E
N
W
E
N
S
Input from NIC
Output to NIC
Cross Bar
Input Frames
Output Frames
Multi-queue


## Slide 33: Cutting Through Multi-queue
S
W
E
N
W
E
N
S
Input from NIC
Output to NIC
Cross Bar
Input Frames
Output Frames
Multi-queue


## Slide 34: A Difficult Lesson
Input packets can move directly into the multi-queue
Requiring them to make their first move productively is an error
    Causes starvation
    Causes asymmetry in the network … and the asymmetry caused the router to slow down
Lesson: Randomizing, adaptive routers (probably all routers) want to be as regular and consistent and symmetric as possible … otherwise traffic will get “caught” and become hot

## Slide 35: Deadlock
Deadlock is a condition in which packets are permanently blocked
Logically impossible for non-minimal routers because a packet can always deroute
Physically, deadlock is a concern because packets monopolize resources
Chaos is deadlock-free by using packet-exchange protocol: A router wanting to send a packet must be willing to receive a packet
Invariant -- 1 of the 4 frames is always available

## Slide 36: Packet Exchange Protocol
E
W
E
W
Outputs Connect to Inputs
Logically, a router should be able to accept a packet by moving it to the multi-queue … unless it is full … but it can’t be full since one frame is always available … when it is used, some packet must deroute to make a frame available, but it can go because accepting gave the router the right to send!

## Slide 37: Livelock
Recall that livelock is the situation where a packet keeps moving, but is never delivered
The standard technique is to use counting or timestamps to measure the “age” of a packet, and never let a packet get too old … everything is eventually delivered
    Timestamps/counts take up valuable payload space
    The number must be tested before a route is committed
    Testing the number for old age is tougher than routing
    Protecting against livelock was a showstopper for adaptive routers before Chaos
3,1:09:20:12345:3.14159

## Slide 38: Livelock for Chaos
Fact 1: Livelock is an extremely rare situation
Fact 2: Chaos routers randomize routes, and randomizes the victim when picking a deroute
So the strategy is, ignore livelock and gamble
Problem: For any packet age, t, it is possible that a Chaos packet can be so unlucky that it is not delivered in t seconds
Conclusion: Chaos Router is not livelock free

## Slide 39: Probabilistic Livelock Freedom
A router is probabilistically livelock free if the probability that a packet remains in the network after t seconds goes to 0 as t increases
    Probabilistically livelock free  deterministic in practice
distance
time
The proof requires a probabilistic argument

## Slide 40: Implementation
Designed by Kevin Bolding
    Degree 4, suitable for mesh and torus routing
    20 phit frames, 16 bit phits, 5 frame multi-queue
    Linear-feedback shift register for random numbers
    Unidirectional channels with alternating opportunity at the end of each packet
    Separate injection and delivery channels
    Node latency is 4 ticks with 15 ns clock
    Technology is 1.2  CMOS, with scalable design rules
    Comparable to the Elko router, an oblivious router designed at Caltech using the same technology

## Slide 41: Chaos Chip
The frames, scoreboard for the MQ logic, and cross bar were custom design

## Slide 42: Timing
Chaos Router has a 4 tick node latency
    One tick to read the header and determine the productive channels
    One tick to set up the cross bar switch
    One tick to increment/decrement the address
    One tick to travel across the wires
The Elko Router has a 3 tick node latency
    One tick to read the header and decide to stop/turn/go
    One tick to increment/decrement the address
    One tick to travel across the wires

## Slide 43: Performance Assessment
Performance Analysis by Melanie Fulgham
    Chaos and Elko routers simulated at the flit level
    Batched means computing 95% confidence intervals
    Expected throughput -- proportion of the network bisection bandwidth that was used
    Expected latency -- a packet’s injection to delivery time exclusive of source queuing
    Learmonth-Lewis prime modulus multiplicative congruential pseudo random number generator
    Traffic Patterns: random (all destinations equally likely, including self), transpose, bit-reversal, complement, perfect-shuffle, hot spots (10 destinations 4x more likely than random)
Elko has 3 tick node latency

## Slide 44: Performance Description
All performance numbers are given in Fulgham’s thesis + IEEE Computer Paper
The main conclusions for 2D torus, 256 nodes
    When 1 packet in network Elko is slightly faster gaining one tick per hop
    Elko and Chaos are comparable to about 40% of BBW
    Throughput peak: Elko is 60% of BBW, Chaos is 96% BBW on random traffic
    Between 40%-90% of BBW, Chaos has significantly better latency
    After 90% of BBW, Chaos has worse latency, but both routers are fully saturated and congested

## Slide 45: Performance Description
On other traffic patterns Chaos is usually better than Elko for both throughput and latency, though sometimes not by a lot
Some patterns are inherently difficult
    Transpose saturates at about 50% BBW
Measuring the point at which saturation occurs -- Chaos is significantly better (often carries 2x the load) except for “bit reversal”
Bottom line: Chaos carries more traffic faster

## Slide 46: Bursts
Chaos router handles bursts well because the wires “fill up” carrying traffic quickly, and the multi-queue can hold “over capacity”
In general Chaos works best at about 90% of saturation, when it is carrying great capacity and latency is still small
A burst that floods the network beyond saturation, however, creates excessive amounts of derouting, wasting channel capacity
Chaos does not transmit “back pressure” well

## Slide 47: Fault Tolerance
Non-minimal adaptive routers are inherently fault-tolerant because a faulty neighbor is indistinguishable from a busy neighbor
Chaos router requires special design considerations to be fault tolerant …
    Back out of an output frame
    Packet reassembly is a good place to recognize lost packets … but they may just be slow
    Time out on reassembly, force a halt, deliver everything, apply diagnostics, restart if everything is OK

## Slide 48: Summary
Introduced network communication and routing
    Circuit switched, packet switched, worm-hole switched
Discussed the physical set-up
    Unidirectional or bidirectional wires
Routing Algorithms
  Oblivious on a mesh
    Hot spots and handling that problem with a torus
  Randomized techniques
  Adaptive techniques
    Minimal adaptive -- busted
    Hot Potato -- too eager
    Chaos -- randomizing
Chaos is a friend of mine
-- Bob Dylan