## Slide 1: Summary of Parallel Computation
We have learned a substantial amount about parallel computation. Today, we summarize the main conclusions.

## Slide 2: But, first latency tolerance

## Slide 3: Latency -- Just Do Something Else
In theory memory a delay of  is not a show stopper; simply switch to other work while waiting for a memory value to be returned
Requires (in theory) P log P threads, but it’s actually P, and grows howevergrows
Threads are often abundant, but it is difficult always to have P threads, e.g. at decision points

## Slide 4: Hardware Implementations
The idea of switching to execute instructions from another thread when memory latency stalls processor has been around a long time
    Early Honeywell machines used related ideas
    Denelcor HEP (~1982) designed by Burton Smith had 8 threads “in the air” at once
    The 1990s saw several efforts to build such machines
We will study two designs
    Alewife from Anant Agarwal’s group at MIT
    The Tera Computer from Burton Smith

## Slide 5: The Hardware Solutions
Focus on keeping 1 processor busy in the presence of long latencies to shared memory, but expect to use many such processors
    Use multithreading
    Requires no special software as long as the compiler can produce more threads than processors
    Handles both predictable and unpredictable situations
    Handles long latencies even as they grow
    Doesn’t affect the memory consistency model, i.e. shared variables must be locked or use other mechanism
utilization = work_time
work_time+switching+idle

## Slide 6: Two Techniques for Multi-threading
Blocked multithreading [Alewife] is like timesharing … continue to execute until the thread is blocked, then switch
    Has lower hardware impact
    Good single thread performance
Interleaved multithreading [Tera] switches execution on threads on each cycle
    Lower logical switching penalty
    Greater impact on hardware design
Keeping multiple contexts is essential

## Slide 7: Four Threads Using Blocked Approach
Threads make memory reference every few instructions
A
B
C
D
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Memory Latency
i
i
i
i

## Slide 8: Utilization of Blocked Approach
Total instruction times: 45
Total work instructions: 24
Total switch time: 21
Total wait time: 0
Utilization = 24/45 = 53%
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
i
i

## Slide 9: Benefits of Available Threads
For the blocked approach the availability of ready threads improves utilization
Number of threads
1 2 3 4 5 6 ...
Processor Utilizaiton
1.0
0.8
0.6
0.4
0.2
Switching time is overhead that is not recovered

## Slide 10: Six Threads With Interleaved Approach
A
B
C
D
E
F
x
x
x
Utilization is 24/27 or 89%

## Slide 11: Basics of Tera Design
Instructions are [arithmetic, control, memory] or [arithmetic, arithmetic, memory]
Ready instructions issue on each tick, but there is a 16 tick minimum issue delay for consecutive instructions from a thread
T
Converts latency from 15 ticks to 69 … U = 7%

## Slide 12: Six Threads Revisited (Tera Design)
A
B
C
D
E
F
Utilization is 23/70 or 33%
i
i
i

## Slide 13: More On Tera II
Since there is a 16 instruction minimum issue delay, it takes 16 threads to execute sequentially without latency hiding
Each (memory) instruction has a 3 bit tag telling how many instructions forward are independent of this memory reference (in this thread)
Average memory latency without contention is 70 cycles

## Slide 14: More On Tera III
Each processor has 128 full contexts
Synchronization latency can even be covered
When everything works, the Tera should approximate a PRAM
Think of the Bulk Synchronous model with completely decentralized supersteps

## Slide 15: Summary

## Slide 16: Our Original Goal
Goal: To give a good idea of parallelism
  Concepts -- look at problems with “parallel eyes”
  Algorithms -- different resources to work with
  Programming -- describe the computation without saying it sequentially
  Languages -- reduce control flow; increase independence
  Architecture -- HW support to share memory not?
  Hardware -- the challenge is communication, not instruction execution
Start with HW, and review (pop) to Concepts ...

## Slide 17: Routing
Chaos routing is effective because “non-minimal” adaptivity can by-pass congestion
  Light traffic, randomize routes over a regular, symmetric, consistent networks, avoids creating hot spots; no point where packets can get “stuck”
  Moderate traffic, wait in a node for a route to clear, this is better than “hot potato” which must route
  Heavy traffic and faults, deroute in the wrong direction to move around the problem
Higher throughput, lower latency, higher load-carrying capacity than other routers

## Slide 18: Chaos Routing (continued)
Deadlock is not possible because of packet exchange protocol
Probabilistically livelock-free,
  As good or better than deterministically livelock-free in practice
  Solves difficult (but rare) problem for adaptive routers by randomizing, and gambling
Chaos is not perfect; not good with wormhole
  Inefficient for long messages; use two nets or pick a variable length packet with large-ish maximum

## Slide 19: Networks
Full cross-bar is not practical
Direct and Indirect Networks are alternatives
  Indirect, e.g. -network
    Has only “long” paths of O(log P), no nearest neighbor
    Multiple references to a location can collide, so try combining at the switches
    In fact, exploit combining with Fetch&Add -- it’s better for shared memory than Test&Set because it “schedules”
    Both Fetch&Adds and Load/Stores can be combined
    Combining requires “smart” switches that slow net
    Analysis shows combining opportunities are rare; hot spots due to colliding references to different locations is the problem
F&A + combine is smart but flawed

## Slide 20: Networks (continued)
Direct Networks
  Short, nearest neighbor paths are available
  Adaptive routing techniques are available
  Much more asynchronous; NIC is extra processor
  Different load properties for different architectures
    Non-shared memory, network carries little overhead
    Shared memory, network carries coherency protocol messages, which can be “proportional to the sharing”
  n-ary, d-cubes are realistic topologies
    Torus is better because of symmetry
    Fat trees also work; hypercube has “log P node degree”
Direct (regular) networks are only choice

## Slide 21: Architecture
Main architecture decision: hardware support for shared memory or not?
  Non-shared memory architectures are successful
    Simpler designs, means faster designs
    Leave memory management to software/programmer
    A single address space is easy and useful
    “Proper HW support for shared memory” is still unknown and getting less realistic as technology improves
    Avoid message passing and its copy/marshal overhead
    One-sided communication (shmem) is very efficient because it reduces communication’s synchronization
    Shmem allows “strided communication” with pipelining
Single address space, 1-sided communication is best

## Slide 22: Architecture (continued)
Shared memory
  Technically very difficult -- and therefore slow -- to keep memory coherent
  DSM can be implemented by a directory scheme
    Record sharers/dirty features for each cache line
    Directory can double the memory requirements of machines, though some simplifications are possible
    Follow distributed version of coherency protocol because no bus for defining “timing sequence”; use mem location
    Homework showed: Even limited sharing can cause much traffic
    Invalidations, acknowledgements increase with sharing
DSM best when not used, i.e. manage mem yourself

## Slide 23: Architecture (continued)
Symmetric-multiprocessors (SMPs) are an effective way to share memory on a small scale
    Cache controllers snoop memory bus
    The bus becomes the “time sequencing” point of the system, where modification order is defined
    Various protocols speed performance with greater complexity
    “DSM Homework sharing” would be reasonably efficient on SMP … cost only about ‘2x’ over non-share
    Bus is serially used, limiting generalization to small #s
SMP is a standard architecture

## Slide 24: Languages
Shared memory is difficult to use (races, synch); not efficiently implemented; not realistic
Message passing with sequential language (C | Fortran) + (MPI | PVM) is current standard
  Least common denominator -- runs everywhere
  A huge amount of work (6x code explosion)
  Only the API is standard; semantics vary, making any program implementation-specific; limit porta’ty
  Message passing is costly on architectures with “good” communication, e.g. 1-sided, SMP
Use msg passing if you must; but there’s a better way

## Slide 25: Languages (continued)
ZPL 1st (and still only) parallel language with performance model (WYSIWYG)
  Designed from first principles to help programmers
  No explicit concurrency, communication, or synch.
  Programmer is insulated from details, but it is possible to write efficient solutions with WYSIWYG
  Compiler is heavily optimized, both seq. and para.
  The communication abstraction is Ironman -- four procedures that mark sender’s/receiver’s active regions -- uses native communication of machine
ZPL is convenient and efficient

## Slide 26: Languages (continued)
ZPL’s performance model
  Allows programmers “to keep their distance” from the implementing hardware -- portable!
  Relies on abstract machine -- CTA
    CTA gives key structural information, memory reference time, processors, characteristics of interconnection net
    CTA gives parallel costs; vN defines sequential costs
    Give ZPL’s runtime model, work & data allocation
    Describe costs of ZPL’s constructs in CTA terms
  No absolute performance possible, but relative is good enough for quality programming -- performs!
The most significant idea of this class

## Slide 27: Programming
Everyone thinks shared memory is the natural parallel extension of sequential computing: “Ignore memory reference time like vN model, and let HW give the flat memory illusion”
Memory reference time is key to good algs:
  Find maximum is the example
    Best ignore-memory-time (PRAM) is Valiant O(log log P)
    Best consider-memory-time (CTA) is tournament O(log P)
    (Actual?) implementation of Valiant’s alg O(log P loglog P)
    Actual implementation of tournament O(log P)
PRAM hides a critical cost => it’s hard to get results

## Slide 28: Programming (continued)
The CTA replaces the PRAM as a realistic, but still abstract model of parallel computation
  CTA models all existing hardware, but is “far enough away” to be independent of all
  CTA is concerned with a few features, processors, non-local memory reference time, , interconnect, which has unspecified topology, low degree
  Practicing programmers writing message passing code are in effect using the CTA
  CTA is key to expressing costs of HLL like vN
A machine model separates SW & HW development

## Slide 29: Concepts
The powerful parallel computation ideas are:
  Pipelining, perform some operations and then pass the task along for completion by other units
  Overlap, perform communication & computation simultaneously since they need separate resources
  Partition, form independent (as possible) tasks and assign separate processors to each
  Most parallel algorithms use a combination of these
    Languages should support these concepts
    ZPL does overlap and partitioning for all computations up to available resources, and has abstraction for pipelining
More abstractly: Decompose into independent parts

## Slide 30: Concepts (continued)
Matrix multiplication -- the most studied parallel algorithm
  Many solutions; van de Geijn,Watts SUMMA best
    Uses broadcast communication of rows/columns
    Restructures the problem to “use data completely”
    Efficiently uses temporary space
    Most natural and convenient (and efficient) ZPL program
    Other algs show ‘problem space promotion’ technique
Problem space promotion is a parallel programming technique in which a problem with d dimensional data d is logically solved in a higher dimension, usually d+1
Avoid iteration

## Slide 31: Concepts (continued)
Summary for successful parallel computation
  Rather than using a shared memory abstraction, use the CTA model; it reflects costs accurately
  Use ZPL for programming to get convenience, speed and portability; use MP as last resort
  Be suspicious of claims like the “problems” with shared memory have been solved by new machine
  When choosing architecture, prefer support for global addressing, 1-sided communication, point-to-point network, (randomizing) non-minimal adaptive routing, SMP nodes
The perfect parallel machine has yet to be built

## Slide 32: Summary’s Summary
This has been an enjoyable class to teach.
Good luck with the remainder of your MS degree.