## Slide 1: Dynamic Scheduling
Why go out of style?
  expensive hardware for the time (actually, still is, relatively)
  register files grew so less register pressure
  early RISCs had lower CPIs

## Slide 2: Dynamic Scheduling
1
<footer>
<date/time>
Why come back?
  higher chip densities
  greater need to hide latencies as:
    discrepancy between CPU & memory speeds increases
    branch misprediction penalty increases from superpipelining
  dynamic scheduling was generalized to cover more than floating point operations
    handles branches & hides branch latencies
    hides cache misses
    commits instructions in-order to preserve precise interrupts
    can be implemented with a more general register renaming mechanism
  processors now issue multiple instructions at the same time
    more need to exploit ILP
2 styles: large physical register file & reorder buffer
(R10000-style) (PentiumPro-style)

## Slide 3: Register Renaming with A Physical Register File
Register renaming provides a mapping between 2 register sets
  architectural registers defined by the ISA
  physical registers implemented in the CPU
    hold results of the instructions committed so far
    hold results of subsequent, independent instructions that have not yet committed
    more of them than architectural registers
      ~ issue width * # pipeline stages between register renaming & commit
  an architectural register is mapped to a physical register during a register renaming stage
  operands thereafter called by their physical register number
    hazards determined by comparing physical register numbers
Effects:
  eliminates WAW and WAR hazards (false dependences)
  increases ILP

## Slide 4: Review: Name Dependences & WAR/WAW Hazards
Cause of the name dependence:
  the compiler runs out of registers, so has to reuse them
  example:
    anti-dependence (potential WAR hazard)
    DIVF _, F1, _
    ADDF F1, _, _
    output dependence (potential WAW hazard)
    DIVF F0, F1, F2
    ADDF F0, F2, F3
Cause of the WAR & WAW hazards:
  instructions take different numbers of cycles: separate functional units (or execution pipelines) for different instructions that have different numbers of stages
  out-of-order execution may allow the second instruction to complete before the first

## Slide 5: A Register Renaming Example

## Slide 6: An Implementation (R10000)
<number>
<footer>
<date/time>
Modular design with regular hardware data structures
Structures for register renaming
  64 physical registers (each, for integer & FP)
  map tables for the current architectural-to-physical register mapping (separate, for integer & FP)
    accessed with an architectural register number
    produces a physical register number
  a destination register is assigned a new physical register number from a free register list (separate, for integer & FP)
    source operands refer to the latest defined destination register, i.e., the current mappings

## Slide 7: An Implementation (R10000)
  Instruction “queues” (integer, FP & data transfer)
    contains decoded & mapped instructions with the current physical register mappings
      instructions entered into free locations in the IQ
      sit there until they are dispatched to functional units
      somewhat analogous to Tomasulo reservation stations without value fields or valid bits
    used to determine when operands are available
      compare each source operand for instructions in the IQ to destinations being written this cycle
    determines when an appropriate functional unit is available
    dispatches instructions to functional units

## Slide 8: An Implementation (R10000)
active list for all uncommitted instructions
  the mechanism for maintaining precise interrupts
    instructions entered in program-generated order
    allows instructions to complete in program-generated order
  instructions removed from the active list when:
    an instruction commits:
      the instruction has completed execution
      all instructions ahead of it have also completed
    branch is mispredicted
    an exception occurs
  contains the previous architectural-to-physical destination register mapping
    used to recreate the map table for instruction restart after an exception
  instructions in the other hardware structures & the functional units are identified by their active list location

## Slide 9: An Implementation (R10000)
busy-register table (integer & FP):
  indicates whether a physical register contains a value
  somewhat analogous to Tomasulo’s register status
  used to determine operand availability
    bit is set when a register is mapped & leaves the free list (not available yet)
    cleared when a FU writes the register (now there’s a value)

## Slide 11: The R10000 in Action 1

## Slide 12: The R10000 in Action 2
1

## Slide 13: The R10000 in Action 3

## Slide 14: The R10000 in Action 4

## Slide 15: The R10000 in Action: Interrupts 1

## Slide 16: The R10000 in Action: Interrupts 2

## Slide 17: The R10000 in Action: Interrupts 3

## Slide 18: The R10000 in Action: Interrupts 4

## Slide 19: R10000 Execution
In-order issue (have already fetched instructions)
  rename architectural registers to physical registers via a map table
  detect structural hazards for instruction queues (integer, memory & FP) & active list
  issue up to 4 instructions to the instruction queues
Out-of-order execution (to increase ILP)
  reservation-station-like instruction queues that indicate when an operand has been calculated
    each instruction monitors the setting of the busy-register table
  set busy-register table entry for the destination register
  detect functional unit structural & RAW hazards
  dispatch instructions to functional units
In-order completion (to preserve precise interrupts)
  this & previous program-generated instructions have completed
  physical register in previous mapping returned to free list
  rollback on interrupts