## Slide 1: Lecture 2: Transport and Hardware
Challenge: No centralized state
Lossy communication at a distance
  Sender and receiver have different views of reality
  No centralized arbiter of resource usage
Layering: benefits and problems

## Slide 2: Outline
Theory of reliable message delivery
TCP/IP practice
Fragmentation paper
Remote procedure call
Hardware: links, Ethernets and switches
Ethernet performance paper

## Slide 3: Simple network model
Network is a pipe connection two computers
Basic Metrics
  Bandwidth, delay, overhead, error rate and message size
Packets

## Slide 4: Network metrics
Bandwidth
  Data transmitted at a rate of R bits/sec
Delay or Latency
  Takes D seconds for bit to progagate down wire
Overhead
  takes O secs for CPU to put message on wire
Error rate
  Probability P that messsage will not arrive intact
Message size
  Size M of data being transmitted

## Slide 5: How long to send a message?
Transmit time T = M/R + D
  10Mbps Ethernet LAN (M=1KB)
    M/R=1ms, D ~=5us
  155Mbps cross country ATM (M=1KB)
    M/R = 50us, D ~= 40-100ms
R*D is “storage” of pipe

## Slide 6: How to measure bandwidth?
Measure how slow link increases gap between packets
Slow bottleneck link

## Slide 7: How to measure delay?
Measure round-trip time
start
stop

## Slide 8: How to measure error rate?
Measure number of packets acknowledged
Slow bottleneck link
Packet
dropped

## Slide 9: Reliable transmission
How do we send a packet reliably when it can be lost?
Two mechanisms
  Acknowledgements
  Timeouts
Simplest reliable protocol: Stop and Wait

## Slide 10: Stop and Wait
Time
Packet
ACK
Timeout
Send a packet, stop and wait until acknowledgement arrives
Sender
Receiver

## Slide 11: Recovering from error
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Time
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
Packet lost
Early timeout

## Slide 12: Problems with Stop and Wait
How to recognize a duplicate transmission?
  Solution: put sequence number in packet
Performance
  Unless R*D is very small, the sender can’t fill the pipe
  Solution: sliding window protocols

## Slide 13: How can we recognize resends?
Use sequence numbers
  both packets and acks
Sequence # in packet is finite -- how big should it be?
  One bit for stop and wait?
    Won’t send seq #1 until got ack for seq #0
Pkt 0
ACK 0
Pkt 0
ACK 1
Pkt 1
ACK 0

## Slide 14: What if packets can be delayed?
Solutions?
  Never reuse a seq #?
  Require in order delivery?
  Prevent very late delivery?
    IP routers keep hop count per pkt, discard if exceeded
    Seq #’s not reused within delay bound
0
0
1
1
0
0
Accept!
Reject!

## Slide 15: What happens on reboot?
How do we distinguish packets sent before and after reboot?
  Can’t remember last sequence # used
Solutions?
  Restart sequence # at 0?
  Assume boot takes max packet delay?
  Stable storage -- increment high order bits of sequence # on every boot

## Slide 16: How do we keep the pipe full?
Send multiple packets without waiting for first to be acked
Reliable, unordered delivery:
  Send new packet after each ack
  Sender keeps list of unack’ed packets; resends after timeout
  Receiver same as stop&wait
What if pkt 2 keeps being lost?

## Slide 17: Sliding Window: Reliable, ordered delivery
Receiver has to hold onto a packet until all prior packets have arrived
Sender must prevent buffer overflow at receiver
Solution: sliding window
  circular buffer at sender and receiver
    packets in transit <= buffer size
    advance when sender and receiver agree packets at beginning have been received

## Slide 18: Sender/Receiver State
sender
  packets sent and acked (LAR = last ack recvd)
  packets sent but not yet acked
  packets not yet sent (LFS = last frame sent)
receiver
  packets received and acked (NFE = next frame expected)
  packets received out of order
  packets not yet received (LFA = last frame ok)

## Slide 19: Sliding Window
LAR
LFS
Send Window
sent
acked
0
1
2
x
x
x
x
x
x
x
x
3
4
5
6
NFE
LFA
Receive Window
recvd
acked
0
1
2
x
x
x
x
x
x
x
3
4
5
6
x

## Slide 20: What if we lose a packet?
Go back N
  receiver acks “got up through k”
  ok for receiver to buffer out of order packets
  on timeout, sender restarts from k+1
Selective retransmission
  receiver sends ack for each pkt in window
  on timeout, resend only missing packet

## Slide 21: Sender Algorithm
Send full window, set timeout
On ack:
  if it increases LAR (packets sent & acked)
  send next packet(s)
On timeout:
  resend LAR+1

## Slide 22: Receiver Algorithm
On packet arrival:
  if packet is the NFE (next frame expected)
  send ack
  increase NFE
  hand packet(s) to application
  else
  send ack
  discard if < NFE

## Slide 23: Can we shortcut timeout?
If packets usually arrive in order, out of order signals drop
  Negative ack
    receiver requests missing packet
  Fast retransmit
    sender detects missing ack

## Slide 24: What does TCP do?
Go back N + fast retransmit
  receiver acks with NFE-1
  if sender gets acks that don’t advance NFE, resends missing packet
    stop and wait for ack for missing packet?
    Resend entire window?
Proposal to add selective acks

## Slide 25: Avoiding burstiness: ack pacing
Sender
Receiver
bottleneck
packets
acks
Window size = round trip delay * bit rate

## Slide 26: How many sequence #’s?
Window size + 1?
  Suppose window size = 3
  Sequence space: 0 1 2 3 0 1 2 3
  send 0 1 2, all arrive
    if acks are lost, resend 0 1 2
    if acks arrive, send new 3 0 1
Window <= (max seq # + 1) / 2

## Slide 27: How do we determine timeouts?
Round trip time varies with congestion, route changes, …
If timeout too small, useless retransmits
If timeout too big, low utilization
TCP: estimate RTT by timing acks
  exponential weighted moving average
  factor in RTT variability

## Slide 28: Retransmission ambiguity
How do we distinguish first ack from retransmitted ack?
  First send to first ack?
    What if ack dropped?
  Last send to last ack?
    What if last ack dropped?
Might never be able to correct too short timeout!
Timeout!

## Slide 29: Retransmission ambiguity: Solutions?
TCP: Karn-Partridge
  ignore RTT estimates for retransmitted pkts
  double timeout on every retransmission
Add sequence #’s to retransmissions (retry #1, retry #2, …)
TCP proposal: Add timestamp into packet header; ack returns timestamp

## Slide 30: Transport: Practice
Protocols
  IP -- Internet protocol
  UDP -- user datagram protocol
  TCP -- transmission control protocol
  RPC -- remote procedure call
  HTTP -- hypertext transfer protocol

## Slide 31: IP -- Internet Protocol
IP provides packet delivery over network of networks
Route is transparent to hosts
Packets may be
  corrupted -- due to link errors
  dropped -- congestion, routing loops
  misordered -- routing changes, multipath
  fragmented -- if traverse network supporting only small packets

## Slide 32: IP Packet Header
Source machine IP address
  globally unique
Destination machine IP address
Length
Checksum (header, not payload)
TTL (hop count) -- discard late packets
Packet ID and fragment offset

## Slide 33: How do processes communicate?
IP provides host - host packet delivery
How do we know which process the message is for?
  Send to “port” (mailbox) on dest machine
Ex: UDP
  adds source, dest port to IP packet
  no retransmissions, no sequence #s
  => stateless

## Slide 34: TCP
Reliable byte stream
  Full duplex (acks carry reverse data)
  Segments byte stream into IP packets
Process - process (using ports)
Sliding window, go back N
  Highly tuned congestion control algorithm
Connection setup
  negotiate buffer sizes and initial seq #s

## Slide 35: TCP/IP Protocol Stack
send buffer
TCP
recv buffer
TCP
TCP
index.html
IP
IP
IP
TCP
inde
IP
x.html
proc
user level
kernel level
write
read
network link
proc

## Slide 36: TCP Sliding Window
Per-byte, not per-packet
  send packet says “here are bytes j-k”
  ack says “received up to byte k”
Send buffer >= send window
  can buffer writes in kernel before sending
  writer blocks if try to write past send buffer
Receive buffer >= receive window
  buffer acked data in kernel, wait for reads
  reader blocks if try to read past acked data

## Slide 37: What if sender process is faster than receiver process?
Data builds up in receive window
  if data is acked, sender will send more!
  If data is not acked, sender will retransmit!
Solution: Flow control
  ack tells sender how much space left in receive window
  sender stops if receive window = 0

## Slide 38: How does sender know when to resume sending?
If receive window = 0, sender stops
  no data => no acks => no window updates
Sender periodically pings receiver with one byte packet
  receiver acks with current window size
Why not have receiver ping sender?

## Slide 39: Should sender be greedy (I)?
Should sender transmit as soon as any space opens in receive window?
  Silly window syndrome
    receive window opens a few bytes
    sender transmits little packet
    receive window closes
Sender doesn’t restart until window is half open

## Slide 40: Should sender be greedy (II)?
App writes a few bytes; send a packet?
  If buffered writes > max packet size
  if app says “push” (ex: telnet)
  after timeout (ex: 0.5 sec)
Nagle’s algorithm
  Never send two partial segments; wait for first to be acked
  Efficiency of network vs. efficiency for user

## Slide 41: TCP Packet Header
Source, destination ports
Sequence # (bytes being sent)
Ack # (next byte expected)
Receive window size
Checksum
Flags: SYN, FIN, RST
why no length?

## Slide 42: TCP Connection Management
Setup
  assymetric 3-way handshake
Transfer
Teardown
  symmetric 2-way handshake
Client-server model
  initiator (client) contacts server
  listener (server) responds, provides service

## Slide 43: TCP Setup
Three way handshake
  establishes initial sequence #, buffer sizes
  prevents accidental replays of connection acks
SYN, seq # = x
SYN, ACK, seq # = y, ack # = x+1
ACK, ack # = y+1
server
client

## Slide 44: TCP Transfer
Connection is bi-directional
  acks can carry response data
ack, data
ack
data
data
ack

## Slide 45: TCP Teardown
Symmetric -- either side can close connection
FIN
ACK
DATA
DATA
FIN
ACK
Half-open connection
Can reclaim connection immediately (must be at least 1MSL after first FIN)
Can reclaim connection after 2 MSL

## Slide 46: TCP Limitations
Fixed size fields in TCP packet header
  seq #/ack # -- 32 bits (can’t wrap in TTL)
    T1 ~ 6.4 hours; OC-24 ~ 28 seconds
  source/destination port # -- 16 bits
    limits # of connections between two machines
  header length
    limits # of options
  receive window size -- 16 bits (64KB)
    rate = window size / delay
    Ex: 100ms delay => rate ~ 5Mb/sec

## Slide 47: IP Fragmentation
Both TCP and IP fragment and reassemble packets. Why?
  IP packets traverse heterogeneous nets
  Each network has its own max transfer unit
    Ethernet ~ 1400 bytes; FDDI ~ 4500 bytes
    P2P ~ 532 bytes; ATM ~ 53 bytes; Aloha ~ 80bytes
  Path is transparent to end hosts
    can change dynamically (but usually doesn’t)
IP routers fragment; hosts reassemble

## Slide 48: How can TCP choose packet size?
Pick smallest MTU across all networks in Internet?
  Packet processing overhead dominates TCP
    TCP message passing ~ 100 usec/pkt
    Lightweight message passing ~ 1 usec/pkt
  Most traffic is local!
    Local file server, web proxy, DNS cache, ...

## Slide 49: Use MTU of local network?
LAN MTU typically bigger than Internet
Requires refragmentation for WAN traffic
  computational burden on routers
    gigabit router has ~ 10us to forward 1KB packet
  inefficient if packet doesn’t divide evenly
  16 bit IP packet identifier + TTL
    limits maximum rate to 2K packets/sec

## Slide 50: More Problems with Fragmentation
increases likelihood packet will be lost
  no selective retransmission of missing fragment
  congestion collapse
fragments may arrive out of order at host
  complex reassembly

## Slide 51: Proposed Solutions
TCP fragment based on destination IP
  On local network, use LAN MTU
  On Internet, use min MTU across networks
Discover MTU on path
  “don’t fragment bit” -> error packet if too big
  binary search using probe IP packets
Network informs host about path
Transparent network-level fragmentation

## Slide 52: Layering
IP layer “transparent” packet delivery
  Implementation decisions affect higher layers (and vice versa)
    Fragmentation
    Packet loss => congestion or lossy link
    Reordering => packet loss or multipath
    FIFO vs. round robin queueing at routers
Which fragmentation solution won?

## Slide 53: Sockets
OS abstraction representing communication endpoint
  Layer on top of TCP, UDP, local pipes
server (passive open)
  bind -- socket to specific local port
  listen -- wait for client to connect
client (active open)
  connect -- to specific remote port

## Slide 54: Remote Procedure Call
Abstraction: call a procedure on a remote machine
  client calls: remoteFileSys->Read(“foo”)
  server invoked as: filesys->Read(“foo”)
Implementation
  request-response message passing
  “stub” routines provide glue

## Slide 55: Remote Procedure Call

## Slide 56: Object Oriented RPC
What if object being invoked is remote?
  Every object has local stub object
    stub object translates local calls into RPCs
  Every object pointer is globally valid
    pointer = machine # + address on machine
    compiler translates pointer dereference into RPC
Function shipping vs. data shipping

## Slide 57: RPC on TCP
How do we reduce the # of messages?
  Delayed ack: wait for 200ms for reply or another pkt arrival
  UDP: reply serves as ack
    RPC system provides retries, duplicate supression, etc.
    Typically, no congestion control
SYN
SYN+ACK
ACK
request
ACK
reply
ACK
FIN
ACK
FIN
ACK

## Slide 58: Reducing TCP packets for RPCs
For repeated connections between the same pair of hosts
  Persistent HTTP (proposed standard)
    Keep connection open after web request, in case there’s more
  T/TCP -- “transactional” TCP
    Use handshake to init seq #s, recover from crash
    after init, request/reply = SYN+data+FIN
Can we eliminate handshake entirely?

## Slide 59: RPC Failure Models
How many times is an RPC done?
  Exactly once?
    Server crashes before request arrives
    server crashes after ack, but before reply
    server crashes after reply, but reply dropped
  At most once?
    If server crashes, can’t know if request was done
  At least once?
    Keep retrying across crashes: idempotent ops

## Slide 60: General’s Paradox
Can we use messages and retries to synchronize two machines so they are guaranteed to do some operation at the same time?
  No.

## Slide 61: General’s Paradox Illustrated

## Slide 62: Exactly once RPC
Two machines agree to do operation, but not at same time
One-phase commit
  Write to disk before sending each message
  After crash, read disk and retry
Two-phase commit
  allow participants to abort if run out of resources

## Slide 63: Hardware Outline
Coding
Clock recovery
Framing
Broadcast media access
Ethernet paper
Switch design

## Slide 64: What happens to a signal?
Fourier analysis -- decompose signal into sum of sine waves
Measure channel on each sine wave
  Frequency response -- “bandwidth”
  Phase response -- ringing
Sum to get output
  physical property of channels -- distort each frequency separately

## Slide 65: Example: Square Wave

## Slide 66: How does distortion affect maximum bit rate?
Function of bandwidth B and noise N
Nyquist limit <= 2B symbols/sec
Shannon limit <= log (S/2N) bits/symbol
Ideal <= 2B log (S/2N) bits/sec
Realistic <= B log (1 + S/2N)

## Slide 67: CDMA Cell Phones
TDMA (time division multiple access)
  only one sender at a time
CDMA (code division multiple access)
  multiple senders at a time
  each sender has unique code
    ex: 1010 vs. 0101 vs. 1100
Unknown whether Shannon limit is higher or lower for CDMA

## Slide 68: Clock recovery
How does receiver know when to sample?
  Garbage if sample at wrong times or wrong rate
Assume a priori agreement on rates
  Ex: autobaud modems

## Slide 69: Clock recovery
Knowing when to start/stop
  well defined bit sequences
Staying in phase despite clock drift
  keep message short
    assumes clocks drift slowly
    low data rate; requires idle time between stop/start
  embed clock into signal
    Manchester encoding: clock in every bit
    4/5 code: clock in every 5 bits

## Slide 70: Framing
Need to send packet, not just bits
Loss recovery
  Burst errors common: lose sequence of bits
  Resynch on frame boundary
  CRC for error detection

## Slide 71: Error Detection: CRCs vs. checksums
Both catch some inadvertent errors
Exist errors one or other will not catch
  checksums weaker for
    burst errors
    cyclic errors (ex: flip every 16th bit)
  Goal: make every bit in CRC depend on every bit in data
Neither catches malicious errors!

## Slide 72: Network Layer
Broadcast (Ethernet, packet radio, …)
  Everyone listens; if not destination, ignore
Switch (ATM, switched Ethernet)
  Scalable bandwidth

## Slide 73: Broadcast Network Arbitration
Give everyone a fixed time/freq slot?
  ok for fixed bandwidth (e.g., voice)
  what if traffic is bursty?
Centralized arbiter
  Ex: cell phone base station
  single point of failure
Distributed arbitration
  Aloha/Ethernet

## Slide 74: Aloha Network
Packet radio network in Hawaii, 1970’s
Arbitration
  carrier sense
  receiver discard on collision (using CRC)

## Slide 75: Problems with Carrier Sense
Hidden terminal
  C will send even if A->B
Exposed terminal
  B won’t send to A if C->D
Solution
  Ask target if ok to send
What if propagation delay >> pkt size/bw?
A
B
D
C

## Slide 76: Problems with Aloha Arbitration
Broadcast if carrier sense is idle
Collision between senders can still occur!
  Receiver uses CRC to discard garbled packet
  Sender times out and retransmits
As load increases, more collisions, more retransmissions, more load, more collisions, ...

## Slide 77: Ethernet
First practical local area network, built at Xerox PARC in 70’s
Carrier sense
  Wired => no hidden terminals
Collision detect
  Sender checks for collision; wait and retry
Adaptive randomized waiting to avoid collisions

## Slide 78: Ethernet Collision Detect
Min packet length > 2x max prop delay
  if A, B are at opposite sides of link, and B starts one link prop delay after A
  what about gigabit Ethernet?
Jam network for min pkt size after collision, then stop sending
Allows bigger packets, since abort quickly after collision

## Slide 79: Ethernet Collision Avoidance
If deterministic delay after collision, collision will occur again in lockstep
If random delay with fixed mean
  few senders => needless waiting
  too many senders => too many collisions
Exponentially increasing random delay
  Infer senders from # of collisions
  More senders => increase wait time

## Slide 80: Ethernet Problems
Fairness -- backoff favors latest arrival
  max limit to delay
  no history -- unfairness averages out
Unstable at high loads
  only for max throughput at min packet sizes at max link distance
Cautionary tale for modelling studies
  But Ethernets can be driven at high load today (ex: real-time video)

## Slide 81: Why Did Ethernet Win?
Competing technology: token rings
  “right to send” rotates around ring
  supports fair, real-time bandwidth allocation
Failure modes
  token rings -- network unusable
  Ethernet -- node detached
Volume
Adaptable to switching (vs. ATM)