## Slide 1: Lecture 3: Routing
Challenge: how do we get a collection of nodes to cooperate to provide some service, in a completely distributed fashion with no centralized state?
  Ethernet arbitration
  Routing
  Congestion control

## Slide 2: Network Layer and Above
Broadcast (Ethernet, packet radio, …)
  Everyone listens; if not destination, ignore
Switch (ATM, switched Ethernet)
  Scalable bandwidth
Internetworking
  Routers as switches, connecting networks

## Slide 3: Broadcast Network Arbitration
Give everyone a fixed time/freq slot?
  ok for fixed bandwidth (e.g., voice)
  what if traffic is bursty?
Centralized arbiter
  Ex: cell phone base station
  single point of failure
Distributed arbitration
  Aloha/Ethernet

## Slide 4: Aloha Network
Packet radio network in Hawaii, 1970’s
Arbitration
  carrier sense
  receiver discard on collision (using CRC)
Collisions common => limited to small packets

## Slide 5: Problems with Carrier Sense
Hidden terminal
  C will send even if A->B
Exposed terminal
  B won’t send to A if C->D
Solution (post-Aloha)
  Ask target if ok to send
What if propagation delay >> pkt size/bw?
A
B
D
C

## Slide 6: CDMA Cell Phones
TDMA (time division multiple access)
  only one sender at a time
CDMA (code division multiple access)
  multiple senders at a time (collisions ok!)
  each sender has unique code known to receiver
    codes chosen to be distinguishable, even when multiple sent at same time
  better when high propagation delay

## Slide 7: Problems with Aloha Arbitration
Broadcast if carrier sense is idle
Collision between senders can still occur!
  Receiver uses CRC to discard garbled packet
  Sender times out and retransmits
As load increases, more collisions, more retransmissions, more load, more collisions, ...

## Slide 8: Ethernet
First practical local area network, built at Xerox PARC in 70’s
Carrier sense
  Wired => no hidden terminals
Collision detect
  Sender checks for collision; wait and retry
Adaptive randomized waiting to avoid collisions

## Slide 9: Ethernet Collision Detect
Min packet length > 2x max prop delay
  if A, B are at opposite sides of link, and B starts one link prop delay after A
  what about gigabit Ethernet?
Jam network for min pkt size after collision, then stop sending
Allows bigger packets, since abort quickly after collision

## Slide 10: Ethernet Collision Avoidance
If deterministic delay after collision, collision will occur again in lockstep
If random delay with fixed mean
  few senders => needless waiting
  too many senders => too many collisions
Exponentially increasing random delay
  Infer senders from # of collisions
  More senders => increase wait time

## Slide 11: Ethernet Problems: Fairness
Backoff favors latest arrival
  max limit to delay
  no history -- unfairness averages out
Solutions?
  Live with it
  Use binary search for arbitration
  centralized allocation (cell phones)
    use one channel to ask for bandwidth
    use other channels to send

## Slide 12: Ethernet Problems: Instability
Ethernet unstable at high loads
Peak throughput worse with
  more hosts -- more collisions needed to identify single sender
  smaller packet sizes -- more frequent arbitration
  longer links -- collisions take longer to observe, more wasted bandwidth

## Slide 13: Modelling vs. Measurement?
Ethernets work in practice
  early over-engineering => usually low load
Modelling shows unstable at high loads
Conclusions?
  Modelling wrong?
  Ethernet won’t work as loads increase?
    Faster CPUs, real-time video

## Slide 14: Ethernet Packet Traces
Ethernet traffic is “self-similar” (fractal)
  bursty at every time scale (msecs to months)
Implication?
  On average, low load
    low load determines average
  Occasional long term peaks
    peaks determine variance

## Slide 15: Token Rings
Packets broadcast around ring
Token “right to send” rotates around ring
  fair, real-time bandwidth allocation
    every host holds token for limited time
    higher latency when only one sender
  higher bandwidth
    point to point links electrically simpler than bus

## Slide 16: Why Did Ethernet Win?
Failure modes
  token rings -- network unusable
  Ethernet -- node detached
Good performance in common case
Volume => cost => volume => cost
Adaptable
  to higher bandwidths (vs. FDDI)
  to switching (vs. ATM)

## Slide 17: Switched Networks
A
B
C
D
H
G
F
E
v
w
z
x
y

## Slide 18: Switched Network Advantages
Higher link bandwidth
  point to point electrically simpler than bus
Much greater aggregate bandwidth
  everyone can send at once
Incremental scaling
Improved fault tolerance
  redundant paths

## Slide 19: Definitions
Name -- mom, cs.washington.edu
  user visible
Address -- phone #, IP address
  globally unique, machine readable
Route
  how do you get from here to there?

## Slide 20: Switch Internals
Crossbar

## Slide 21: How Does the Switch Know Where to Send the Packet
Source routing (Myrinet)
  packet carries path
Table of global addresses (IP)
  stateless routers
Table of virtual circuits (ATM, MPLS)
  small headers, small tables

## Slide 22: Source Routing (Myrinet)
List entire path in packet
  Ex: A-> F (east, south, south)
Advantages
  Switches can be very simple and fast
Disadvantages
  Variable (unbounded) header size
  Sources must know topology (e.g., failures)
Typical use: machine room networks

## Slide 23: Global Addresses (IP)
Each packet has destination address
Each switch has forwarding table of destination -> next hop
  At v and x: F -> east
  At w and y: F-> south
  At z: F-> north
Distributed algorithm for calculating tables

## Slide 24: Router Table Size
One entry for every host on the Internet
  100M entries,doubling every year
One entry for every LAN
  every host on LAN shares prefix
  still too many, doubling every year
One entry for every organization
  every host in organization shares prefix
  requires careful, sparse allocation

## Slide 25: IP Address Allocation
Originally, 4 address classes
  A: 0 | 7 bit network | 24 bit host (1M each)
  B: 10 | 14 bit network | 16 bit host (64K)
  C: 110 | 21 bit network | 8 bit host (255)
  D: 1110 | 28 bit multicast group #
Assign net # centrally, host # locally
  UW has class B address

## Slide 26: IP Address Issues
We can run out
  4B IP addresses; 4B micros in 1997
We’ll run out faster if sparsely allocated
  Rigid structure causes internal fragmenting
Need address aggregation to keep tables small
  2M class C networks!

## Slide 27: Efficient IP Address Allocation
Subnets
  split net addresses between multiple sites
Supernets
  assign adjacent net addresses to same org
  classless routing (CIDR)
    combine routing table entries whenever all nodes with same prefix share same hop
Hardware support for fast prefix lookup

## Slide 28: IPV6 -- 128 bit addresses
Allow every device (PDA, toaster, etc.) to be assigned its own address
Modifies packet format
  Tunnel IPV6 packets over IPV4 network
How do IPV4 systems communicate with IPV6 ones?

## Slide 29: Network Address Translation
Allows multiple machines to be assigned same IPV4 address
NAT separates internal from ext. hosts
  Hosts only need internally unique address
NAT translates each packet
  internal IP -> dynamically allocated ext. IP
What if NAT crashes?

## Slide 30: Global Addresses
Advantages
  stateless => simple error recovery
Disadvantages
  Every switch knows about every destination
    aggregate table entries for nearby destinations
  single path routing
    all packets to destination take same route

## Slide 31: Virtual Circuits (ATM)
Each switch has forwarding table of connection -> next hop
  at connection setup, allocate virtual circuit ID (VCI) at each switch in path
  packet contains VCI, swizzled at each hop
  (input #, input VCI) -> (output #, output VCI)
    At v: (west=A, 12) -> (east=w, 2)
    At w: (west=v, 2) -> (south=y, 7)
    At y: (north=w, 7) -> (south=F, 4)

## Slide 32: Virtual Circuits
Advantages
  more efficient lookup (smaller tables)
  more flexible (different path for each circuit)
  can reserve bandwidth at connection setup
Disadvantages
  still need to route connection setup request
  more complex failure recovery

## Slide 33: Comparison

## Slide 34: How do we set up routing tables?
Graph theory to compute “shortest path”
  switches = nodes
  links = edges
  delay, hops = cost
Need dynamic computation to adapt to changes in topology

## Slide 35: Two Approaches
Distance vector (RIP, BGP)
  exchange routing tables with neighbors
  no one knows complete topology
  now used between admin domains
Link state (OSPF)
  send everyone your neighbors
  everyone computes shortest path
  now used within admin domains

## Slide 36: Distance Vector Algorithm
Initially, can get to self with cost 0
Iterate
  exchange tables with neighbors
  if neighbor has lower cost, update table

## Slide 37: Distance Vector Example
Step 0: v knows about itself
Step 1: v learns about A, B
Step 2: v learns about C, G, H
Step 3: v learns about D, E, F
  D from both w and z
Step 4: v learns about alternate routes

## Slide 38: Why Hop Count?
Latency used in original ARPAnet
  dynamically unstable
  penalized satellite links
Hop count yields unique loop-free path
  reflects router processing overhead consumed by packet
Can we design a dynamically stable adaptive routing algorithm?

## Slide 39: Distance Vector Problem
A
B
C
25*x
x
1
What if A->C fails?

## Slide 40: Solutions?
Hack distance vector
  Example: “poison reverse”
  Hard to make robust
BGP: send entire path with update
  can check if path has loop!
Link state routing
  only send what you know is true

## Slide 41: Link State
Each node gets complete topology via reliable flooding
  each node identifies direct neighbors, puts in numbered link state packet
  if get link state packet from neighbor Q
    if seen before drop
    else process and forward everywhere but Q
Given complete topology, compute shortest path using graph algorithm

## Slide 42: Question
Does link state algorithm guarantee routing tables are loop free?
  Yes if everyone has the same information
  No if updates are propagating
Is path-based distance vector loop free?
  Same problem

## Slide 43: Summary
Distance vector: node talks only to neighbors, tells them everything it knows or has heard
Link state: node talks to everyone, tells them only about its neighbors (what it knows for sure)

## Slide 44: Hierarchical Routing
Internet composed of many autonomous systems (AS’s)
  correspond to administrative domains
Each AS can choose its own routing alg.
  typically link state
BGP used to route between AS’s
  default: shortest number of AS’s in path
  sysadmins can express policy control

## Slide 45: Internet Routing in Practice
Paxson, Frequency of Routing Pathologies
Savage, Frequency of Routing Inefficiency
Floyd, Synchronization of Routing Messages

## Slide 46: Paxson Methodology
Traceroute
  Increase TTL field by 1, until get to dest
  When TTL expires, router replies with error packet
Traced all pairs of 27 - 33 sites, spread over globe
1994, 1995 (anecdotally, similar today)

## Slide 47: Routing Pathologies
Persistent loops: 0.13 - 0.16%
Temporary loops: 0.055 - 0.078%
Erroneous routing: 0.004 - 0.004%
Mid-stream change: 0.16 // 0.44%
Infrastructure failure: 0.21 // 0.48%
Outage >= 30 sec: 0.96 // 2.2%
Total pathologies: 1.5 // 3.4%

## Slide 48: Route Flap
Prevalence
  median 82%
Persistence
  minutes ~ 9% change
  hours ~ 23% change
  days ~ 68% change

## Slide 49: Routing Assymetry
Evidence of policy routing
  if shortest path, assymetry should be rare
Half of measurements show assymetric routes

## Slide 50: Problems with Internet routing
Packets don’t always take the “best” path
  No performance metrics
  Local routing policies
  Limited traffic exchange
How often and how badly does this happen?
(Times in milliseconds)

## Slide 51: Internet path selection study
Measure conditions between host pairs
  Latency, loss rate, bandwidth
  Calculate long term averages
Extrapolate “potential” alternate paths
  Compose host pairs to make synthetic path
  e.g. For hosts A and B, is there a host C such that the latency of AC + CB < AB?

## Slide 52: Latency and packet loss rate

## Slide 53: Bandwidth

## Slide 54: Confidence intervals

## Slide 55: Diurnal effects

## Slide 56: What would you expect?
Hop based routing ignores performance
  unlikely it would yield optimal routes
Can we synthetically generate results?
  Random points on plane
    latency = distance + random #

## Slide 57: Routing Synchronization
Observation: lots of periodic anomalies in the Internet. Why?
  Packet losses
  Routing storms
Synchronized behavior results in worse network performance
  Ex: everyone leaves work at 5pm
Study in context of routing

## Slide 58: Methodology and Results
Construct simple analytical model of router interaction
Does model predict synchronization?
  Occam’s Razor -- use simplest explanation that is sufficient
Result: yes!
  But is model accurate? Does it matter?
Solution: add randomness