## Slide 1: Lecture 5: Congestion Control
Challenge: how do we efficiently share network resources among billions of hosts?
  Last time: TCP
  This time: Alternative solutions

## Slide 2: Wide Design Space
Router based
  DECbit, Fair queueing, RED
Control theory
  packet pair, TCP Vegas
ATM
  rate control, credits
economics and pricing

## Slide 3: Standard “Drop Tail” Router
“First in, first out” schedule for outputs
Drop any arriving packet if no room
  no explicit congestion signal
Problems:
  If send more packets, get more service
  synchronization: free buffer => host send
  more buffers can actually increase congestion

## Slide 4: Router Solutions
Modify both router and hosts
  DECbit -- congestion bit in packet header
Modify router, hosts use TCP
  Fair queueing
    per-connection buffer allocation
  RED -- Random early detection
    drop packet or set bit in packet header

## Slide 5: DECbit routers
Router tracks average queue length
  regeneration cycle: queue goes from empty to non-empty to empty
  average from start of previous cycle
  If average > 1, router sets bit for flows sending more than their share
  If average > 2, router sets bit in every packet
  bit can be set by any router in path
Acks carry bit back to source

## Slide 6: DECbit source
Source averages across acks in window
  congestion if > 50% of bits set
  will detect congestion earlier than TCP
Additive increase, multiplicative decrease
  Decrease factor = 0.875 (7/8 vs. TCP 1/2)
  After change, ignore DECbit for packets in flight (vs. TCP ignore other drops in window)
No slow start

## Slide 7: Random Early Detection
Goal: improve TCP performance with minimal hardware changes
  avoid TCP synchronization effects
  decouple buffer size from congestion signal
Compute average queue length
  exponentially weighted moving average
  If avg > low threshold, drop with low prob
  If avg > high threshold, drop all

## Slide 8: Max-min fairness
At a single router
  Allocate bandwidth equally among all users
  If anyone doesn’t need share, redistribute
  maximize the minimum bandwidth provided to any flow not receiving its request
Network-wide fairness
  If sources send at minimum (max-min) rate along path
  What if rates are changing?

## Slide 9: Implementing max-min fairness
General processor sharing
  Per-flow queueing
  Bitwise round robin among all queues
Why not simple round robin?
  Variable packet length => can get more service by sending bigger packets
  Unfair instantaneous service rate
    what if arrive just before/after packet departs?

## Slide 10: Fair Queueing
Goals
  allocate resources equally among all users
  low delay for interactive users
  protection against misbehaving users
Approach: simulate general processor sharing (bitwise round robin)
  need to compute number of competing flows, at each instant

## Slide 11: Scheduling Background
How do you minimize avg response time?
  By being unfair: shortest job first
Example: equal size jobs, start at t=0
  round robin => all finish at same time
  FIFO => minimizes avg response time
Unequal size jobs
  round robin => bad if lots of jobs
  FIFO => small jobs delayed behind big ones

## Slide 12: Resource Allocation via Pricing
Internet has flat rate pricing
  queueing delay = implicit price
  no penalty for being a bad citizen
Alternative: usage-based pricing
  multiple priority levels with different prices
  users self-select based on price sensitivity, expected quality of service
    high priority for interactive jobs
    low priority for background file transfers

## Slide 13: Congestion Control Classification
Explicit vs. implicit state measurement
  explicit: DECbit, ATM rates, credits
  implicit: TCP, packet-pair
Dynamic window vs. dynamic rate
  window: TCP, DECbit, credits
  rate: packet-pair, ATM rates
End to end vs. hop by hop
  end to end: TCP, DECbit, ATM rates
  hop by hop: credits, hop by hop rates

## Slide 14: Packet Pair
Implicit, dynamic rate, end to end
Assume fair queueing at all routers
Send all packets in pairs
  bottleneck router will separate packet pair at exactly fair share rate
Average rate across pairs (moving avg)
Set rate to achieve desired queue length at bottleneck

## Slide 15: TCP Vegas
Implicit, dynamic window, end to end
Compare expected to actual throughput
  expected = window size / round trip time
  actual = acks / round trip time
If actual < expected, queues increasing => decrease rate before packet drop
If actual > expected, queues decreasing => increase rate

## Slide 16: ATM Forum Rate Control
Explicit, dynamic rate, end to end
Periodically send rate control cell
  switches in path provide min fair share rate
  immediate decrease, additive increase
  if source goes idle, go back to initial rate
  if no response, multiplicative decrease
  fair share computed from
    observed rate
    rate info provided by host in rate control cell

## Slide 17: ATM Forum Rate Control
If switches don’t support rate control
  switches set congestion bit (as in DECbit)
  exponential decrease, additive increase
  interoperability prevents immediate increase even when switches support rate control
Hosts evenly space cells at defined rate
  avoids short bursts (would foil rate control)
  hard to implement if multiple connections per host

## Slide 18: Hop by Hop Rate Control
Explicit, dynamic rate, hop by hop
Each switch measures rate packets are departing, per flow
  switch sends rate info upstream
  upstream switch throttles rate to reach target downstream buffer occupancy
Advantage is shorter control loop

## Slide 19: Hop by Hop Credits
Explicit, dynamic window, hop by hop
Never send packet without buffer space
  Downstream switch sends credits as packets depart
  Upstream switch counts downstream buffers
With FIFO queueing, head of line blocking
  buffers fill with traffic for bottleneck
  through traffic waits behind bottleneck

## Slide 20: Head of Line Blocking
Crossbar
aaaaa
bbbbb
ececec
ddddd
adcba
e e

## Slide 21: Avoiding Head of Line Blocking
Myrinet: make network faster than hosts
AN2: per-flow queueing
Static buffer space allocation?
  Link bandwidth * latency per flow
Dynamic buffer allocation
  more buffers for higher rate flows
  what if flow starts and stops?
    Internet traffic is self-similar => highly bursty

## Slide 22: TCP vs. Rates vs. Credits
What would it take for web response to take only a single RTT?
  Today: if send all at once => more losses

## Slide 23: Sharing congestion information
Intra-host sharing
  Multiple web connections from a host
  [Padmanabhan98, Touch97]
Inter-host sharing
  For a large server farm or a large client population
  How much potential is there?

## Slide 24: Destination locality

## Slide 25: Sharing Congestion Information
Internet
Subnet
Enterprise/Campus Network
Border Router
Congestion
Gateway

## Slide 26: Time to Rethink?
End to end
principle

## Slide 27: Multicast Preview
Send to multiple receivers at once
  broadcasting, narrowcasting
  telecollaboration
  group coordination
Revisit every aspect of networking
  Routing
  Reliable delivery
  Congestion control