## Slide 1: Lecture 6: Multicast
Challenge: how do we efficiently send messages to a group of machines?
  Need to revisit all aspects of networking
    Routing
    Autonomous systems and admin control
    Address allocation
    Congestion control (next time?)
    Reliable delivery (next time)
    Ordered delivery (next time)

## Slide 2: Multicast Motivation
Send data to multiple receivers at once
  broadcasting, narrowcasting
  telecollaboration
  software update
  group coordination, subcasting
Send question to unknown receiver
  resource discovery
  distributed database
  anonymous directory services

## Slide 3: Multicast Efficiency
Send data only once down link shared by multiple receivers
R
R
R
R
Sender

## Slide 4: MBone Deployment
How do we provide multicast services without router support?
MBone as virtual network
  PC routers, forward multicast traffic by tunneling over Internet
  Distance vector for routing between PCs
  Limit tunnel bw to avoid interfering with TCP
Widespread use!

## Slide 5: IP Multicast Service Model
Provided by (inter) network
  with help from LAN
  deployed as virtual network (MBone)
Delivery
  best effort (unreliable, unordered, …)
  packets addressed to group
    group address allocated from special range in IP
TTL for scope control (ex: send one hop)

## Slide 6: IP Multicast Service Model
Receivers
  zero, one or many receivers
  dynamic -- anyone can join, leave
  can belong to any number of groups
Senders
  Any number of senders
    just send packet to group address
  May or may not be in group
what about multicast virtual circuits?

## Slide 7: LAN Multicast Routing
Directly supported on shared media LANs (Ethernet, FDDI)
  App subscribes to group
  IP layer notifies Ethernet card to listen to packets with group address
What about switched LANs? (switched Ethernet, ATM)
  ARP already requires broadcast support!

## Slide 8: Flooding
If haven’t seen a packet before
  forward it on every link but incoming
  requires switches to remember each pkt!
R
R
R
Sender

## Slide 9: Spanning Tree
Ensures every host gets one copy (retransmission needed for drops)

## Slide 10: Computing a Spanning Tree
One (simple) approach
  Elect a leader (ex: node with lowest id)
  Spanning tree is shortest path to leader
  Re-compute if topology changes
Another (simple) approach
  distribute topology everywhere, compute in parallel (aka link state)

## Slide 11: Switched LAN Multicast Routing
What if only few receivers?
  Data sent needlessly over some links
  => prune links if no receivers
What if large scale LAN?
  No single tree efficient for all conditions
  => spanning tree per group
  => spanning tree per source
Same solutions as in Internet!

## Slide 12: Internet Multicast Routing
How do we distribute packets across thousands of LANs?
  Each router responsible for its attached LAN
Reduces to:
  How do we forward packets to all interested routers? (DVMRP, M-OSPF, MBone)
  How do hosts declare interest to their routers? (IGMP)

## Slide 13: Spanning Trees
Tree per group or tree per source?
  Scalability: router table entry per group vs. entry per group * per source
  Efficiency: worst case factor of 2 latency
  Bandwidth: can spread load with per-source trees
  Rendezvous: per source can leverage unicast routing tables

## Slide 14: Basic Approaches
Broadcast data and prune where there are no members
  based on distance vector routing (DVMRP)
Broadcast membership and compute forwarding tables
  based on link state routing (MOSPF)
Broadcast rendezvous for group addresses
  independent of unicast routing (PIM)

## Slide 15: Distance Vector Multicast
Intuition: unicast routing tables form inverse tree from senders to destination
  why not use backwards for multicast?
  Various refinements to eliminate useless transfers
Implemented in DVMRP (Distance Vector Multicast Routing Protocol)
  in use in MBone

## Slide 16: Reverse Path Flooding (RPF)
Router forwards packet from S iff packet came via shortest path back to S
R
R
R
S
s
s

## Slide 17: Redundant Sends
RPF will forward packet to router, even if it will discard
  each router gets pkt on all of its input links!
Each router connected to LAN will broadcast packet
Ethernet

## Slide 18: Reverse Path Broadcast (RPB)
With distance vector, neighbors exchange routing tables
Only send to neighbor if on its shortest path back to source
Only send on LAN if have shortest path back to source
  break ties arbitrarily

## Slide 19: Truncated RPB
End hosts tell routers if interested
Routers forward on LAN iff there are receivers
Challenges:
  robust to router/host failures
  avoid overloading LAN with announcements

## Slide 20: Internet Group Management Protocol (IGMP)
To join, host multicasts join requests to hosts in group + routers on LAN, TTL=1
Routers periodically query hosts for group membership
  stop forwarding if receiver crashes
Hosts set random timer
  When expire, multicast join
  Other hosts in group disable timer

## Slide 21: IGMP (step 1)
Elect one router periodically query about all groups (TTL=1)
Q

## Slide 22: IGMP (step 2)
One group member responds to group with TTL=1, everyone else defers
Q
G
G
G

## Slide 23: Reverse Path Multicast (RPM)
Forward packets only to those areas of the network with receivers
“Broadcast and prune”
  Use IGMP to tell if LAN if no members
  If no children are members, propagate prune to parent in tree
Assume membership and prune if wrong vs. assume non-membership and explicit join

## Slide 24: How does a receiver join?
Graft (prune cancellation)
  Routers remember where they sent prunes
    where multicast traffic came from
  If child joins, send graft in same direction(s)
Requires ARQ
  what if graft is dropped?
  What if prune is dropped?

## Slide 25: Phase 1: Truncated Broadcast
g
s
g
g

## Slide 26: Phase 2: Pruning
g
s
g
g
prune(s,g)
prune(s,g)

## Slide 27: Phase 3: Grafting
g
s
g
g
graft(s,g)
graft(s,g)
g
report g

## Slide 28: Phase 4: Steady State
g
s
g
g
g

## Slide 29: RPM Mechanics
Data-driven -- prune only when packet arrives
  Why?
Periodically time out prunes
  Why?
Are loops possible in routing tree?

## Slide 30: Link State Multicast
MOSPF (Multicast OSPF)
Use IGMP to determine LAN members
Flood topology/group changes
Each router gets complete topology, group membership
  compute shortest path spanning tree
  recompute tree every time topology changes
  add/delete links if membership changes

## Slide 31: Link State Mechanics
Unicast link state
  precompute routes for all destinations
    all-to-all shortest path
  Use CIDR to reduce table size
Multicast link state
  precompute routes for all source-group pairs?
  compute on demand when packet arrives?
Are loops possible in routing tables?

## Slide 32: PIM Motivation
PIM = Protocol Independent Routing
What about sparse groups -- groups that involve only a few members?
  Ex: narrowcasting -- chat rooms, virtual corporations, … => could be common use
Distance vector + link state =>
  periodic broadcast to every router in Internet!

## Slide 33: PIM Approach
Every multicast group has a set of predefined rendezvous points (RP)
  need multiple for failure redundancy
Receiver join: send packet to one RP
Source join: send to all RP’s
If infrequent traffic, use tree per group
  rooted at rendezvous points
Add/delete links via reference counting

## Slide 34: What if frequent traffic?
Want to specialize with tree per source
  All routers below RP observe traffic
  If lots of packets from one source
    router sends join to source
    source sends traffic to router in addition to RPs
    once router gets traffic from source, prune

## Slide 35: PIM Shared Tree
g
s
g
g
RP

## Slide 36: PIM Receiver Join
g
s
g
g
RP
Join *,g
Report g
g
What if
join here?

## Slide 37: PIM Shared Tree After Join
g
s
g
g
g
RP
g

## Slide 38: PIM Source Based Tree
g
s
g
g
g
RP
g
Join s,g

## Slide 39: PIM Source Based Tree
g
s
g
g
g
RP
g
What if join s,g?
What if source?

## Slide 40: PIM Protocol Independence?
Packets sent to specific targets using unicast routing services
  Receiver join: send to RP
  Source join: send to RPs
  Source based tree creation: send to source
  Multicast packets: send to RPs, routers
Multiaccess links confuse reference counting: all routers listen for add/prune

## Slide 41: How do we decide on RP’s?
Need consensus of which RP to use for each group, or nothing works
Current thinking
  Replicated bootstrap manager
  RP candidates register with manager
  Manager broadcasts candidate RP list
  Hosts use consistent hash to select RP

## Slide 42: Hierarchical Routing Motivation
Decompose routing problem into sub-problems
Allow each organization to choose their own algorithm
Reduce table size by aggregating addresses

## Slide 43: Hierarchical Broadcast and Prune
Reverse Path Flooding
  Discard incoming packet if not from reverse path
  Multicast incoming packet to all borders
Reverse Path Multicast
  For each neighbor AS, compute if we’re on reverse path to source
  Multicast incoming packets to useful borders
  Propagate prunes across AS back to source

## Slide 44: Hierarchical Link State
Broadcast topology, group membership within each AS
Broadcast AS topology, group membership, to all AS’s
Compute multicast tree across AS’s
  identify incoming/outgoing borders
Compute multicast tree within each AS

## Slide 45: Hierarchical PIM
Explicit sender and receiver joins
Protocol independence
=> border routers propagate joins across boundaries
Hard to interoperate PIM with broadcast&prune

## Slide 46: Hierarchical Routing Mechanics
What if each AS uses its own algorithm?
  Incoming multicast packet may arrive on any border router
  How do we detect routing loops?
  Propagate explicit joins in PIM
How do we reduce table size using aggregates?
  Combine nearby sources? similar groups?

## Slide 47: Multicast Address Allocation
More dynamic than unicast allocation
Groups cross organizational boundaries
Central server?
  Blocks of addresses for internal groups
  Leases for global addresses
Random allocation?
  Can listen to tell if address is in use
  Need conflict resolution protocol

## Slide 48: Scope Control Motivation
Efficiency with reverse path multicast
  sender prunes receivers
Administrative control over listeners
  anyone can listen to multicast conversation!
  snooping more difficult in unicast
Coordinate sub-group actions
  elect a leader/suppress duplicate actions
  locate nearest receiver

## Slide 49: Scope Control Mechanisms
Administrative TTL boundaries
  Sender uses TTL = max diameter of local intranet
  At border router, forward pkts iff > local TTL
Allocate block of “local” addresses
  At border router, forward only global addresses

## Slide 50: Expanding Ring Multicast
Locate “nearest” receiver
Progressively send to more and more of group
  Send first to all receivers within one hop, then two hops, then three, …

## Slide 51: Layered Multicast
What if receivers have different bandwidths?
R
R
R
S
100Mb/s
100Mb/s
100Mb/s
1Mb/s
1Mb/s
56Kb/s

## Slide 52: Layered Multicast
Transmit signal at multiple granularities
  56Kb/s - voice only
  1Mb/s - choppy video
  100Mb/s - high quality video
Drop packets at router if can’t handle rate?
  Which packets?
  Leads to persistent congestion at bottleneck
  Wastes upstream resources

## Slide 53: Receiver-Driven Layered Multicast
Receivers dynamically adapt to available capacity
Each layer a separate group
  receiver subscribes to max layer that will get through with minimal drops
Use packet drops as congestion signal
  No drops => try subscribing to higher layer
  Drops => unsubscribe to layer

## Slide 54: RLM Mechanics
Receivers periodically try subscribing to higher layer
If unsuccessful, overwhelms bottleneck router
  Causes packet losses for other receivers?
  => other receivers drop layers?
  What if two conflicting subscribes at same time?

## Slide 55: RLM Receiver Coordination
Receiver advertises intent to add layer
Other receivers
  ignore congestion signal during experiment
  avoid conflicting experiments
Receiver advertises result when done. Example of shared learning:
  if successful, other receivers add layer
  if unsuccessful, wait longer until next retry