## Slide 1: Lecture 6: Multicast
Challenge: how do we efficiently send messages to a group of machines?
  Need to revisit all aspects of networking
  Last time
    Routing
  This time
    Reliable delivery
    Ordered delivery
    Congestion control

## Slide 2: Multicast Address Allocation
Unicast IP addresses
  allocated statically to hosts
  allocated hierarchically by hosts’ org
Multicast IP addresses
  allocated per connection
  groups cross admin boundaries

## Slide 3: Address Allocation Solutions
Central server?
  Blocks of addresses for internal groups
  Leases for global addresses
Random allocation?
  Send to group to ask if address is in use
  Need conflict resolution protocol

## Slide 4: Scope Control Motivation
Efficiency with reverse path multicast
  sender prunes receivers
Administrative control over listeners
  anyone can listen to multicast conversation!
  snooping more difficult in unicast
Coordinate sub-group actions
  elect a leader/suppress duplicate actions
  locate nearest receiver

## Slide 5: Scope Control Mechanism #1
Administrative TTL boundaries
  Sender uses TTL = max local diameter
  At border router, forward pkts out iff > TTLmax
Internet
s
TTL thresh = 8

## Slide 6: Scope Control Mechanism #2
Allocate block of “local” addresses
  At border router, forward only global addresses
Internet
s
Don’t forward addresses
0xffff0000-0xffff2000

## Slide 7: Expanding Ring Multicast
Locate “nearest” receiver by sending to more and more of group
s
g
g
g
g
g
TTL=1
TTL=3
TTL=5
TTL=2
g
g

## Slide 8: Reliable Multicast
How do we make sure each receiver gets a copy of each message?
R
R
R
Sender
R
R

## Slide 9: Ack Implosion
If each receiver acks each packet, sender gets overwhelmed!
R
R
R
Sender
R
R

## Slide 10: Negative Acks
Possible solution: only send back to source if missing data
  missing sequence number (2, 3, 5, 6, 7, …)
  ping if no data being sent, to detect if missing last packet
Fewer packets if losses are infrequent
  note TCP uses acks for pacing new sends

## Slide 11: Nack Implosion
If lose packet near sender, overwhelm sender with nacks!
R
R
R
Sender
R
R
X

## Slide 12: Hop by Hop Retransmission
Router keeps copy of all packets
Resends if negative ack or timeout
R
R
R
Sender
R
R
X
retransmission

## Slide 13: Scalable Reliable Multicast
Use multicast services to recover from packet losses!
  If missing packet, multicast NACK
    anyone get the packet?
    Tell others to suppress NACK
  Receivers with packet will multicast reply
    anyone else missing the packet?
    Tell others to suppress reply
Assumes packets are signed by source

## Slide 14: SRM Scalability?
If everyone multicasts NACK
  NACK implosion everywhere!
If everyone multicasts reply
  data implosion everywhere!
Goal: minimize simultaneous NACKs and replies

## Slide 15: SRM Scalability
Use random delay before sending NACK/reply
  less likely for more than one to send at once
Bias delay to reduce competition
  NACK delay based on distance to source
  Reply delay based on distance to NACK
  distance est. using periodic session msgs
Doesn’t matter which host NACKs, replies

## Slide 16: SRM Example
R3 detects loss, multicasts NACK
R1 sees NACK, multicasts reply
R5
R2
R4
Sender
R3
R1
X

## Slide 17: SRM Timer Adaptation
Want system to be robust to topologies, group sizes, congestion
  Adapt average delays to minimize redundant NACKs, replies
  Analogous to RTT estimation in TCP
Examples
  if too many NACKs, increase average delay
  if NACK once, reduce delay so NACK again

## Slide 18: What if multiple drops?
Can use TTL expanding ring search for local recovery
R
R
R
Sender
R
R
R
R
X
X
X

## Slide 19: SRM Evaluation
Scalability?
  What happens as we increase # of hosts?
  What about diversity of link bandwidths?
Stability?
  What happens as load increases?
Security
  reply with corrupted packet
  denial of service => NACK everything!

## Slide 20: Application Level Framing
Allow application to control how data is packetized on network
  each RPC, object on packet boundaries
  by contrast, TCP/IP transmits byte stream
Advantages?
Disadvantages?

## Slide 21: Multicast Packet Ordering
Easy to order unicast packets => seq #s
Easy to order multicast packets from a single source => seq #s
What if multiple sources?
  Packets can arrive in different order at different receivers
  Is this bad?
  If so, what can we do to fix it?

## Slide 22: Multicast Ordering Example
s
s
g
g
g
g
abc
xyz
axbycz
abxcyz
abcxyz
xyzabc
g
g
xaybzc

## Slide 23: Example: Email Groups
A
C
B
D
Meet for lunch?
Need to hold
design review
Meet at noon?
Noon for what?
Confirmed!
Confirmed!
Oh, ok!
Anytime other
than noon!

## Slide 24: Example: Deterministic Replicas
Replicate server for higher throughput, fault tolerance
  Read from any replica
  Write to all replicas
How do we keep replicas consistent?
  Provide all replicas exactly same sequence of messages
  Each replica behaves deterministically, reaches same state as all other replicas

## Slide 25: Multicast Total Ordering
All packets are delivered in same order everywhere
Single seq # for all packets to group
  every source sends packets to arbiter
  arbiter assigns sequence #
  if arbiter fails, elect new one
  receivers don’t process packets out of order

## Slide 26: Multicast Causal Ordering
Total ordering inefficient for subcasts
Instead, causal ordering
  packets are never delivered before packets that could have “caused” them
    receiver must have gotten all the packets source has seen
  packets that originate concurrently can be delivered in any order

## Slide 27: Implementing Causal Ordering
Packets carry per-host sequence #
  increment on each send
Each host maintains a “version vector”
  max seq #’s seen (in order) from each host
  put version vector in each outgoing packet
At receiver, delay packet until host vector > packet vector, for all sources

## Slide 28: Causal Ordering Example
A
C
B
D
Meet for lunch?
Need to hold
design review
Meet at noon?
Defer packet
Defer packet
Confirmed!
11 am?
Anytime other
than 11am!
0,0,0,0
0,0,0,0
0,0,0,0
0,0,0,0
0,1,0,0
0,0,0,1
0,1,1,0
How about noon?

## Slide 29: Multicast Congestion Control
What if receivers have very different bandwidths?
Send at max?
Send at min?
Send at avg?
R
R
R
S
100Mb/s
100Mb/s
100Mb/s
1Mb/s
1Mb/s
56Kb/s
R

## Slide 30: Layered Multimedia
Transmit signal at multiple granularities
  56Kb/s - voice only
  1Mb/s - choppy video
  100Mb/s - high quality video
Layers can be
  independent (redundant)
  dependent (progressive refinement)

## Slide 31: Drop Policies for Layered Multicast
Priority
  packets for low bandwidth layers are kept, drop queued packets for higher layers
  requires router support (hard to deploy!)
  wastes upstream resources
Uniform (e.g., drop tail, RED)
  packets arriving at congested router are dropped regardless of their layer

## Slide 32: Receiver-Driven Layered Multicast
Each layer a separate group
  receiver subscribes to max group that will get through with minimal drops
Dynamically adapt to available capacity
  use packet losses as congestion signal
Assume no special router support
  packets dropped independently of layer

## Slide 33: How does receiver know which layers to add?
User decides based on observed quality?
  Won’t add layer if no benefit
System dynamically adapts to available capacity
  Use packet drops as congestion signal
  No drops => try subscribing to higher layer
  Drops => unsubscribe to layer

## Slide 34: RLM Join Experiment
Receivers periodically try subscribing to higher layer
If enough capacity, no congestion, no drops => keep layer (& try next layer)
If not enough capacity, congestion, drops => drop layer (& increase time to next retry)
  what about impact on other receivers?

## Slide 35: RLM Join Example
R4
R1
R3
S
100Mb/s
100Mb/s
100Mb/s
1Mb/s
1Mb/s
56Kb/s
R2
R4 joins layer 1,
fails at layer 2
R2,R3 join layer 1,
join layer 2
fails at layer 3
R1 joins layer 1,
joins layer 2
joins layer 3

## Slide 36: RLM Scalability?
What happens with more receivers?
Increased frequency of experiments?
  more likely to conflict (false signals)
  network spends more time congested
Reduce # of experiments per host?
  Takes longer to converge

## Slide 37: RLM Receiver Coordination
Receiver advertises intent to add layer
Other receivers
  avoid conflicting experiments
  if experiment fails, will see increased drops => don’t try adding layer! (shared learning)
  OK to try adding lower layer during higher layer experiment
    won’t cause drops at higher layer!

## Slide 38: RLM Interactions
With other multicast groups?
With unicast TCP traffic?
With RED?
With fair queuing?
With priority for lower layers?

## Slide 39: Drop Policies for Layered Multicast
Priority
  packets for low bandwidth layers are kept, drop queued packets for higher layers
Uniform
  packets arriving at congested router are dropped regardless of their layer
Which is better?
  Intuition vs. reality!

## Slide 40: RLM Intuition
Uniform offers better incentives to well-behaved users
  if oversend, performance rapidly degrades
Uniform offers clearer congestion signal
  allows shared learning
RLM approaches optimal operating point
  uniform is already deployed

## Slide 41: RLM Intuition

## Slide 42: Bajaj et al. Intuition
Priority offers much better performance
  particularly with bursty traffic
RLM will perform badly with bursty traffic
  unable to adapt to congestion transients
Uniform offers better incentives
  but socially optimal != individually optimal

## Slide 43: Bajaj et al. Intuition

## Slide 44: Model Details
Compare alternatives using total utility
Utility of low layers > utility of high layers
Utility of layer even if some drops
  independent of drops on other layers
Drop tail router
Both simulation and analytical model

## Slide 45: Model Results
Smooth traffic: RLM is close to optimal
Bursty traffic: RLM < uniform < priority
  but not by much!
  RLM worse if low layers not valuable
Incentive to oversubscribe with both uniform and priority
Slight disincentive to send/receive => individual = socially optimal

## Slide 46: Multicast Summary
Multicast needed for efficiency, group coordination
Need to revisit all aspects of networking
  Routing
  Administration
  Reliable delivery
  Ordered delivery
  Congestion control