## Slide 1: 588 Section 2
Neil Spring
April 13, 1999

## Slide 2: Schedule
traceroute (context)
Paxson’s Pathologies
Dijkstra’s (shortest path) Algorithm
Subnetting
Homework Questions
Programming Assignment Questions

## Slide 3: traceroute
ttl = 1
while ( not yet at host )
  send UDP message to host with ttl
  print sender of time exceeded ICMP
  ttl = ttl+1
Where is the ttl stored?

## Slide 4: traceroute example
poplar:~> traceroute www.sdsc.edu
traceroute to www.sdsc.edu (198.202.75.101), 30 hops max, 40 byte packets
1 hoover-V3.cac.washington.edu (128.95.3.100) 0.865 ms 0.826 ms 0.808 ms
2 uwbr2-FE1-1-0.cac.washington.edu (140.142.153.24) 0.844 ms 0.685 ms 0.682 ms
3 adsgpop1-FE5-0-0.snnap.net (198.32.170.1) 0.822 ms 0.789 ms 1.088 ms
4 cs-pos.sej.vbns.net (198.48.91.2) 1.876 ms 1.874 ms 2 ms
5 cs-atm0-0-21.sdsc.vbns.net (204.147.129.81) 27.587 ms 27.697 ms 27.524 ms
6 medusa.sdsc.edu (198.17.46.10) 28.011 ms 27.67 ms 33.596 ms
7 webfarm1.sdsc.edu (198.202.75.201) 28.239 ms 27.798 ms 27.857 ms

## Slide 5: traceroute example II
poplar:~> traceroute www.cs.monash.edu.au
traceroute to shelob.cs.monash.edu.au (130.194.64.159), 30 hops max, 40 byte packets
1 hoover-V3.cac.washington.edu (128.95.3.100) 0.85 ms 1.223 ms 0.708 ms
2 uwbr2-FE1-1-0.cac.washington.edu (140.142.153.24) 0.74 ms 0.589 ms 0.588 ms
3 fe3-0.wes-as3942.nw.verio.net (198.32.170.19) 1.381 ms 1.145 ms 1.52 ms
4 sl-gw3-sea-5-0.sprintlink.net (144.228.96.25) 2.067 ms 1.833 ms 1.395 ms
5 sl-bb10-sea-4-1.sprintlink.net (144.232.6.41) 1.055 ms 1.127 ms 1.331 ms
6 sl-bb4-sea-0-0-0.sprintlink.net (144.232.6.10) 2.074 ms 2.595 ms 1.897 ms
7 core2-hssi3-0.Seattle.cw.net (206.157.77.153) 3.483 ms 4.334 ms 5.447 ms
8 core4-hssi5-0-0.WestOrange.cw.net (206.157.77.105) 70.998 ms core4-hssi0-0-0.WestOrange.cw.net (206.157.77.109) 70.09 ms core4-hssi5-0-0.WestOrange.cw.net (206.157.77.105) 75.674 ms
9 cwusa-mciworldcom.WestOrange.cw.net (166.49.11.142) 216.362 ms 70.449 ms 71.93 ms
10 207.124.127.34 (207.124.127.34) 93.276 ms 92.253 ms 91.878 ms
11 nyd-7513-1-f5-0.cwix.net (206.142.243.1) 92.658 ms 90.659 ms 100.49 ms
12 sfd-7513-2-a10-0-2.cwix.net (207.124.107.74) 117.85 ms 131.157 ms 128.031 ms
13 g-sfd-br-02-f1-0.gn.cwix.net (206.142.242.1) 97.64 ms 98.739 ms 105.248 ms
14 cwi-optus.cwix.net (207.124.109.58) 448.903 ms 451.08 ms 444.254 ms
15 h21-4.ia2.optus.net.au (202.139.7.137) 459.292 ms 448.061 ms 453.086 ms
16 atm50-4.ia3.optus.net.au (202.139.7.149) 477.353 ms 529.946 ms 510.437 ms
17 192.65.88.194 (192.65.88.194) 520.156 ms 502.582 ms 475.863 ms
18 monash-gw.vrn.edu.au (203.21.130.135) 463.963 ms 468.625 ms 465.674 ms
19 eng-gw.monash.edu.au (130.194.14.50) 476.322 ms 462.563 ms 468.388 ms
20 shelob.cs.monash.edu.au (130.194.64.159) 466.978 ms 453.821 ms 460.588 ms

## Slide 6: traceroute example III
FROM www.sdsc.edu TO www.cs.monash.edu.au at Tue Apr 13 13:18:31 PDT 1999.
traceroute to shelob.cs.monash.edu.au (130.194.64.159), 30 hops max, 40 byte packets
1 medusa.sdsc.edu (198.202.75.10) 1 ms 0 ms 0 ms
2 192.12.207.9 (192.12.207.9) 1 ms 11 ms 1 ms
3 atm2-0-6.san-bb1.cerf.net (134.24.12.25) 5 ms 3 ms 3 ms
4 pos0-0-155M.san-bb6.cerf.net (134.24.29.130) 4 ms !H * *
5 atm6-0-2-622M.lax-bb4.cerf.net (134.24.32.62) 6 ms 7 ms 7 ms
6 pos6-0-622M.sfo-bb3.cerf.net (134.24.29.233) 17 ms !H * 16 ms
7 pos11-0-0.sfo-bb2.cerf.net (134.24.29.198) 15 ms * 17 ms
8 att-gcsi-gw.sfo-bb2.cerf.net (134.24.45.6) 27 ms 21 ms 19 ms
9 205.174.74.166 (205.174.74.166) 19 ms 17 ms 19 ms
10 h21-4.ia2.optus.net.au (202.139.7.137) 360 ms 373 ms 364 ms
11 202.139.7.54 (202.139.7.54) 350 ms 349 ms 342 ms
12 192.65.88.194 (192.65.88.194) 358 ms 352 ms 358 ms
13 monash-gw.vrn.edu.au (203.21.130.135) 366 ms 364 ms 362 ms
14 eng-gw.monash.edu.au (130.194.14.50) 363 ms 373 ms 360 ms
15 * shelob.cs.monash.edu.au (130.194.64.159) 365 ms 366 ms

## Slide 7: traceroute example IV
traceroute to ares.fedworld.gov (192.239.92.47), 30 hops max, 40 byte packets
1 hoover-V3.cac.washington.edu (128.95.3.100) 0.835 ms (255) 0.844 ms (255) 0.86 ms (255)
2 uwbr2-FE5-1-0.cac.washington.edu (140.142.154.24) 0.656 ms (254) 0.588 ms (254) 0.703 ms (254)
3 fe3-0.wes-as3942.nw.verio.net (198.32.170.19) 1.618 ms (253) 1.162 ms (253) 1.18 ms (253)
4 sl-gw3-sea-5-0.sprintlink.net (144.228.96.25) 2.516 ms (252) 2.721 ms (252) 2.239 ms (252)
5 sl-bb10-sea-4-1.sprintlink.net (144.232.6.41) 2.181 ms (251) 1.879 ms (251) 1.708 ms (251)
6 sl-bb3-sea-0-0-0.sprintlink.net (144.232.6.18) 2.357 ms (250) 1.739 ms (250) 1.436 ms (250)
7 hssi5-1-0.br1.sea1.alter.net (137.39.250.50) 2.51 ms (249) 2.104 ms (249) 3.763 ms (249)
8 105.atm2-0.xr2.sea1.alter.net (146.188.200.70) 2.761 ms (248) 2.034 ms (248) 2.523 ms (248)
9 194.atm3-0.tr2.sea1.alter.net (146.188.200.118) 3.238 ms (247) 2.432 ms (247) 1.838 ms (247)
10 110.atm7-0.tr2.dca1.alter.net (146.188.136.233) 80.31 ms (244) 77.324 ms (244) 74.776 ms (244)
11 198.atm6-0.xr2.tco1.alter.net (146.188.161.177) 85.166 ms (245) 81.341 ms (245) 78.24 ms (245)
12 192.atm10-0-0.gw3.tco1.alter.net (146.188.161.117) 80.006 ms (244) 68.574 ms (244) 76.293 ms (244)
13 * * *
14 fedworld-gw.customer.ALTER.NET (157.130.34.194) 62.019 ms (243) !A * *
15 * * fedworld-gw.customer.ALTER.NET (157.130.34.194) 63.617 ms (243) !A
16 * fedworld-gw.customer.ALTER.NET (157.130.34.194) 64.511 ms (243) !A *

## Slide 8: Paxson’s Pathologies
loops
fluttering
outages

## Slide 9: Stabilities
Prevalence
Persistence
Symmetry
  not really a stability,
How do you build a real time application?

## Slide 10: Dijkstra’s Algorithm
Sets:
  found: initialized to source
  reachable but not found: stored in a heap
while set 2 not empty
  take closest, add to found set
  update
  http://carnap.ss.uci.edu/java/dijkstra/DijkstraApplet.html

## Slide 11: Dijkstra’s Algorithm (practice)
Confirmed = found set
Tentative = reachable but not found
while Tentative not empty
  closest  Confirmed
  if new neighbors, add to tentative
  if Tentative neighbors, maybe reduce cost

## Slide 12: Why routing is hard

## Slide 13: Subnetting
Class A, B, C provide limited hierarchy
Hierarchy within networks

## Slide 14: ifconfig (context)
calvin:~> /sbin/ifconfig le0
le0: flags=863<UP,BROADCAST,NOTRAILERS,RUNNING,MULTICAST> mtu 1500
inet 128.95.1.10 netmask ffffff00 broadcast 128.95.1.255
saba:~> /sbin/ifconfig eth0
eth0 Link encap:10Mbps Ethernet HWaddr 00:A0:24:D1:51:E8
inet addr:128.95.4.58 Bcast:128.95.4.255 Mask:255.255.255.0
UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
RX packets:14088923 errors:0 dropped:0 overruns:0
TX packets:7022055 errors:0 dropped:0 overruns:0
Interrupt:3 Base address:0xff00

## Slide 15: host routing table (more context)
poplar:~> netstat -nr
Kernel IP routing table
Destination Gateway Genmask Flags MSS Window irtt Iface
128.95.3.0 0.0.0.0 255.255.255.0 U 1500 0 0 eth0
127.0.0.0 0.0.0.0 255.0.0.0 U 3584 0 0 lo
0.0.0.0 128.95.3.100 0.0.0.0 UG 1500 0 0 eth0
commands to generate:
route add -net 128.95.3.0 netmask 255.255.255.0 eth0
route add default gw 128.95.3.100
What class of address is 128.95.3.16?
What’s the implied class of this address?

## Slide 16: Address Space Utilization