## Slide 1: 588 Section 3
Neil Spring
April 20, 1999

## Slide 2: Schedule
Homework Post-mortem
  two, eight, nine
tcpdump (context)
Balakrishnan’s link strategies
Programming Assignment Questions

## Slide 3: Late Policy
Seven slip days
Yes, discussing answers to the homework now conflicts with having slip days.
There’s probably a good solution.
The benefit you’ll get by waiting until after I’ve discussed these problems is at most 25% / 3 homeworks / 3 problems, or 2.8% of your grade.
Be honorable.

## Slide 4: Homework Question #2
The user provides an 8 bit flag aSbc; whenever you find S in the data, add an extra bit b’ after it.
Fails on {a,S,b,c}= {0, 11011, 1, 1}
Where 0110111111 is in the user stream
Transformed to 01101101111
Other solutions possible

## Slide 5: Homework Question #8
TCP uses a 16 bit checksum per segment, typically 576 bytes. Is link level error correction really necessary? What is the maximum link layer bit error rate you would be willing to rely on TCP to catch? Defend your answer.
  Checksum is:
    easy to compute
    calculated by adding the words.
    just a backup.
    vulnerable to bit exchanges.
Common answers:
  1/576
  1/(288*8)
  it depends.
  2-16 [IEN 45]=10-5
  CRC is better

## Slide 6: Homework Question #8
Some errors will make it past checksum
The most likely is the 2 bit error 0->1, 1->0
Has to happen in the right place, within the same packet.
(Bits in packet) * Link Err2 * ½ * 16/162
P(undetected err) = Link Err2 * Pkt size2 / 64
Undetected = 0.01% -> 1/57,600 bits
2

## Slide 7: Homework Question #9
Internet supports “probe” packets. Routers will reply when a packet’s hop count reaches 0. Explain how a source can use the elapsed round trip time of these packets to infer the bandwidth and delay of every link between the source and the destination. First, show how it can be done for the first hop, then recursively. Assume symmetry.

## Slide 8: Homework Question #9
Pictures from Van Jacobson’s Pathchar talk
ftp://ftp.ee.lbl.gov/pathchar/

## Slide 9: Homework Question #9
ICMP response time slide

## Slide 10: Homework Question #9
Delay is unloaded RTT.
T (Size) = Delay + Size / Bandwidth
T(big) - T(small) = Delay - Delay + big /BW - small/BW
T(big) - T(small) = big/bw-small/bw
BW = (big-small) / (T(big) - T(small))
Extend with increasing TTL as in traceroute.

## Slide 11: The real world of Question #9
Queues don’t delay uniformly

## Slide 12: The real world of Question #9
Take the minimum of samples

## Slide 13: tcpdump
Tool used to watch packets on the network.
Network interface into “promiscuous mode”
  doesn’t filter out packets not destined for its hardware address.
Can get timing information, retransmission rates, other protocol stuff

## Slide 14: Connection Overview
Startup: SYN, SYN/ACK, ACK
Teardown: FIN, ACK, FIN, ACK
In between: segments and acknowledgments

## Slide 15: Tcpdump (example)
15:54:08.003367 c16.1042 > poplar.webcache: S 10715744:10715744(0) win 8192 <mss 1460,nop,wscale 0,nop,nop,timestamp[|tcp]> (DF) [tos 0x3]
15:54:08.003367 poplar.webcache > c16.1042: S 2425854216:2425854216(0) ack 10715745 win 16352 <mss 1460>
15:54:08.003367 c16.1042 > poplar.webcache: . ack 1 win 8760 (DF) [tos 0x3]
15:54:08.013366 c16.1042 > poplar.webcache: P 1:366(365) ack 1 win 8760 (DF) [tos 0x3]
15:54:08.013366 poplar.webcache > c16.1042: P 1:1461(1460) ack 366 win 16352 (DF) [tos 0x3]
15:54:08.013366 poplar.webcache > c16.1042: . 1461:2921(1460) ack 366 win 16352 (DF) [tos 0x3]
15:54:08.013366 c16.1042 > poplar.webcache: . ack 2921 win 8760 (DF) [tos 0x3]
15:54:08.023366 poplar.webcache > c16.1042: . 2921:4381(1460) ack 366 win 16352 [tos 0x3]
15:54:08.023366 poplar.webcache > c16.1042: . 4381:5841(1460) ack 366 win 16352 [tos 0x3]
15:54:08.023366 poplar.webcache > c16.1042: . 5841:7301(1460) ack 366 win 16352 [tos 0x3]
15:54:08.023366 c16.1042 > poplar.webcache: . ack 5841 win 8760 (DF) [tos 0x3]
15:54:08.023366 poplar.webcache > c16.1042: . 7301:8761(1460) ack 366 win 16352 [tos 0x3]
15:54:08.023366 c16.1042 > poplar.webcache: . ack 8761 win 8760 (DF) [tos 0x3]
15:54:08.023366 poplar.webcache > c16.1042: P 8761:10129(1368) ack 366 win 16352 (DF) [tos 0x3]
15:54:08.153362 c16.1042 > poplar.webcache: . ack 10129 win 7392 (DF) [tos 0x3]
15:54:24.012817 poplar.webcache > c16.1042: F 10129:10129(0) ack 366 win 16352 [tos 0x3]
15:54:24.012817 c16.1042 > poplar.webcache: . ack 10130 win 7392 (DF) [tos 0x3]
Web transfer, Sequence numbers (normalized), MSS negotiation
Packets include acks, my timer is poor.

## Slide 16: Tcpdump (example #2)
tcpdump: listening on eth0
11:34:08.368899 c16.1031 > poplar.webcache: S 925773:925773(0) win 8192 <mss 1460,nop,wscale 0,nop,nop,timestamp[|tcp]> (DF) [tos 0x6] (ttl 128, id 14848)
11:34:08.368899 poplar.webcache > c16.1031: S 3659357311:3659357311(0) ack 925774 win 16352 <mss 1460> (ttl 64, id 5350)
11:34:08.368899 c16.1031 > poplar.webcache: . ack 1 win 8760 (DF) [tos 0x6] (ttl 128, id 15360)
11:34:08.368899 c16.1031 > poplar.webcache: P 1:297(296) ack 1 win 8760 (DF) [tos 0x6] (ttl 128, id 15616)
11:34:08.368899 poplar.webcache > c16.1031: P 1:181(180) ack 297 win 16352 (DF) [tos 0x6] (ttl 64, id 5352)
11:34:08.388899 c16.1031 > poplar.webcache: P 297:654(357) ack 181 win 8580 (DF) [tos 0x6] (ttl 128, id 16128)
11:34:08.388899 poplar.webcache > c16.1031: P 181:360(179) ack 654 win 16352 (DF) [tos 0x6] (ttl 64, id 5353)
11:34:08.588892 poplar.webcache > c16.1031: P 181:360(179) ack 654 win 16352 (DF) [tos 0x6] (ttl 64, id 5354)
11:34:08.588892 c16.1031 > poplar.webcache: . ack 360 win 8401 (DF) [tos 0x6] (ttl 128, id 16640)
11:34:25.508314 poplar.webcache > c16.1031: F 360:360(0) ack 654 win 16352 [tos 0x6] (ttl 64, id 5375)
11:34:25.508314 c16.1031 > poplar.webcache: . ack 361 win 8401 (DF) [tos 0x6] (ttl 128, id 17152)
11:34:28.488212 c16.1031 > poplar.webcache: R 926427:926427(0) win 0 (DF) [tos 0x6] (ttl 128, id 17408)
Timeout, Sequence numbers, Window sizes, TTL

## Slide 17: Wireless Stuff
Problems:
  Loss doesn’t necessarily mean congestion
  Handoff between cells affects
    ability to keep state in network
    intermittent connectivity
TCP congestion control affects performance
In order transfer (single hop wireless links) means duplicate acks are really useful.

## Slide 18: The Snoop Protocol
Link-layer protocol
TCP aware
Snoop agent
  software module
  at the base station
Suppresses duplicate ACKs
Retransmits lost packets

## Slide 19: SACKs and SMARTs
SACK
  range of acknowledged blocks
  more information passed
SMART
  it’s a sort of SACK
  which segment caused the acknowledgement
  less overhead

## Slide 20: Conclusions we already knew
Selective Acknowledgements (SACK)
  Deal better with loss
  Can be end-to-end
Split connections
  Isolate the sender from the lossy link
  Violate the protocol a bit.