## Slide 1: A Shape-based Image Retrieval System for Assisting Intervention Planning
Jill Lin
Biomedical and Health Informatics
Notes: Need to give a short blurb about
1) PLSA graphical representation
2) Spectral Clustering
3) Similarity Measure
4) Content-based image retrieval system

## Slide 2: Outline
Background
Related Work
Preliminary Studies / Progress Report
Research Design and Methods
Conclusion
Notes: The structure of my talk is as follows: …

## Slide 3: Background
Craniosynostosis is a serious condition of childhood, affecting 1 in 2500 individuals
It is caused by the early fusion of the sutures of skull which results in severe malformations in skull shapes
Skull abnormalities are frequently associated with impaired central nervous system functions due to intra-cranial pressure, hydrocephalus, and brain anomalies
Notes: Craniosynostosis is a serious and common pediatric disease, affecting 1 in 2500 children.
Normally, a child is born with open sutures, or fibrous skull joints, allowing for the expansion of the brains. However, in children with craniosynostosis, one or more of these sutures close prematurely which results in severe malformation in skull shapes. Depending on where the fusion is, skull shapes may be different.
Skull abnormalities are frequently associated with impaired central nervous system functions due to increased pressure and excess fluid inside the brain, and brain anomalies

## Slide 4: Background Cont.
Skull grows perpendicular to the fused suture resulting in different head shapes
Sagittal Synostosis
Metopic Synostosis
Normal
Sagittal suture fused
Metopic suture fused
Notes: Once the suture is fused, the skull grows perpendicularly to the fused suture resulting in different head shapes. Here showing are two types of craniosysnotosis. In sagittal synostosis, because the sagittal sutures are fused, skull grows perpendicularly to the suture resulting in an elongation of the skull. Metopic synostosis is characterized by the triangular head shape that is caused by the early fusion of the metopic suture.

## Slide 5: Background Cont.
Physicians and surgeons have been using similar cases in the past experience as “guidelines” in preparation and evaluation of the reconstruction of the skull
Similar cases are defined by similar shapes in case of craniosynostosis
This “case-based” clinical decision support technique produces a need to retrieve images of similar shapes in patients with craniosynostosis objectively and reproducibly
Notes: Even though no concrete evidence suggests whether or not surgical complications and neurobehavioral developments are directly affected by different skull shapes, radiologists and surgeons have long been using cases of similar shapes that were previously resolved as guidelines to prepare for pre-surgical planning and post-surgical evaluation. Both short-term and long-term outcomes from the treatment of the craniofacial malformations are also predicted based on previously established cases.
This “case-based” clinical decision support technique produces a need to retrieve similar images of shapes in patients with craniosynostosis objectively and reproducibly. It is then critical to design a shape-based image retrieval system to aid the radiologists and surgeons in the decision making analysis of the reconstruction of the skull.

## Slide 6: Problem 1
No image retrieval system currently exists for the surgeons and radiologists to retrieve cases of similar shapes
  “Retrieval” of cases with similar shapes are based on physicians and surgeons memories and experiences – subjective and not reproducible
Notes: However, no image retrieval system currently exists for the surgeons and radiologists to retrieve cases of similar shapes. “Retrieval” of cases with similar shapes are based on their memories and experiences. The identification of similarities and differences between shapes suffer from high interobserver variability and poor reproducibility.

## Slide 7: Problem 2
Unavailability of quantitative methods to describe skull shapes handicaps attempts to define craniofacial phenotypes
  Currently, the diagnosis of craniosynostosis and interpretation of these images are largely confined to radiologists’ subjective judgment
  Shape descriptions remain constrained to gross generalizations of the predominant form and are limited to traditional terms
  Hinders quantitative and objective methods to define and measure the similarities and differences between skull shapes
Notes: In addition, despite the recent advances in multi-detector CT technology and computer graphics techniques enable unprecedented accuracy in the detection of fused calvarial sutures and detailed rendering of consequent skull malformations, the current diagnosis of craniosynostosis and interpretation of these images are largely confined to radiologists’ subjective interpretation and judgement. This interpretation suffers again from poor reproducibility and high interoverserver variability.
Overall, shape descriptions remain constrained to gross generalizations of the predominant form and are limited to traditional terms. In addition, most imaging studies in patients with craniosynostosis emphasize the description of qualitative but not quantitative measure to compare patients with similar or different skull shapes to determine inter or intra-class differences.
This unavailability of quantitative methods to describe skull shapes handicaps attempts for objective image retrieval and disables further research on potential correlations bewteen shapes and neurocognitive development.

## Slide 8: Goal
Design an automatic shape-based image retrieval system to aid the process of retrieving cases of similar shapes that are treated by different surgeons and at different craniofacial centers for “case-based” clinical decision making.
Notes: Therefore, to advance the study of craniosynostosis and to improve the clinical care of these patients, the ultimate goal of my Ph.D. research proposal is to design an automatic shape-based image retrieval system to aid the process of retrieving cases of similar shapes that are treated by different surgeons and at different carniofacial cetners for “case-based” clinical decision making.

## Slide 9: Aims
Develop novel shape descriptors and efficient algorithms for quantification of skull shapes
Discover subsets of shapes that share similar geometric properties
Determine possible correlations between patients’ head skulls and neurocognitive development
Design a shape-based image retrieval system
Notes: In order to achieve the goal, we need to address several relevant engineering and informatics issues:
We need to develop novel shape descriptors and efficient algorithms to quantify and objectively detect the similarities and differences of skull shapes.
The ability to discover subsets of patients that share similar geometric aspects in skull shapes that are different from others will enable the identification of potential developmental differences between these subsets.
Given the shape information and neurocogntiive data, we want to determine possible correlations between patients’ head skulls and neurocognitive development. This step is critical in that it can be used to predict neurobehavioral data of children affected by single-suture synostoses in the future.
Finally, having our shape descriptors, ability to discover subsets of data, and neurobehavioral data, we can design a shape-based image retrieval system that incoporates the shape descriptors and neurobehavioral data for case-based reasoning and intervention planning.

## Slide 10: Related Work

## Slide 11: Scaphocephaly Severity Indices (SSI)
The ratio of head width to length, β/α, at the three bone slices, SSI-A, SSI-F, and SSI-M
Gold Standard Clinically
Notes: Several different shape descriptors have been developed for the study of craniosynostosis.
One of the simplest shape descriptor is taking the ratio of the width and the length, and we call it the scaphocephaly severity indices in our project. We take the ratio of the head width to length at the three planes discussed in the earlier slide.
This is a simple and easy to understand shape descriptor and thus is used pretty commonly clinically. However, the limitation of this shape descriptor is that it disregards the broad range of variations in shapes caused by frontal bossing, occipital bossing and central narrowing.

## Slide 12: Cranial Spectrum (CS)
Represent an outline as a periodic function
Decompose the periodic function using Fourier analysis
The outline is oriented: there is a direction associated with each outline (CCW direction)
Notes: Another type of traditional shape descriptor is called the cranial spectrum. Cranial spectrum first represent an outline as a periodic function. The outline in our case is oriented. In other words, there is a direction associated with each outline and this direction is a counterclockwise direction. The periodic function is then decomposed into a weighted sum of basis outlines using the Fourier analysis. The magnitudes of the coefficients of the weighted sum of the basis outlines become our shape descriptor. This is a one-to-one relationship between the magnitudes of coefficients and the oriented outline.

## Slide 13: Cranial Image (CI) – Single Plane
Matrix representation of pairwise normalized square distances for all the vertices of an outline
The matrix is defined up to a periodic shift along the main diagonal line because the outline is oriented
Sagittal
Metopic
Normal
Notes: The shape descriptor we propose in our project is called the cranial image. Cranial image in general is a matrix representation of pairwise normalized square distances for all the vertices of an outline. Each outline is first discretized into N evenly spaced vertices. The distances between each vertex to all the vertices of the outline is computed and normalized by the longest distance of the outline. The result is a large distance matrix. Because the outline is oriented, the matrix is defined up to a periodic shift along the main diagonal line.

## Slide 14: Cranial Image – Multiple Planes
Accomplished by computing inter and intra-oriented outline distances of a skull.
Superimposed
Notes: Cranial image can be exteneded to incoporate an arbitrary number of oriented outlines. Cranial images of multiple outlines can be accomplished by computing inter and intra-oriented outline distances of a skull.

## Slide 15: Cranial Image – Multiple Planes Cont.
The worst case computational complexity of the classification function is
O(ML3N3)
    L=3 is the number of planes and
    N=200 is the number of vertices per outline
    M=112 is number of elements in the training set
Notes: Even though both CS and CI are able to represent multiple layers of 2D cross-sections and can capture information of the entire contour, the computational complexity of either method is high. Specifically, the worst case computational complexity at the classification time is …
High computational complexity limits the practical use of CIs in applications where several outlines are required to represent a 3-D skull shape.

## Slide 16: Landmark-based Descriptor
Manual placement of landmarks – subjective and prone to variations
High cross-validation error rates (32-40% average for sagittal synostosis, and 18-27% average for metopic synostosis) – Lale and Richtsmier

## Slide 17: Symbolic Shape Descriptors - Motivation
High computational complexity
Limited generalizability
Lack of ability to detect intra-class differences
Notes: In our preliminary work, we developed a novel shape descriptor called the symbolic shape descriptor.
This development has been motivated by
High computational complexity
Limited in their generalizability
Detect intra-class differences

## Slide 18: Performance Test
Given a population of M skull shapes (training set) labeled as sagittal (1), metopic (2), and normal (3), predict with high accuracy the label of a new skull using our novel shape descriptors
Notes: Here is the performance test to evaluate our work.

## Slide 19: Data Acquisition
CT scan images from 60 sagittal patients, 13 metopic patients, and 40 normal subjects
3 manually selected planes based on brain landmarks
  A-plane: top of the lateral ventricle
  F-plane: Foramina of Munro
  M-plane: maximal dimension of the fourth ventricle
Skull Base Plane
Notes: Our data consists of CT scan images collected from 60 sagittal patients, 13 metopic patients and 40 normal subjects.
To standardize our measurements, we extracted the contours of the skull images based on internal anatomical landmarks. We first find the baseplane on the image and then we move this plane superiorly until we reach the 3 planes. A plane is the top of the lateral ventrical, F-plane is the Foramina of Munro, and the M-plane is the maximal dimension of the fourth ventricle. These three planes, individually and collectively, are used in our analysis and development of shape descriptors.

## Slide 20: Training Algorithm - Step 1: Forming BOW (1)
d11 d12 …. d1n
dn1 dn2 …. dnn
d21 d22 …. d2n
-------
Notes: The first step of the training algorithm in the symbolic shape descriptors is identical to that of CIs. Because CIs capture the information of the entire contour, we start our algorithm with the matrix from CI. We first discritize the contour into N evenly spaced vertices …

## Slide 21: Training Algorithm - Step 1: Forming BOW (2)
d11 d12 …. d1n
dn1 dn2 …. dnn
d21 d22 …. d2n
-------
K-means
Document S1 =
{‘CAA’ ‘AAB’ ‘ABB’
‘BBC’ ‘BCD’ ‘CDB’
‘DBC’ ‘BCA’}
C
A
A
B
B
C
D
B
Notes: We then cluster each distance vector for each vertex using k-means clustering metric. We assign each k-means cluster with a symbol such as A, B, C,.. Vertices that are grouped into a specific cluster will be assigned the same symbol as the cluster. We then construct our bag of words from these labeled vertices. For example… We do the same thing for all the subects in our training data and we then get a corpus of words or vocabulary.

## Slide 22: Training Algorithm - Step 2: Compute Co-occurrence Matrix
Compute the frequency of each word in our vocabulary occurring in each document of the training set.
Notes: We the construct our co-occurrence matrix by computing the frequency of each word (or a string of labels) in our vocabulary occuring in each document of the training set.
Even though it is evident/obvious that different classes of shape possess different composition and frequency of terms, the dimensionality of this specific representation is way too high. We cannot use this as our shape descriptors.

## Slide 23: Training Algorithm
Dimensionality reduction can be used to approximate the data and lower the complexity of the classification function
We utilize a model called Probabilistic Latent Semantic Analysis (Hofmann 2001) that is commonly used in document and text retrieval to reduce complexity
Notes: So we need to apply a dimensionality reduction method to approximate the data and lower the complexity of the classification function.
Since we have already converted the images into a bag of words or documents with words, we utilized a model called PLSA that is commonly used in document and text retrieval to reduce complexity.

## Slide 24: Training Algorithm - Step 3: Compute PLSA (1)
Introduces a latent variable, which in our case is the topic, to the words and documents
Each word in a document is a sample of a mixture model and is generated from a single topic
Each document thus is represented as a list of mixing proportions for these mixture models
Notes: PLSA is an aspect model used in text and document retrieval. In plain English, PLSA introduces a latent variable, which in our case a topic, to the documents and words. Each word in a document is a sample of a mixture model, where the mixture components are multinomial random variables that can be regarded as representation of topics. Thurs each word is generated from a single topic, and different words in a document can be generated from different topics. Each document thus is represented as a list of mixing proportions for these mixture components, and thereby reduced to a probability distribution on a fixed set of topics. Therefore, each skull, or the document, is not “described” by a set of probabilities given a fixed set of topics.

## Slide 25: Training Algorithm - Step 3: Compute PLSA (2)
Introduces a latent variable z
d
z
w
P(d)
P(z|d)
P(w|z)
Asymmetric parameterization
P(d,w) = ∑ P(z)P(d|z)P(w|z)
z
d = document (skull)
w = word
z = topic (related to shape)
Notes: Graphically, PLSA can be represented by…

## Slide 26: Training Algorithm - Step 3: Compute PLSA (3)
Uses Expectation-Maximization (EM) algorithm for the estimation of the latent variable model
Symbolic Shape Descriptors are
[P(Si|Z1), P(Si|Z2), … , P(Si|Zp)]

## Slide 27: Training Algorithm - Step 4: Model Selection
Use off-the-shelf Support Vector Machines (SVMs) as our classification tool
Use a radial basis function kernel
Use bootstrap and leave-one-out techniques for model selection
Notes: Now that we have the shape descriptors to represent different classes of shapes, we need a classification function to help us classify these classes. The classification tool that we used in our project is the off-the-shelf Support Vector Machines. SVM uses kernel function to map the input values to a feature space and separate different classes in the feature space by constructing hyperplanes. The kernel function that we use in our project is the radial basis function. We also use bootstrap and leave-one-out techniques for model selection or the selection of the parameters for the kernel function.

## Slide 28: Classification Algorithm - Step 1: Inputs
d11 d12 …. d1n
dn1 dn2 …. dnn
d21 d22 …. d2n
-------

## Slide 29: Classification Algorithm - Step 2: Compute BOW
Use the k-means cluster centers from training and a nearest neighbor rule to assign symbolic labels to the vertices
BOW representation {‘BDA’, ‘DAC’, ‘ACB’, … ‘DBD’}
Compute the co-occurrence matrix of all skulls to include all new words from Snew
D
A
C
B
C
A
D
B

## Slide 30: Classification Algorithm - Step 3: Compute PLSA
Apply PLSA to the new co-occurrence matrix and compute P(snew|z) for the test skull Snew to form the symbolic shape descriptor [P(snew|z1),…, P(snew|zp)]
Predict the label of Snew using the v-SVM classification function and the symbolic shape descriptors of Snew.

## Slide 31: Computational Complexity
Improved complexity at classification time:
O(P)
    P=15 is the number of latent variables in the PLSA model

## Slide 32: Co-Occurrence matrix

## Slide 33: Classification Results – Single Plane
Sagittal vs. metopic synostoses vs. normal skull shapes in the F-plane
 | S | M | N
S | 0.93 | 0.00 | 0.00
M | 0.00 | 0.85 | 0.51
N | 0.07 | 0.15 | 0.49
 | S | M | N
S | 1.00 | 0.00 | 0.07
M | 0.00 | 0.92 | 0.05
N | 0.00 | 0.08 | 0.88
 | S | M | N
S | 0.95 | 0.00 | 0.00
M | 0.00 | 0.92 | 0.00
N | 0.05 | 0.08 | 0.90
SSI
CI
SSD
Notes: Showing here are the confusion matrices using three different methods. Ideally, the values in diagonal lines would be 1.00. The classification performance of the sagittal and normal on the A-plane using the CI is comparable to earlier results. However, the classification performance of metopics is very low regardless of what methods we use.

## Slide 34: Classification Results – Multiple Planes
 | Sagittal | Metopic | Normal
Sagittal | 1.00 [0.99 1.00] | 0.00 [0.00 0.01] | 0.07 [0.05 0.09]
Metopic | 0.00 [0.00 0.01] | 1.00 [0.98 1.00] | 0.00 [0.00 0.02]
Normal | 0.00 [0.00 0.01] | 0.00 [0.00 0.06] | 0.93 [0.90 0.96]

## Slide 35: Subclasses Identification
Notes: In addition to the good classification result, we were also able to identify subsets of shapes in our preliminary results. For example, aspect 12 and aspect 14 are patients from sagittal population. However, patients in aspect 12 tend to have flatter tops than those in aspect 14. The importance of these subclasses will be discussed further later in the talk.