## Slide 1: Edge Detection
CSE P 576
Larry Zitnick (larryz@microsoft.com)

## Slide 2
What is an edge?
Cole et al. Siggraph 2008, results of 107 humans.

## Slide 3
Edges are caused by a variety of factors
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity
Origin of edges

## Slide 4
Illusory contours

## Slide 5
The gradient of an image:
The gradient points in the direction of most rapid change in intensity
Image gradient

## Slide 6
The gradient direction is given by:
  How does this relate to the direction of the edge?
The edge strength is given by the gradient magnitude
Image gradient
How would you implement this as a filter?

## Slide 7
Sobel operator
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
-1 | -2 | -1
0 | 0 | 0
1 | 2 | 1
Magnitude:
Orientation:
In practice, it is common to use:

## Slide 8
Sobel operator
Original
Orientation
Magnitude

## Slide 9: Effects of noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Where is the edge?

## Slide 10: Solution: smooth first
Where is the edge?
Look for peaks in

## Slide 11
Check if pixel is local maximum along gradient direction
  requires checking interpolated pixels p and r
Non-maximum suppression

## Slide 12: Effect of  (Gaussian kernel spread/size)
Canny with
Canny with
original
The choice of depends on desired behavior
  large detects large scale edges
  small detects fine features

## Slide 13: An edge is not a line...
How can we detect lines ?

## Slide 14: Finding lines in an image
Option 1:
  Search for the line at every possible position/orientation
  What is the cost of this operation?
Option 2:
  Use a voting scheme: Hough transform

## Slide 15: Finding lines in an image
Connection between image (x,y) and Hough (m,b) spaces
  A line in the image corresponds to a point in Hough space
  To go from image space to Hough space:
    given a set of points (x,y), find all (m,b) such that y = mx + b
x
y
m
b
m0
b0
image space
Hough space

## Slide 16: Finding lines in an image
Connection between image (x,y) and Hough (m,b) spaces
  A line in the image corresponds to a point in Hough space
  To go from image space to Hough space:
    given a set of points (x,y), find all (m,b) such that y = mx + b
  What does a point (x0, y0) in the image space map to?
x
y
m
b
image space
Hough space
    A: the solutions of b = -x0m + y0
    this is a line in Hough space
x0
y0

## Slide 17: Hough transform algorithm
Typically use a different parameterization
  d is the perpendicular distance from the line to the origin
   is the angle
  Why?

## Slide 18: Hough transform algorithm
Basic Hough transform algorithm
  Initialize H[d, ]=0
  for each edge point I[x,y] in the image
    for  = 0 to 180
      H[d, ] += 1
  Find the value(s) of (d, ) where H[d, ] is maximum
  The detected line in the image is given by
What’s the running time (measured in # votes)?

## Slide 19: Hough transform algorithm
http://www.cs.utah.edu/~vpegorar/courses/cs7966/
Notes: Sketch this parameterization on the board

## Slide 20: Hough transform algorithm
http://www.cs.utah.edu/~vpegorar/courses/cs7966/
Notes: Sketch this parameterization on the board

## Slide 21: Extensions
Extension 1: Use the image gradient
  same
  for each edge point I[x,y] in the image
    compute unique (d, ) based on image gradient at (x,y)
      H[d, ] += 1
  same
  same
What’s the running time measured in votes?
Extension 2
  give more votes for stronger edges
Extension 3
  change the sampling of (d, ) to give more/less resolution
Extension 4
  The same procedure can be used with circles, squares, or any other shape
Notes: Ask: what are the axes for a circle Hough space? What does a point in the image map to in the Hough space?