## Slide 1: Practical Aspects of Modern Cryptography
Josh Benaloh
Brian LaMacchia
Winter 2011

## Slide 2: Agenda
Guest lecture: Tolga Acar, Distributed Key Management and Cryptographic Agility
Hardware crypto tokens
  Smart cards
  TPMs (v1.2 & “.Next”) – tokens for PCs
Virtualization and virtualized crypto tokens

## Slide 3: Agenda
Guest lecture: Tolga Acar, Distributed Key Management and Cryptographic Agility
Hardware crypto tokens
  Smart cards
  TPMs (v1.2 & “.Next”) – tokens for PCs
Virtualization and virtualized crypto tokens

## Slide 4: Slide Acknowledgements
Some of these slides are based on slides created by the following folks at MS:
  Shon Eizenhoefer
  Paul England
  Himanshu Raj
  David Wootten

## Slide 5: Agenda
Guest lecture: Tolga Acar, Distributed Key Management and Cryptographic Agility
Hardware crypto tokens
  Smart cards
  TPMs (v1.2 & “.Next”) – tokens for PCs
Virtualization and virtualized crypto tokens

## Slide 6: What is a smart card?
Long history, invented in the 1970s
Integrated Circuit Cards - ICC
Initially used for pay phone systems in France
Most successful deployment: GSM cell phones
Payment: EMV – Europay, MasterCard and VISA
Strong User Authentication. Some examples:
  National eID programs in Asia and Europe
  DoD CAC cards
Notes: Eirik
Smart card is not just credit card sized. Can be badges, SIMs or even key fobs.

## Slide 7: Benefits of smart cards
Provides secure storage for private keys & data
  Tamper resistant
  Cryptographically secure
Provides two factor authentication
  Something you have – The Card
  Something you know – The PIN (Also referred to as Card Holder Verification- CHV)
Programmable cards
  Ex.: JavaCards, .NET Cards
Notes: Eirik

## Slide 9: Possible eID scenarios
Woodgrove Bank
Nicholas
Smartcard + Reader / PIN pad
Web Banking
Domain Logon
Dial Corp
Government eID Bank Smartcard …
Government Tax Agency
Abby
Email, IM, …
eID Issuance
Name Address Submit/sign form …

## Slide 10: Stages in a Smart Card’s Life Cycle
Initial Issuance
PIN unblock
Renewal
Retirement
Revocation
Forgotten Smart Card

## Slide 11: Agenda
Guest lecture: Tolga Acar, Distributed Key Management and Cryptographic Agility
Hardware crypto tokens
  Smart cards
  TPMs (v1.2 & “.Next”) – tokens for PCs
Virtualization and virtualized crypto tokens

## Slide 12: Recall DKM-TPM Motivation from Tolga’s talk:
Secret Protection Technology:
Approach sits between a pure HSM solution and a full software solution.
Expensive Moderate Inexpensive
Cost:
Very Secure More Secure Moderate (OS-Dependent)
Security:
Hard Easier Easy
Deployment:
HSM
Hardware Security Module
TPM-based
Crypto
Software Crypto
No Hardware

## Slide 13: What Is A Trusted Platform Module (TPM)?
Smartcard-like module on the motherboard
Protects secrets
Performs cryptographic functions
  RSA, SHA-1, RNG
Performs digital signature operations
Anchors chain of trust for keys and credentials
Protects itself against attacks
Holds Platform Measurements (hashes)
Can create, store and manage keys
  Provides a unique Endorsement Key (EK)
  Provides a unique Storage Root Key (SRK)
TPM 1.2 spec: www.trustedcomputinggroup.org

## Slide 14: TPM v1.2 Key Features
Platform measurements
  TPM can “measure” (hash w/ SHA-1) instruction sequences & store the results in “platform configuration registers” (PCRs)
Encryption
  TPM can encrypt arbitrary data using TPM keys (or keys protected by TPM keys)
Sealed Storage
  TPM can encrypt arbitrary data, using TPM keys (or keys protected by TPM keys) and under a set of PCR values
  Data can only be decrypted later under the same PCR configuration
Attestation (in a moment)

## Slide 15: Sealed Storage
Why is Sealed Storage useful?
Provides a mechanism for defending against boot-time attacks
Example: Full Volume Encryption (FVE)
  BitLocker™ Drive Encryption on Windows

## Slide 16: Information Protection Threats
Internal threats are just as prevalent as external threats
Intentional
Accidental
Targeted
Data intentionally compromised
Thief steals asset based on value of data
Loss due to carelessness
System disposal or repurposing without data wipe
System physically lost in transit
Insider access to unauthorized data
Offline attack on lost/stolen laptop
Theft of branch office server (high value and volume of data)
Theft of executive or government laptop
Direct attacks with specialized hardware

## Slide 17: Booting w/ TPM measurements

## Slide 18: Disk Layout And Key Storage
OS Volume Contains
Encrypted OS
Encrypted Page File
Encrypted Temp Files
Encrypted Data
Encrypted Hibernation File
Where’s the Encryption Key?
SRK (Storage Root Key) contained in TPM
SRK encrypts FVEK (Full Volume Encryption Key) protected by TPM/PIN/USB Storage Device
FVEK stored (encrypted by SRK) on hard drive in the OS Volume
System
OS Volume
System Volume Contains:
MBR, Boot manager, Boot Utilities
(Unencrypted, small)
3
2
FVEK
1
SRK

## Slide 19: Attestation
Sealed Storage lets a TPM encrypt data to a specific set (or subset) of PCR values
Attestation is an authentication technology
  But more than “simple signing”
Attestation allows a TPM to sign data and a set (or subset) of the current PCR values
  So the TPM “attests” to a certain software configuration (whatever was measured into those PCR registers) as part of its digital signature
  “Quoting”

## Slide 20: Key Recovery Scenarios
Lost/Forgotten Authentication Methods
  Lost USB key, user forgets PIN
Upgrade to Core Files
  Unanticipated change to pre-OS files (BIOS upgrade, etc…)
Broken Hardware
  Hard drive moved to a new system
Deliberate Attack
  Modified or missing pre-OS files (Hacked BIOS, MBR, etc…)

## Slide 21: TPM.Next
The TPM architecture after TPM v1.2
More than 3 years of specification development
Current work on TPM.Next is happening within the Trusted Computing Group (TCG) consortium
The actual TPM.Next specification is currently confidential
  The only publicly available information is not very technical
I can talk about things that Microsoft has submitted to the TCG
  But this may or may not show up in TPM.Next

## Slide 22: Cryptographic Algorithm Agility
TPM 1.2 is based on RSA 2048-bit and SHA-1 with little variability possible.
SHA-1 is being phased out.
Support for new asymmetric algorithms (ECC) is needed in some important markets.
Requirements to be able to support localization.
Can’t react quickly to a broken algorithm.

## Slide 23: Potential Solutions
Every use of a cryptographic algorithm should allow the TPM user to specify the algorithm to be used.
    Much wider range of algorithm options while maintaining interface compatibility
Every data structure should be tagged to indicate the algorithms used to construct it.
    No assumptions required or allowed.
Define sets of algorithms for interoperability.
    Set is a combination of asymmetric, symmetric, and hash algorithms.
Allow multiple sets to be used simultaneously.
    Support different security and localization needs.
  Make it easy to replace broken algorithms without having to develop an entirely new specification or product.

## Slide 24: TPM Management
User has a difficult time understanding the TPM controls.
    What is the difference between TPM enable and activate?
Security and privacy functions use the same controls.
    Need to take ownership of TPM to use the Storage Root Key but that also enables Endorsement Key operations which are privacy sensitive.
PCR sealing model is brittle.
    Makes it difficult to manage keys that rely on PCR values.
    System updates that change a PCR measurement can be very disruptive.

## Slide 25: PCR “Brittleness”
Many configuration changes leading to PCR changes are benign
  But still result in keys becoming unusable, etc.
Sometimes if you plan ahead you can prevent this
  E.g. seal to a future known good configuration
Sometimes we can fix this with smarter external software
  E.g. extend hashes of authorized signing keys and check certificates
But it’s caused enough problems that TPM support makes sense

## Slide 26: Potential Solutions
Change to simpler model for control – on/off
Should split controls.
    Security functions based on Storage Root Key – default on
    Identity/privacy functions based on Endorsement Key – default off
    Provisioning functions based on BIOS controls – always on
Allow a recognized authority to approve different PCR settings.
    An authority over the PCR environment in which the key may be used much like migration authority controls the hierarchy in which a key may be used.

## Slide 27: Ecosystem Issues
TPM/TCM are not interchangeable.
    No BIOS level abstraction for a security token (TPM/TCM) as there is for a disk (read/write logical blocks).
    Makes it hard to adopt boot code for alternative algorithms.
Trusted computing crosses national boundaries.
    Neither the TPM nor the TCM has the ability to meet both local and international cryptographic requirements at the same time.
  The sunset of SHA1 has demonstrated the importance of not being tied to a fixed set of algorithms.
    It will be a major upset to the ecosystem (chip, system, software) to switch to a new TPM with a new software interface.
Changing the TPM algorithms is going to cause a major upheaval in the ecosystem.

## Slide 28: Potential Solutions
TPM.next should have an interface that is not tied to a specific set of algorithms.
    Boot code can use the BIOS interface without being aware of the underlying cryptographic algorithms.
    Makes for a better abstraction.
TPM.next should allow multiple sets of algorithms to co-exist at the same time on the same TPM.
    Give the ability simultaneously to support both local and international standards.
TPM.next should allow new algorithms to be introduced as needed without having to re-specify the interface.
    Avoid future upset of the ecosystem when an algorithm is broken or better algorithms are needed.

## Slide 29: Summary
TPM.next tries to keep the best ideas of the TPM and incorporate the best ideas from the TCM.
TPM.next tries to improve the sub-optimal parts of the TPM and TCM especially with respect to algorithm flexibility.
TPM.next is intended to be an international standard that can address local requirements while maintaining software compatibility over a broad range of applications.
Please join with TCG to create a TPM.next design which will satisfy both China-market and international requirements through a single unified world-wide standard.

## Slide 30: Agenda
Guest lecture: Tolga Acar, Distributed Key Management and Cryptographic Agility
Hardware crypto tokens
  Smart cards
  TPMs (v1.2 & “.Next”) – tokens for PCs
Virtualization and virtualized crypto tokens

## Slide 31: Virtualization
Sharing a single physical platform among multiple virtual machines (VMs) with complete isolation among VMs
Benefits
  Consolidation of workloads, Fault tolerance, Extensibility, Ease of Management, Better security

## Slide 32: Virtualization
With increasing h/w support, performance degradation is becoming minimal
With multi-core, we can envision pervasive adoption
  Solutions available for server, client, and mobile platforms
  E.g., virtualized data centers (EC2, Azure)
  And, Dilbert running his office VM on home computer

## Slide 33: Virtual TPM
Challenge: physical TPM itself is hard to virtualize
  By design, TPM resists virtualization
TPM emulation
  Complete s/w emulation, TCG interface: vTPM [Berger06]
Para-virtualized TPM sharing [England08]
  Hypercall interface with Hv as mediator

## Slide 34: vTPM
VMM
TPM
Service VM
vTPM
Guest 0
Guest 1
vTPM

## Slide 35: vTPM
Pros
  Standard TCG interface
  High fidelity: full legacy support
  Vendors can add VM use-cases
    Migration, suspend/resume, rollback
Cons
  Low resistance to physical attack
  Reduced resistance to software attack
    Hypervisor is more complex and exposed than TPM embedded OS
  Trust model for TPM is complex
    Hypervisor security model influences vTPM security
VMM
TPM
Service VM
vTPM
Guest 0

## Slide 36: vTPM
Each vTPM has its independent key hierarchy
  EK, SRK, AIKs …
  May take extra precaution while storing these in memory
    Wrapped with physical TPM’s SRK?
  Attestation using vTPM
    In a manner similar to physical TPM
    E.g., a signed statement using an AIK that is linked to vTPM’s EK

## Slide 37: Para-Virtualized TPM Sharing
VMM
TPM
Guest 0
Guest 1
TPM Access Mediation
Guest 0 state
Guest 1 state

## Slide 38: Para-Virtualized TPM Sharing
Roll of Access Mediation Layer
  Schedule access to TPM
  Authenticate guests to TPM
    Store guest measurement in resettable PCR
  Protect Hv from guests and guests from each other
Designed as minimal SW-stack for TPM sharing
Minimal or no application changes
Important Observation
TPM
OS
App 1
App 2
TPM
Hypervisor
OS 1
OS 2
≈
VMM
TPM
Guest 0
Guest 1
TPM Access Mediation

## Slide 39: Para-Virtualized TPM
Pros
  Simple
  Hardware protection for asymetric keys
Cons
  Requires software changes, at least at the library level
    Hypercall based interface
    Meaning of seal/unseal/quote
      Which physical PCRs are mixed?
      Ordering of vPCRs
      Actual operation against PCR 15
  We can only provide a “virtualization-friendly” subset of the TPM
    similar to OS-friendly subset
VMM
TPM
Guest 0
Guest 1
TPM Access Mediation

## Slide 40: Para-Virtualized TPM - Examples
TPM
RNG
Hypervisor
TPM Multiplexing
Guest 0
Guest 1
RNG
TPM
Hypervisor
TPM Partitioning
Guest 0
Guest 1
NV Storage

## Slide 41: Para-Virtualized TPM - Attestation
HvQuote(TCB, nonce)
TPM
PCR0
PCR1
…
Resettable PCR
VPCR0
VPCR1
Guest 0
Guest 1
VPCR0
VPCR1
VPCR1
PcrReset(15)
PcrExtend(15,VPCR1)
Quote((0,15), nonce)

## Slide 42: Para-Virtualized TPM
TVP binds a VM to a physical platform
Must re-establish the key hierarchy after migration
  Need to signal VM about migration
  Is this a good thing?

## Slide 43: Backup