## Slide 1: Information Access and Communication Networks in the Developing-world
Umar Saif
LUMS, Pakistan
umar@lums.edu.pk | umar@mit.edu
Notes: <number>

## Slide 2: Overview
Poor Man’s Broadband
  Poor Man’s Cache
  Packet Containment
TEK Internet Search
Inverse Multiplexing of Cellular Connections
Teleputer (Time permitting)

## Slide 3: Motivation
Average End-user Bandwidth via ISP
< 10 kb/sec
Average End-user Bandwidth via ISP
> 100 kb/sec
Bulk Data Transfer on the Internet
< 15%
Bulk Data Transfer on the Internet
> 70%
2 MB Internet Connection
> $4000
2 MB Internet Connection
< $40
Developed World
Developing World
Digital Divide
Notes: <number>

## Slide 4: Internet in Pakistan
Facts of life in the developing world
  Expensive International Bandwidth
  No real peering points
  Internet used over dialup
    Poor “Scratch card” provisioning
Notes: <number>

## Slide 5: Internet in Pakistan
Average Dialup Bandwidth
  Less than 10 kb/sec
Almost Never Used for
  Exchanging
  Disseminating
  Accessing
  …. Content larger than a couple of hundred kilobyes
Notes: <number>

## Slide 6: How I Stumbled Upon this?
“Good research solves real problems in a practical way”
  Started last year when I wanted to exchange a 3.5 MB PDF file with my dad
  Two laptops sitting next to each other
  No way to exchange data if you don’t have portable storage!
    We actually went our and bought a CDR to exchange data….
Notes: <number>

## Slide 7: Problem
Internet
<10kb/sec
~ 56kb/sec
Not a Last Mile Problem
Notes: <number>

## Slide 8: Solution
~ 56kb/sec
Bypass the Internet when exchanging large
Internet
Notes: <number>

## Slide 9: Email Attachments
Time to exchange a 3.5 MB file on the Internet ~ 1 hours (16 Kb/sec)
  30 mins upload and download
  Assuming no disconnections
Time now (40 kb/sec)
  12 mins!!
Notes: <number>

## Slide 10: Disruptive Technology
Of course Internet also started as an overlay over the phone lines
A new kind of Internet
Reminiscent of Pre-Internet days
  FidoNet
  UUCP
Notes: <number>

## Slide 11: Why is this Practical?
Phone bills are becoming “Flat”
  Rs 199/month -- free nation-wide calls
But cannot always connect to the server
As long as one can identify a “close-by” host, “broadband access” is free
P2P systems already follow a similar model
  Incentive-based BitTorrent
Notes: <number>

## Slide 12: Dialup P2P-ISP Interleaving
Peer-to-peer dialup connections
Line-speed (~40kb/s) dialup connections
Internet
Dialup Underlay
Key Idea: Use Internet as a directory service, not as digital pipe
Interleaving of ISP-P2P dialup connections
Notes: <number>

## Slide 13: Dialup BitTorent
BitTorrent in a sequential mode
Notes: <number>

## Slide 14: Other Challenges
Overhead of Peer connections: ~30 sec
Offline Block Discovery
Last Block Problem
Flash Crowds (Backoff for congestion control)
Budget-based Download
Notes: <number>

## Slide 15: Peer Connection Overhead
Notes: <number>

## Slide 16: Offline Block Discovery
2
3
7
9
1
3
6
8
6
A
B
1
3
6
8
2
3
7
9
A
B
Virally Spread Knowledge of File Blocks
Notes: <number>

## Slide 17: Offline Block Discovery
Notes: <number>

## Slide 18: Last Block Problem
Grab rare blocks first
Favor those who will finish at the end of the connection
Notes: <number>

## Slide 19: Flash crowds
Each busy-tone costs ~10 secs
Wait between calls (nominal)
Back-off in times of congestion (busy tones)
Notes: <number>

## Slide 20: Budget-based Download
Notes: <number>

## Slide 21: Three Evolving Applications
P2P file-sharing
Web-browsing
Large Email attachments
http://dittorrent.sourceforge.net
Notes: <number>

## Slide 22: Can we do the same on the “Internet”
Contain packets within the developing-world
  Routing paths are screwed up
    “All roads lead to Rome” i.e. transit out of the country
Low cache hit-rates
  Too many small ISPs, no sharing of cached content
  Misconfigured “Proxies”
  Hit rates < 30% (instead of >60%)
Poor DNS support

## Slide 23: Work-in-progress
Indirect Routing
  Force routing paths by vectoring messages through intermediate nodes
  Initial results show improvement across all traffic metrics
An ISP-independent distributed cache
  Similar to CoralCDN
An ISP-independent DNS

## Slide 24: ChoupalLink
Inverse Multiplexing over cellular connections
High-bandwidth Virtual Channel
Inverse multiplexing over GSM/GPRS/
Notes: <number>

## Slide 25: TEK: Time Equals Knowledge
Web Search for Low-bandwidth, intermittently connected users
One of the first examples of mainstream ICTD research ~circa 2000
Renewed interest with DTNs coming in vogue

## Slide 26: TEK
Internet in the developing-world
  Expensive
  Intermittent
An Email-based Internet Search Facility
  Asynchronous Dialup model
  Search optimized for bandwidth and latency rather than speed
  Heavy client-side caching

## Slide 27: TEK

## Slide 28: TEK Server
Remove Duplicate Content
Cluster results
Distinguish Content from links
Remove images
Remove background code
Compress results

## Slide 29: Rationale
Lower operational costs
  Caching vs internet download
  ISP-host connection
    Reliable
    Higher Bandwdith
    Cheaper: email-only account
  Better utilization of Internet Connection

## Slide 30: Our Teleputer
Notes: <number>

## Slide 31: Multi-user devices
Notes: <number>

## Slide 32: Teleputer
Zero-configuration
Text-free Interface
Sensor-actuator
Cell-phone integrated
Shared Computing
Server-style processing
Notes: <number>

## Slide 33: Teleputer Sensors
Notes: <number>

## Slide 34: Teleputer Operation
Notes: <number>

## Slide 35
    Thank you!
    umar@lums.edu.pk
    http://www.dritte.org
Notes: <number>