## Slide 1: Transmission Control Protocol (TCP)
Reliable bi-directional byte stream
Connection-oriented
Flow control
  prevent sender from overrunning receiver buffers
Highly tuned congestion control algorithm
  Sliding window, go back N/SACK, RTT est, …

## Slide 2: Outline
Reliability
  Retransmissions
  Sequence numbers
  Timeouts/RTTs
Connections
Sliding Window
  Multiple in-flight messages
  Flow control
Congestion Control

## Slide 3: Reliable Transmission
How do we send packets reliably?
Two mechanisms
  Acknowledgements
  Timeouts
Simplest reliable protocol: Stop and Wait

## Slide 4: Reliability: Stop and Wait
Time
Packet
ACK
Timeout
Send a packet, wait until ack arrives
  retransmit if no ack within timeout
Receiver acks each packet as it arrives
Sender
Receiver

## Slide 5: Reliability: Recovering from error
Packet
ACK
Timeout
Packet
ACK
Timeout
Time
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
Early timeout
Packet
Timeout
Packet
ACK
Timeout
Packet lost
Packet
Next Packet
ACK
Success
ACK
Use a unique sequence number to recognize resends!
Notes: What’s wrong here
Success and ACK lost is indistinguishable. Deliver twice
Cant recognize resends!

## Slide 6: Reliability: What happens on reboot?
How do we distinguish packets sent before and after reboot?
Solutions?
  Restart sequence # at 0?
  Remember last sequence number?
  Include epoch number in packet (stored on disk)?
  Ask other side what the last sequence # was?
  TCP sidesteps this problem with random initial seq # (in each direction)

## Slide 7: Reliability: Handling resends
Use unique ID for each pkt
  for both packets and acks
Start from a random initial sequence number
Pkt 0
ACK 0
Pkt 0
ACK 1
Pkt 1
ACK 0
Timeout

## Slide 8: Reliability: How do we determine timeouts?
If timeout too small, useless retransmits
  can lead to congestion collapse (and did in 86)
  as load increases, longer delays, more timeouts, more retransmissions, more load, longer delays, more timeouts …
  Dynamic instability!
If timeout too big, inefficient
  wait too long to send missing packet
Timeout should be based on actual round trip time (RTT)
  varies with destination subnet, routing changes, congestion, …

## Slide 9: Reliability: Estimating RTTs
Idea: Adapt based on recent past measurements
  For each packet, note time sent and time ack received
  Compute RTT samples and average recent samples for timeout
  EstimatedRTT = 0.9*EstimatedRTT + 0.1*SampleRTT
  This is an exponentially-weighted moving average (low pass filter) that smoothes the samples.
  Set timeout to small multiple (2) of the estimate

## Slide 10: Reliability: Estimated Retransmit Timer

## Slide 11: Reliability: What about retransmissions?
How do we distinguish first ack from retransmitted ack?
  First send to first ack?
    What if ack dropped?
  Last send to last ack?
    What if last ack dropped?
Might never be able to fix too short a timeout!
Timeout!

## Slide 12: Reliability: Retransmission ambiguity
TCP: Karn-Partridge
  ignore RTT estimates for retransmitted pkts
  double timeout on every retransmission
Add sequence #’s to retransmissions (retry #1, retry #2, …)
Modern TCP (RFC 1323): Add timestamp into packet header; ack returns timestamp

## Slide 13: Reliability: Jacobson/Karels Algorithm
Problem:
  Variance in RTTs gets large as network gets loaded
  Average RTT isn’t a good predictor when we need it most
Solution: Track variance too.
  Difference = SampleRTT – EstimatedRTT
  EstimatedRTT = EstimatedRTT + ( x Difference)
  Deviation = Deviation + (|Difference|- Deviation)
  Timeout =  x EstimatedRTT +  x Deviation
  In practice,  = 1/8,  = 1 and  = 4

## Slide 14: Reliability: Estimate with Mean + Variance

## Slide 15: Outline
Time
Packet
ACK
Timeout
Sender
Receiver
What’s next:
Example: BW = 1Mbps RTT = 100ms  10pks/sec
  10Mbps?
Let’s send send multiple packets without waiting for first to be acked
What we have:

## Slide 16: Outline
Reliability
  Retransmissions
  Sequence numbers
  Timeouts/RTTs
Connections
Sliding Window
  Multiple in-flight messages
  Flow control
Congestion Control

## Slide 17: Connections: What are they good for?
Allows both sides to
  allocate state for buffer size, state variables, …
  calculate estimated RTT, estimated MTU, etc.
Helps prevent
  Duplicates across incarnations
  Intentional hijacking
    random nonces => weak form of authentication

## Slide 18
Opens both directions for transfer
Active participant
(client)
Passive participant
(server)
SYN, SequenceNum =
x
SYN + ACK, SequenceNum =
y
,
ACK, Acknowledgment =
y
+
1
Acknowledgment =
x
+
1
+data
Connections: Three-Way Handshake
Notes: Syns are retransmitted if lost

## Slide 19: Connections: State Transitions
CLOSED
LISTEN
SYN_RCVD
SYN_SENT
ESTABLISHED
CLOSE_WAIT
LAST_ACK
CLOSING
TIME_WAIT
FIN_WAIT_2
FIN_WAIT_1
Passive open
Close
Send/
SYN
SYN/SYN + ACK
SYN + ACK/ACK
SYN/SYN + ACK
ACK
Close
/FIN
FIN/ACK
Close
/FIN
FIN/ACK
Timeout after two
segment lifetimes
FIN/ACK
ACK
ACK
ACK
Close
/FIN
Close
CLOSED
Active open
/SYN
Notation: send/receive
Notes: Trace syn->syn ack->ack
What happens when both initiate at the same time

## Slide 20: Connections: Teardown
Symmetric: either side can close connection (or RST!)
Web server
Web browser
FIN
ACK
data, ACK
FIN
data, ACK
ACK
Half-open connection; data can be continue to be sent
Can reclaim connection right away (must be at least 1MSL after first FIN)
Can reclaim connection after 2 MSL
Notes: Draw the easier case

## Slide 21: Connections: Why wait for 2MSL?
We wait 2MSL (two times the maximum segment lifetime of 60 seconds) before completing the close
Why?
ACK might have been lost and so FIN will be resent
Could interfere with a subsequent connection

## Slide 22: Connections: TCP Handshake in an Uncooperative Internet
TCP SYN flood
  server maintains state for every open connection
  if attacker spoofs source addresses, can cause server to open lots of connections
  eventually, server runs out of memory
Malicious attacker
Server
SYN, SequenceNum =
x
SYN + ACK, y, x + 1
SYN, p
SYN, q
SYN, r
SYN, s

## Slide 23: Connections: TCP SYN cookies
Solution: SYN cookies
  Server keeps no state in response to SYN; instead makes client store state
  Server picks return seq # y = © that encrypts x
  Gets © +1 from sender; unpacks to yield x
Client
Server
SYN, SequenceNum =
x
SYN + ACK, ©, x + 1
ACK, © + 1

## Slide 24: Outline
Reliability
  Retransmissions
  Sequence numbers
  Timeouts/RTTs
Connections
Sliding Window
  Multiple in-flight messages
  Flow control
Congestion Control

## Slide 25: Stop and Wait is slow
Example: BW = 1Mbps, RTT = 100ms
 10pks/sec
What about 10Mbps?
Let’s send send multiple packets without waiting for first to be acked

## Slide 26: Sliding Window: Reliable, ordered delivery
Two constraints:
  Receiver can’t deliver packet to application until all prior packets have arrived
  Sender must prevent buffer overflow at receiver
Solution: sliding window
  Allows W packets to be outstanding
  Advance when sender and receiver agree packets at beginning have been received

## Slide 27: Sliding Window: Sender
Sender buffers up to W segments until they are acknowledged
  LFS=Last Frame Sent, LAR=Last Ack Received
  Sends while LFS – LAR <= W
Acked
Unacked
Unsent
LAR
LFS
W=5

## Slide 28: Sliding Window: Sender
Transport accepts another segment of data from the Application…
  Transport sends it (as LFS-LAR  5)
Acked
Unacked
Unsent
LAR
LFS
W=5

## Slide 29: Sliding Window: Sender
Next higher ACK arrives from peer…
  Window advances, buffer is freed
  LFS - LAR  4 (can send one more)
Acked
Unacked
Unsent
LAR
LFS
W=5

## Slide 30: Sliding Window: Cumulative Ack
Receiver keeps only a single packet buffer for the next segment
  State variable, LAS = Last Ack Sent
On receiver:
  If seq. number is LAS+1, accept and pass it to app, update LAS, send ACK
  Otherwise discard (as out of order)
Notes: Now let’s look at the receiver
I’ll present two approaches. First the one that TCP originally used, then the one it uses today.
…
The problems is that, if we only lose one packet, we spend a lot of time retransmitting everything else.

## Slide 31: Sliding Window: Selective Ack
Receiver passes data to app in order, and buffers out-of-order segments to reduce retransmissions
ACK conveys highest in-order segment, plus hints about out-of-order packets

## Slide 32: Sliding Window: Retransmissions
Cumulative Ack sender uses a single timer to detect losses
  On timeout, resends buffered packets starting at LAR+1
Selective Ack sender uses a timer per unacked packet to detect losses
  On timeout for packets, resend it
  Hope to resend fewer packets

## Slide 33: Sliding Window: Shortcut timeout
If packets usually arrive in order, out of order delivery is (probably) a packet loss
  TCP Fast retransmit
  if sender gets acks that don’t advance LAR, resends missing packet

## Slide 34: Sliding Window: Receiver
Consider receiver with W buffers
  LAS = Last Ack Sent
  App pulls in-order data from buffer with recv() call
Finished
Out of range
LAS
W=5

## Slide 35: Sliding Window: Receiver
Suppose the next two segments arrive, but app does not call recv()
Finished
Out of range
LAS
W=5

## Slide 36: Sliding Window: Receiver
Suppose the next two segments arrive, but app does not call recv()
  LAS rises, but we can’t slide window!
Finished
Out of range
LAS
W=5
Acked

## Slide 37: Sliding Window: Receiver
If further segments arrive (even in order) we can fill the buffer
  Must drop segments until app recvs!
Finished
Out of range
LAS
W=5
Acked
Notes: You may think, what if we didn’t raise LAS? No Ack => timeout
  if data is acked, sender will send more!
  If data is not acked, sender will retransmit!

## Slide 38: Sliding Window: Flow Control
Avoid loss at receiver by telling sender the available buffer space
  WIN=#Free, not W (from LAS)
  In TCP, WIN is measured in bytes
Finished
Out of range
LAS
WIN=3
Acked
Notes: W knows anyway
WIN measured from LAS
Communicated with ACKS

## Slide 39: Sliding Window: Flow Control
Sender uses the lower of the sliding window and flow control window (WIN) as the effective window size
Finished
Out of range
LAS
WIN=3
Acked

## Slide 40: Sliding Window: When to resume sending?
If receive window = 0, sender stops
  no data => no acks => no window updates
Sender periodically pings receiver with one byte packet
  receiver acks with current window size

## Slide 41: Sliding Window: Very slow senders/receivers
What happens when the sender/receiver can only handle a few bytes at a time?
  Silly window syndrome
    receive window opens a few bytes
    sender transmits little packet
    receive window closes
Solution (Clark, 1982): sender doesn’t resume sending until window is half open

## Slide 42: Outline
Reliability
  Retransmissions
  Sequence numbers
  Timeouts/RTTs
Connections
Sliding Window
  Multiple in-flight messages
  Flow control
Congestion Control
Notes: We now know how to send multiple….. Without overwhelming the receiver, but now we need to talk about how we send multiple messages without overwhelming the network.

## Slide 43: Importance of Congestion Control
TCP originally did not have congestion control
Congestion control dynamically varies the size of the window to match available bandwidth
  Sliding window uses minimum of cwnd, the congestion window, and the advertised flow control window
The big question: how do we decide what size the window should be?
Notes: Instead it used a fixed sliding window size that would mostly either underutilized the network or congest it.
This ended up being really bad
Goodput vs load
Increase in load results in a decrease in useful work done
We want to operate in a network right before congestion

## Slide 44: Bandwidth Allocation
Efficient:
  Most capacity used but there is no congestion
Fairness:
  different users should get their fair share of the bandwidth

## Slide 45: Efficiency
Buffer absorbs bursts when input rate > output
If sending rate is persistently > drain rate, queue builds
Dropped packets represent wasted work
Window size = round trip delay * bit rate
Destination
1.5-Mbps DSL link
Router
Source
1
100-Mbps Ethernet
Packets dropped here
50ms

## Slide 46: Fairness vs Efficiency
If we care about fairness:
  AB: ½, BC: ½, and AC: ½
  Total traffic carried is 1 ½
If we care about efficiency:
  AB: 1, BC:1, and AC: 0
  Total traffic rises to 2!
A
B
C
1
1

## Slide 47: Fairness
First, need to define what is a fair allocation.
  Consider n flows, each wants a fraction fi of the bandwidth
Max-min fairness:
  First satisfy all flows evenly up to the lowest fi.. Repeat with the remaining bandwidth.
f1
f2
f3
f4

## Slide 48: Tracking the Bottleneck Bandwidth
Additive increase
  Ack arrives => no drop => increase window size by one packet/window
    and therefore increase sending rate a little
Multiplicative decrease
  Timeout => dropped packet => cut window size in half
    and therefore cut sending rate in half

## Slide 49: TCP “Sawtooth”
Oscillates around bottleneck bandwidth
  adjusts to changes in competing traffic

## Slide 50: What if two TCPs share link?
Reach equilibrium independent of initial bw
  assuming equal RTTs, “fair” drops at the router

## Slide 51: Why AIMD?
Two users competing for bandwidth:
Consider the sequence of moves from AIMD, AIAD, MIMD, MIAD.

## Slide 52: What if TCP and UDP share link?
Independent of initial rates, UDP will get priority! TCP will take what’s left.

## Slide 53: Slow start
How do we find bottleneck bandwidth?
  Start by sending a single packet
    start slow to avoid overwhelming network
  Multiplicative increase until get packet loss
    quickly find bottleneck
  Remember previous max window size
    shift into linear increase/multiplicative decrease when get close to previous max ~ bottleneck rate
    called “congestion avoidance”

## Slide 54: Slow Start
Quickly find the bottleneck bandwidth

## Slide 55: Avoiding burstiness: ack pacing
Sender
Receiver
bottleneck
packets
acks
Window size = round trip delay * bit rate

## Slide 56: Putting It All Together
Timeouts dominate performance!

## Slide 57: Fast Retransmit
Can we detect packet loss without a timeout?
  Receiver will reply to each packet with an ack for last byte received in order
Duplicate acks imply either
  packet reordering (route change)
  packet loss
TCP Tahoe
  resend if sender gets three duplicate acks, without waiting for timeout
1
2
3
4
5
1
1
1
1
1
2
5

## Slide 58: Fast Retransmit Caveats
Assumes in order packet delivery
  Recent proposal: measure rate of out of order delivery; dynamically adjust number of dup acks needed for retransmit
Doesn’t work with small windows (e.g. modems)
  what if window size <= 3
Doesn’t work if many packets are lost
  example: at peak of slow start, might lose many packets

## Slide 59: Fast Retransmit
Chart: Slow Start + Congestion Avoidance + Fast Retransmit
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0
 | 1 | 2 | 4 | 8 | 16 | 1 | 2 | 4 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 1 | 2 | 4 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16

## Slide 60: Fast Recovery
When doing fast retransmit, don’t use slow start
Instead, go straight to congestion avoidance

## Slide 61: Fast Recovery
Chart: Slow Start + Congestion Avoidance + Fast Retransmit + Fast Recovery
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0
 | 1 | 2 | 4 | 8 | 16 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 8 | 9 | 10 | 11 | 12

## Slide 62: TCP: This is your life...
1975
1980
1985
1990
1982
TCP & IP
RFC 793 & 791
1974
TCP described by
Vint Cerf and Bob Kahn
In IEEE Trans Comm
1983
BSD Unix 4.2
supports TCP/IP
1984
Nagel’s algorithm
to reduce overhead
of small packets;
predicts congestion collapse
1987
Karn’s algorithm
to better estimate round-trip time
1986
Congestion collapse
observed
1988
Van Jacobson’s algorithms
congestion avoidance and congestion control
(most implemented in 4.3BSD Tahoe)
1990
4.3BSD Reno
fast retransmit
delayed ACK’s
1975
Three-way handshake
Raymond Tomlinson
In SIGCOMM 75

## Slide 63: TCP: After 1990
1993
1994
1996
1994
ECN
(Floyd)
Explicit
Congestion
Notification
1993
TCP Vegas
(Brakmo et al)
real congestion avoidance
1994
T/TCP
(Braden)
Transaction
TCP
1996
SACK TCP
(Floyd et al)
Selective Acknowledgement
1996
Hoe
Improving TCP startup
1996
FACK TCP
(Mathis et al)
extension to SACK
2006
SPDY

## Slide 64: Slow Start Problems
Bursty traffic source
  will fill up router queues, causing losses for other flows
  solution: ack pacing
Slow start usually overshoots bottleneck
  will lose many packets in window
  solution: remember previous threshold
Short flows
  Can spend entire time in slow start!
  solution: persistent connections?

## Slide 65: What if TCP connection is short?
Slow start dominates performance
  What if network is unloaded?
  Burstiness causes extra drops
Packet losses unreliable indicator
  can lose connection setup packet
  can get drop when connection near done
  signal unrelated to sending rate
In limit, have to signal every connection
  50% loss rate as increase # of connections