## Slide 1: Topic
We’ve talked about signals representing bits. How, exactly?
  This is the topic of modulation
…10110
10110…
Signal
Notes: Slides from CS 461

## Slide 2: A Simple Modulation
Let a high voltage (+V) represent a 1, and low voltage (-V) represent a 0
  This is called NRZ (Non-Return to Zero)
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0
+V
-V

## Slide 3: A Simple Modulation (2)
Let a high voltage (+V) represent a 1, and low voltage (-V) represent a 0
  This is called NRZ (Non-Return to Zero)
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0
+V
-V

## Slide 4: Modulation
NRZ signal of bits
Amplitude shift keying
Frequency shift keying
Phase shift keying
Notes: Figure derived from CN5E figures #2-23. Write “baseband” under NRZ.

## Slide 5: Topic
How rapidly can we send information over a link?
  Nyquist limit (~1924) »
  Shannon capacity (1948) »
Practical systems are devised to approach these limits

## Slide 6: Key Channel Properties
The bandwidth (B), signal strength (S), and noise strength (N)
  B limits the rate of transitions
  S and N limit how many signal levels we can distinguish
Bandwidth B
Signal S,
Noise N

## Slide 7: Nyquist Limit
The maximum symbol rate is 2B
Thus if there are V signal levels, ignoring noise, the maximum bit rate is:
R = 2B log2V bits/sec
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1

## Slide 8: Claude Shannon (1916-2001)
Father of information theory
  “A Mathematical Theory of Communication”, 1948
Fundamental contributions to digital computers, security, and communications
Credit: Courtesy MIT Museum
Electromechanical mouse that “solves” mazes!
Notes: Hi, This photo is negative number CES 7 in our collection. We allow free use of our images at 72dpi and under 730px/side for educational purposes, as long as proper credit is given; if the image below is suitable for your needs, please use it with the credit line "Courtesy MIT Museum". http://webmuseum.mit.edu/images/DIAmed/C/CES_7.jpg Additional photos of Claude Shannon in our collection may be viewed here: http://webmuseum.mit.edu/detail.php?t=people&type=all&f=&s=shannon&record=2 and more information on the maze being demonstrated in the photo is available here: http://museum.mit.edu/150/20 Please let me know if there's anything else I can do to help! Best regards, Ariel Weinberg Curatorial Associate, Science & Technology Collections MIT Museum, Building N52 265 Massachusetts Avenue Cambridge MA 02139-4307 tel: 617-253-3378 fax: 617-253-8994 http://web.mit.edu/museum On Jan 10, 2013, at 12:21 PM, Mary Anne Hansen wrote: > Hello Professor, > > The image in question does not belong to the News Office. > > By way of this email, I am forwarding your request to my colleague Ariel Weinberg, > Curatorial Associate at the MIT Museum who may be able to assist you. > > Best regards, > Mary Anne Hansen > Senior Administrative Assistant > MIT News Office, 11-400 > 617-253-8608 > > From: David Wetherall <djw@cs.washington.edu> > Date: Thursday, January 10, 2013 11:48 AM > To: "newsoffice@MIT.EDU" <newsoffice@MIT.EDU> > Subject: permissions request > > Hi, > > I am a professor teaching a massive free online course on Coursera (https://www.coursera.org/course/comnetworks). I came across your article on the Shannon limit: > > http://web.mit.edu/newsoffice/2010/explained-shannon-0115.html > > I'm asking for permission to reuse the photo in my videos and slides, which will be posted online. > > Please let me know how to proceed. > > Thank you, > > David

## Slide 9: Shannon Capacity
How many levels we can distinguish depends on S/N
  Or SNR, the Signal-to-Noise Ratio
  Note noise is random, hence some errors
SNR given on a log-scale in deciBels:
  SNRdB = 10log10(S/N)
0
1
2
3
N
S+N
Notes: Go over examples

## Slide 10: Shannon Capacity (2)
Shannon limit is for capacity (C), the maximum information carrying rate of the channel:
C = B log2(1 + S/N) bits/sec

## Slide 11: Wired/Wireless Perspective
Wires, and Fiber
  Engineer link to have requisite SNR and B
  Can fix data rate
Wireless
  Given B, but SNR varies greatly, e.g., up to 60 dB!
  Can’t design for worst case, must adapt data rate

## Slide 12: Wired/Wireless Perspective (2)
Wires, and Fiber
  Engineer link to have requisite SNR and B
  Can fix data rate
Wireless
  Given B, but SNR varies greatly, e.g., up to 60 dB!
  Can’t design for worst case, must adapt data rate
Engineer SNR for data rate
Adapt data rate to SNR

## Slide 13: Putting it all together – DSL
DSL (Digital Subscriber Line, see §2.6.3) is widely used for broadband; many variants offer 10s of Mbps
  Reuses twisted pair telephone line to the home; it has up to ~2 MHz of bandwidth but uses only the lowest ~4 kHz
Notes: Draw lines to home, say rate depends on dist/quality
Home from openclipart.org, building from cisco icon library.

## Slide 14: DSL (2)
DSL uses passband modulation (called OFDM §2.5.1)
  Separate bands for upstream and downstream (larger)
  Modulation varies both amplitude and phase (called QAM)
  High SNR, up to 15 bits/symbol, low SNR only 1 bit/symbol
Upstream
Downstream
26 – 138
kHz
0-4
kHz
143 kHz to 1.1 MHz
Telephone
Freq.
Voice
Up to 1 Mbps
Up to 12 Mbps
ADSL2:

## Slide 15: Topic
Multiplexing is the network word for the sharing of a resource
Classic scenario is sharing a link among different users
  Time Division Multiplexing (TDM) »
  Frequency Division Multiplexing (FDM) »

## Slide 16: Time Division Multiplexing (TDM)
Users take turns on a fixed schedule
2
2
2
2
Notes: CN5E slides #2-38

## Slide 17: Frequency Division Multiplexing (FDM)
Put different users on different frequency bands
Overall FDM channel
Notes: CN5E slides #2-36

## Slide 18: TDM versus FDM
In TDM a user sends at a high rate a fraction of the time; in FDM, a user sends at a low rate all the time
Rate
Time
FDM
TDM

## Slide 19: TDM versus FDM (2)
In TDM a user sends at a high rate a fraction of the time; in FDM, a user sends at a low rate all the time
Rate
Time
FDM
TDM

## Slide 20: TDM/FDM Usage
Statically divide a resource
  Suited for continuous traffic, fixed number of users
Widely used in telecommunications
  TV and radio stations (FDM)
  GSM (2G cellular) allocates calls using TDM within FDM

## Slide 21: Multiplexing Network Traffic
Network traffic is bursty
  ON/OFF sources
  Load varies greatly over time
Rate
Time
Rate
Time

## Slide 22: Multiplexing Network Traffic (2)
Network traffic is bursty
  Inefficient to always allocate user their ON needs with TDM/FDM
Rate
Time
Rate
Time
R
R

## Slide 23: Multiplexing Network Traffic (3)
Multiple access schemes multiplex users according to their demands – for gains of statistical multiplexing
Rate
Time
Rate
Time
Rate
Time
R
R
R’<2R
Two users, each need R
Together they need R’ < 2R

## Slide 24: Topic
How do nodes share a single link? Who sends when, e.g., in WiFI?
  Explore with a simple model
Assume no-one is in charge; this is a distributed system
Notes: Icon from Cisco icon library.

## Slide 25: Topic (2)
We will explore random multiple access control (MAC) protocols
  This is the basis for classic Ethernet
  Remember: data traffic is bursty
Zzzz..
Busy!
Ho hum
Notes: Icon from Cisco icon library.

## Slide 26: ALOHA Network
Seminal computer network connecting the Hawaiian islands in the late 1960s
  When should nodes send?
  A new protocol was devised by Norm Abramson …
Hawaii
Notes: Map from wikipedia commons, public domain. Radio from openclipart.org

## Slide 27: ALOHA Protocol
Simple idea:
  Node just sends when it has traffic.
  If there was a collision (no ACK received) then wait a random time and resend
That’s it!

## Slide 28: ALOHA Protocol (2)
Some frames will be lost, but many may get through…
Good idea?
Notes: From CN5E figures #4-2

## Slide 29: ALOHA Protocol (3)
Simple, decentralized protocol that works well under low load!
Not efficient under high load
  Analysis shows at most 18% efficiency
  Improvement: divide time into slots and efficiency goes up to 36%
We’ll look at other improvements

## Slide 30: Classic Ethernet
ALOHA inspired Bob Metcalfe to invent Ethernet for LANs in 1973
  Nodes share 10 Mbps coaxial cable
  Hugely popular in 1980s, 1990s
: © 2009 IEEE
Notes: Photo from IEEE GHN. Figure from CN5E slides #4-22

## Slide 31: CSMA (Carrier Sense Multiple Access)
Improve ALOHA by listening for activity before we send (Doh!)
  Can do easily with wires, not wireless
So does this eliminate collisions?
  Why or why not?

## Slide 32: CSMA (2)
Still possible to listen and hear nothing when another node is sending because of delay

## Slide 33: CSMA (3)
CSMA is a good defense against collisions only when BD is small
X

## Slide 34: CSMA/CD (with Collision Detection)
Can reduce the cost of collisions by detecting them and aborting (Jam) the rest of the frame time
  Again, we can do this with wires
X X X X X X X X
Jam!
Jam!

## Slide 35: CSMA/CD Complications
Want everyone who collides to know that it happened
  Time window in which a node may hear of a collision is 2D seconds
X

## Slide 36: CSMA/CD Complications (2)
Impose a minimum frame size that lasts for 2D seconds
  So node can’t finish before collision
  Ethernet minimum frame is 64 bytes
X

## Slide 37: CSMA “Persistence”
What should a node do if another node is sending?
Idea: Wait until it is done, and send
What now?

## Slide 38: CSMA “Persistence” (2)
Problem is that multiple waiting nodes will queue up then collide
  More load, more of a problem
Now!
Now!
Uh oh

## Slide 39: CSMA “Persistence” (3)
Intuition for a better solution
  If there are N queued senders, we want each to send next with probability 1/N
Send p=½
Whew
Send p=½

## Slide 40: Binary Exponential Backoff (BEB)
Cleverly estimates the probability
  1st collision, wait 0 or 1 frame times
  2nd collision, wait from 0 to 3 times
  3rd collision, wait from 0 to 7 times …
BEB doubles interval for each successive collision
  Quickly gets large enough to work
  Very efficient in practice

## Slide 41: Classic Ethernet, or IEEE 802.3
Most popular LAN of the 1980s, 1990s
  10 Mbps over shared coaxial cable, with baseband signals
  Multiple access with “1-persistent CSMA/CD with BEB”
Notes: Figure from CN5E slides #4-22

## Slide 42: Modern Ethernet
Based on switches, not multiple access, but still called Ethernet
  We’ll get to it in a later segment
Switch
Twisted pair
Switch ports
Notes: Figure from CN5E #4-27

## Slide 43: Topic
How do wireless nodes share a single link? (Yes, this is WiFi!)
  Build on our simple, wired model
Send?
Send?
Notes: Icon from Cisco icon library. AP from pixabay.

## Slide 44: Wireless Complications
Wireless is more complicated than the wired case (Surprise!)
  Nodes may have different areas of coverage – doesn’t fit Carrier Sense »
  Nodes can’t hear while sending – can’t Collision Detect »
≠ CSMA/CD
Notes: Icon from Cisco icon library. AP from pixabay.

## Slide 45: Different Coverage Areas
Wireless signal is broadcast and received nearby, where there is sufficient SNR
Notes: CN5E slides #4-18

## Slide 46: Hidden Terminals
Nodes A and C are hidden terminals when sending to B
  Can’t hear each other (to coordinate) yet collide at B
  We want to avoid the inefficiency of collisions
Notes: CN5E slides #4-18

## Slide 47: Exposed Terminals
B and C are exposed terminals when sending to A and D
  Can hear each other yet don’t collide at receivers A and D
  We want to send concurrently to increase performance
Notes: CN5E slides #4-18

## Slide 48: Nodes Can’t Hear While Sending
With wires, detecting collisions (and aborting) lowers their cost
More wasted time with wireless
Time
XXXXXXXXX
XXXXXXXXX
Wireless
Collision
Resend
X
X
Wired
Collision
Resend

## Slide 49: Possible Solution: MACA
MACA uses a short handshake instead of CSMA (Karn, 1990)
  802.11 uses a refinement of MACA (later)
Protocol rules:
  A sender node transmits a RTS (Request-To-Send, with frame length)
  The receiver replies with a CTS (Clear-To-Send, with frame length)
  Sender transmits the frame while nodes hearing the CTS stay silent
  Collisions on the RTS/CTS are still possible, but less likely

## Slide 50: MACA – Hidden Terminals
AB with hidden terminal C
  A sends RTS, to B
D
C
B
A
Notes: CN5E slides #4-18

## Slide 51: MACA – Hidden Terminals (2)
AB with hidden terminal C
  B sends CTS, to A, and C too
D
C
B
A
RTS
Notes: CN5E slides #4-18

## Slide 52: MACA – Hidden Terminals (3)
AB with hidden terminal C
  B sends CTS, to A, and C too
D
C
B
A
RTS
CTS
CTS
Alert!
Notes: CN5E slides #4-18

## Slide 53: MACA – Hidden Terminals (4)
AB with hidden terminal C
  A sends frame while C defers
Frame
Quiet...
Notes: CN5E slides #4-18

## Slide 54: MACA – Exposed Terminals
BA, CD as exposed terminals
  B and C send RTS to A and D
D
C
B
A
Notes: CN5E slides #4-18

## Slide 55: MACA – Exposed Terminals (2)
BA, CD as exposed terminals
  A and D send CTS to B and C
D
C
B
A
RTS
RTS
Notes: CN5E slides #4-18

## Slide 56: MACA – Exposed Terminals (3)
BA, CD as exposed terminals
  A and D send CTS to B and C
D
C
B
A
RTS
RTS
CTS
CTS
All OK
All OK
Notes: CN5E slides #4-18

## Slide 57: MACA – Exposed Terminals (4)
BA, CD as exposed terminals
  A and D send CTS to B and C
D
C
B
A
Frame
Frame
Notes: CN5E slides #4-18