## Slide 1
Routing Overview

## Slide 2: Routing versus Forwarding
Forwarding is the process of sending a packet on its way
Routing is the process of deciding in which direction to send traffic
Forward!
packet
Which way?
Which way?
Which way?

## Slide 3: Improving on the Spanning Tree
Spanning tree provides basic connectivity
  e.g., some path BC
Routing uses all links to find “best” paths
  e.g., use BC, BE, and CE
A
B
C
D
E
F
A
B
C
D
E
F
Unused

## Slide 4: Goals of Routing Algorithms
We want several properties of any routing scheme:
Property | Meaning
Correctness | Finds paths that work
Efficient paths | Uses network bandwidth well
Fair paths | Doesn’t starve any nodes
Fast convergence | Recovers quickly after changes
Scalability | Works well as network grows large

## Slide 5: Rules of Routing Algorithms
Decentralized, distributed setting
  All nodes are alike; no controller
  Nodes only know what they learn by exchanging messages with neighbors
  Nodes operate concurrently
  May be node/link/message failures
Who’s there?

## Slide 6: Delivery Models
Different routing used for different delivery models
Unicast
(§5.2)
Multicast
(§5.2.8)
Anycast
(§5.2.9)
Broadcast
(§5.2.7)

## Slide 7
Shortest Path Routing
(§5.2.1-5.2.2)

## Slide 8: Topic
Defining “best” paths with link costs
  These are shortest path routes
Best?
A
B
C
D
E
F
G
H
Notes: CN5E slides #5-10

## Slide 9: What are “Best” paths anyhow?
Many possibilities:
  Latency, avoid circuitous paths
  Bandwidth, avoid slow links
  Money, avoid expensive links
  Hops, to reduce switching
But only consider topology
  Ignore workload, e.g., hotspots
A
B
C
D
E
F
G
H
Notes: CN5E slides #5-10

## Slide 10: Shortest Paths
We’ll approximate “best” by a cost function that captures the factors
  Often call lowest “shortest”
Assign each link a cost (distance)
Define best path between each pair of nodes as the path that has the lowest total cost (or is shortest)
Pick randomly to any break ties

## Slide 11: Shortest Paths (2)
Find the shortest path A  E
All links are bidirectional, with equal costs in each direction
  Can extend model to unequal costs if needed
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Notes: CN5E slides #5-10

## Slide 12: Shortest Paths (3)
ABCE is a shortest path
dist(ABCE) = 4 + 2 + 1 = 7
This is less than:
  dist(ABE) = 8
  dist(ABFE) = 9
  dist(AE) = 10
  dist(ABCDE) = 10
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Notes: CN5E slides #5-10

## Slide 13: Shortest Paths (4)
Optimality property:
  Subpaths of shortest paths are also shortest paths
ABCE is a shortest path
  So are ABC, AB, BCE, BC, CE
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Notes: CN5E slides #5-10

## Slide 14: Sink Trees
Sink tree for a destination is the union of all shortest paths towards the destination
  Similarly source tree
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Notes: CN5E slides #5-10

## Slide 15: Sink Trees (2)
Implications:
  Only need to use destination to follow shortest paths
  Each node only need to send to the next hop
Forwarding table at a node
  Lists next hop for each destination
  Routing table may know more
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Notes: CN5E slides #5-10

## Slide 16: Dijkstra’s Algorithm
Algorithm:
Mark all nodes tentative, set distances from source to 0 (zero) for source, and ∞ (infinity) for all other nodes
While tentative nodes remain:
  Extract N, the one with lowest distance
  Add link to N to the shortest path tree
  Relax the distances of neighbors of N by lowering any better distance estimates

## Slide 17: Dijkstra’s Algorithm (2)
Initialization
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
∞
∞
∞
∞
∞
∞
We’ll compute shortest paths to/from A
∞

## Slide 18: Dijkstra’s Algorithm (3)
Relax around A
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
∞
∞
10
4
∞
∞
∞

## Slide 19: Dijkstra’s Algorithm (4)
Relax around B
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
∞
8
4
Distance fell!
6
7
7
∞

## Slide 20: Dijkstra’s Algorithm (5)
Relax around C
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
7
4
Distance fell
again!
6
7
7
8
9

## Slide 21: Dijkstra’s Algorithm (6)
Relax around G
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
7
4
Didn’t fall …
6
7
7
8
9

## Slide 22: Dijkstra’s Algorithm (7)
Relax around F
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
7
4
Relax has no effect
6
7
7
8
9

## Slide 23: Dijkstra’s Algorithm (8)
Relax around E
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
7
4
6
7
7
8
9

## Slide 24: Dijkstra’s Algorithm (9)
Relax around D
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
7
4
6
7
7
8
9

## Slide 25: Dijkstra’s Algorithm (10)
Finally, H …
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
0
7
4
6
7
7
8
9

## Slide 26: Dijkstra Comments
Dynamic programming algorithm; leverages optimality property
Runtime depends on efficiency of extracting min-cost node
Gives us complete information on the shortest paths to/from one node
  But requires complete topology

## Slide 27
Distance Vector Routing (§5.2.4)

## Slide 28: Topic
How to compute shortest paths in a distributed network
  The Distance Vector (DV) approach
Here’s my vector!
Here’s mine
Notes: CN5E slides #5-10

## Slide 29: Distance Vector Routing
Simple, early routing approach
  Used in ARPANET, and “RIP”
One of two main approaches to routing
  Distributed version of Bellman-Ford
  Works, but very slow convergence after some failures
Link-state algorithms are now typically used in practice
  More involved, better behavior

## Slide 30: Distance Vector Setting
Each node computes its forwarding table in a distributed setting:
Nodes know only the cost to their neighbors; not the topology
Nodes can talk only to their neighbors using messages
All nodes run the same algorithm concurrently
Nodes and links may fail, messages may be lost

## Slide 31: Distance Vector Algorithm
Each node maintains a vector of distances to all destinations
Initialize vector with 0 (zero) cost to self, ∞ (infinity) to other destinations
Periodically send vector to neighbors
Update vector for each destination by selecting the shortest distance heard, after adding cost of neighbor link
  Use the best neighbor for forwarding

## Slide 32: Distance Vector (2)
Consider from the point of view of node A
  Can only talk to nodes B and E
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
To | Cost
A | 0
B | ∞
C | ∞
D | ∞
E | ∞
F | ∞
G | ∞
H | ∞
Initial
vector

## Slide 33: Distance Vector (3)
First exchange with B, E; learn best 1-hop routes
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
A’s Cost | A’s Next
0 | --
4 | B
∞ | --
∞ | --
10 | E
∞ | --
∞ | --
∞ | --
To | B says | E says
A | ∞ | ∞
B | 0 | ∞
C | ∞ | ∞
D | ∞ | ∞
E | ∞ | 0
F | ∞ | ∞
G | ∞ | ∞
H | ∞ | ∞
B +4 | E +10
∞ | ∞
4 | ∞
∞ | ∞
∞ | ∞
∞ | 10
∞ | ∞
∞ | ∞
∞ | ∞
Learned better route

## Slide 34: Distance Vector (4)
Second exchange; learn best 2-hop routes
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
A’s Cost | A’s Next
0 | --
4 | B
6 | B
12 | E
8 | B
7 | B
7 | B
∞ | --
To | B says | E says
A | 4 | 10
B | 0 | 4
C | 2 | 1
D | ∞ | 2
E | 4 | 0
F | 3 | 2
G | 3 | ∞
H | ∞ | ∞
B +4 | E +10
8 | 20
4 | 14
6 | 11
∞ | 12
8 | 10
7 | 12
7 | ∞
∞ | ∞

## Slide 35: Distance Vector (4)
Third exchange; learn best 3-hop routes
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
A’s Cost | A’s Next
0 | --
4 | B
6 | B
8 | B
7 | B
7 | B
7 | B
9 | B
To | B says | E says
A | 4 | 8
B | 0 | 3
C | 2 | 1
D | 4 | 2
E | 3 | 0
F | 3 | 2
G | 3 | 6
H | 5 | 4
B +4 | E +10
8 | 18
4 | 13
6 | 11
8 | 12
7 | 10
7 | 12
7 | 16
9 | 14

## Slide 36: Distance Vector (5)
Subsequent exchanges; converged
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
A’s Cost | A’s Next
0 | --
4 | B
6 | B
8 | B
8 | B
7 | B
7 | B
9 | B
To | B says | E says
A | 4 | 7
B | 0 | 3
C | 2 | 1
D | 4 | 2
E | 3 | 0
F | 3 | 2
G | 3 | 6
H | 5 | 4
B +4 | E +10
8 | 17
4 | 13
6 | 11
8 | 12
7 | 10
7 | 12
7 | 16
9 | 14

## Slide 37: Distance Vector Dynamics
Adding routes:
  News travels one hop per exchange
Removing routes
  When a node fails, no more exchanges, other nodes forget
But partitions (unreachable nodes in divided network) are a problem
  “Count to infinity” scenario

## Slide 38: Dynamics (2)
Good news travels quickly, bad news slowly (inferred)
“Count to infinity” scenario
Desired convergence
X
Notes: CN5E #5-16

## Slide 39: Dynamics (3)
Various heuristics to address
  e.g.,“Split horizon, poison reverse” (Don’t send route back to where you learned it from.)
But none are very effective
  Link state now favored in practice
  Except when very resource-limited

## Slide 40
Link State Routing (§5.2.5)

## Slide 41: Topic
How to compute shortest paths in a distributed network
  The Link-State (LS) approach
Flood!
… then compute
Notes: CN5E slides #5-10

## Slide 42: Link-State Routing
One of two approaches to routing
  Trades more computation than distance vector for better dynamics
Widely used in practice
  Used in Internet/ARPANET from 1979
  Modern networks use OSPF and IS-IS

## Slide 43: Link-State Algorithm
Proceeds in two phases:
Nodes flood topology in the form of link state packets
  Each node learns full topology
Each node computes its own forwarding table
  By running Dijkstra (or equivalent)

## Slide 44: Topology Dissemination
Each node floods link state packet (LSP) that describes their portion of the topology
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Seq. # | 
A | 10
B | 4
C | 1
D | 2
F | 2
Node E’s LSP flooded to A, B, C, D, and F

## Slide 45: Route Computation
Each node has full topology
  By combining all LSPs
Each node simply runs Dijkstra
  Some replicated computation, but finds required routes directly
  Compile forwarding table from sink/source tree
  That’s it folks!

## Slide 46: Forwarding Table
To | Next
A | C
B | C
C | C
D | D
E | --
F | F
G | F
H | C
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
Source Tree for E (from Dijkstra)
E’s Forwarding Table

## Slide 47: Handling Changes
Nodes adjacent to failed link or node will notice
  Flood updated LSP with less connectivity
A
B
C
D
E
F
G
H
2
1
10
2
2
4
2
4
4
3
3
3
XXXX
Seq. # | 
A | 4
C | 2
E | 4
F | 3
G | 3
B’s LSP
Seq. # | 
B | 3
E | 2
G | 4
F’s LSP
Failure!

## Slide 48: Handling Changes (2)
Link failure
  Both nodes notice, send updated LSPs
  Link is removed from topology
Node failure
  All neighbors notice a link has failed
  Failed node can’t update its own LSP
  But it is OK: all links to node removed

## Slide 49: Handling Changes (3)
Addition of a link or node
  Add LSP of new node to topology
  Old LSPs are updated with new link
Additions are the easy case …

## Slide 50: DV/LS Comparison
Property | Distance Vector | Link-State
Correctness | Distributed Bellman-Ford | Replicated Dijkstra
Efficient paths | Approx. with shortest paths | Approx. with shortest paths
Fair paths | Approx. with shortest paths | Approx. with shortest paths
Fast convergence | Slow – many exchanges | Fast – flood and compute
Scalability | Excellent – storage/compute | Moderate – storage/compute

## Slide 51
Equal-Cost Multi-Path Routing
(§5.2.1)

## Slide 52: Topic
More on shortest path routes
  Allow multiple shortest paths
Use ABCE and
ABE from AE
A
B
C
D
E
F
G
H
Notes: CN5E slides #5-10

## Slide 53: Multipath Routing
Allow multiple routing paths from node to destination be used at once
  Topology has them for redundancy
  Using them can improve performance
Questions:
  How do we find multiple paths?
  How do we send traffic along them?

## Slide 54: Equal-Cost Multipath Routes
One form of multipath routing
Extends shortest path model
  Keep set if there are ties
Consider AE
  ABE = 4 + 4 = 8
  ABCE = 4 + 2 + 2 = 8
  ABCDE = 4 + 2 + 1 + 1 = 8
  Use them all!
A
B
C
D
E
F
G
H
2
2
10
1
1
4
2
4
4
3
3
3
Notes: CN5E slides #5-10

## Slide 55: Source “Trees”
With ECMP, source/sink “tree” is a directed acyclic graph (DAG)
  Each node has set of next hops
  Still a compact representation
Tree
DAG
Notes: CN5E slides #5-10

## Slide 56: Source “Trees” (2)
Find the source “tree” for E
  Procedure is Dijkstra, simply remember set of next hops
  Compile forwarding table similarly, may have set of next hops
Straightforward to extend DV too
  Just remember set of neighbors
A
B
C
D
E
F
G
H
2
2
10
1
1
4
2
4
4
3
3
3
Notes: CN5E slides #5-10

## Slide 57: Source “Trees” (3)
Source Tree for E
E’s Forwarding Table
A
B
C
D
E
F
G
H
2
2
10
1
1
4
2
4
4
3
3
3
Node | Next hops
A | B, C, D
B | B, C, D
C | C, D
D | D
E | --
F | F
G | F
H | C, D
New for
ECMP

## Slide 58: ECMP Forwarding
Could randomly pick a next hop for each packet based on destination
  Balances load, but adds jitter
Instead, try to send packets from a given source/destination pair on the same path
  Source/destination pair is called a flow
  Hash flow identifier to next hop
  No jitter within flow, but less balanced

## Slide 59: ECMP Forwarding (2)
A
B
C
D
E
F
G
H
2
2
10
1
1
4
2
4
4
3
3
3
Multipath routes from F to H
E’s Forwarding Choices
Flow | Possible next hops | Example choice
F  H | C, D | D
F  C | C, D | D
E  H | C, D | C
E  C | C, D | C
Use both paths to get
to one destination

## Slide 60: Recall
IP addresses are allocated in blocks called IP prefixes, e.g., 18.31.0.0/16
  Hosts on one network in same prefix
A “/N” prefix has the first N bits fixed and contains 232-N addresses
  E.g., a “/24” has 256 addresses
Routers keep track of prefix lengths
  Use it as part of longest prefix matching

## Slide 61: Recall (2)
IP addresses are allocated in blocks called IP prefixes, e.g., 18.31.0.0/16
  Hosts on one network in same prefix
A “/N” prefix has the first N bits fixed and contains 232-N addresses
  E.g., a “/24” has 256 addresses
Routers keep track of prefix lengths
  Use it as part of longest prefix matching
Routers can change prefix lengths without affecting hosts

## Slide 62: Prefixes and Hierarchy
IP prefixes already help to scale routing, but we can go further
  We can use a less specific (larger) IP prefix as a name for a region
I’m the whole region
Region
1
2
3
IP /16
IP1 /18
IP2 /18
IP3 /18

## Slide 63: Subnets and Aggregation
Subnets
  Internally split one large prefix into multiple smaller ones
Aggregation
  Externally join multiple smaller prefixes into one large prefix

## Slide 64: Subnets
Internally split up one IP prefix
32K addresses
One prefix sent to rest of Internet
16K
8K
4K
Company
Rest of Internet
Notes: CN5E #5-64

## Slide 65: Aggregation
Externally join multiple separate IP prefixes
One prefix sent to rest of Internet
\
ISP
Rest of Internet
Notes: CN5E slides #5-65

## Slide 66
Routing with Policy (BGP) (§5.6.7)

## Slide 67: Structure of the Internet
Networks (ISPs, CDNs, etc.) group hosts as IP prefixes
Networks are richly interconnected, often using IXPs
CDN C
Prefix C1
ISP A
Prefix A1
Prefix A2
Net F
Prefix F1
IXP
IXP
IXP
IXP
CDN D
Prefix D1
Net E
Prefix E1
Prefix E2
ISP B
Prefix B1

## Slide 68: Internet-wide Routing Issues
Two problems beyond routing within an individual network
Scaling to very large networks
  Techniques of IP prefixes, hierarchy, prefix aggregation
Incorporating policy decisions
  Letting different parties choose their routes to suit their own needs
Yikes!

## Slide 69: Effects of Independent Parties
Each party selects routes to suit its own interests
  e.g, shortest path in ISP
What path will be chosen for A2B1 and B1A2?
  What is the best path?
Prefix B2
Prefix A1
ISP A
ISP B
Prefix B1
Prefix A2

## Slide 70: Effects of Independent Parties (2)
Selected paths are longer than overall shortest path
  And asymmetric too!
This is a consequence of independent goals and decisions, not hierarchy
Prefix B2
Prefix A1
ISP A
ISP B
Prefix B1
Prefix A2

## Slide 71: Routing Policies
Capture the goals of different parties – could be anything
  E.g., Internet2 only carries non-commercial traffic
Common policies we’ll look at:
  ISPs give transit service to customers
  ISPs give peer service to each other

## Slide 72: Routing Policies – Transit
One party (customer) gets transit service from another party (ISP)
  ISP accepts traffic for customer from the rest of Internet
  ISP sends traffic from customer to the rest of Internet
  Customer pays ISP for the privilege
Customer 1
ISP
Customer 2
Rest of
Internet
Non-
customer

## Slide 73: Routing Policies – Peer
Both party (ISPs in example) get peer service from each other
  Each ISP accepts traffic from the other ISP only for their customers
  ISPs do not carry traffic to the rest of the Internet for each other
  ISPs don’t pay each other
Customer A1
ISP A
Customer A2
Customer B1
ISP B
Customer B2

## Slide 74: Routing with BGP (Border Gateway Protocol)
BGP is the interdomain routing protocol used in the Internet
  Path vector, a kind of distance vector
ISP A
Prefix A1
Prefix A2
Net F
Prefix F1
IXP
ISP B
Prefix B1
Prefix F1 via ISP B, Net F at IXP

## Slide 75: Routing with BGP (2)
Different parties like ISPs are called AS (Autonomous Systems)
Border routers of ASes announce BGP routes to each other
Route announcements contain an IP prefix, path vector, next hop
  Path vector is list of ASes on the way to the prefix; list is to find loops
Route announcements move in the opposite direction to traffic

## Slide 76: Routing with BGP (3)
Prefix
Notes: CN5E slides #5-82

## Slide 77: Routing with BGP (4)
Policy is implemented in two ways:
Border routers of ISP announce paths only to other parties who may use those paths
  Filter out paths others can’t use
Border routers of ISP select the best path of the ones they hear in any, non-shortest way

## Slide 78: Routing with BGP (5)
transit: AS1 says [B, (AS1, AS3)], [C, (AS1, AS4)] to AS2
Notes: CN5E slides #5-81

## Slide 79: Routing with BGP (6)
customer (other side of transit): AS2 says [A, (AS2)] to AS1
Notes: CN5E slides #5-81

## Slide 80: Routing with BGP (7)
peer: AS2 says [A, (AS2)] to AS3, AS3 says [B, (AS3)] to AS2
Notes: CN5E slides #5-81

## Slide 81: Routing with BGP (8)
AS2 hears two routes to B (via AS1, AS3) and chooses AS3 (Free!)
Notes: CN5E slides #5-81

## Slide 82: BGP Thoughts
Much more beyond basics to explore!
Policy is a substantial factor
  Can we even be independent decisions will be sensible overall?
Other important factors:
  Convergence effects
  How well it scales
  Integration with intradomain routing
  And more …