## Slide 1: Topic
Multiplexing is the network word for the sharing of a resource
Classic scenario is sharing a link among different users
  Time Division Multiplexing (TDM) »
  Frequency Division Multiplexing (FDM) »

## Slide 2: Time Division Multiplexing (TDM)
Users take turns on a fixed schedule
2
2
2
2
Notes: CN5E slides #2-38

## Slide 3: Frequency Division Multiplexing (FDM)
Put different users on different frequency bands
Overall FDM channel
Notes: CN5E slides #2-36

## Slide 4: TDM versus FDM
In TDM a user sends at a high rate a fraction of the time; in FDM, a user sends at a low rate all the time
Rate
Time
FDM
TDM

## Slide 5: TDM versus FDM (2)
In TDM a user sends at a high rate a fraction of the time; in FDM, a user sends at a low rate all the time
Rate
Time
FDM
TDM

## Slide 6: TDM/FDM Usage
Statically divide a resource
  Suited for continuous traffic, fixed number of users
Widely used in telecommunications
  TV and radio stations (FDM)
  GSM (2G cellular) allocates calls using TDM within FDM

## Slide 7: Multiplexing Network Traffic
Network traffic is bursty
  ON/OFF sources
  Load varies greatly over time
Rate
Time
Rate
Time

## Slide 8: Multiplexing Network Traffic (2)
Network traffic is bursty
  Inefficient to always allocate user their ON needs with TDM/FDM
Rate
Time
Rate
Time
R
R

## Slide 9: Multiplexing Network Traffic (3)
Multiple access schemes multiplex users according to their demands – for gains of statistical multiplexing
Rate
Time
Rate
Time
Rate
Time
R
R
R’<2R
Two users, each need R
Together they need R’ < 2R

## Slide 10: Multiple Access
We will look at two kinds of multiple access protocols
Randomized. Nodes randomize their resource access attempts
  Good for low load situations
Contention-free. Nodes order their resource access attempts
  Good for high load or guaranteed quality of service situations

## Slide 11: Topic
How do nodes share a single link? Who sends when, e.g., in WiFI?
  Explore with a simple model
Assume no-one is in charge; this is a distributed system
Notes: Icon from Cisco icon library.

## Slide 12: Topic (2)
We will explore random multiple access control (MAC) protocols
  This is the basis for classic Ethernet
  Remember: data traffic is bursty
Zzzz..
Busy!
Ho hum
Notes: Icon from Cisco icon library.

## Slide 13: ALOHA Network
Seminal computer network connecting the Hawaiian islands in the late 1960s
  When should nodes send?
  A new protocol was devised by Norm Abramson …
Hawaii
Notes: Map from wikipedia commons, public domain. Radio from openclipart.org

## Slide 14: ALOHA Protocol
Simple idea:
  Node just sends when it has traffic.
  If there was a collision (no ACK received) then wait a random time and resend
That’s it!

## Slide 15: ALOHA Protocol (2)
Some frames will be lost, but many may get through…
Good idea?
Notes: From CN5E figures #4-2

## Slide 16: ALOHA Protocol (3)
Simple, decentralized protocol that works well under low load!
Not efficient under high load
  Analysis shows at most 18% efficiency
  Improvement: divide time into slots and efficiency goes up to 36%
We’ll look at other improvements

## Slide 17: Classic Ethernet
ALOHA inspired Bob Metcalfe to invent Ethernet for LANs in 1973
  Nodes share 10 Mbps coaxial cable
  Hugely popular in 1980s, 1990s
: © 2009 IEEE
Notes: Photo from IEEE GHN. Figure from CN5E slides #4-22

## Slide 18: CSMA (Carrier Sense Multiple Access)
Improve ALOHA by listening for activity before we send (Doh!)
  Can do easily with wires, not wireless
So does this eliminate collisions?
  Why or why not?

## Slide 19: CSMA (2)
Still possible to listen and hear nothing when another node is sending because of delay

## Slide 20: CSMA (3)
CSMA is a good defense against collisions only when BD is small
X

## Slide 21: CSMA/CD (with Collision Detection)
Can reduce the cost of collisions by detecting them and aborting (Jam) the rest of the frame time
  Again, we can do this with wires
X X X X X X X X
Jam!
Jam!

## Slide 22: CSMA/CD Complications
Want everyone who collides to know that it happened
  Time window in which a node may hear of a collision is 2D seconds
X

## Slide 23: CSMA/CD Complications (2)
Impose a minimum frame size that lasts for 2D seconds
  So node can’t finish before collision
  Ethernet minimum frame is 64 bytes
X

## Slide 24: CSMA “Persistence”
What should a node do if another node is sending?
Idea: Wait until it is done, and send
What now?

## Slide 25: CSMA “Persistence” (2)
Problem is that multiple waiting nodes will queue up then collide
  More load, more of a problem
Now!
Now!
Uh oh

## Slide 26: CSMA “Persistence” (3)
Intuition for a better solution
  If there are N queued senders, we want each to send next with probability 1/N
Send p=½
Whew
Send p=½

## Slide 27: Binary Exponential Backoff (BEB)
Cleverly estimates the probability
  1st collision, wait 0 or 1 frame times
  2nd collision, wait from 0 to 3 times
  3rd collision, wait from 0 to 7 times …
BEB doubles interval for each successive collision
  Quickly gets large enough to work
  Very efficient in practice

## Slide 28: Classic Ethernet, or IEEE 802.3
Most popular LAN of the 1980s, 1990s
  10 Mbps over shared coaxial cable, with baseband signals
  Multiple access with “1-persistent CSMA/CD with BEB”
Notes: Figure from CN5E slides #4-22

## Slide 29: Ethernet Frame Format
Has addresses to identify the sender and receiver
CRC-32 for error detection; no ACKs or retransmission
Start of frame identified with physical layer preamble
Packet from Network layer (IP)
Notes: Figure derived from CN5E slides #4-23

## Slide 30: Modern Ethernet
Based on switches, not multiple access, but still called Ethernet
  We’ll get to it in a later segment
Switch
Twisted pair
Switch ports
Notes: Figure from CN5E #4-27

## Slide 31: Topic
How do wireless nodes share a single link? (Yes, this is WiFi!)
  Build on our simple, wired model
Send?
Send?
Notes: Icon from Cisco icon library. AP from pixabay.

## Slide 32: Wireless Complications
Wireless is more complicated than the wired case (Surprise!)
  Nodes may have different areas of coverage – doesn’t fit Carrier Sense »
  Nodes can’t hear while sending – can’t Collision Detect »
≠ CSMA/CD
Notes: Icon from Cisco icon library. AP from pixabay.

## Slide 33: Different Coverage Areas
Wireless signal is broadcast and received nearby, where there is sufficient SNR
Notes: CN5E slides #4-18

## Slide 34: Hidden Terminals
Nodes A and C are hidden terminals when sending to B
  Can’t hear each other (to coordinate) yet collide at B
  We want to avoid the inefficiency of collisions
Notes: CN5E slides #4-18

## Slide 35: Exposed Terminals
B and C are exposed terminals when sending to A and D
  Can hear each other yet don’t collide at receivers A and D
  We want to send concurrently to increase performance
Notes: CN5E slides #4-18

## Slide 36: Nodes Can’t Hear While Sending
With wires, detecting collisions (and aborting) lowers their cost
More wasted time with wireless
Time
XXXXXXXXX
XXXXXXXXX
Wireless
Collision
Resend
X
X
Wired
Collision
Resend

## Slide 37: Possible Solution: MACA
MACA uses a short handshake instead of CSMA (Karn, 1990)
  802.11 uses a refinement of MACA (later)
Protocol rules:
  A sender node transmits a RTS (Request-To-Send, with frame length)
  The receiver replies with a CTS (Clear-To-Send, with frame length)
  Sender transmits the frame while nodes hearing the CTS stay silent
  Collisions on the RTS/CTS are still possible, but less likely

## Slide 38: MACA – Hidden Terminals
AB with hidden terminal C
  A sends RTS, to B
D
C
B
A
Notes: CN5E slides #4-18

## Slide 39: MACA – Hidden Terminals (2)
AB with hidden terminal C
  B sends CTS, to A, and C too
D
C
B
A
RTS
Notes: CN5E slides #4-18

## Slide 40: MACA – Hidden Terminals (3)
AB with hidden terminal C
  B sends CTS, to A, and C too
D
C
B
A
RTS
CTS
CTS
Alert!
Notes: CN5E slides #4-18

## Slide 41: MACA – Hidden Terminals (4)
AB with hidden terminal C
  A sends frame while C defers
Frame
Quiet...
Notes: CN5E slides #4-18

## Slide 42: MACA – Exposed Terminals
BA, CD as exposed terminals
  B and C send RTS to A and D
D
C
B
A
Notes: CN5E slides #4-18

## Slide 43: MACA – Exposed Terminals (2)
BA, CD as exposed terminals
  A and D send CTS to B and C
D
C
B
A
RTS
RTS
Notes: CN5E slides #4-18

## Slide 44: MACA – Exposed Terminals (3)
BA, CD as exposed terminals
  A and D send CTS to B and C
D
C
B
A
RTS
RTS
CTS
CTS
All OK
All OK
Notes: CN5E slides #4-18

## Slide 45: MACA – Exposed Terminals (4)
BA, CD as exposed terminals
  A and D send CTS to B and C
D
C
B
A
Frame
Frame
Notes: CN5E slides #4-18

## Slide 46: 802.11, or WiFi
Very popular wireless LAN started in the 1990s
Clients get connectivity from a (wired) AP (Access Point)
It’s a multi-access problem 
Various flavors have been developed over time
  Faster, more features
Access Point
Client
To Network
Notes: CN5E slides #4-32

## Slide 47: 802.11 Physical Layer
Uses 20/40 MHz channels on ISM bands
  802.11b/g/n on 2.4 GHz
  802.11 a/n on 5 GHz
OFDM modulation (except legacy 802.11b)
  Different amplitudes/phases for varying SNRs
  Rates from 6 to 54 Mbps plus error correction
  802.11n uses multiple antennas; see “802.11 with Multiple Antennas for Dummies”
Notes: Figure from CN5E slides #4-22

## Slide 48: 802.11 Link Layer
Multiple access uses CSMA/CA (next); RTS/CTS optional
Frames are ACKed and retransmitted with ARQ
Funky addressing (three addresses!) due to AP
Errors are detected with a 32-bit CRC
Many, many features (e.g., encryption, power save)
Packet from Network layer (IP)
Notes: CN5E slides #4-38

## Slide 49: 802.11 CSMA/CA for Multiple Access
Sender avoids collisions by inserting small random gaps
  E.g., when both B and C send, C picks a smaller gap, goes first
Time
Send?
Send?

## Slide 50: The Future of 802.11 (Guess)
Likely ubiquitous for Internet connectivity
  Greater diversity, from low- to high-end devices
Innovation in physical layer drives speed
  And power-efficient operation too
More seamless integration of connectivity
  Too manual now, and limited (e.g., device-to-device)